## Slide 1
31/07/26
MBA 12/08
Density of a regular solid
Method
Measure mass using a balance
Measure width, length and height using a ruler
Calculate volume ( V = w x l x h )
Calculate density ( ρ = m / V )
Results
m = ______ g
w = ______ cm; l = ______ cm; h = ______ cm
V = w x l x h = ___ x ___ x ___ = _____ cm3
ρ = m / V = ___ / ___ = _____ g/cm3
Notes: <number>

## Slide 2
31/07/26
MBA 12/08

## Slide 3
31/07/26
MBA 12/08
Density of a liquid
Method
Measure mass of empty measuring cylinder using a balance
Measure mass of liquid and measuring cylinder
Subtract 1 from 2 to calculate the mass of the liquid
Measure volume of liquid by using the measuring cylinder (Note: measure to the bottom of the meniscus)
Calculate density ( ρ = m / V )
Results
mcylinder= ______ g
mcylinder+liquid= ______ g
mliquid = mcylinder+liquid – mcylinder = ____ - ____ = ____ g
V = ______ ml = _____ cm3
ρ = m / V = ___ / ___ = _____ g/cm3
Notes: <number>

## Slide 4
31/07/26
MBA 12/08
So now you’ve measured the density of water and oil, predict whether oil will float or sink in water.
How about wood in water?
How about aluminium in water?
How about steel in mercury?
Notes: <number>

## Slide 5
31/07/26
MBA 12/08
Density of an irregular solid
Method
Measure mass using a balance
Measure volume by using the “displacement” method (submerge solid in a “Eureka” can and collect the overflow in a measuring cylinder)
Calculate density ( ρ = m / V )
Results
m = ______ g
V = _____ cm3
ρ = m / V = ___ / ___ = _____ g/cm3
Notes: <number>