## Slide 1
30. Juli 2026
MBA 12/08
Pressure Calculations – Model Answers
3. p = F / A
100,000 = F / 10
F = 1,000,000 N or 1,000 kN or 1MN
Something to think about:
This is a huge force. It’s about the same as 1,000 fat people standing on the wall. So why doesn’t the wall fall over?
Answer on the next slide!
Notes: <number>

## Slide 2
30. Juli 2026
MBA 12/08
Pressure Calculations – Model Answers
Explanation:
The reason that the wall doesn’t fall over is because there’s exactly the same force acting on the other side of the wall, so the two forces cancel out.
If you removed the force from the other side of the wall by removing the air (creating a vacuum) then the 1,000,000N force would knock the wall down!
Notes: <number>

## Slide 3
30. Juli 2026
MBA 12/08
Pressure Calculations – Model Answers
7. a. p = F / A
p = 500 / 5
p = 100 N/cm2
Or A = 5cm2 = 5 / 10,000 = 0.0005m2
p = F / A
p = 500 / 0.0005
p = 1,000,000Pa or 1,000 kPa
Notes: <number>

## Slide 4
30. Juli 2026
MBA 12/08
Pressure Calculations – Model Answers
Note - the pressure in both pistons is the same (see objective 5.5!)
7. b. p = F / A
100 = F / 20
F = 2,000N or 2kN
Or A = 20cm2 = 20 / 10,000 = 0.002m2
p = F / A
1,000,000 = F / 0.002
F = 2,000N or 2kN
.
Notes: <number>