## Slide 1
Long Chain Hydrocarbons have limited use
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C16H34
Present in paraffin, fuel oil and diesel

## Slide 2
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C16H34
They could be made more useful by breaking the chains into shorter lengths

## Slide 3
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C16H34
They could be made more useful by breaking the chains into shorter lengths
The two fragments formed are not stable molecules and must rearrange.

## Slide 4
Cracking: breaking long chains into shorter ones
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C11H24
C16H34
C5H10

## Slide 5
C
C
C
C
C
One of the molecules has insufficient H atoms to form an alkane

## Slide 6
C
C
C
C
C
Molecules of C and H with C=C bonds are called alkenes

## Slide 7
C
C
C
C
C
Molecules of C and H with C=C bonds are said to be unsaturated because they will react with hydrogen gas

## Slide 8
C
C
C
C
C
C
C
C
C
C
C
Molecules of C and H with no C=C bonds are said to be saturated because they will not react with hydrogen gas

## Slide 9
C
C
C
C
C
C
C
C
C
C
C
Alkanes are saturated
C
C
C
C
C
Alkenes are unsaturated

## Slide 10
Cracking in the Laboratory
Cracking is achieved by passing the vapour of the alkane over a heated catalyst: aluminium oxide or porous pot fragments are often used.

## Slide 11
Cracking in the Laboratory
Note that although the paraffin that is being cracked is liquid, one of the products is a gas.

## Slide 12
The breaking of the bonds is random, so a mixture of alkanes and alkenes results.
Write equations that would represent cracking of:
C20H42
C24H50

## Slide 13
Go to Cracking animation
Industrial Cracker Unit

## Slide 14: Summary Cracking is useful because:
It produces light, valuable fractions such as petrol from heavy less valuable fractions
It is a useful source of alkenes
Alkenes are used to make polymers and other useful chemicals

## Slide 15: Summary Cracking conditions in laboratory:
Heat liquid alkane
Pass vapour over heated catalyst
Catalyst is aluminium oxide or porous pot
Collect gases formed over water
Liquid product condense in water and can be separated

## Slide 16: Summary Cracking conditions in industry:
Vapourise heavy fractions
Mix vapour with hot zeolite catalyst
Gaseous products separate
Catalyst becomes covered in carbon
Catalyst is heated to clean it
Catalyst then recycled
Hydrocarbon products separated by fractional distillation