## Slide 1: Model Answers
29/07/26
MBA 03/10
Question 1a
Formula Q = I x t 1 mark
Substitution Q = 4 x 20 1 mark
Answer+Units Q = 80C 2 marks
Question 1b
Formula Q = I x t 1 mark
Substitution 100 = I x 10 1 mark
Answer+Units I = 10A 2 marks

## Slide 2: Model Answers
29/07/26
MBA 12/08
Question 1c
Formula Q = I x t 1 mark
Substitution Q = 2 x (2 x 60) 1 mark
Answer+Units Q = 240C 2 marks

## Slide 3: Model Answers
29/07/26
MBA 12/08
Question 2a
Formula E = V x Q 1 mark
Substitution E = 10 x 5 1 mark
Answer+Units E = 50J 2 marks
Question 2b
Formula E = V x Q 1 mark
Substitution 30 = 6 x Q 1 mark
Answer+Units Q = 5C 2 marks

## Slide 4: Model Answers
29/07/26
MBA 12/08
Question 3a
Formula E = V x I x t 1 mark
Substitution E = 5 x 2 x 10 1 mark
Answer+Units E = 100J 2 marks
Question 3b
Formula E = V x I x t 1 mark
Substitution 200 = V x 2 x 100 1 mark
Answer+Units V = 1V 2 marks

## Slide 5: Model Answers
29/07/26
MBA 12/08
Question 4a
Formula V = I x R 1 mark
Substitution 6 = I x 3 1 mark
Answer+Units I = 2A 2 marks
Question 4b
Formula Q = I x t 1 mark
Substitution Q = 2 x 100 1 mark
Answer+Units Q = 200C 2 marks

## Slide 6: Model Answers
29/07/26
MBA 12/08
Question 4c
Formula E = V x I x t 1 mark
Substitution E = 6 x 2 x 100 1 mark
Answer+Units E = 1200J or 1.2kJ 2 marks
or
Formula E = V x Q 1 mark
Substitution E = 6 x 200 1 mark
Answer+Units E = 1200J or 1.2kJ 2 marks

## Slide 7: Model Answers
29/07/26
MBA 12/08
Question 5a
Formula V = I x R 1 mark
Substitution V = 2 x 5 1 mark
Answer+Units V = 10V 2 marks
Question 5b
Formula Q = I x t 1 mark
Substitution Q = 2 x (5 x 60) 1 mark
Answer+Units Q = 600C 2 marks

## Slide 8: Model Answers
29/07/26
MBA 12/08
Question 5c
Formula E = V x I x t 1 mark
Substitution E = 10 x 2 x (5 x 60) 1 mark
Answer+Units E = 6000J or 6kJ 2 marks
or
Formula E = V x Q 1 mark
Substitution E = 10 x 600 1 mark
Answer+Units E = 6000J or 6kJ 2 marks

## Slide 9: Model Answers
29/07/26
MBA 12/08
Question 5d
Energy comes from Chemical Potential Energy of the battery
Transferred to thermal energy in the resistor
The resistor heats up