## Slide 1
Securing Real-Time Distributed LVC Simulations at Scale with Data Distribution Service TM (DDS)
Presenter 1, Rob Proctor/Real-Time Innovations
Presenter 2, Dan King/Real-Time Innovations

## Slide 2: Agenda
Intro to Data Distribution Service (DDS), Object Management Group (OMG) Standard
  What it is, what it does, how it came to be
  DDS is ‘under the hood’ of many standards
  RTPS wire protocol, DCPS API, Quality of Service
Intro to DDS Secure, OMG Standard
  Authentication, Role Based Access Control, Encryption, Data Tagging and Event Logging
  Securing individual data topics
Examples of securing real-time distributed LVC simulations with DDS
DDS within Simulation Interoperability Standards Organization (SISO)
  Common Image Generator Interface (CIGI)
  Layered Simulation Architecture (LSA)
Notes: Tutorial Title: (10 words or less)
Securing Distributed LVC Simulations with Data Distribution Service (DDS)
Abstract: (400 words or less)
Integrating simulation and training systems is hard. Legacy systems use differing standards for data, voice, and video. Modern architectures demand the use of cloud-based and distributed assets. New security requirements challenge integrators to become experts in information assurance. While these challenges drive integration time up, meeting today’s emerging threats requires training environments that can be quickly assembled and reconfigured from ready-made components. Attend this tutorial to learn how Data Distribution Service (DDS) eases integration while providing NSA-tested security in real-time systems.
The Data Distribution Service (DDS) is an open standard managed by the Object Management Group. DDS is the connectivity framework that successfully meets the stringent interoperability and real-time requirements of the defense industry in hundreds of deployed systems. DDS seamlessly stitches together legacy simulations while adding humans and hardware in the loop to create new secure live, virtual, and constructive environments sharing real, augmented, and virtual realities. These run in a single lab or across multiple sites while matching physics-speed response times.
This tutorial gives an introduction to the DDS and DDS Secure standards. You will learn how to use DDS Secure to secure real-world Hardware-In-Loop (HIL) systems that already communicate over DDS to distributed Live, Virtual, Constructive (LVC) Simulations. The tutorial will describe how to integrate DDS with existing simulation-based standards such as HLA and DIS while adding robust security. Finally, the tutorial will provide some recent experiences of the use of DDS in NATO M&S groups and an overview of deployed systems using DDS today. This tutorial is intended for all audiences; however, some familiarity with basic principles of distributed computing is recommended.

## Slide 3: Tutorial Learning Objectives
After taking this tutorial you should be able to:
Describe the DDS standard
Explain the principles of the DDS Secure standard for securing communications between distributed simulations over WAN/Cloud/RF/Lossy networks
Explain how DDS works with the simulation architectures TENA, HLA and DIS
Summarize how DDS works with real-world Hardware In the Loop (HIL) for secure distributed LVC simulations at scale
Describe how DDS is working within SISO

## Slide 4: The OMG Data Distribution Service Standard
From OMG, systems software standards organization
  UML, XML, IDL, CORBA, DDS
  Standard can be downloaded for free by anyone
  More than a dozen commercial implementations available
First version of the DDS standard was released in 2004
  Most recent updates were May 2019
A family of 13 standards covering API, wire protocol, security, type evolution, etc.

## Slide 5
The OMG Data Distribution Service Standard
DDS is a standard for data-centric connectivity and interoperability for real-time systems
Data-Centric Publish-Subscribe model for distributed application communication and integration
Standardizes wire protocol, serialization format and API
DDS is open and multi-vendor
  Open Standard and Open Source
  12+ implementations
Interoperability between source written for different vendors
Interoperability between applications running on different implementations
DDS APIs: Data Centric Publish Subscribe (DCPS)
Distribution Fabric
Real-Time Publish Subscribe
Wire Protocol (RTPS)
DDS Security
Plug-In
QoS
QoS
QoS

## Slide 6: The OMG Data Distribution Service Standard
DDS is Publish-Subscribe, Data-Centric and Peer-to-Peer
  DDS also supports request-reply patters: Multiple Replies, Multiple Repliers
Designed for real-time mission critical and safety critical systems
  Started in Robotics and SW Defined Radios using Tactical Data Links
  Navy wanted it turned into an open standard, it now ‘floats the Navy’
DDS applications share large amounts of data quickly, securely and reliably at massive scale
DDS provides location transparency, decentralized operation, dynamic scalability and real-time performance
  Every DDS Vendor will tell you why theirs is the fastest
Its widespread use in distributed real-time military systems has led to strong interest in the modeling, simulation and training community

## Slide 7: The OMG Data Distribution Service Standard
Data-centric design that simplifies application development
  The interface is the DATA, not in worrying about messages
Strongly typed, loosely coupled and extensible
  Can easily take DIS PDUs or TENA / HLA FOMs and convert them to DDS Topics
  Programming language / Operating System independent
DDS Secure has been vetted at the Cybersecurity Warfare ranges at Quantico, VA and Orlando, FL
  USAF has funded a SBIR project for Multi-Level Security for LVC simulations
DDS is a natural fit for Multi-Domain Operations systems
  Joint Battle Command Platform (JBC-P)
  Integrated Air and Missile Defense Battle Control System (IBCS)
  Cooperative Engagement Capability (CEC)
  Universal Ground Control Station (UGCS)
  All branches of the military, including Space Force, use DDS

## Slide 8: That’s nice, but

## Slide 9: But Why?
Ok, so what? That sounds a little like the ‘big three’ simulation interoperability standards. Dr. Powell is right…
  Yes, it is Pub/Sub
  But DDS has no data model of simulation entities; No FOMs or PDUs here
So if DDS is not a simulation interoperability standard, what is it?
  An interoperability framework for Real-Time systems
  That uses the notion of a logical software-based Databus
  DDS supports ANY data model
  In fact the DDS connectivity framework is something that you build upon when you set out to create a new interoperability standard based on an industry-specific data model
  The result is that DDS underpins a lot of familiar standards…

## Slide 10: DDS is under the hood of many standards
Standard | Industry
Advanced Modular Mannequin (AMM) | Simulation / Healthcare
ALert MAnagement Service (ALAMS) | Defense
Application Management and Systems Monitoring (AMSM) | Defense
Future Airborne Capabilities Environment (FACE) | Defense
Generic Vehicle Architecture (GVA) NATO Generic Vehicle Architecture (NGVA) | Defense
Land Open Systems Architecture (LOSA) | Defense
Medical Simulation Training Architecture (MSTA) | Simulation / Healthcare
Open Field Message Bus (OpenFMB) | Power / Energy
Open Mission Systems (OMS) | Aerospace
Open Process Automation Forum (OPAF) | Process Automation
Standard | Industry
Open Robotics Robotic Operating System v2 (ROS2) | Horizontal / Robotics
Sensor Open System Architecture (SOSA) | Defense
Tactical Microgrid Standards Consortium (TMSC) | Energy
Unmanned Systems (UxS) Control Segment (UCS) Architecture | Defense
Unmanned Systems (UxS) Control Segment (UCS) Architecture | Defense / Aerospace
Joint Architecture for Unmanned Systems (JAUS) | Defense / Robotics
Naval Open Systems Architecture (OSA) | Defense
Control Architecture for Robotic Agent Command and Sensing (CARACaS) | Aerospace / Robotics
Multi-Robot Operator Control Unit (MOCU) | Aerospace / Robotics
Unmanned Maritime Autonomy Architecture (UMAA) | Defense / Robotics

## Slide 11: Why is DDS so widely used ‘under the hood’ for these standards?
Well, consider these guys…
HTTP – universal transport
REST – universal API
  Used together they build the vast majority of web-based applications
  Good for human speed, but tends to be 1-1; you connect to the bank, email, website, etc.
But what about real-time applications?
  And what about live real-time systems that might be:
    1 to many
    many to 1
    many to many
    with real-time speeds and security requirements

## Slide 12: DDS is made for real-time interoperability
DDS defines
  Open API for portability
  Open wire protocol for interoperability
    Transport agnostic
  Open explicit defined QoS and discovery
    Highly configurable
Multiple language bindings
  C, C++, Java, C# .NET, Ada
  LabView, Matlab/Simulink
  Python, NodeJS
Multi platform support
  Windows, Linux, Unix, embedded OS, Docker, Kubernetes
DDS Middleware
Operating System
UDP
TCP
Shmem
Qs/ports
Application
Standard API
Standard Protocol

## Slide 13: Data-Centric Publish Subscribe
Global Data Space
DDS Databus
Reliable
100 Hz
Altitude < 5000 ft
Reliable
25 Hz
Best effort
2x / Sec
Sensor | 
Source** | string
Speed | float
Altitude | float
Actuator | 
Id** | string
Command | string
Status | float

## Slide 14: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Notes: Introduction to definitions

## Slide 15: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Domain
Notes: Introduction to definitions

## Slide 16: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Topic
Notes: Introduction to definitions

## Slide 17: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
  Key is a generalization of subject
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Key (subject)
Notes: Introduction to definitions

## Slide 18: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
  Key is a generalization of subject
  Instance individual update
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Instance
Notes: Introduction to definitions

## Slide 19: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
  Key is a generalization of subject
  Instance individual update
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
YQC 4149 | 68 | 48% | 28.3903, -81.5141
Notes: Introduction to definitions

## Slide 20: DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
  Key is a generalization of subject
  Instance individual update
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
YQC 4149 | 68 | 48% | 28.3903, -81.5141
YQC 4149 | 70 | 47% | 28.4118, -81.4802
Notes: Introduction to definitions

## Slide 21: DDS Data Centric Publish Subscribe API
The DDS API lets applications publish data to, and subscribe to data from the DDS Databus
This DDS API is called Data Centric Publish Subscribe (DCPS)
The API is standardized in the DDS v1.4 standard, as a “Platform Independent Model” (PIM)
API operations are mapped to different languages through a “Platform Specific Model” (PSM)
The DCPS API is divided up into “entities” (way different than a simulation entity) which allow an application to:
  connect to the DDS Databus
  create topics
  get notified of infrastructure-level events (new subscriber, new publisher, …)
  publish and subscribe to application data
Each DDS entity has a set of QoS settings that determine the behavior of the entity

## Slide 22: DDS Publish Subscribe API: Entities
Create & manage connection to DDS Databus
DomainParticipant

## Slide 23: DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Create a proxy to a topic in the application
<< creates >>

## Slide 24: DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Manages group of DataWriters
Publisher
Subscriber
Manages group of DataReaders
<< creates >>
<< creates >>
DataWriter
DataReader
<< creates >>
<< creates >>

## Slide 25: DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Publisher
Subscriber
DataWriter
DataReader
<< uses >>
<< uses >>
Publishes data to DDS Topic
Subscribes to data from DDS Topic
<< creates >>
<< creates >>

## Slide 26: DDS Publish Subscribe API: Entities
DataReaders (DRs) and DataWriters (DWs) are strongly typed
Their APIs are generated from IDL
struct ShapeType {
string<128> color;
long x;
long y;
long shapesize;
};
ShapeTypeDataWriter_write
ShapeTypeDataWriter_dispose
ShapeTypeDataReader_read
ShapeTypeDataReader_take

## Slide 27: DDS Topic Data Types
struct MyType {
long sensorID; //@Key
long plantID; // @Key
float sensorVal0;
float sensorVal1;
float sensorVal2;
float sensorVal3;
float sensorVal4;
Version version;
Time currentTime;
}
struct Version {
string firmwareVersion;
string hardwareVersion;
string modelNumber;
string serialNumber;
}
Strongly Typed

## Slide 28: DDS Topic Data Types
struct MyType {
long sensorID; //@Key
long plantID; // @Key
float sensorVal0;
float sensorVal1;
float sensorVal2;
float sensorVal3;
float sensorVal4;
Version version;
Time currentTime;
}
struct Version {
string firmwareVersion;
string hardwareVersion;
string modelNumber;
string serialNumber;
}
Strongly Typed
struct MyType {
string data;
}
Where data =
<SENSOR>
<SensorID>438</SensorID>
<PlantID>192</PlantID>
<Value0>21.0546</Value0>
<Value1>43.6</Value0>
<Value2>56.34</Value0>
<Value3>12.11</Value0>
<Value4>20.00</Value0>
<firmware>1.24b</firmware>
<hardware>2.39</hardware>
<model>M56A743</model>
<serial>1429709<serial>
</SENSOR>
Loosely Typed

## Slide 29: DDS Topic Data Types
struct MyType {
long sensorID; //@Key
long plantID; // @Key
float sensorVal0;
float sensorVal1;
float sensorVal2;
float sensorVal3;
float sensorVal4;
Version version;
Time currentTime;
}
struct Version {
string firmwareVersion;
string hardwareVersion;
string modelNumber;
string serialNumber;
}
Strongly Typed
struct MyType {
string data;
}
Where data =
<SENSOR>
<SensorID>438</SensorID>
<PlantID>192</PlantID>
<Value0>21.0546</Value0>
<Value1>43.6</Value0>
<Value2>56.34</Value0>
<Value3>12.11</Value0>
<Value4>20.00</Value0>
<firmware>1.24b</firmware>
<hardware>2.39</hardware>
<model>M56A743</model>
<serial>1429709<serial>
</SENSOR>
Loosely Typed
struct MyType {
long sensorID; //@Key
long plantID; // @Key
string data;
string version;
}
Where data =
<SENSOR>
<Value0>21.0546</Value0>
<Value1>43.6</Value0>
<Value2>56.34</Value0>
<Value3>12.11</Value0>
<Value4>20.00</Value0>
</SENSOR>
version =
<VERSION>
<firmware>1.24b</firmware>
<hardware>2.39</hardware>
<model>M56A743</model>
<serial>1429709<serial>
</VERSION>
Mixed Type

## Slide 30: Data Type Extensibility
struct Track {
long id; //@key
float range;
float bearing;
}
struct AirTrack {
long id; //@key
float range;
float bearing;
float elevation;
}
struct Track {
long id; //@key
float range;
float bearing;
}
struct AirTrack {
long id; //@key
float elevation;
}
struct Track {
long id; //@key
float range;
float bearing;
}
Final Type
  Type definitions are strictly defined
Extensible Type
  Newer applications can add fields to existing base types
Mutable Type
  Type representations can differ from each other with Additions, Deletions and Transpositions
  Support for Optional Fields
struct Track {
long id; //@key
float range;
float bearing;
}

## Slide 31: Simple API Interface
void publisher_main(int domain_id) {
// Initialize
dds::domain::DomainParticipant participant (domain_id);
// Create a Topic
dds::topic::Topic<dds::core::StringTopicType> topic (participant, "MyTopic");
// Create a Data Writer
dds::pub::DataWriter<dds::core::StringTopicType> writer(dds::pub::Publisher(participant), topic);
// Create some data
dds::core::StringTopicType sample("Hello World");
// Write the data
writer.write(sample);
}

## Slide 32: Common Distributed Application Challenges
1-1, 1-Many
No Reliability
1 to 1
Reliability
Transport
Flow Control
UDP
TCP
Deadine
Reliability
History
Liveliness
Time Based Filter
Batching
Durability
Ownership
Partition
Presentation
Lifespan
In-Order Delivery
Resource Limits
Latency Budget
Flow Control
User, Group, Topic Data
Content Filtering
Transports
Multi-Channel
Async Publisher
DDS QoS Features

## Slide 33: Using DDS QoS to Shape Data Flow
Discovery matches publishers and subscribers of a topic
Topics tied to Data type, allowing smarter databus
Quality of Service describing application data needs must be compatible to communicate
Specifying and relying only on these data properties enables decoupled, resilient systems
Subscriber
Subscriber
Subscriber
Collision avoidance application
Radar Track
Topic
Publisher
Reliable; 1 Hz; get history
Best effort; 0.2 HZ; get history
ATC Sim
Nearby tracks with altitude < 5000m
Publish reliably
10 Hz
600 sample history
NOC Sim

## Slide 34: Content Filtered Topics
The Filter Expression and Arguments will determine which instances of the Topic will be received by the subscriber

## Slide 35: DDS Publish Subscribe API: QoS conflicts
DataWriter
The DataReader and DataWriter QoS must match if connectivity is to be established
QoS does not need to be equal. It is ok if a DataWriter offers “more” than what a DataReader asks for
    Example: DW = Reliable, DR = Best Effort
DataReader
DataReader
BEST EFFORT
BEST EFFORT
RELIABLE

## Slide 36: OMG DDS Security Standard
OMG released the DDS Security specification (v1.1) in July 2018
Collaboratively developed by several DDS vendors
Defines:
  DDS Security Model
  Service Plugin Interface (SPI) Architecture

## Slide 37: Practical Security Needs Many Layers
DDS Security
System edge
Host
  Machine/OS/Applications/Files
Network transport
  Media access (layer 2)
  Network (layer 3)
  Session/Endpoint (layer 4/5)
Dataflow
  Control application interaction
Secure systems need all four

## Slide 38: DDS: Data-Centric, Fine-Grained Security
Per-Data-Topic Security
  Control r,w access for each function
  Ensures proper dataflow operation
Complete Protection
  Discovery authentication
  Data-centric access control
  Cryptography
  Tagging and logging
  Non-repudiation
  Secure multicast
  100% standards compliant
Operator
Fire
Data Topics
Applications
Control
Visualize
Simulate
BaseEntity
Detonation
Data Topic Security model:
Simulate: Fire(r), BaseEntity(w)
Visualize: BaseEntity(r), Detonation(w)
Control: BaseEntity(r), Fire(w)
Operator: *(r), Fire(w)

## Slide 39: Pluggable Architecture
Requires trivial or no change to existing DDS apps and adapters
Includes default plugins; customizable
Runs over any transport
  Including low bandwidth, unreliable
  Does not require TCP or IP
  Multicast for scalability, low latency
Completely decentralized
  High performance and scalability
  No single point of failure
Secure DDS Library
Authentication
Access Control
Encryption
Logging
Application
Any Transport (e.g., TCP, UDP, multicast, shared memory…)
Data Tagging

## Slide 40: Standard Capabilities (Built-in Plugins)
Authentication | X.509 Public Key Infrastructure (PKI) with a pre-configured shared Certificate Authority (CA) Digital Signature Algorithm (DSA) with Diffie-Hellman and RSA for authentication and key exchange
Access Control | Configured by domain using a (shared) Governance file Specified via permissions file signed by shared CA Control over ability to join systems, read or write data topics
Cryptography | aes-128-ctr for encryption HMAC-SHA256 for message authentication and integrity aes-128-gcm, aes-192-gcm and aes-256-gcm for encryption with authentication Certicom and Windows CNG for FIPS 140-2
Logging | Log security events to a file or distribute securely over DDS
Data Tagging | Tags specify security metadata, such as classification level Can be used to determine access privileges (via plugin)

## Slide 41: Configuring & Deploying DDS Security
Domain Governance
Document
Identity CA Certificate
Permissions CA Certificate
P2 Identity Certificate
P2 Private Key
P2
P2 Permissions File
P1 Identity Certificate
P1 Private Key
P1
P1 Permissions File
Shared By All Participants

## Slide 42: Domain Governance File
The domain governance document is an XML document that specifies which DDS domain IDs shall be protected and the details of the protection
It is signed by the permissions CA

## Slide 43: A Sample Governance File

## Slide 44: Configuration Possibilities
Are “legacy” or un-identified applications allowed in the Domain?
  If yes, an unauthenticated application will:
    See the “unsecured” discovery Topics
    Be allowed to read/write the “unsecured” Topics
Is a particular Topic discovered over protected discovery?
  If so, it can only be seen by “authenticated applications”
Is access to a particular Topic protected?
  If so, only authenticated applications with the correct permissions can read/write
Is data on a particular Topic protected? How?
  If so, data will be sent signed or encrypted then signed
Are all protocol messages signed? Encrypted?
  If so, only authenticated and authorized applications will see anything

## Slide 45: Permissions Document
For each participant, specifies:
  What domains it can join
  What Topics it can read/write
  What Tags are associated with Readers & Writers

## Slide 46: A Sample Permissions File

## Slide 47: Using DDS with distributed LVC simulations
Can leverage/ integrate existing system software
  Hundreds of DoD systems (Navy, Air, Army) already being built using DDS
    DDS is mandated by Navy OA for combat management systems
    DDS specified by US DoD for the unmanned vehicle control (OSD-UCS)
    DDS specified by UK-MOD for army vehicle communications
With DDS, simulation systems could easily reuse and integrate software components from actual systems
  This has already been happening for years

## Slide 48: DDS in Simulation: JMETC

## Slide 49: Securing distributed LVC simulations with DDS
Can leverage/integrate mission data
  Recorded data from actual mission execution could be combined with simulation data and be used for training
    This approach is already followed in the US Navy OATM
  Rapid feedback from mission to training is key to an agile and effective force.
Can leverage/integrate DDS Security into new distributed simulations
  Secure training and simulations over WAN/Cloud/RF/Lossy Networks/TDL
  Role-based access allow for joint Coalition forces to train alongside US forces
  Multiple SBIRs with different defense agencies for secure LVC simulations

## Slide 50: USAF Live Mission Operations Capability (LMOC) Multi Level Secure (MLS) capability for LVC Simulations

## Slide 51: Global Connectivity for USAF Training Simulations

## Slide 52: Missile Defense Agency – Objective Simulation Framework
Fully Distributed, Real-Time,
Secure Cyber Situational Awareness for MDA OSF

## Slide 53: Mixed-Reality Wargaming Platform
Cloud
Real World Twin
Management
Logging
Analytics
Secure Global DDS Databus
Secure
Gateway
Secure Cross-System DDS Databus (Local/Regional)
Simulation DataBus
Simulation DataBus
Simulation Connext DataBus
Sim@ SOCOM
DataBus
Gateway
Sim@ NATO 1
Sim@ NATO 2
Management
Logging
Analytics
One World
Terrain
Protocol/Data Interoperability
Data Routing/Filtering
Other
Services
A Hierarchical, Loosely-Coupled Design Enables:
Local Ownership
Disconnected Operation
Open Architecture
Capability-as-a-Service
  e.g., AI, Simulation, Data, Devices
AI/ML/DL
Augmented
Reality
Autonomous Systems
Maritime
Air
Helo
Ground
AI Training
Scenarios
Unity
Unreal
OtherSim
Local Mgmt
Simulated Worlds
Real World
Digital
Twins
Simulated
Actors
Edge
Processing Location Agnostic / Transparent
Protocol
Gateway
Protocol XYZ
DDS

## Slide 54: CCDC Aviation & Missile Center - SED System Integration Labs
Hardware-in-the-Loop labs for the UH-60V, CH-47F and AH-64E Army Helicopters

## Slide 55: CCDC AvMC S3I - Apache AH-64E
Database
DDS
Flight Model
LabVIEW
RadAlt Model
ADC Model
EGI Model
Aberdeen I/O
Data Record /
Playback
Data Analysis
Workstation
Visuals
Visuals
Image Generators
Flight
Controls
HAT/HOT
Science
Experiments
TBD

## Slide 56: PEO Aviation - Combat Aviation Brigade Architecture Integration Lab (CABAIL)
AH-64E and CH-47F SILs already use DDS to reduce hardware and development costs for HIL experimentation
JBC-P Network Operations Center(NOC) was re-architected using DDS for significant code reduction and performance improvement

## Slide 57: Using DDS with Simulation Standards
The DDS specification has been be leveraged for the middleware APIs as well as the wire protocol
  APIs could use the DDS API
  Wire protocol communications could use the Interoperability Wire protocol from DDS
  This combination would leverage the performance, scalability, robustness and interoperability from DDS.
The simulation entities from TENA/HLA/DIS could be leveraged
  They would provide the “entity data model dictionary”
  This would leverage the conventions and semantics of the simulation standards
The simulation defined types could be described using the DDS Extensible Types
  This leverages the extensibility, dynamic APIs and backwards compatible path to type evolution of the DDS Type system
Gateways/brokers exist
  HLA-RTI provider supports multiple DDS Vendors

## Slide 58: SISO CIGI and DDS
Common Image Generator Interface (CIGI) is an on-the-wire data protocol that allows communication between an Image Generator and its host simulation
The interface is designed to promote a standard way for a host device to communicate with an image generator (IG) within the industry
“CIGI Next” now rebranded as the Synthetic Environment Generation Interfaces (SEGI) is considering using DDS as a transport
  Could eliminate the need for hosts, you would communicate directly to the IG
  Please join the SISO CIGI PDG!

## Slide 59: DDS ‘Under the hood’ at SISO?
Layered Simulation Architecture
  Study Group at SISO
  Putting DDS ‘under the hood’ of HLA/DIS
    Use DDS RTPS with Simulation Entities as topics
  Study Group recommended that LSA become a SISO standard; stalled at that point
Need a collation of the willing to revive this
  Open source prototype would be needed
  DDS Secure was not considered at the time of this study group, but could easily be added and add much needed security to the Simulation standards

## Slide 60: DDS with MOSA Requirement
Tri-Service acquisition memorandum signed by the Secretaries of the U.S. armed services – directed using Modular Open Systems Approach (MOSA)
Specifically cites standards
  Sensor Open Systems Architecture (SOSA)
  Open Mission Systems/Universal Command and Control Interface (OMS/UCI)
  Future Airborne Capability Environment (FACE)
  Vehicular Integration for C4ISR/EW Interoperability (VICTORY)
  …“as vital to our success”
DDS is certified conformant and/or aligned to every standard called out in the provided memorandum

## Slide 61: Conclusions
DDS is a mature standard from OMG
  Platform neutral: Operating Systems and Programming Languages
  Mandated and deployed worldwide in military systems with demanding real-time applications
  Portable API DCPS and Interoperable Wire Protocol RTPS
  Deployed DDS Security Standard specification
DDS focuses on efficient data-distribution for real-time & high-performance systems
DDS is suited for integration of distributed training systems that have security requirements
  Authentication, Role-Based Access to data, Multiple Levels of Security (MLS)
  Evolvable Type System
  Real-Time Quality of Service (QoS)
  Eases integration and reuse of system software and mission data

## Slide 62: Original Tutorial Learning Objectives
After taking this tutorial you should be able to:
Describe the DDS standard
Explain the principles of the DDS Secure standard for securing communications between distributed simulations over WAN/Cloud/RF/Lossy networks
Explain how DDS works with the simulation architectures TENA, HLA and DIS
Summarize how DDS works with real-world Hardware In the Loop (HIL) for secure distributed LVC simulations at scale
Describe how DDS is working within SISO