## Slide 1
Securing Real-Time Distributed LVC Simulations at Scale with Object Management Group (OMG) Data Distribution Service TM (DDS)
Presenter 1, Rob Proctor/Real-Time Innovations
Presenter 2, Dan King/Real-Time Innovations

## Slide 2: Agenda
Introduction to Interoperability and Interconnectivity
  What are the different levels of interoperability
  What are the requirements for semantic interoperability
Intro to Data Distribution Service (DDS) an Object Management Group (OMG) Standard
  The history and makeup up the OMG DDS standards
  How OMG DDS is a data-centric publish-subscribe protocol
  How do the features of OMG DDS provide interoperability within and between systems, including APIs, Quality of Service (QoS), Discovery, and Wide Area Network (WAN) connectivity
Intro to OMG DDS Secure, OMG Standard
  Authentication, Role-Based Access Control, Encryption, Data Tagging, and Event Logging
  Fine-grained security configuration including securing individual data topics
Examples of securing real-time distributed LVC simulations with OMG DDS
OMG DDS within Simulation Interoperability Standards Organization (SISO)
  Common Image Generator Interface (CIGI)
  Layered Simulation Architecture (LSA)

## Slide 3: Tutorial Learning Objectives
After taking this tutorial you should be able to:
Understand the different layers of interoperability
Describe the OMG DDS standard
Explain the principles of the OMG DDS Secure standard for securing communications between distributed simulations over WAN/Cloud/RF/Lossy networks
Explain how OMG DDS works with the simulation architectures TENA, HLA and DIS
Summarize how OMG DDS works with real-world Hardware In the Loop (HIL) for secure distributed LVC simulations at scale
Describe how OMG DDS is working within SISO

## Slide 4: Levels of Interoperability
Shared data context
Shared data structure
Shared opaque data
Notes: IIRA defines: Connectivity = Infrastructure for Communications Interoperability
Example: Two people are integrable (level 1) if both are able to speak and listen; interoperable (level 2) if they speak the same language; and composable (level 3+) if they share similar educational background so that enables them to collaborate on specific tasks.
Syntactic interoperability: make it easy to share types. Evolve those types. Be typesafe
Semantic interoperability: select an existing or industry-specific model and use it. Generic data modeling is hard. Mandate all lower levels.
Stop here. Above this is human work
Level 0: Stand-alone systems. No Interoperability.
Level 1: Technical Interoperability. A communication protocol exists for exchanging data between participating systems. On this level, a communication infrastructure is established allowing systems to exchange bits and bytes, and the underlying networks and protocols are unambiguously defined.
Level 2: Syntactic Interoperability. A common structure to exchange information; i.e., a common data format is used. On this level, a common protocol to structure the data is used; the format of the information exchange is unambiguously defined. This layer defines structure.
Level 3: Semantic Interoperability. The meaning of the data is shared; the content of the information exchange requests are unambiguously defined. This layer defines (word) meaning. There is a related but slightly different interpretation of the phrase semantic interoperability, which is closer to what is here termed Conceptual Interoperability, i.e. information in a form whose meaning is independent of the application generating or using it.
Level 4: Pragmatic Interoperability is reached when the interoperating systems are aware of the methods and procedures that each system is employing. In other words, the use of the data – or the context of its application – is understood by the participating systems; the context in which the information is exchanged is unambiguously defined. This layer puts the (word) meaning into context.
Level 5: Dynamic Interoperability: As a system operates on data over time, the state of that system will change, and this includes the assumptions and constraints that affect its data interchange....
Level 6: Conceptual Interoperability …

## Slide 5: IIoT Connectivity Stack Model
Connectivity
Information
Networking
IICF Focus
Information (Data in Context)
Participant X
Transport
Link
Framework
Distributed Data
Interoperability and Management
Physical
Network
Participant Y
Data (State, Events, Streams)
Messages
Packets
Frames
Bits
Transport
Link
Framework
Distributed Data
Interoperability and Management
Physical
Network
Technical
Interoperability
(bytes)
Syntactic
Interoperability
(data structures)
Semantic
Interoperability
(data context)
Notes: Framework & Transport Layer
  How to get interoperable data?
  What is the lingua franca?
  Get all parties to communicate!
Assume, Networking layer already setup
  People know how to do this
Recognize the other layers

## Slide 6: Connectivity Transport Layer
Transport
Link
Distributed Data Interoperability & Management
Framework
Connectivity
Transport
Functions
Physical
Network
Messaging Protocol
Endpoint
Addressing
Connectedness
Prioritization
Timing & Synchronization
Security
Communication Modes
Technical
Interoperability

## Slide 7: Connectivity Framework Layer
Transport
Link
Distributed Data Interoperability & Management
Framework
Quality of Service (QoS)
Security
Publish-Subscribe
Request-Reply
Discovery
Data Resource Model
Id and Addressing
Data Type System
Lifecycle (CRUD)
Exception Handling
State Management
Connectivity
Framework
Functions
Physical
Network
API
Governance
Syntactic
Interoperability
Notes: Data Resource Model = Meta-Model for modeling application data/resources
Exception Handling = e.g. disconnects. Or when QoS cannot be met. System detects changes that cannot be healed.

## Slide 8: OMG DDS Interoperability
OMG DDS is
  An interoperability framework for Real-Time systems
  That uses the notion of a logical software-based Databus
  OMG DDS supports ANY data model
  In fact, the OMG DDS connectivity framework is something that you build upon when you set out to create a new interoperability standard based on an industry-specific data model
  The result is that OMG DDS underpins a lot of familiar standards…
OMG DDS provides interoperability between
  Other implementations of OMG DDS
  Any communication standards (DIS, TENA, HLA, Modbus, OPC-UA, etc.)
  100s of DoD live systems
Notes: Current simulation standards are a great what and why. DDS is the best how.

## Slide 9: OMG DDS is under the hood of many standards
Standard | Industry
Open Robotics Robotic Operating System v2 (ROS2) | Horizontal / Robotics
Sensor Open System Architecture (SOSA) | Defense
Tactical Microgrid Standards Consortium (TMSC) | Energy
Unmanned Systems (UxS) Control Segment (UCS) Architecture | Defense
Unmanned Systems (UxS) Control Segment (UCS) Architecture | Defense / Aerospace
Joint Architecture for Unmanned Systems (JAUS) | Defense / Robotics
Naval Open Systems Architecture (OSA) | Defense
Control Architecture for Robotic Agent Command and Sensing (CARACaS) | Aerospace / Robotics
Multi-Robot Operator Control Unit (MOCU) | Aerospace / Robotics
Unmanned Maritime Autonomy Architecture (UMAA) | Defense / Robotics
Standard | Industry
Advanced Modular Mannequin (AMM) | Simulation / Healthcare
ALert MAnagement Service (ALAMS) | Defense
Application Management and Systems Monitoring (AMSM) | Defense
Future Airborne Capabilities Environment (FACE) | Defense
Generic Vehicle Architecture (GVA) NATO Generic Vehicle Architecture (NGVA) | Defense
Land Open Systems Architecture (LOSA) | Defense
Medical Simulation Training Architecture (MSTA) | Simulation / Healthcare
Open Field Message Bus (OpenFMB) | Power / Energy
Open Mission Systems (OMS) | Aerospace
Open Process Automation Forum (OPAF) | Process Automation

## Slide 10: Why is OMG DDS so widely used ‘under the hood’ for these standards?
Well, consider these guys…
Hypertext Transfer Protocol (HTTP) – universal transport Representational State Transfer (REST) – universal API
  Used together they build the vast majority of web-based applications
  Good for human speed, but tends to be 1-1; you connect to the bank, email, website, etc.
But what about real-time applications?
  And what about live real-time systems that might be:
    1 to many
    many to 1
    many to many
    with real-time speeds and security requirements

## Slide 11: OMG Data Distribution Service Standard
From OMG, systems software standards organization
  UML, XML, IDL, CORBA, DDS
  Standard can be downloaded for free by anyone
  More than a dozen commercial implementations available
First version of the OMG DDS standard was released in 2004
  Most recent updates were May 2019
A family of 13 standards covering API, wire protocol, security, type evolution, etc.

## Slide 12
OMG Data Distribution Service Standard
OMG DDS is a standard for data-centric connectivity and interoperability for real-time systems
Data-Centric Publish-Subscribe model for distributed application communication and integration
Standardizes wire protocol, serialization format and API
OMG DDS is open and multi-vendor
  Open Standard and Open Source
  12+ implementations
Interoperability between source written for different vendors
Interoperability between applications running on different implementations
OMG DDS APIs: Data Centric Publish Subscribe (DCPS)
Distribution Fabric
Real-Time Publish Subscribe
Wire Protocol (RTPS)
OMG DDS Security
Plug-In
QoS
QoS
QoS

## Slide 13: OMG Data Distribution Service Standard
OMG DDS is Publish-Subscribe, Data-Centric, and Peer-to-Peer
  OMG DDS also supports request-reply and queueing
Designed for real-time mission critical and safety critical systems
  Started in Robotics and SW Defined Radios using Tactical Data Links
  Navy wanted it turned into an open standard, now widely used in the Navy
OMG DDS applications share large amounts of data quickly, securely, and reliably at massive scale
OMG DDS provides location transparency, decentralized operation, dynamic scalability, and real-time performance
Its widespread use in distributed real-time military systems has led to strong interest in the modeling, simulation and training community

## Slide 14: OMG DDS is made for real-time interoperability
OMG DDS defines
  Open API for portability
  Open wire protocol for interoperability
    Transport agnostic
  Open explicit defined QoS and discovery
    Highly configurable
Multiple language bindings
  C, C++, Java, C# .NET, Ada
  LabVIEW, MATLAB/Simulink
  Python, NodeJS
Multi platform support
  Windows, Linux, Unix, embedded OS, Docker, Kubernetes
OMG DDS Middleware
Operating System
UDP
TCP
Shmem
RT-WAN
Application
Standard API
Standard Protocol
Data Management (QoS)
OMG DDS Security

## Slide 15: Data-Centric Publish Subscribe
Global Data Space
OMG DDS Databus
Reliable
100 Hz
Altitude < 5000 ft
Reliable
25 Hz
Best effort
2x / Sec
Sensor | 
Source** | string
Speed | float
Altitude | float
Actuator | 
Id** | string
Command | string
Status | float

## Slide 16: OMG DDS Data-Centric Model
Data objects addressed by Domain ID, Topic and Key
  Domains provide a level of isolation
  Topic groups homogeneous subjects (same data-type & meaning)
  Key is a generalization of subject
Data Writer
Data Writer
Data Writer
Data Reader
Data Reader
Data Reader
License Plate | Speed | Battery Remaining | GPS Location
DKW 8307 | 41 | 73% | 39.9524, -75.1636
YQC 4149 | 64 | 55% | 28.3794, -81.5494
Traffic Light | State | Time Left | Operational Mode
35803 | Green | 23 sec | Automatic
82915 | Red | 6 sec | Manual Override
Data Writer
Key (subject)
Topic
Instance
Domain
YQC 4149 | 68 | 48% | 28.3903, -81.5141
YQC 4149 | 70 | 47% | 28.4118, -81.4802
Notes: Introduction to definitions

## Slide 17: Common Distributed Application Challenges
1-1, 1-Many
No Reliability
1 to 1
Reliability
Transport
Flow Control
UDP
TCP
Deadline
Reliability
History
Liveliness
Time Based Filter
Batching
Durability
Ownership
Partition
Presentation
Lifespan
In-Order Delivery
Resource Limits
Latency Budget
Flow Control
User, Group, Topic Data
Content Filtering
Transports
Multi-Channel
Async Publisher
OMG DDS QoS Features

## Slide 18: Using OMG DDS QoS to Shape Data Flow
Discovery matches publishers and subscribers of a topic
Topics tied to Data type, allowing smarter databus
Quality of Service describing application data needs must be compatible to communicate
Specifying and relying only on these data properties enables decoupled, resilient systems
Subscriber
Subscriber
Subscriber
Collision avoidance application
Radar Track
Topic
Publisher
Reliable; 1 Hz; get history
Best effort; 0.2 HZ; get history
ATC Sim
Nearby tracks with altitude < 5000m
Publish reliably
10 Hz
600 sample history
NOC Sim

## Slide 19: Content Filtered Topics
The Filter Expression and Arguments will determine which instances of the Topic will be received by the subscriber

## Slide 20: OMG DDS Publish Subscribe API: QoS conflicts
DataWriter
The DataReader and DataWriter QoS must match if connectivity is to be established
QoS does not need to be equal. It is ok if a DataWriter offers “more” than what a DataReader asks for
    Example: DW = Reliable, DR = Best Effort
DataReader
DataReader
BEST EFFORT
BEST EFFORT
RELIABLE

## Slide 21: Wide Area Distributed Applications
Asset at the Edge
On-site Operation Center
INTELLIGENT LOGGING AND ANALYTICS, ASSISTANCE
MULTI-VEHICLE ANALYTICS, ASSIST, STORE & FORWARD LOGGING
Cloud
MULTI-SITE ANALYTICS & ML, STORE LOGGING
OMG DDS WAN Databus
NAT
NAT
NAT
Remote Monitoring, Analytics and Assistance
Wide area distributed applications have more technical challenges
Network changes over time (ex. Wi-Fi to Cellular)
Scalability of data transport and cloud services
Edge device authentication and data security

## Slide 22: Data Flow Over the Wide Area Network (WAN)
Require:
High performance connectivity across diverse networks
Device mobility support across networks
Scalability with a much larger number of endpoints
Data security at minimal cost (bandwidth, latency etc.)
NAT traversal support

## Slide 23: OMG DDS real-time WAN Transport
Smart transport enabling secure, scalable, and high-performance communication over WANs, including public networks
Features include:
UDP based WAN connectivity
Network Address Translator (NAT) traversal
Support for IP mobility
No third-party system dependence, such as STUN servers
Direct Edge-Edge communication
Gateway
OMG DDS Databus @ WAN
OMG DDS Databus @ Edge
Real-Time WAN Transport
OMG DDS Application
Real-Time WAN Transport

## Slide 24: OMG DDS Across a WAN
Edge
Systems
System Component
NAT
Real-Time WAN Transport
Databus
Data
Center
Real-Time WAN Transport
NAT
OMG DDS WAN Databus
Databus
Analyze
Store
Aggregate
Edge-to-Data Center connectivity across a WAN
Edge-to-Edge connectivity across a WAN
OMG DDS connectivity within Data Centers and Edge Systems
Notes: Not only can edge systems communicate back to a central system, but they can also communicate with each other.

## Slide 25: Peer-to-Peer Connectivity Over the WAN
OMG DDS Databus @ WAN
Real-Time WAN Transport
OMG DDS Application
Applications can communicate peer-to-peer over the WAN using the WAN Transport
Notes: Note - that the participants will be fixed, since multicast is not available.. and only if each participant is accessible through a public address

## Slide 26: OMG DDS Data Centric Publish Subscribe API
The OMG DDS API lets applications publish data to, and subscribe to data from the OMG DDS Databus
This OMG DDS API is called Data Centric Publish Subscribe (DCPS)
The API is standardized in the OMG DDS v1.4 standard, as a “Platform Independent Model” (PIM)
API operations are mapped to different languages through a “Platform Specific Model” (PSM)
The DCPS API is divided up into “entities” (way different than a simulation entity) which allow an application to:
  connect to the DDS Databus
  create topics
  get notified of infrastructure-level events (new subscriber, new publisher, …)
  publish and subscribe to application data
Each OMG DDS entity has a set of QoS settings that determine the behavior of the entity

## Slide 27: OMG DDS Publish Subscribe API: Entities
Create & manage connection to OMG DDS Databus
DomainParticipant

## Slide 28: OMG DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Create a proxy to a topic in the application
<< creates >>

## Slide 29: OMG DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Manages group of DataWriters
Publisher
Subscriber
Manages group of DataReaders
<< creates >>
<< creates >>
DataWriter
DataReader
<< creates >>
<< creates >>

## Slide 30: OMG DDS Publish Subscribe API: Entities
DomainParticipant
Topic
Publisher
Subscriber
DataWriter
DataReader
<< uses >>
<< uses >>
Publishes data to OMG DDS Topic
Subscribes to data from OMG DDS Topic
<< creates >>
<< creates >>

## Slide 31: OMG DDS Publish Subscribe API: Entities
DataReaders (DR) and DataWriters (DW) are strongly typed
Their APIs are generated from Interface Definition Language (IDL)
struct ShapeType {
string<128> color;
long x;
long y;
long shapesize;
};
ShapeTypeDataWriter_write
ShapeTypeDataWriter_dispose
ShapeTypeDataReader_read
ShapeTypeDataReader_take

## Slide 32: OMG DDS Topic Data Types
struct MyType {
long sensorID; //@Key
long plantID; // @Key
float sensorVal0;
float sensorVal1;
float sensorVal2;
float sensorVal3;
float sensorVal4;
Version version;
Time currentTime;
}
struct Version {
string firmwareVersion;
string hardwareVersion;
string modelNumber;
string serialNumber;
}
Strongly Typed
struct MyType {
string data;
}
Where data =
<SENSOR>
<SensorID>438</SensorID>
<PlantID>192</PlantID>
<Value0>21.0546</Value0>
<Value1>43.6</Value0>
<Value2>56.34</Value0>
<Value3>12.11</Value0>
<Value4>20.00</Value0>
<firmware>1.24b</firmware>
<hardware>2.39</hardware>
<model>M56A743</model>
<serial>1429709<serial>
</SENSOR>
Loosely Typed
struct MyType {
long sensorID; //@Key
long plantID; // @Key
string data;
string version;
}
Where data =
<SENSOR>
<Value0>21.0546</Value0>
<Value1>43.6</Value0>
<Value2>56.34</Value0>
<Value3>12.11</Value0>
<Value4>20.00</Value0>
</SENSOR>
version =
<VERSION>
<firmware>1.24b</firmware>
<hardware>2.39</hardware>
<model>M56A743</model>
<serial>1429709<serial>
</VERSION>
Mixed Type
Notes: Tesla vs Hybrid vs DDS as a Truck

## Slide 33: Data Type Extensibility
struct Track {
long id; //@key
float range;
float bearing;
}
struct AirTrack {
long id; //@key
float range;
float bearing;
float elevation;
}
struct Track {
long id; //@key
float range;
float bearing;
}
struct AirTrack {
long id; //@key
float elevation;
}
struct Track {
long id; //@key
float range;
float bearing;
}
Final Type
  Type definitions are strictly defined
Extensible Type
  Newer applications can add fields to existing base types
Mutable Type
  Type representations can differ from each other with Additions, Deletions and Transpositions
  Support for Optional Fields
struct Track {
long id; //@key
float range;
float bearing;
}
Notes: Standard provides a mechanism for a chain of extensibility to evolve over time

## Slide 34: Simple API Interface
void publisher_main(int domain_id) {
// Initialize
dds::domain::DomainParticipant participant (domain_id);
// Create a Topic
dds::topic::Topic<foo::TopicType> topic (participant, "MyTopic");
// Create a Data Writer
dds::pub::DataWriter<foo::TopicType> writer(dds::pub::Publisher(participant), topic);
// Create some data
foo::TopicType sample("Hello World");
// Write the data
writer.write(sample);
}

## Slide 35: Practical Security Needs Many Layers
OMG DDS Security
System edge
Host
  Machine/OS/Applications/Files
Network transport
  Media access (layer 2)
  Network (layer 3)
  Session/Endpoint (layer 4/5)
Dataflow
  Control application interaction
Secure systems need all four

## Slide 36: OMG DDS Security Standard
OMG released the DDS Security specification (v1.1) in July 2018
Collaboratively developed by several OMG DDS vendors
Defines:
  OMG DDS Security Model
  Service Plugin Interface (SPI) Architecture

## Slide 37: OMG DDS Security Standard
Security Plugs into OMG DDS Middleware
  Secures data-in-motion throughout the system
  Can easily take DIS PDUs or TENA / HLA FOMs and convert them to Secure OMG DDS Topics
  Programming language and Operating System interoperability
Decentralized, Peer-to-Peer, and Highly Configurable
  Fine-grained access control and security levels for each topic and partition
  Each participant separately authenticated through mutual authentication
OMG DDS Security has been vetted at the Cybersecurity Warfare ranges at Quantico, VA and Orlando, FL
  USAF has funded a SBIR project for Multi-Level Security for LVC simulations
OMG DDS Security is a natural fit for Multi-Domain Operations systems
  Joint Battle Command Platform JBC-P
  Integrated Air and Missile Defense Battle Control System IBCS
  Cooperative Engagement Capability CEC
  Universal Ground Control Station UGCS
  All branches of the military, including Space Force, use OMG DDS

## Slide 38: OMG DDS: Data-Centric, Fine-Grained Security
Per-Data-Topic Security
  Control r,w access for each function
  Ensures proper dataflow operation
Complete Protection
  Discovery authentication
  Data-centric access control
  Cryptography
  Tagging and logging
  Non-repudiation
  Secure multicast
  100% standards compliant
Operator
Fire
Data Topics
Applications
Control
Visualize
Simulate
BaseEntity
Detonation
Data Topic Security model:
Simulate: Fire(r), BaseEntity(w)
Visualize: BaseEntity(r), Detonation(w)
Control: BaseEntity(r), Fire(w)
Operator: *(r), Fire(w)

## Slide 39: Pluggable Architecture
Requires trivial or no change to existing OMG DDS apps and adapters
Includes default plugins; customizable
Runs over any transport
  Including low bandwidth, unreliable
  Does not require TCP or IP
  Multicast for scalability, low latency
Completely decentralized
  High performance and scalability
  No single point of failure
OMG DDS Security Library
Authentication
Access Control
Encryption
Logging
Application
Any Transport (e.g., TCP, UDP, multicast, RT-WAN, shared memory…)
Data Tagging

## Slide 40: Standard Capabilities (Built-in Plugins)
Authentication | X.509 Public Key Infrastructure (PKI) with a pre-configured shared Certificate Authority (CA) Digital Signature Algorithm (DSA) with Diffie-Hellman and RSA for authentication and key exchange
Access Control | Configured by domain using a (shared) Governance file Specified via permissions file signed by shared CA Control over ability to join systems, read or write data topics
Cryptography | aes-128-ctr for encryption HMAC-SHA256 for message authentication and integrity aes-128-gcm, aes-192-gcm and aes-256-gcm for encryption with authentication Certicom and Windows CNG for FIPS 140-2
Logging | Log security events to a file or distribute securely over OMG DDS
Data Tagging | Tags specify security metadata, such as classification level Can be used to determine access privileges (via plugin)

## Slide 41: Domain Governance File
The domain governance document is an XML document that specifies which OMG DDS domain IDs shall be protected and the details of the protection
It is signed by the permissions CA

## Slide 42: A Sample Governance File

## Slide 43: Configuration Possibilities
Are “legacy” or un-identified applications allowed in the Domain?
  If yes, an unauthenticated application will:
    See the “unsecured” discovery Topics
    Be allowed to read/write the “unsecured” Topics
Is a particular Topic discovered over protected discovery?
  If so, it can only be seen by “authenticated applications”
Is access to a particular Topic protected?
  If so, only authenticated applications with the correct permissions can read/write
Is data on a particular Topic protected? How?
  If so, data will be sent signed or encrypted then signed
Are all protocol messages signed? Encrypted?
  If so, only authenticated and authorized applications will see anything

## Slide 44: Permissions Document
For each participant, specifies:
  What domains it can join
  What Topics it can read/write
  What Partitions allowed for publish and subscribe
  What Tags are associated with Readers & Writers

## Slide 45: A Sample Permissions File

## Slide 46: OMG DDS Publish Subscribe API: Entities
OMG DDS Security
OMG DDS Security
DomainParticipant
Topic
Publisher
Subscriber
DataWriter
DataReader
<< uses >>
<< uses >>
<< creates >>
<< creates >>

## Slide 47: Configuring & Deploying OMG DDS Security
Shared By All Participants
Domain Governance
Document
Identity CA Public Certificate
Permissions CA Public Certificate
Participant 2
P2 Identity Certificate
P2 Private Key
P2 App
P2 Permissions File
Participant 1
P1 Identity Certificate
P1 Private Key
P1 App
P1 Permissions File

## Slide 48: Configuring & Deploying OMG DDS Security
Shared By All Participants
Domain Governance
Document
Identity CA Public Certificate
Permissions CA Public Certificate
Participant 2
P2 Identity Certificate
P2 Private Key
P2 App
P2 Permissions File
Participant 1
P1 Identity Certificate
P1 Private Key
P1 App
P1 Permissions File
Security Administration (Out of Band)
Permissions CA Private Certificate
Identity CA Private Certificate

## Slide 49: Using OMG DDS with distributed LVC simulations
Can leverage/ integrate existing system software
  Over one thousand separate DoD systems (Navy, Air, Army) use OMG DDS
    OMG DDS is mandated by Navy OA for combat management systems
    OMG DDS specified by US DoD for the unmanned vehicle control (OSD-UCS)
    OMG DDS specified by UK-MOD for army vehicle communications
    OMG DDS is a transport for MOSA standards, FACE, SOSA, OMS, UCI
With OMG DDS, simulation systems could easily reuse and integrate software components from actual systems
  This has already been happening for years

## Slide 50: OMG DDS in Simulation: JMETC

## Slide 51: Securing distributed LVC simulations with OMG DDS
Can leverage/integrate mission data
  Recorded data from actual mission execution could be combined with simulation data and be used for training
    This approach is already followed in the US Navy OATM
  Rapid feedback from mission to training is key to an agile and effective force.
Can leverage/integrate OMG DDS Security into new distributed simulations
  Secure training and simulations over WAN/Cloud/RF/Lossy Networks/TDL
  Role-based access allow for joint Coalition forces to train alongside US forces
  Multiple SBIRs with different defense agencies for secure LVC simulations

## Slide 52: Multi Level Secure MLS, Live Virtual Constructive LVC Simulations

## Slide 53: Global Connectivity for USAF Training Simulations

## Slide 54: Missile Defense Agency – Objective Simulation Framework
Fully Distributed, Real-Time,
Secure Cyber Situational Awareness for MDA OSF

## Slide 55: Mixed-Reality Wargaming Platform
Cloud
Real World Twin
Management
Logging
Analytics
Secure Global OMG DDS Databus
Secure
Gateway
Secure Cross-System OMG DDS Databus (Local/Regional)
Simulation DataBus
Simulation DataBus
Simulation Connext DataBus
Sim@ SOCOM
DataBus
Gateway
Sim@ NATO 1
Sim@ NATO 2
Management
Logging
Analytics
One World
Terrain
Protocol/Data Interoperability
Data Routing/Filtering
Other
Services
A Hierarchical, Loosely-Coupled Design Enables:
Local Ownership
Disconnected Operation
Open Architecture
Capability-as-a-Service
  e.g., AI, Simulation, Data, Devices
AI/ML/DL
Augmented
Reality
Autonomous Systems
Maritime
Air
Helo
Ground
AI Training
Scenarios
Unity
Unreal
OtherSim
Local Mgmt
Simulated Worlds
Real World
Digital
Twins
Simulated
Actors
Edge
Processing Location Agnostic / Transparent
Protocol
Gateway
Protocol XYZ
OMG DDS

## Slide 56: Air Force’s Simulators Common Architecture Requirements and Standards (SCARS) program

## Slide 57: CCDC Aviation& Missile Center - SED System Integration Labs
Hardware-in-the-Loop labs for the UH-60V, CH-47F and AH-64E Army Helicopters

## Slide 58: CCDC AvMC S3I - Apache AH-64E
Database
OMG DDS
Flight Model
LabVIEW
RadAlt Model
ADC Model
EGI Model
Aberdeen I/O
Data Record /
Playback
Data Analysis
Workstation
Visuals
Visuals
Image Generators
Flight
Controls
HAT/HOT
Science
Experiments
TBD

## Slide 59: PEO Aviation - Combat Aviation Brigade Architecture Integration Lab CABAIL
AH-64E and CH-47F SILs already use OMG DDS to reduce hardware and development costs for HIL experimentation
JBC-P Network Operations Center(NOC) was re-architected using OMG DDS for significant code reduction and performance improvement

## Slide 60: Using OMG DDS with Simulation Standards
The OMG DDS specification has been be leveraged for the middleware APIs as well as the wire protocol
APIs could use the OMG DDS API
Wire protocol communications could use the Interoperability Wire protocol from OMG DDS
This combination would leverage the performance, scalability, robustness and interoperability from OMG DDS.
The simulation entities from TENA/HLA/DIS could be leveraged
They would provide the “entity data model dictionary”
This would leverage the conventions and semantics of the simulation standards
The simulation defined types could be described using the OMG DDS Extensible Types
This leverages the extensibility, dynamic APIs and backwards compatible path to type evolution of the DDS Type system
Gateways/brokers exist
HLA-RTI provider supports multiple OMG DDS Vendors

## Slide 61: SISO CIGI and OMG DDS
Common Image Generator Interface (CIGI) is an on-the-wire data protocol that allows communication between an Image Generator and its host simulation
The interface is designed to promote a standard way for a host device to communicate with an image generator (IG) within the industry
“CIGI Next” now rebranded as the Synthetic Environment Generation Interfaces (SEGI) is considering using OMG DDS as a transport
  Could eliminate the need for hosts, you would communicate directly to the IG
  Please join the SISO CIGI PDG!

## Slide 62: Using OMG DDS at SISO?
Layered Simulation Architecture
  Study Group at SISO
  Putting OMG DDS ‘under the hood’ of HLA/DIS
    Use OMG DDS RTPS with Simulation Entities as topics
  Study Group recommended that LSA become a SISO standard; stalled at that point
Need a coalition of the willing to revive this
  Open-source prototype would be needed
  OMG DDS Security was not considered at the time of this study group, but could easily be added and add much needed security to the Simulation standards

## Slide 63: OMG DDS with MOSA Requirement
Tri-Service acquisition memorandum signed by the Secretaries of the U.S. armed services – directed using Modular Open Systems Approach (MOSA)
Specifically cites standards
  Sensor Open Systems Architecture (SOSA)
  Open Mission Systems/Universal Command and Control Interface (OMS/UCI)
  Future Airborne Capability Environment (FACE)
  Vehicular Integration for C4ISR/EW Interoperability (VICTORY)
  …“as vital to our success”
OMG DDS is certified conformant and/or aligned to every standard called out in the provided memorandum

## Slide 64: The Demand for Data-Centricity also applies to LVC
DoD Data Strategy
Unleashing Data to Advance the National Defense Strategy
“It is the responsibility of all DoD leaders to treat data as a weapon system and manage, secure, and use data for operational effect”
Vision: “The DoD is a data-centric organization that uses data at speed and scale for operational advantage and increased efficiency”
Notes: Vision: “The DoD is a data-centric organization that uses data at speed and scale for operational advantage and increased efficiency”
One of the guiding principles:
Data for Artificial Intelligence Training – Data sets for A.I. training and
algorithmic models will increasingly become the DoD’s most valuable digital
assets and we must create a framework for managing them across the data lifecycle
that provides protected visibility and responsible brokerage.

## Slide 65: 7 Goals to Becoming a Data-Centric DoD
Notes: VAUL&I: are core DDS data-centric, data-model capabilities
T&S: Trustworthy and Secure are enable by DDS Secure
1. Make Data Visible -- Consumers can locate the needed data
2. Make Data Accessible -- Consumers can retrieve the data
3. Make Data Understandable -- Consumers can recognize the content, context, and applicability
4. Make Data Linked - Consumers can exploit data elements through innate relationships
5. Make Data Interoperable -- Consumers have a common representation / comprehension of data
6. Make Data Trustworthy -- Consumers can be confident in all aspects of data for decision-making
7. Make Data Secure -- Consumers know that data is protected from unauthorized use / manipulation
So, sims for training need to be interoperable meanwhile there are these new MOSA and Data-Centric requirement mandates.

## Slide 66: Conclusions
DDS is a mature standard from OMG
  Platform neutral: Operating Systems and Programming Languages
  Mandated and deployed worldwide in many military systems with demanding real-time applications
  Portable API DCPS and Interoperable Wire Protocol RTPS
  Deployed DDS Security Standard specification
OMG DDS focuses on efficient data-distribution for real-time & high-performance systems
OMG DDS is suited for integration of distributed training systems
  Authentication, Role-Based Access to data, Multiple Levels of Security (MLS)
  Evolvable Type System
  Real-Time Quality of Service (QoS)
  Integration and reuse of system software and mission data

## Slide 67: Original Tutorial Learning Objectives
After taking this tutorial you should be able to:
Describe how OMG DDS enables semantic interoperability
Describe the OMG DDS standard
Explain the principles of the OMG DDS Secure standard for securing communications between distributed simulations over WAN/Cloud/RF/Lossy networks
Explain how OMG DDS works with the simulation architectures TENA, HLA and DIS
Summarize how OMG DDS works with real-world Hardware In the Loop (HIL) for secure distributed LVC simulations at scale
Describe how OMG DDS is working within SISO