## Slide 1
Introduction to U.S. Department of Defense Modeling and Simulation
John Daly, Booz Allen Hamilton
Dr. James Coolahan, Coolahan Associates
November 2021

## Slide 2: Learning Objectives
  Explain the scope and the fundamental terms and concepts associated with Defense Modeling and Simulation
  Identify key policies and procedures for US DoD Modeling and Simulation
  Summarize key Defense Activities enabled by Modeling and Simulation
  Discover US DoD Modeling and Simulation information resources

## Slide 3: What is Modeling and Simulation?
A representation
of real world:
    Equipment
    People
    Activities
    Processes
    Environments

## Slide 4: Example of a Famous Simulation
“Whatever can go wrong, will go wrong”
Edwards AFB 1940: all 18 Accelerometers mounted backwards!
Murphy’s Law
Lt. Edward Murphy
Ref: https://www.youtube.com/channel/UCpuofAxlrUAgnu7QEwKQwxw (DoD YouTube Channel)

## Slide 5: Agenda
PART 1
Basic Modeling and Simulation Concepts
Why model or simulate?
Modeling and Simulation (M&S) definitions and explanations
Types of models and simulations in military use
Key Enabling Concepts
PART 2
Key Defense Activities Enabled by M&S:
    Systems Engineering
    Analysis
    Experimentation and Technology
    Intelligence
    Medical
    Planning
    Test and Evaluation
    Training
Supporting US DoD Organizations and Resources

## Slide 6: Why Model Or Simulate?
Affordability: Simulating operations and processes allows us to determine the most cost-effective options. For example, test firing a $1M missile to determine its dynamic characteristics in flight, or simulating it in a virtual testbed - avoiding the $1M cost.
Feasibility & Safety: With a simulation, you can access hazardous or denied areas and operating ranges, speed up the passage of time and pause it, and determine how to safely operate our equipment in performing a task and what the safe limits of a process or capability are. For example, we routinely train air, shipboard and vehicle crews on safe operation of their platform using simulation.

## Slide 7: Why Model Or Simulate?
Research and Development: For problems with no simple solution, simulations allow human reasoning and mathematical analysis to complement each other, creating problem solving synergy. Modeling and simulation allow us to explore and develop new technologies and their application to military missions; before we build. For example, Hypersonic flight.
Prediction: Modeling and simulation enable us to look into the “future” by creating a simulation of it, based on our best information from the present and physics/insight. An example is the common weather forecast, predicting storm paths and danger zones.
Insight: Modeling and simulation allow us to analyze and understand complex systems that we may not even be able to demonstrate/test physically. For example, Electronic Warfare systems – these are designed and even tested using simulation.

## Slide 8: Key Modeling and Simulation Definitions
Model: A physical, mathematical, or otherwise logical representation of a system, entity, phenomenon, or process.
Simulation: A method for implementing a model over time.
Modeling and Simulation: The discipline that comprises the development and/or use of models and simulations.
Ref: Department of Defense Modeling and Simulation (M&S) Glossary, July 1, 2013.
Available at http://www.msco.mil/MSGlossary.html
There are a number of definitions of models, simulations, and Modeling and Simulation (M&S). For the purposes of this tutorial, we will adopt the definitions published by the U.S. Department of Defense (DoD), below.
Mathematical Model
Wire Frame Model

## Slide 9: Physical Model
Physical Model. A model whose physical characteristics resemble the physical characteristics of the system being modeled - a “mock-up”. DoD M&S Glossary

## Slide 10: Mathematical Model
Mathematical Model. A symbolic model whose properties are expressed in mathematical symbols and relationships. DoD M&S Glossary
In case of a car with uniform acceleration, there are three equations of motion which are also known as the laws of constant acceleration.
v = u + at
v² = u² + 2as
s = ut + ½at²
Where: s = displacement; u = initial velocity; v = final velocity; a = acceleration; t = time of motion

## Slide 11: Process Model
Process Model. Model that defines the functional decomposition and the flow of inputs and outputs for a system. DoD M&S Glossary

## Slide 12: Example of a Mathematical Traffic Simulation
Mathematical Model Simulating Auto Traffic on Limited Access Highway
an On-ramp situation
Ref: http://www.traffic-simulation.de/onramp.html

## Slide 13: Modeling/Simulation “Pyramids”
Most M&S application areas have a hierarchical means of categorizing models and simulations in that area, by resolution level.
Human Body M&S Pyramid
Molecule
System
Human
Cell
Cardiac-centric example
Whole body
Cardio-vascular
Heart
Ca++
Myocyte
Organ
More aggregation
Shorter run time
Less aggregation
Longer run time
Engineering
Mission
Campaign
Engagement
Military Simulation Pyramid
PATRIOT-centric example
Gulf War
Air defense
Missile intercept
Terminal guidance
Mission Simulation
Domain
Engineering Modeling Domain
11

## Slide 14
Live simulation: A simulation involving real people operating real systems
  Examples: exercises, operational tests
Virtual simulation: A simulation involving real people operating simulated systems
  Examples: cockpit simulator, driving simulator
Constructive simulation: A simulation involving simulated people (or no people) operating simulated systems
  Examples: military campaign simulation, missile 6-degree-of-freedom simulation
People
Real Simulated
Systems
Simulated Real
Categorizing Simulations by Human-System Interaction
Live
Virtual
Constructive
?
Autonomous?

## Slide 15: Example of a Live Simulation
Characteristics:
Physical models
Real people
Real Time
Real Systems
An example could be a mass casualty drill with people, simulated injuries, emergency equipment, vehicles, and operations

## Slide 16: Example of a Virtual Simulation
HMMWV Egress Assistance Trainer (HEAT)
Other examples could be a flight simulator or a combat command center team trainer

## Slide 17: Example of a Constructive Simulation
Constructive simulations are robust computer-generated simulations that offer the ability to:
  analyze concepts
  predict possible outcomes
  support decision-making
  stress large organizations
  make measurements
  generate statistics
  perform analyses
An example is the complex aerodynamic and RF physics, and crew dynamics simulated in a missile intercept scenario.

## Slide 18: Distributed Simulations
OR
World -wide
Virtual
Constructive
Live
Locally
Constructive
Virtual
Live
An example could be a Navy ship pier-side in Norfolk, Va., directing an exercise air strike mission flown by pilots in aircraft simulators located in San Diego, Ca, and Whidbey Island, WA.
Characterized by the distributed nodes where interactions with the simulation occur
LVC= Live + Virtual + Constructive

## Slide 19: Resolution, Aggregation, and Fidelity
Aggregation: The ability to group entities while preserving the salient effects of entity behavior and interaction while grouped
  “Campaign-level” simulations often aggregate military entities into larger groups (e.g., brigades vs. battalions)
Refs: [1] DoD Modeling and Simulation (M&S) Glossary, July 1, 2013
[2] DoD Directive 5000.59-P, DoD Modeling and Simulation (M&S) Master Plan, 1995
Resolution: The degree of detail and precision used in the representation of an item or the real world aspects in a model or simulation Models and simulations at lower levels of M&S “pyramid” tend to exhibit more resolution; this does not necessarily imply more accuracy
Fidelity: The accuracy of the representation when compared to the real world [2]
  Greater fidelity does not imply greater resolution
Entity
Count
1
Entity
Count
3
Entity
Count
12

## Slide 20: Agenda
PART 1
Basic Basic Modeling and Simulation Concepts
Key Enabling Concepts
Architectures and Standards
Interoperability
Simulation Development Process
Verification, Validation, and Accreditation (VV&A) Process
PART 2
Key Defense Activities Enabled by M&S:
    Systems Engineering
    Analysis
    Experimentation and Technology
    Intelligence
    Medical
    Planning
    Test and Evaluation
    Training
Supporting US DoD Organizations and Resources

## Slide 21: Simulation Architectures
Large problems are addressed by
  Breaking the problem into manageable pieces
  Solving individual pieces
  Re-assembling the pieces to create the solution
Simulations are built in much the same way
  Individual pieces are built by the experts on that piece
  Pieces developed separately are re-assembled using architectures
US DoD has 3 primary distributed simulation architectures: DIS, HLA, TENA
  Often, larger distributed exercises combine these different architectures
  Gateways (software modules) translate from one architecture to another
Gaming architectures and simulation frameworks are now becoming more widely used. These can leverage IT cloud capabilities to distribute simulation content and interactivity with participants.

## Slide 22: US DoD Distributed Simulation Architectures
DIS: Distributed Interactive Simulation (earliest)
  IEEE 1278 – DIS is a standard
  The standard specifies that data is passed using a protocol data unit or PDU
  DIS is widely used in simulators and will be used for the lifetime of those simulators
HLA: High Level Architecture (IEEE 1516)
  Interface specification document defines how HLA-compliant simulations interact with the Run-Time Infrastructure (RTI).
  Object Model Template (OMT) specifies what information is communicated between simulations and how it is documented.
  HLA Rules that simulations must obey to be compliant with the standard
TENA: Test and Training Enabling Architecture
  Enables interoperability among range systems, facilities, simulations, and C4ISR systems in a quick, cost-efficient manner
  Based on same foundation as HLA but specialized for needs of test ranges
There are full tutorials on each of these architectures

## Slide 23: Standards
Standards are critical enablers for M&S
  DIS and HLA are architecture standards under IEEE
  TENA is a standard within US DoD’s T&E community
Standards provide essential functionality
  Communication: ability to move data and link execution across different machines and sometimes across large distances
  Interoperability: ability to exchange data and the ability to interpret it consistently (common context)
  Reusability: ability to adapt components (e.g., ideas, whole simulations, lines of code) for new simulations
  Cost Savings:
    Avoids expenses of moving people and equipment – allow use of unique resources
    Seeks to build once and use many times

## Slide 24: Interoperability in M&S
M&S Interoperability. Is the ability of a model or simulation to provide services to and accept services from other models and simulations, and to use these exchanged services to operate effectively together.
DoD M&S Glossary
Virtual Simulation
Constructive Simulation

## Slide 25: Simulation Development Process
Ref: Benjamin, P., Patki, M, and Mayer, R., “Using Ontologies for Simulation Modeling”, proceedings of the Winter Simulation Conference, 2006.
Real World
Done?
Establish Purpose & Scope
Formulate Conceptual Model
Acquire & Analyze Data
Design Detailed Model
Verify & Validate Model
Design Experiments
Execute Simulation
Analyze Output
Refine & Optimize Model
0
0
0
0
Model
Development
Model
Application
Start
Yes
No
Fig. 1: The Simulation Modeling Process

## Slide 26: Environment in Simulation
Simulations require specific environment phenomena and their resulting impacts at varying degrees of fidelity
Example: NGA Geospatial 3-D Terrain (FG3D)
National Geospatial Agency GEOINT Basic Doctrine Publication 1.0; https://www.nga.mil/resources/1597163164750_GEOINT_Basic_Doctrine_Publication_10_.html
3D Simulation model data that Incorporates
elevation, time, and motion

## Slide 27: Verification, Validation, and Accreditation (VV&A) Process
Verification ‑ The process of determining that a model or simulation implementation and its associated data accurately represent the developer's conceptual description and specifications
  Did we build the model right?
Validation ‑ The process of determining the degree to which a model or simulation and its associated data are an accurate representation of the real world from the perspective of the intended uses of the model
  Did we build the right model?
Accreditation ‑ The official certification that a model or simulation and its associated data are acceptable for use for a specific purpose
  Is this the right model to use for this purpose?
Ref: DoD Instruction (DoDI) 5000.61 DoD Modeling and Simulation (M&S) Verification, Validation, and Accreditation (VV&A), December 9, 2009. Available at www.dtic.mil/whs/directives/corres/pdf/500061p.pdf

## Slide 28: Verification
Verification. The process of determining that a model or simulation implementation and its associated data accurately represent the developer’s conceptual description and specifications. DoD M&S Glossary
“Did I build it right?”

## Slide 29: Validation
Validation. The process of determining the degree to which a model or simulation and its associated data are an accurate representation of the real world from the perspective of the intended uses of the model. DoD M&S Glossary
“Did I build the right thing?”

## Slide 30: Accreditation
Accreditation. The official certification that a model or simulation and its associated data are acceptable for use for a specific purpose. DoD M&S Glossary
“It meets my specific needs for…….”

## Slide 31: Agenda
PART 1
Basic M&S Concepts
Key Enabling Concepts
PART 2
Key Defense Activities Enabled by M&S:
    Systems Engineering
    Analysis
    Experimentation and Technology
    Intelligence
    Medical
    Planning
    Test and Evaluation
    Training
Supporting US DoD Organizations and Resources

## Slide 32: Some Key Defense M&S Users
Systems Engineering
Planning
Training
Analysis
Intelligence
Test & Evaluation
Medical
Experimentation and Technology

## Slide 33: M&S use in Systems Engineering: Digital Engineering
Ref: DoD Digital Engineering Strategy June 2018 https://ac.cto.mil/digital_engineering/
Figure 6 provides examples of models, simulations and analyses throughout the life cycle.
“An integrated digital approach that uses authoritative sources of systems’ data and models as a continuum across disciplines to support life cycle activities from concept through disposal”
The U.S. DoD has established the formal planning,
development and use of models as an integral part of performing engineering activities as a continuum across the lifecycle – resulting in a continuous
end-to-end digital representation of the system of interest.
Relies on M&S for engineering analysis and systems engineering functionality

## Slide 34: M&S use in Systems Engineering: Mission Engineering
Figure 6 provides examples of models, simulations and analyses throughout the life cycle.
“The deliberate planning, analyzing, organizing, and integrating of current and emerging operational and system capabilities to achieve desired warfighting mission effects… Systems and SoS in an operational mission context. “
Mission‐focused analysis to evaluate solutions, advise on development of requirements and inform technology investment decisions
Feedback from Mission space back to individual System
Ref: DoD Mission Engineering Guide November 2020 https://ac.cto.mil/wp-content/uploads/2020/12/MEG-v40_20201130_shm.pdf
Relies on M&S to determine System’s Mission Performance

## Slide 35: M&S use in Systems Engineering: Model-Based SE
Figure 6 provides examples of models, simulations and analyses throughout the life cycle.
“Model-Based Systems Engineering (MBSE) is the formalized application of
modeling to support system requirements, design, analysis, verification and
validation activities beginning in the conceptual design phase and continuing
throughout development and later life cycle phases.”
Ref: INCOSE SE Vision 2020 (INCOSE-TP-2004-004-02, Sep 2007) http://www.ccose.org/media/upload/SEVision2020_20071003_v2_03.pdf
Relies on M&S to perform Systems Engineering with the System Perspective
MBSE is part of a long-term trend toward model-centric approaches adopted by other engineering disciplines, including mechanical, electrical and software
Formalizes the practice of Systems Engineering (SE) and systems development through modeling
Broad in scope; Includes multiple modeling domains across life cycle from SOS to component
Results in more quality/productivity & lower risk

## Slide 36: M&S use in Analysis
US DoD analysts use models and simulations to conduct studies and assessments of:
- Strategy
- Resource Allocation
- Operations
- Doctrinal Concepts
- Tactics
- Program Evaluation
- Logistics/Supply Chain analysis
Example: C4I Network Simulation and Analysis:
Dynamic modeling of Networks in mission scenarios
Cyber vulnerabilities identification
Analysis of mission capability
Cost analysis in network design/procurement
Future Conflicts

## Slide 37: M&S use in Experimentation and Technology
Examine present and future security challenges
Explore new concepts, tactics, processes
Investigate cause-and-effect relationships underlying capability development
Investigate futuristic scenarios without risking harm to humans and/or infrastructure
Integrate experiments into training and/or operational tests
Prototyping capabilities in realistic conditions
Mitigate risk for technical advancements
Example: Performance Modeling Virtual Hypersonic vehicle:
Mission success evaluation
System degradation effects
Dynamic simulation in regions beyond
Wind tunnel capability/practicability

## Slide 38: M&S use in Intelligence
Forecast Analysis • Adversary intent • Scenario driven • Political, Military, Economic, Social, Information and Infrastructure and Counter Terrorism Analytical Framework
Foreign Force Modeling • Threat representation • Foreign capabilities • Authoritative data
Example: “Red Force” Capability Simulation:
Accurate models (“twins”) of Red Capabilities
Counter mission success evaluation
Analysis of physical and virtual capabilities (e.g. AI)
Forecasting trends
Can include human, socioeconomic, manufacturing and technology considerations
Leveraged for use in “Blue” acquisition

## Slide 39: M&S use in Test & Evaluation
Virtual prototype satellite model
Supports test design
Expands test scenario possibilities
Assists in testing complex systems
Helps guide selection of test conditions
Supports analysis of test and evaluation results
Virtual testing of complex and non-physical systems
Example: Virtual Cyber Range:
Virtual range for virtual capabilities
Rapidly and realistically represent operational environments at different levels of security, fidelity, and/or scale
Precise control of the test environment

## Slide 40: M&S use in Medical
US DoD Medical uses:
Education & training
  Exposure to high-risk emergencies
  Doctor to Corpsman
  Mass casualty/Disaster relief
  Sustainment training
Capabilities
  Task trainers
  Full size mannequins
  Virtual trainers with haptic feedback
Ref: American Society of Anesthesiologists (ASA): https://www.asahq.org
Example: Anesthesiologist virtual interactive training

## Slide 41: M&S use in Operational Planning
Operational planning
Force structure analysis
Operational concept development
Logistics Planning
Time-Phased Force & Deployment Data (TPFDD) projections
Example: Naval Operational Supply System:
Near real-time/accurate logistics readiness picture
Distance support solutions
Enterprise decision making/execution,
Cost savings and increased readiness
Supply Chain planning and pre-positioning

## Slide 42: M&S use in Training
Trainers use M&S to:
Train commanders, staffs, units, and operators
Practice new processes and
tactics
Refine standard procedures
Exercise new equipment and
technologies
Example: Training Displays at IITSEC
Look anywhere on the floor!!

## Slide 43: Agenda
PART 1
Basic M&S Concepts
Key Enabling Concepts
PART 2
Key Defense Activities Enabled by M&S
Supporting US DoD M&S Organizations and Resources

## Slide 44: Modeling and Simulation in the US DoD: OSD
https://www.msco.mil

## Slide 45: Modeling and Simulation in the US DoD: ARMY
https://www.ms.army.mil/

## Slide 46: Modeling and Simulation in the US DoD: Air Force
https://www.afams.af.mil/

## Slide 47: Modeling and Simulation in the US DoD: Marines
https://www.mccdc.marines.mil/Units/OAD/MCMSO.aspx

## Slide 48: Modeling and Simulation in the US DoD: Navy
https://www.mccdc.marines.mil/Units/OAD/MCMSO/NMSO//
WELCOME TO THE NAVY MODELING & SIMULATION OFFICE
The Navy Modeling and Simulation Office (NMSO) is chartered to promote the discovery and reuse of modeling and simulation (M&S) resources, provide information on policy, data, and services, and to serve as the "action arm" of the Navy Modeling and Simulation Governance Board. As such, NMSO provides administrative support for the Navy Community Leads as well as the M&S community of users. Additionally, NMSO provides core services and products to improve M&S within, between, and across organizations. Finally, NMSO provides assistance to promote and implement cross-cutting M&S projects that improve Navy M&S capabilities. NMSO is part of the Deputy Assistant Secretary of the Navy Research, Development, Test and Evaluation (DASN(RDT&E)) organization

## Slide 49: Resources for Development and VV&A
https://vva.msco.mil/

## Slide 50
Defense M&S Catalog
Catalog Application:
https://mscatalog.msco.mil
Note: this is a CAC-enabled site – restricted access
Information available to public:
https://www.msco.mil/DoDTools/DoDEnterpriseManagementTools/MSCatalog.aspx

## Slide 51
Further Information
https://www.msco.mil

## Slide 52: Learning Objectives
  Explain the scope and the fundamental terms and concepts associated with Defense Modeling and Simulation (M&S)
  Identify key policies and concepts for US DoD M&S
  Summarize key Defense Activities enabled by M&S
  Discover US DoD M&S information resources