## Slide 1
LVC Interoperability 101
Mr. Kurt Lessmann, Chief Technology Officer, Trideum Corporation
Mr. Damon Curry, Business Development, Pitch Technologies

## Slide 2: Agenda
Learning Objectives
LVC Interoperability Overview
Interoperability Through Standards
Interoperability Using Gateways and Cross Domain Solutions
LVC Interoperability Use Case
Summary

## Slide 3: 1. Learning Objectives
The tutorial is intended for decision makers who need a top-level understanding of Live, Virtual and Constructive (LVC) interoperability and the supporting standards, technology and processes.
The tutorial will provide:
  An overview of recommended concepts, processes and tools needed to achieve interoperability
  Use Case that demonstrates interoperability solutions meeting a military training need
  Summary with recommendations
The objective of this tutorial is to provide managers and those new to LVC technology the high-level insight needed to support intelligent decision making when encountering a need for interoperability

## Slide 4: 2. LVC Interoperability Overview
Simulation Definitions
LVC Interoperability Definitions
Distributed Environment Overview
Notes: Thinking we need to describe simulation and interoperability

## Slide 5: LVC Interoperability Overview
Simulation
  A software model that runs over time
  All but war is simulation
Simulation Interoperability
  The ability of connected systems to communicate and function together
  Interoperable components can be combined to create an application… applications can be composed to create a system, and systems can be combined to create a System of Systems (SoS)
Notes: Thinking we need to describe simulation and interoperability

## Slide 6: Live Virtual Constructive (LVC) Definition
Live Simulation
“Real people operating real systems”
Virtual Simulation
“Real people operating simulated systems”
Constructive Simulation
“Simulated People operating simulated systems”
Computer Generated Forces (CGF)
Virtual Environment
Faster/slower than real-time
Various kinds of platform simulators
Virtual Environment
Real-time
Real environment
Real systems
Real people
Real-time

## Slide 7: Distributed Simulation
A distributed simulation is a system that:
  Involves several independent processes executing on one or more computational nodes
  Interoperates using a common services and/or protocol over a network
Simulations can be distributed over a number of different components, ideally loosely coupled or “federated”
  Allows growth over time
  Allows components to be replaced or upgraded easily
  Add additional computational power if needed
Distributed Simulation can be used to support
  Warfighter Training, Command Post Exercises, Enhanced Modeling and Simulation Objectives, Research, Development Test and Evaluation (RDT&E), etc
Notes: Thinking we need to describe simulation and interoperability

## Slide 8: Distributed LVC Event
Distributed LVC Event
  An activity to integrate and execute LVC simulations in a virtual environment so that “real-world” processes and “things” can be exercised to investigate and solve complex issues
    Real-time for live systems, Can be faster than real-time for virtual and constructive systems
  Technique used to enhance weapons system development, test and training
  Can be an effective tool to enhance effectiveness, reduce risk, reduce cost
  Examples include
    Stimulating a ”real” fire control radar with simulated targets to conduct common operator training exercises at multiple training locations
Integrated with
Connected LVC systems
Virtual and/or Real Environment
Running over time
LVC Event
Notes: Thinking we need to describe simulation and interoperability

## Slide 9: Interoperability Requirements
Interoperability Requires
  An ability to meaningfully communicate
    A common “language” to describe the LVC systems
    A data distribution mechanism with well-defined rules and/or services
    A reliable network
  A common context
    A common understanding of the environment and time
    A common technical process
Efficient software reuse and composability is enabled by
  Well-defined software interfaces and access to reusable components
  The ability to replace models at the component level, without interrupting the larger system or requiring software changes or recompilation to other system components

## Slide 10: Typical Interoperability Discussions
It’s a unique language and skill set that takes time to understand and adopt
  Involvement with the interoperability community optimizes this process
Applying standard architectures, processes, technologies and lexicon is a key to success
What is the conceptual model of the entire exercise?
What is the Information Data Exchange Model?
Which coordinate systems are used? Conversions?
What logical sequences of interactions are required?
Fair fight?
What object names (marking) are used? Object types?
What algorithms (such as line of sight) need to be shared?
What representation of the environment is used?
Time handling? Starting and stopping? Scenario handling?

## Slide 11: LVC Distributed Event Environment
Joint Mission Environment Test Capability (JMETC) vision of Standards-based LVC Event Environment

## Slide 12: 3. Interoperability through Standards
The Value of Standards
Past and Current Interoperability Standards
  DIS, HLA and TENA
Recommended LVC Integration Approach

## Slide 13: The Value of Interoperability Standards
Use my proprietary architecture!
Use my proprietary architecture!
Use my proprietary architecture!
Use my proprietary architecture!
Good for me right now
Remove Stovepipes
Open Standard
Solutions
Data Model
Application Programmers Interface (API)
Integration Processes
Good for all
now and in the future
13

## Slide 14: Goals of Interoperability Standards
Enable efficient distributed simulation
  Throughput, latency, scalability etc.
Support simulation specific requirements
  Not limited to data distribution
  Provide common services (Remote Methods, Time Management, Ownership (control over data elements), etc.)
Isolate simulator from physical transport method (i.e. network)
  Avoid technology lock-in
Promote interoperability and reuse
  Leverage exiting solutions for other needs
  Increased customer support
Vendor independent
  Vendors and organizations equally comfortable with the standard
  Open standard for contributions and influence
  Easily replace interoperability implementation
Domain neutral
  Support the simulation market as a whole, multi-purpose
  Possibility to attract a large number of vendors and users
Technical Aspects
Business Aspects
14

## Slide 15: Interoperability Approaches of the Past
Standardize on a vendor solution
  Optimized for a specific need
  Creates a vendor-lock situation for computers and/or software
Standardize on programming language
  Optimized for a specific need
  Problems may occur when maintaining code developed using older programming languages and compilers…the remember ADA mandate?
Incorporation of new software technologies becomes very difficult (Service Oriented Architectures (SOA), cloud based solutions, scripting languages, etc.)
  This approach was adopted when reuse, composability and interoperability were not high priorities
15

## Slide 16: Modern Interoperability Approaches
Standardize on the Data Model
  Data Model is the defined network protocol or message format
  This defines the data needed to interoperate
Standardize on a software Application Programmers Interface (API)
  Provides software interface to interoperability services and solutions for distributed simulations
Standardize on Processes
  These Modular Open Systems Architecture (MOSA) concepts enable success and solution flexibility … now and in the future
16

## Slide 17: Interoperability Standard: Data Models
Technical Level
(networking)
Syntactic Level
(data exchange)
Semantic Level
(information exchange)
Pragmatic/Dynamic Level
(common use of information)
Conceptual Level
(common understanding
of information)
Levels of Interoperability (Tolk)
Object Model
A document describing the data that will be exchanged
Enable semantic interoperability among simulation applications
Provide the “common language” that all simulation applications use to communicate
Data Models = Object Model(OM) = Data Exchange Agreement (DEM)
Airplane!
17
Notes: The FOM describes the information exchange in a federation. It is different for defense, space, manufacturing, etc
The HLA standard defines a format or an Object Model Template for how to define the language needed to exchange the required data.
With the HLA Evolved update of the standard it is possible to use FOM modules and extend existing modules without ´breaking backward compatibility.

## Slide 18: Interoperability Standard: API
Application Programmers Interface (API) is a software interface to software services that enable interoperability
  Time Management
    Manage and synchronize time between participating applications
  Quality of Service (in simulation)
    Services for managing how data is distributed on the network
  Ownership Management
    Transfer of modelling responsibility from one participating application to another
  Data Distribution Management, DDM
    Data filtering based on regions or any other attribute to reduce data load
  Remote Method Invocation, RMI
    Participating applications can have methods that can be remotely invoked by other applications
  These services have made significant enhancements to LVC interoperability. Understanding these capabilities and implementing them using common practices improves performance and reduces risk
18

## Slide 19: Interoperability Standards: Integration Process
A well-defined Integration Process is critical to success
  First step in planning for an LVC Environment is identification and adoption of a proven process to support the design, integration and execution of the environment
  To ensure the environment is designed and configured to meet the event requirements, a structured process is necessary to properly identify needs, deigns and solutions.
    Several standard, and proven, processes exist.
    Do not add risk to your program by “winging it” through a very complex endeavor

## Slide 20: Open Standards
According to the Software Engineering Institute a system is open if:
  It is fully defined
  Available to the public
  Maintained according to group consensus
Support Organizations for Interoperability Standards include:
  Institute of Electrical and Electronics Engineers (IEEE) https://www.ieee.org/standards/index.html
  Simulation Interoperability Standards Organization(SISO) https://www.sisostds.org/
  TENA Architecture Management Team https://www.tena-sda.org
20

## Slide 21: The “Big 3” LVC Interoperability Architecture Standards
Test and Training Enabling Architecture (TENA)
  API standard –auto-generated user software for quality and usability
  Semantic model expressed in a Standard Object Model
  Includes standard object model, extensive middleware services and a set of interoperability & event support tools
High Level Architecture (HLA) – IEEE 1516-2010 and NATO STANAG 4603
  API standard
  Separate semantic model expressed in a (Federation) Object Model
  Services standard – A rich set of interoperability services
Distributed Interactive Simulation (DIS) - IEEE 1278
  Protocol standard
  Covers several levels of interoperability
  Broadcast/Multicast UDP (Best effort)
Interoperability Standard:
Data Model
Interoperability Standard:
Data Model, API & Process
Interoperability Standard:
Data Model, API & Process
21

## Slide 22: Interoperability vs Interconnectivity
LVC “Interoperability” requires data exchange with other systems without requiring modification to already connected systems, thus permitting flexible connections.
“Interconnectivity” involving some data exchange protocols requires system-wide changes, recompilations of source code, re-linking to new software libraries, etc, thus implementing specific connections.
Many (an infinite number?) of data messaging methods exist. Examples are:
22

## Slide 23: Interoperability vs Interconnectivity
Data Distribution Service (DDS)
  API standard
    Available through the Object Management Group (OMG) … www.omg.org
    For real-time interconnectivity of systems exchanging data via DDS
    Common application is for “Internet of Things” (IoT), to enable interconnected systems to exchange data over a network
  DDS uses some similar concepts as TENA and High Level Architecture (HLA)
    Publish-Subscribe architecture
    Data model … HLA has a “Federation Object Model” … DDS has a “Data Space”
  Targeted use = interconnectivity, e.g. Internet of Things (IoT) applications
  Does not provide runtime interoperability services (e.g. time management) like HLA
  Cannot be used in place of HLA but could be used in conjunction with HLA
  Often confused item:
    HLA has a “Run Time Infrastructure” (RTI) … DDS has no equivalent
    The best known company providing DDS software is “Real-Time Innovations” (RTI)
23

## Slide 24: Timeline Of Interoperability Standards
DIS v7
2012
Space FOM
2018
NATO standard NETN FOM
2013
2010
early 2023
RPR FOM
DIS v8
2023+
TENA V6.0.5
2016
TENA V6.0.7
2019
24
TENA V6.0.8
2021
TENA V6.0.6
2018
TENA V6.0.9
2022

## Slide 25: Distributed Interactive Simulation (DIS) Overview
DIS IEEE 1278 is an “Over the Wire” specification
  Defines the structure of data sent over the network
  using a Protocol Data Unit (PDU)
  Is a binary protocol where individual bits are defined and bit order and byte order is mandated
  Defines behavior of message handling. Receiving participants must review each packet for applicability
  Does not include an “API” or implementation details or solutions
  Follows the COTS and Open Source business models
  Primarily focuses on military systems/requirements
DIS participants must Broadcast or Multicast data on a local network using UDP network transfer protocol
DIS
Applications
Network
25

## Slide 26: Distributed Interactive Simulation (DIS) Example PDU
Examples: DIS “Entity Type” PDU
  USAF F-16C Falcon
    Entity Kind = 1
    Domain = 2
    Country = 225
    Category = 1
    Sub Category = 3
    Specific = 3
    Extra = 0
DIS
Applications
Network
26
  USAF F-22B Raptor
    Entity Kind = 1
    Domain = 2
    Country = 225
    Category = 1
    Sub Category = 6
    Specific = 2
    Extra = 0

## Slide 27: High Level Architecture (HLA) Overview
Defines services for simulation data exchange and coordination provided by a Run-Time Infrastructure (RTI)
Services are accessed through a standardized interface.
A data model (Federation Object Model FOM) expressed in a standardized text file, using the xml standard, defines how objects interact with each other
Information exchange governed by Federation Agreements and supporting federation Information Data Exchange Models (IDEM)
  e.g. when, where and how to utilize the service to distribute data in order to exchange information
Uses COTS and Open Source business models
Federates
RTI Services
HLA API
Federation Management
Declaration Management
Object Management
Federation Object Model
<FOM>
<Shared object classes>
<Shared interaction classes>
<More>
</FOM>
Ownership Management
Time Management
Data Distribution Management
27

## Slide 28: DIS and HLA Data Model & Standardization
“Objectification”
DIS IEEE 1278 Data Model
Physical Entities
Aggregates
Radio
Logistics
Synthetic Environment
Warfare
Underwater
Acoustics
Minefield
Simulation Management
Emissions
DIS and HLA are maintained through SISO
- Government
Industry
Academia
- Etc
- COTS, GOTS
In-house
Open source
- Other
Research
Student projects
Courses
HLA Real-time Platform Reference FOM (RPR-FOM) SISO-STD-001
IEEE is the external standards body for SISO
28

## Slide 29: TENA Overview
What does TENA enable?
  Interoperability between inter- and intra-range systems
  Elimination of proprietary interfaces to range instrumentation
  Efficient incremental upgrades range capabilities
  Integration of Live, Virtual, and Constructive assets (locally or distributed)
  Sharing and reuse of common capabilities across existing and new investments
What is included in the TENA architecture?
  Customizable “data contracts” that standardize repeatable information exchange
  Interoperability-enabling, auto-code generated software libraries
  A core set of tools that address common test and training requirements
  Collaboration mechanisms that facilitate sharing and reuse
TENA is continuing to be evolved and has institutional funding from DoD
TENA is the DoD GOTS live range integration architecture

## Slide 30
TENA-Enabled Interoperability
Common specifications for test and training data
Data Dissemination across variable applications, platforms,
programming languages, networks, and classification levels
Data Collection and Playback
Local and Remote Command and Control
Health & Status Monitoring
Simulation Interoperability(Virtual, Constructive, Digital Twin)
Integration of live sensors and instrumentation
Connecting range systems using Gateways, Adaptors and Transmogrifiers
Eliminating proprietary interfaces to range instrumentation
Sharing and reuse of common range tools and capabilities
Online Collaboration and File Sharing
Data Management
Event Management
Sharing & Reuse
LVC Integration

## Slide 31: Test and Training Enabling Architecture (TENA) Overview
Non-TENA Applications
Range Resource
Application
Reusable Applications
Reusable Applications
Non-TENA Communications
TENA
Range Resource
Application
Data Collectors
HWIL
Range Resource
Application
Repository Utilities
TENA
Object
TENA
Object
TENA
Object
Infrastructure Management and Planning Utilities
Object Model Utilities
TENA Utilities
TENA Common Infrastructure
TENA Applications
Non-TENA System
Non-TENA System
TENA Tools
Gateways
TENA Middleware
TENA
Repository
TENA Middleware
Logical Range Data Archive
100% Government off the Shelf (GOTS)
  Initially developed to support the demands of live system testing
  Provides tools for common Event Planning, Execution, and Analysis functions
  Provides Subject Matter Experts to support distributed exercise and system integration
  Community-managed Open Architecture and Standards
  Constantly improved to meet new user requirements
  Download TENA Middleware and tool set
    http://www.tena-sda.org
31

## Slide 32: TENA Data Model & Standardization
The DoD maintains the extensive and extendable TENA Standard Object Model V2.0
TENA-LVC OMs align with DIS IEEE 1278 PDUs
32

## Slide 33
TENA-Enabled Interoperability
Gateways – Applications that enables interoperability with existing protocols (TENA to Many)
Adapters – Similar to Gateways but are purpose built to a legacy system (TENA to One)
Transmogrifiers – Fun name given to a gateway that enables interoperability between legacy TENA and current TENA OMs

## Slide 34: TENA Tools
34

## Slide 35: TENA Adapter Library

## Slide 36: Recommended Integration Approach
Identify a Common Architecture
  Utilize horizontal Integration using Enterprise Service Bus (ESB) concept (HLA, TENA, etc.) when possible
ESB Provides Ability to Meaningfully Communicate for Reuse and Composability
  Standard Data Model to describe the data communicated
  Standard Services Interfaces (API)
    Software provides the Standard Services using Standard APIs
          e.g. Services to distribute the data model
Subsystems are called Federates. The Integrated System is called a Federation.
Federates
Software infrastructure
API and
Data Models
36

## Slide 37: Identify Integration Process
Suggested standards and guidelines include
  IEEE Std 1730-2010 - IEEE Recommended Practice for Distributed Simulation Engineering and Execution Process (DSEEP)
  IEEE Std 1730.1-2013 - IEEE Recommended Practice for Distributed Simulation Engineering and Execution Process Multi-Architecture Overlay (DMAO)
  TENA Concepts of Operations (CONOPS)
HLA Distributed Simulation Engineering and Execution Process (DSEEP) Overview
  IEEE 1730-2010 was developed based on authoritative systems engineering processes that were adopted and extended to address distributed simulation requirements
  Identifies and describes the sequence of activities necessary to construct and run distributed simulations
  A high-level process that is relevant to and can facilitate the development of solutions
  Is independent of interoperability architectures
6
5
4
3
1
Perform Conceptual Analysis
2
Analyze Data and Evaluate Results
7
Define Simulation Environment Objectives
Design Simulation Environment
Develop Simulation Environment
Integrate and Test Simulation Environment
Execute Simulation Environment

## Slide 38: Focus on Integration Process and Communication
Tools that enable the process are effective at communicating event design across the team
  Clear communication reduces risk and optimizes event execution and data collection
  These diagrams ensure clear communication and ensures event implementation mirrors design
  Key data includes: Location, IP, Port, Protocol, messages, and system names
Notional Interface Matrices and Connectivity Diagrams
For additional information and diagram clarity, please attend I/ITSEC 2022
“Distributed LVC Event Process Workshop”
Zinzer, LeSueuer, Boren, O’Connor
Friday 0800, Room 307C

## Slide 39: 4. Interoperability Using Gateways
Complex LVC environments may require interoperability between simulation federations using different architectures
Gateways are bridges between different simulation architectures
  Examples:
    TENA used at a test range interoperating with other facilities using DIS, HLA, or both
    Legacy DIS-based system interoperating with newer HLA-based system
DIS v7
HLA/DIS Gateway
HLA 1516-2010
HLA
DIS
Example gateway
39

## Slide 40: Interoperability Using Gateways
Gateways
  Translate data and services between different middleware, object models, and services
  Can filter data, transferring some data while blocking other data
  Can provide logging, monitoring, and detection and notification of errors or issues
Caution: Placing a gateway may create a single point of failure for the system. Careful system design can minimize this potential problem.
A top level “system design” trade-off analysis that considers schedules, costs, technical factors, etc., should determine the best of two implementation methods
  Selecting a common architecture for the entire LVC environment, or
  Implementing, integrating, testing, operating and maintaining gateways.
40

## Slide 41: Interoperability Using Gateways
Commonly used gateways are available as Commercial Off-The-Shelf (COTS) products from numerous vendors.
  Check carefully the product’s list of translated data types, models, and services!!
TENA-related gateways can be downloaded from the TENA website.
Sometimes unique modifications are needed, especially when a gateway is interfaced to a “stove-piped” (non-standards-based) system.
41

## Slide 42: Multiple Levels of Security
Definitions:
Security Domain
  System or group of systems operating under a common security policy
Cross Domain Solution (CDS) … aka Multi Domain Operations (MDO)
  An information assurance solution that provides the ability to access or transfer information between two or more security domains
  Enables data transfers between Unclassified, Secret, Top Secret, Top Secret/SCI
When establishing a complex distributed environment, information transfer between two or more security domains may be needed
  Most organizations do not have any effective means to address this issue
    As a result, too often the “solution” is a brute-force denial of access to information, thus severely limiting system effectiveness

## Slide 43: Purpose of Cross Domain Solutions
Low Security Domain
Network 1
High Security Domain
Network 2
Filter Decisions
Block
Sanitize
Pass
Rule Set
Logic, Math, & Comparative Operations
Enforces Relevant Security Classification Guidance
  The CDS default state is to block all traffic.
  Data owner guidance is implemented through user-definable, event-specific, Rule Sets.
  Rule Sets define if and how designated traffic can pass through.
    Rules must support event objectives and classification guidance.
      Logical operations (e.g. AND, OR, NOT)
      Mathematical operations involving object attributes (e.g. addition, subtraction, multiplication, division, exponents, logs, trig)
      Comparative operations (<, ≤, >, ≥, =): how object attributes relate to fixed values
Level of Trust
(totally open)
(totally protected)

## Slide 44: CDS: Multiple Protocol Example
Gateways enable broader use of existing CDSs
CDS
HLA/TENA Gateway
HLA Source
HLA Destination
Unclassified Network
Classified Network
There are two federations running in different Security domains, each using HLA to interoperate
The example CDS meets requirements yet has a native interface
Gateways are used to translate between HLA-based simulations and TENA
Approach enables HLA-based environments to use existing TENA-based CDS
HLA/TENA Gateway
TENA
HLA

## Slide 45: 5. LVC Interoperability Use Case
The Task: A ground-based Command and Control (C2) system is being enhanced and must be tested.
  The present test method stimulates the C2 system under test with real data sent from a live aircraft via a Tactical Data Link (radio).
  This is a *very* expensive way to test a ground-based C2 system.
  Great savings would be achieved if the tests used a flight simulator instead of a real aircraft.
C2 system under test
Tactical Data Link (TDL), e.g. Link16

## Slide 46: LVC Interoperability Use Case
An available flight simulator has a Link 16 “Data Link Processor” (interface), so the flight simulator can be used to stimulate the C2 system under test.
C2 system under test
Tactical Data Link (TDL), e.g. Link16
Data Link Processor
  Everything’s good … right?

## Slide 47: LVC Interoperability Use Case
Analysis of the “real world” reveals:
  The flight simulator has an older HLA 1.3 interface … and uses a vendor-modified version of the RPR-FOM (“Didn’t anyone tell them to avoid building stove-pipes?!!”)
  A scenario generator, with DIS & SIMPLE interfaces, is available to insert simulated tracks of other aircraft into the Link 16 network.
  The data link processor has a SIMPLE interface.
  Link 16 is represented in two ways, standards-based and non-standards-based.
C2 system under test
Tactical Data Link (TDL), e.g. Link16
Data Link Processor
HLA 1.3 with proprietary additions to FOM
Scenario
Generator
SIMPLE
DIS

## Slide 48: LVC Interoperability Use Case
C2 system under test
Tactical Data Link (TDL), e.g. Link16
Data Link Processor
HLA 1.3 with proprietary additions to FOM
Scenario
Generator
SIMPLE
DSEEP-driven feasibility study suggested:
  Use HLA as the common interoperability solution
  Insert an HLA to HLA bridge to filter/modify vendor-specific (non-standard) RPR-FOM extensions
  Use a gateway from HLA/RPR-FOM to DIS, to connect with the Scenario Generator
Some Limitations Accepted:
  Simulator data is accepted as the “ground truth”
  “J messages” from flight simulator are not bridged
  No voice communications
Gateway
HLA-DIS
Bridge
HLA 1.3 to
HLA 1516
DIS
standard HLA 1516

## Slide 49: LVC Interoperability Use Case
Integration spiral demonstrated:
  Selecting HLA as a standard was appropriate due to HLA technology and performance plus existing HLA-based solutions and experience
  RPR-FOM extensions, HLA to DIS gateway, and HLA to HLA bridge concepts were acceptable
  The DIS network did not work due to computer clocks not being in sync (or set correctly)
  The scenario generator’s DIS interface only worked in one direction
  Security aspects needed further analysis
Success! Initial tests produced good results with previously known limitations
Additional actions required:
  Updating the Scenario Generator’s DIS interface
  Getting approval from responsible authorities to synchronize the computer clocks
  Getting approval to run tests with a dedicated Link16 network and the participating real aircraft on the ground (when the flight simulator was not being used as a substitute for the real aircraft, and to validate data)
49

## Slide 50: 6. Summary: Standards
There are several standards available for Live-Virtual-Constructive interoperability
  Some are especially made to support simulation
  Some are focused on use with live systems
Standards needs to be maintained and updated
  New requirements emerge over time
Standards need to be balanced between stability and flexibility
  Stable enough to allow systems to be developed that support the same version of the standard
  Flexible enough to be useful and support current requirements plus new and evolving requirements

## Slide 51: Summary: Standards (2)
Standards should not be selected only on technical merits
  A “Community of Users” helps tremendously
    Ensures long-term use of a standard … avoids obsolescence
    Promotes evolution of a standard
    Communication forum about common LVC applications, problems, and solutions
  Industry Support (the marketplace) is very important
    Government and Commercial Off-The-Shelf (GOTS/COTS) products, generally costing less than custom-developed solutions
    On-demand training courses
    On-demand technical assistance
    Promotes adoption and evolution of standards (e.g. trade show demos)
Organizations should try to use a limited number of interoperability LVC standards
  Deviations must be expected to fit unusual situations
  Develops “in-house” skills and experience that will be needed on future programs
  Adopt Gateways as initial approach to integrate disparate architectures

## Slide 52: Summary: Standards (3)
Integrating LVC-based systems via distributed simulation is a powerful capability
  LVC interoperability across domains, e.g. involving multiple military groups, creates operationally realistic environments
        Supplementing a single system with other LVC systems greatly enhances realism of training
          The whole is greater than the sum of its parts
        Integrating C2 systems with LVC systems builds environments that are operationally realistic
            “Train As We Fight”
  Standards enhance integration and reuse of other LVC assets, tools and technologies
  Standards eliminate or greatly reduce time, cost, and performance risks of developing specialized systems (remember: “Avoid stove-pipes.”)
  Standards-based instrumentation and management functions within an environment provide coordination of planning and execution, data collection and analysis, and repeatability
  Leveraging existing standards and existing networks let program managers “do more with less”

## Slide 53: Summary: Standards (4)
Distributed simulation has advanced greatly since first attempts in the 1980’s. Simulation developers today can establish LVC environments to solve very complex problems, at the System of Systems level, relatively easily and quickly.
  Selection of the appropriate interoperability architecture … DIS, HLA, or TENA … is sometimes at the user’s discretion, but other factors may favor one architecture over the others, such as technical features, the need to connect with systems already in place, or organizational policies.
  Be sure to choose between DIS, HLA, or TENA, based on current information!
    We’re in the year 2022 now, not 1986, 2000, or even 2010
Best advice…Get involved!!!
53

## Slide 54: Bibliography
IEEE Std 1278.1-2012 - IEEE Standard for Distributed Interactive Simulation Application Protocols, IEEE Standard 1278.1, 2012.
IEEE Std 1516.1-2010 (Revision of IEEE Std 1516.1-2000) - IEEE Standard for Modeling and Simulation (M&S) High Level Architecture (HLA)-- Federate Interface Specification, IEEE Standard 1516.1,2010
IEEE Std 1516-2010 (Revision of IEEE Std 1516-2000) - IEEE Standard for Modeling and Simulation (M&S) High Level Architecture (HLA)-- Framework and Rules, IEEE Standard 1516,2010
IEEE Std 1730-2010 - IEEE Recommended Practice for Distributed Simulation Engineering and Execution Process (DSEEP) , IEEE Standard 1730, 2010
Powell, Edward, et al (2006). Test and Training Enabling Architecture (TENA) Architecture Reference Document (ARD), Office of the USD(AT&L) Test Resources Management Center (TRMC), 2016
Tolk, Andreas, et al (2003) The Levels of Conceptual Interoperability Model, 2003 Fall Simulation Interoperability Workshop, 2003
Websites
TENA Project: https://www.tena-sda.org/.