## Slide 1
Sharing Environmental Data for LVC using RIEDP
(Tutorial 22T32 )
Reuse and Interoperation of Environmental Data and Processes (RIEDP)
Jean-Louis GOUGEAT (jlgougeat@sogitec.fr )

## Slide 2: Tutorial Objectives
At the completion of this tutorial the attendee will be able to:
  Identify the main interoperability and reuse issues associated with use of terrain/environmental data in distributed simulation
  Discuss the general process steps in creation of environmental databases, and the various data involved
  Describe the two SISO RIEDP Products, their role, and their main components
  Employ the appropriate RIEDP products and principles to efficiently share environmental databases
  Contrast details of the RIEDP components with the issues to solve
  Judge the use of RIEDP in a simulation project
  Support the evolution of the RIEDP Products
Product = Result of a SISO standardization effort
Non-commercial !
RIEDP : Reuse and Interoperation of Environmental Data and Processes

## Slide 3: Problem – Importance - Relevance
What is the problem
  Building terrain databases still very expensive
  Sharing saves cost, and also increases consistency, but …
  Shared data often not clear - Conventions and Semantics not always uniform or standardized
  This leads to interoperability problems and high costs
Why is this important
  Consistency in Terrain Representation key to Fair Fight in Distributed Simulation / LVC
  Consistency required for Services, Joint and International /Coalition Training
Who should care
  Customers/Users, Program Managers, Engineers in Distributed Simulation / LVC
  Interested in stand-alone or networked M&S applications, including visualization, training, analysis, rehearsal, testing (using traditional, VR, or AR visualizations)

## Slide 4: How RIEDP adresses this
RIEDP is a SISO standard for communicating and sharing environmental data
Building M&S environmental data products (or databases) requires various types of source data, including (but not limited to) data in popular GIS formats
RIEDP leverages those popular formats and standardizes a comprehensive framework comprising:
  A data generation process model to align/understand completeness of shared terrain data
  A data model to represent and organize terrain data, and
  The semantics, rules, methods and conventions to unambiguously share the data
RIEDP does not impose internal solutions on data producers
RIEDP : Reuse and Interoperation of Environmental Data and Processes

## Slide 5: Agenda
The Operational Context
The RIEDP Approach
The RIEDP Components
  RPM Stages
  RADM
  RADM Parts
Semantics for RIEDP data sharing
RIEDP and Other Similar Initiatives
Summary and Q/A
RIEDP : Reuse and Interoperation of Environmental Data and Processes

## Slide 6: The Operational Context

## Slide 7: Live Virtual Constructive Training
At Stake : Avoiding duplication of costs, Inconsistency during execution, …
Solution : Standard? But not if every Organization has its own!
HLA or other Protocol
Ground Based Air Defence
Computer Generated Forces
Real Actors
Exercise Controller
Heavy Constraints on
Synthetic Environment
Full Mission Sim 1
Full Mission Sim 2

## Slide 8: SE Requirements for an Aircraft Simulator (1/7)
Large Areas
Diversity of Terrain Natures

## Slide 9: SE Requirements for an Aircraft Simulator (2/7)
Large Areas
Diversity of Terrain Natures

## Slide 10: SE Requirements for an Aircraft Simulator (3/7)
Large Areas
Diversity of Terrain Natures

## Slide 11: SE Requirements for an Aircraft Simulator (4/7)
Large Areas
Diversity of Terrain Natures
Diversity of Target applications
(Visual, Sensors, IOS, CGF, C2…)

## Slide 12: SE Requirements for an Aircraft Simulator (5/7)
© Images courtesy of Aditerna
Can you see the Tank at the edge of the treeline ?
Well, it is not really in the edge of the treeline !!

## Slide 13: SE Requirements for an Aircraft Simulator (6/7)
NATO “Missionland”
2000x2000 km

## Slide 14: SE Requirements for an Aircraft Simulator (7/7)
  Elevation Grid: 25 m
  Elevation Grid: 1 m

## Slide 15: Building a Simulator Database
Source
Data
Database
Creation
Target
Databases
Visual DB
Radar DB
Infra Red DB
Other Sensors
Maps
CGF DB
Others
Geospatial & Others
Find the data
Solve IPR
Clean the data
Correlate the data
Create missing data
Format the data
Intensify the data
Specialize the data
Operate !
€ / $
Database Requirements
Not so Easy

## Slide 16: Terrain Database Generation – A Universal Process
Images courtesy of their respective programs
It looks very similar
But the Devil is in the details

## Slide 17: Additional issues for Distributed Simulation / LVC Reuse – Correlation – Interoperability …. (1/2)
Sim A - Provider 1
Sim C – Provider 3
Sim B - Provider 2
Requirements

## Slide 18: Additional issues for Distributed Simulation / LVC Reuse – Correlation – Interoperability …. (2/2)
Sim A - Provider 1
Sim C – Provider 3
Duplication of efforts
Duplication of Cost
Time to market
Consistency ?
Schedule ?
Sim B - Provider 2
Requirements
M&S Interoperability is
even more critical in the International Arena
with
Multiple Providers and Multiple M&S Solutions

## Slide 19: Examples of Interoperability issues in Large Exercises
Events: I/ITSEC Operation Blended Warrior (OBW), NATO MSG-165 Spartan
Typical Issues
  Many points of view: Ops Team, Tech Team, Sim. providers, data providers/consumers …
  Different understanding – sometimes wrong understanding – of the concepts
  Communication/Miscommunication, Semantics (Example case – Sample dialog)
Significant contributors to these Semantics problems:
  Terrain-related issues
  Interchange standards
Interoperability and reuse suffer from these issues
  Critical in the International Arena with Multiple Providers and Multiple M&S Solutions

## Slide 20: M&S Interoperability
What it is NOT
  The same Product and associated Solutions for everyone
    Does not work, certainly not in the International Arena
    Puts Innovation at risk
    What product to choose? Single Solution sufficient? What constraints?
What it is
  Consistency in Modelling, associated Data and Semantics at Component Level
  Allowing Components to work together at System & System-of-Systems Levels
  Fostering Multiple-Provider Solutions (e.g. : I/ITSEC/OBW Federations)
Simulation Interoperability relies on Appropriate Standards
  Open, based on Consensus, not Vendor Specific
  Within the simulation community : SISO
SISO : Simulation Interoperability Standard Organization

## Slide 21: The RIEDP approach

## Slide 22: Data Transformation Process – Two main phases (1/3)
Database
Creation
Target
Databases
Visual DB
Radar DB
IR DB
Other Sensors
Maps
CGF DB
Others
Source
Data

## Slide 23: Data Transformation Process – Two main phases (2/3)
Target
Databases
Phase 1
Data
Cleaning &
Enhancement
Phase 2
Target
DBs
Generation
Visual DB
Radar DB
IR DB
Other Sensors
Maps
CGF DB
Others
Source
Data
Synthetic
Environment
Intermediate
Data
GIS World
M&S World

## Slide 24: Data Transformation Process – Two main phases (3/3)
Target
Databases
Phase 1
Data
Cleaning &
Enhancement
Phase 2
Target
DBs
Generation
Visual DB
Radar DB
IR DB
Other Sensors
Maps
Manual Work: 80% 20%
Computation Time: 20% 80%
CGF DB
Others
Source
Data
Synthetic
Environment
Intermediate
Data
GIS World
M&S World
Standardize here
at appropriate Intermediate stages

## Slide 25: Source Data from Various Origins
  From GIS world : DTED, DFAD, VMAP, SHAPEFILE, GEOTIFF, GML, KML, …
    Application to simulation
      Elevation, Vector (roads, rivers and building positions), Geo-referenced satellite imagery
  From Photography World : BMP, ECW, JPEG, JPEG 2000, RGB, TIFF™
    Application to simulation
      Texture for Terrain or objects to add visual realism, without complex geometric models
  From Architecture/Game Worlds : COLLADA, OpenFlight™, VRML, X3D, …
    Application to simulation
      Formats from 3D modelers (e.g. 3DS ™, Maya ™, Creator ™, ... )
      Application to simulation : Dedicated to 3D Objects modeling for visual Systems.
Notes: 25

## Slide 26: Phase1 : Generation of the Intermediate Datasets
Source Dataset
Elevation
Imagery
Planimetry
3D Models
Intermediate
Dataset
Elevation (Tiled )
Imagery (Tiled )
Classification
Planimetry
& Attribution
3D Models
Projection Conversions
Format Conversions
Tiling (mosaïc)
Harmonisation (between Tiles)
Corrections of Source errors
Reconciliation between Layers
Material Classification
Attribution Definition
Assignation of 3D models to Classes
Definition of Procedural Generation Rules for Features (Off or on line)
Attribution Definition
Creation of new models in Library
Geographical
Added Value
Simulation
Added Value

## Slide 27: Phase 2 : Generation of Target DBs
Creation of 3D Terrain (Polygons, Levels of Detail, …)
Texturation (projection of images on the 3D Terrain)
3D Terrain
Geo-specific
Textures
Enrichment of terrain with 3D elements (Cultures, Buildings, Networks,..)
3D objects
Competition  Proprietary
Solutions & Formats
Intermediate
Datasets
Elevation (Tiled )
Images (Tiled )
Classification
Features
& Attribution
3D Models
Runtime DB

## Slide 28: Data Transformation Process – Possible Improvement (1/4)
The process may be made more efficient in Mission Training via Distributed Simulation (MTDS)
Though Manuel work
being reduced with AI/ML

## Slide 29: Data Transformation Process – Possible Improvement (2/4)
The process may be made more efficient in Mission Training via Distributed Simulation (MTDS)
Hardly Reusable
(Unless same target platforms)
Competition
Various Trade-offs

## Slide 30: Data Transformation Process – Possible Improvement (3/4)
The process may be made more efficient in Mission Training via Distributed Simulation (MTDS)
  If Source data is comprehensive and consistent
    Within each and between the layers  Depends on Data Providers
  If previous creation efforts may be reused
    At Source Data Level (Linked to GIS World)
Discovery & Access
Metadata
Repository
Data Diversity
Data Quality
Providers
Hardly Reusable
(Unless same target platforms)
Competition
Various Trade-offs

## Slide 31: Data Transformation Process – Possible Improvement (4/4)
The process may be made more efficient in Mission Training via Distributed Simulation (MTDS)
  If Source data is comprehensive and consistent
    Within each and between the layers  Depends on Data Providers
  If previous creation efforts may be reused
    At Source Data Level (Linked to GIS World)
    At Intermediate Level
    Requires Common Processes, Representations, and Formats at this level
Discovery & Access
Metadata
Reuse of Intensification efforts
Repository
RIEDP
Data Diversity
Data Quality
Providers
Hardly Reusable
(Unless same target platforms)
Competition
Various Trade-offs

## Slide 32: Key Topics for Database sharing
When reusing data from a partner, you need to know
  How the database was built  Tasks performed or not
  How the database is represented  Conceptual Model
  How the database is spatially referenced  Spatial Reference Model
  How the database is structured  Physical data model
  How the database is organized on the media  Files/Folders/Hierarchies
  How well the database conforms to Standards  Compliancy & Profiles
  Information about the data product  Metadata
No existing solution fully satisfies all of these requirements

## Slide 33: International M&S Initiatives & Standardization Efforts (1/2)
Nature | M&S standards |  | Projects / Initiatives |  |  |  |  |  | Geospatial
Name | SIF | SEDRIS | NPSI | AFCD | MDB | CDB | Mission Land | Other | OGC CDB
Origin | US DOD | US DOD | US Navy | USAF | US Army | US SOCOM | NATO | e.g. French Air Force | PRESAGIS
Introduction Date | 1991 | 1994 | 2004 | 2006 | 2008 | 2004 | 2010 | 2006 | 2013
Publication Date | Yes | 2005 | - | - | - |  |  |  | 2016
Standard | Yes | Formal ISO/IEC | User Standard | User Standard | User Standard | User & Commercial Standard | User Standard | User Standard | Formal OGC
Open Standard | Format according to standard | Yes | limited | limited | limited | Limited | limited | limited | Yes
Approach | Obsolete | Standardized Semantics and Data Model + Format according to standard |  |  |  |  |  |  | Similar to US SOCOM CDB but with formalized semantics and Conceptual Data Model
Availability of Commercial Support Tools | SIF | Tools developed in SEDRIS COI |  |  |  |  |  |  | PRESAGIS tools
  AFCD: Air Force Common Dataset
  EDS: Enterprise Data Services
  NPSI: NAVAIR Portable Source Initiative
  CDB: Common Database MDB : SE Core Master Data Base
  SIF: SSDB (Standard Simulator Database) Interchange Format
Process oriented
DB oriented
Based on de-facto standard formats (GIS Source)
but
- No consistent Semantics or Data Model
- Similar but not Standard Data Generation Process
Commercial tools
for commercial & standard formats

## Slide 34: International M&S Initiatives & Standardization Efforts (2/2)
Nature | M&S standards |  | Projects / Initiatives |  |  |  |  |  | Geospatial
Name | SIF | SEDRIS | NPSI | AFCD | MDB | CDB | Mission Land | Other | OGC CDB
Origin | US DOD | US DOD | US Navy | USAF | US Army | US SOCOM | NATO | e.g. French Air Force | PRESAGIS
Introduction Date | 1991 | 1994 | 2004 | 2006 | 2008 | 2004 | 2010 | 2006 | 2013
Publication Date | Yes | 2005 | - | - | - |  |  |  | 2016
Standard | Yes | Formal ISO/IEC | User Standard | User Standard | User Standard | User & Commercial Standard | User Standard | User Standard | Formal OGC
Open Standard | Format according to standard | Yes | limited | limited | limited | Limited | limited | limited | Yes
Approach | Obsolete | Standardized Semantics and Data Model + Format according to standard |  |  |  |  |  |  | Similar to US SOCOM CDB but with formalized semantics and Conceptual Data Model
Availability of Commercial Support Tools | SIF | Tools developed in SEDRIS COI |  |  |  |  |  |  | PRESAGIS tools
  AFCD: Air Force Common Dataset
  EDS: Enterprise Data Services
  NPSI: NAVAIR Portable Source Initiative
  CDB: Common Database MDB : SE Core Master Data Base
  SIF: SSDB (Standard Simulator Database) Interchange Format
Process oriented
DB oriented
Based on de-facto standard formats (GIS Source)
but
- No consistent Semantics or Data Model
- Similar but not Standard Data Generation Process
Commercial tools
for commercial & standard formats
RIEDP addresses these Topics
(see how in RPM and RADM)

## Slide 35: RIEDP – Two Products
RIEDP provides what is needed to share Environmental data :
  A Reference Process Model (RPM)
  A Reference Abstract Data Model (RADM)
  A Tiling Scheme and Spatial Referencing
  A List of Formats from the GIS and M&S worlds
  A Consistent Semantics (through Features, attribution rules)
  An Organization on the Media
  A Metadata structure
  A set of Exchange Profiles
Product 1: RIEDP Data Model Foundations
Product 2: RIEDP Detailed Features Description

## Slide 36: Status of RIEDP Products
Product 1 - Published in 2018 as SISO-GUIDE-007-2018
  Included by NATO Standardization Office (NSO) in AMSP-01
    NATO Modelling And Simulation Standards Profile
  Used by NATO Group MSG-156 for semantics in Dynamic Terrain
  Ideas from Product 1 are used in a few initiatives (but w/o credit to RIEDP!)
Product 2 - Development of semantics is in-progress
  Expected completion: 2023
  Addressing challenging problems for the representation of sensor/material semantics while providing non-proprietary XML-based solution
AMSP : Alliance Modelling and Simulation Publication

## Slide 37: Building on existing work – Bibliography
Partial bibliography of documents used in Product 1 and/or Product 2
Reference | Date
RIEDP Data Model Foundations - SISO-GUIDE-007 | August 2018
Environmental Data Coding Specification (EDCS) - ISO/IEC 18025:2014 | February 2014
ESRI Shapefile Technical Description - ESRI White Paper | July 1998
GeoTIFF Format Specification - Rev 1.0 - Specification Version 1.8.2 | November 1995
JPEG 2000 image coding system: Core coding system- ISO/IEC 15444-1:2004 | September 2004
OpenFlight Scene Description Database Specification - version 16.5 | February 2016
Portable Network Graphics (PNG): Functional specification - ISO/IEC 15948:2004 | March 2004
SGI (RGB-RG) Image File Format - Draft version 1.00 (ftp://ftp.sgi.com/grafica/sgiimage.html) | 1996
Reference for Enumerations for Simulation Interoperability - SISO-REF-010-2019 (V27) | 14 October 2019
Spatial Reference Model (SRM) - ISO/IEC 18026:2009 | July 2009
Unified Modeling Language (UML) Version 1.4.2 - ISO/IEC 19501:2005 | April 2005
Data elements and interchange formats - Information interchange Representation of dates and times - ISO 8601:2004 | December 2004
Codes for the representation of names of countries and their subdivisions - Parts 1-3 - ISO 3166:2013 | November 2013
AMSP-01 - NATO Modelling And Simulation Standards Profile | 2022

## Slide 38: The RIEDP Components: The RPM
Reference Process Model

## Slide 39: RIEDP Reference Process Model / Process Flow (1/2)
  Standardized model of Typical Generation Process for a Database

## Slide 40: RIEDP Reference Process Model / Process Flow (2/2)
  Standardized model of Typical Generation Process for a Database
Requirements
7 Creation Stages
Target DB Stage
Export Stage
Using RIEDP does not require
changes to the user’s workflow

## Slide 41: RIEDP Reference Process Model - Data Flow
Runtime Stage
Export Stage
See RPM details in Product 1 - § 4.2.2

## Slide 42: The RIEDP Components: The RADM
Reference Abstract Data Model

## Slide 43: Main Components of a Database
Elevation
Imagery
Repository
Features
Catalog
Layers
Tiling
Library
3D Models
Textures
Feature Templates
Reference Tables
Metadata
Metadata
DB
Metadata
Metadata
Special Areas
Spatial
Reference Frame
Other Raster
Attribution

## Slide 44: RIEDP Reference Abstract Data Model (upper part - 1/2)

## Slide 45: RIEDP Reference Abstract Data Model (upper part - 2/2)
DB
Repository
Catalogue
Metadata
3D Models
Textures
Feature Templates
Reference Tables
Special Areas

## Slide 46: RIEDP Reference Abstract Data Model (Lower part)

## Slide 47: RIEDP Reference Abstract Data Model (Lower part)
Metadata
3D Models
Textures
Feature Templates
Reference Tables
Special Areas
Attribution
Layers
Library

## Slide 48: RIEDP Reference Abstract Data Model (Full)
Metadata
DB
Repository
Catalogue
Metadata
See RADM details in Product 1 - § 4.3.3

## Slide 49: RIEDP Reference Abstract Data Model
Convergence
Common format
Variability
High Level Concepts of a Database
Showing areas of convergence and variability among initiatives
Tiles, Layers Library,
COTS
Metadata,
Attribution

## Slide 50: The RIEDP Components: The RADM Parts
List of Formats
Spatial Reference Frame
Attribution Model
Data Organization on the Media
Metadata Schema
Profiles

## Slide 51: RIEDP-required formats
The data formats required for RIEDP-compliant data exchange:
  GeoTIFF (revision 1.0 October 1995), for terrain elevation data.
  ESRI Shapefile (technical description White Paper July 1998), for instances, and possibly for classes of terrain features and vector data.
  GeoTIFF (revision 1.0 October 1995) or JPEG 2000 (ISO/IEC 15444 – Part 1) for terrain imagery data, as well as other raster-based data.
  OpenFlight (version 16.0 or higher), for 3D models, both natural and man-made, placed on the terrain or dynamically included in the environment.
  PNG (ISO/IEC 15948:2004), SGI RGB or SGI RGBA, image formats for texture maps, used in portraying object surfaces and some terrain surfaces.
  In addition, XML (and associated XML schema) is used to provide those RIEDP-required data that is not supported through the above formats.
NOTE :
  RIEDP does NOT impose RIEDP-required Formats for use within a Data Producer’s internal Processes
  The list of RIEDP-required formats may be extended, updated, or modified through amendment or revision of this specification. Condition : Candidate formats shall comply with the RADM principles.
See details in Product 1 - § 4.4
See details in Product 1 - § 4.6

## Slide 52: Export Database
GeoTIFF
Shapefiles
XML
OpenFlight
PNG RGB
RIEDP Exchange Formats
XML
Additional formats can be introduced through
SISO EDRS Product Support Group

## Slide 53: RIEDP Geospatial Conventions / Tiling
Tiling:
  Division of the area of interest
  1square degree
Region
  Single Block
  For those who do not consider Tiles
See details in Product 1 - § 4.3.3.2.7

## Slide 54: RIEDP Geospatial Conventions / Spatial Reference
RIEDP-compliant <Database> conforms to the following:
  Database_SRF: GEODETIC_WGS_1984
  Database_Origin: longitude value, latitude value, (and optionally, height value)
  Database_Spatial_Domain:
    Coordinate values : longitude, latitude, (and optionally height)
    for the Lower Left and Upper Right corners of the database, in that order
  3DModel_SRF: LOCAL_SPACE_RECTANGULAR_3D SRF
  OrientationVectorSpace_SRF: LOCAL_TANGENT_SPACE_EUCLIDEAN
  Orientation_Values_Convention: Intrinsic_Euler_ZYX or ZY’X”
See details in Product 1 - § 4.3.3.2.5

## Slide 55: RIEDP Attribution Model
Related to Feature instances and Templates
  Detailed Characterization of their Properties
    For Geospatial information
    For Formats Organization (structure of the data in a format)
    For Process guidance (how to eventually process the data)
  Factored out into Library through Templates
Example : A road
  Concept from the Real World : Polyline + Size + Lanes Number + Type
  Based on GIS Attributes from the Provider
  Augmented with attributes of the instance or from a template in the Library
    Cross Section, Visual representation, Sensor representation
    Rules for conforming to the terrain
    Detailed properties captured in Reference Tables
Standardized Semantics and Attribution Schema (next Part of the Brief)
See details in Product 1 - § 4.3.3.3

## Slide 56: RIEDP Data Organization
Physical Organization on the Media
  Layers in Tiles or Region Folder
  Library
  Metadata
See details in Product 1 - § 4.5

## Slide 57: RIEDP Metadata - Organization
Successful data exchange relies heavily on the appropriate use of metadata
RIEDP Compliant Data products shall include the appropriate metadata classes, as specified by the RADM
  Structured metadata
  Based on XML files for each component of the RADM
  According to rules captured in XML schemas
Metadata
See details in Product 1 - § 4.3.3.4

## Slide 58: RIEDP Profiles
  RIEDP-compliant Data Products shall conform to one of the RIEDP Profiles
  A Profile specifies:
    A stage in the RPM
    Mandatory and Optional Data in accordance with the RADM
See details in Product 1 - § 4.7.

## Slide 59: Conformance
RIEDP specifies the conformance requirements for the use of:
  RIEDP RPM stages,
  RIEDP RADM classes,
  RIEDP Profiles, and
  RIEDP-compliant data products.
The conformance requirements apply to any of the following:
  Database generation systems or processes,
  Data models that represent RIEDP products,
  Interchange of RIEDP data products,
  Applications that produce or consume RIEDP data products.
Conformance requirements define the degree of flexibility allowed for all uses of RIEDP.
See details in Product 1 - § 5

## Slide 60: Semantics for RIEDP data sharing

## Slide 61: Areas of data semantics in RADM
7
1
3
4
6
2
Feature Instances & Feature Templates
Lights Characteristics
Material Characteristics
3D Model Characteristics
Visual Characteristics
Other Characteristics
Elevation and Imagery Attribution
And Process Attributes (which apply within areas above for data generation and consumption)
5

## Slide 62: Product 2 - Detailed Features Description - Goal
Improve Data Interoperability through:
  Identification of List of concepts and associated definitions (next slide)
  Providing the Information needed by the International Training Community
  Allowing future Evolution
  Not reinventing the wheel by using to Standard Dictionaries
    EDCS, + DFDD and AMDB for Airport as needed
    and RIEDP notions when not enough
    Use of Existing definitions (Changes to be requested to Source Organization)
    RIEDP own Code Space

## Slide 63: Relating Features and Attributes
List of Tables Related to the Semantics of Features and/or Attributes
  Features
  Attributes
    Including Process-related attributes
  Associated enumerations
  Supplementary
    Including Themes, Units , Scales…
  Prescribed feature-attribute combinations along with their:
    Valid value ranges,
    Their specific enumerations (if any),
    Default values (including enumerates)
    Applicable units, scale
These tables are evaluated through test DB conversion efforts
Table structures are specified in Product 2

## Slide 64: Feature Instance & Feature Templates
Note: The RADM representation for Features is not specific to Shapefiles
A template allows to factor out common characteristics of features
(saved in Library).

## Slide 65: Vector data in shapefiles
  A Shapefile stores geographic features (point, linear, and areal) and attribute data as a collection of files
    .shp - the file that stores the geometry of feature instances.
      Each record describes a shape with a list of its vertices.
    .dbf - the dBASE file that stores the attribute information of feature instances.
      Each record contains attributes for a feature.
    .shx - the file that connects the geometry file and the attributes file via index values.
Records
Shape 1
Shape 2
Shape n
Attrib 1 | Attrib 2 |  | Attrib n
Values |  |  | 
.shp
.dbf
.shx

## Slide 66: RIEDP Attribution Model : Features (Shapefiles + XML)
Characterization of Feature instances and Templates

## Slide 67: Example : Material Characteristics (1/3)
12 Feb 2020
Tutorial RIEDP - SISO SIW 20
<Feature_Templates>
  <FTEntry>
    <Name>TemplateX
      <Attribute n>
      <LinkTo_LightChar></LinkTo_LightChar>
      <LinkTo_MatChar> Wood</LinkTo_MatChar>
      <LinkTo_VisualChar></LinkTo_VisualChar>
      <LinkTo_OtherChar></LinkTo_OtherChar>
  </FTEntry>
  <FTEntry>
    <Name>TemplateY
    <Name>TemplateZ
<MatChar_Table>
  <MatChar_Entry> Name « Wood »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Metal »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Soil »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
Areal
x
y
z
LinkTo_Template |  |  |  | LinkTo_MatChar | 
TemplateX |  |  |  |  | 
TemplateY |  |  |  |  | 
 |  |  |  | Wood | 
For Basic rendering
For Physics Experts
For Training purposes

## Slide 68: Example : Material Characteristics (2/3)
Areal
x
y
z
LinkTo_Template |  |  |  | LinkTo_MatChar | 
TemplateX |  |  |  |  | 
TemplateY |  |  |  |  | 
 |  |  |  | Wood | 
12 Feb 2020
Tutorial RIEDP - SISO SIW 20
<Feature_Templates>
  <FTEntry>
    <Name>TemplateX
      <Attribute n>
      <LinkTo_LightChar></LinkTo_LightChar>
      <LinkTo_MatChar> Wood</LinkTo_MatChar>
      <LinkTo_VisualChar></LinkTo_VisualChar>
      <LinkTo_OtherChar></LinkTo_OtherChar>
  </FTEntry>
  <FTEntry>
    <Name>TemplateY
    <Name>TemplateZ
<MatChar_Table>
  <MatChar_Entry> Name « Wood »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Metal »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Soil »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
For Basic rendering
For Physics Experts
For Training purposes

## Slide 69: Example : Material Characteristics (3/3)
12 Feb 2020
Tutorial RIEDP - SISO SIW 20
<Feature_Templates>
  <FTEntry>
    <Name>TemplateX
      <Attribute n>
      <LinkTo_LightChar></LinkTo_LightChar>
      <LinkTo_MatChar> Wood</LinkTo_MatChar>
      <LinkTo_VisualChar></LinkTo_VisualChar>
      <LinkTo_OtherChar></LinkTo_OtherChar>
  </FTEntry>
  <FTEntry>
    <Name>TemplateY
    <Name>TemplateZ
<MatChar_Table>
  <MatChar_Entry> Name « Wood »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Metal »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
  <MatChar_Entry> Name « Soil »
    <Group> « Basic_Mode »
    <Group> « Advanced_Mode »
    <Group> « Expert_Mode »
3D Model/Polygon/Texture
Wood
Metal
or OtherRaster Layer
Raster/Pixel
Mapping Table
RVB - Index  MatChar_Entry
0/0/255 – 1  « Water »
or for 3D Model
Areal
x
y
z
LinkTo_Template |  |  |  | LinkTo_MatChar | 
TemplateX |  |  |  |  | 
TemplateY |  |  |  |  | 
 |  |  |  | Wood | 
Does it make sense for features ?
Yes, for Predominant Material
For Basic rendering
For Physics Experts
For Training purposes

## Slide 70: Product 2 Preview - Feature Template Constructs
RIEDP Attribution Model: Features (Shapefiles + XML)
Feature Theme |  | Theme Label |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | Geo Attributes List |  |  |  | Org Attributes List |  |  |  |  | Proc Attributes List |  |  |  | 
Feature Type | FT Name* | FT Descr | Feature Label* | 1st Geo RA Label |  | nth Geo RA Label |  | 1st Org RA Label |  |  | lth Org RA Label |  | 1st Proc RA Label |  |  | mth Proc RA Label | 
Point | 1st FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
 | … |  | … | … | … | … |  | … |  | … | … |  | … |  | … | … | 
 | nth FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
Linear | 1st FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
 | … |  | … | … | … | … |  | … |  | … | … |  | … |  | … | … | 
 | nth FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
Areal | 1st FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
 | … |  | … | … | … | … |  | … |  | … | … |  | … |  | … | … | 
 | nth FT Name |  | RF Label | Value for attribute | … | Value for attribute |  | Value for attribute |  | … | Value for attribute |  | Value for attribute |  | … | Value for attribute | 
Logical Description of the Table
Realized in XML

## Slide 71: Product 2 Preview Materials, Sensor Bands, and Directionality
Directionality value used in the Expert Modes of Visual Characteristics and Material Characteristics to modulate the intensity depending on the angle of observation and also on the wavelength
/ | Band 1 (or 1 or 1) |  |  |  |  |  |  |  |  |  |  |  |  | Band 2 / 2/2 |  |  |  | 
 | 1 |  |  |  | 2 |  |  |  | … | n |  |  |  | 1 |  | … | n | 
 | 1 | 2 | … | n | 1 | 2 | … | n |  | 1 | 2 | … | n | 1 | n |  | 1 | n
Mat 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mat 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mat n |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 72: Product 2 – Summary
Detailed Semantics for all components of the RADM
  For Geomatic objects in § 5.2 Ready for review
  for Content Organization in § 5.3 and Ready for review
  for Data Processing in § 5.4 In progress
Including
  Layers Conventions Ready for review
  Detailed Construction and Structure of Reference Tables In progress
    Light, Visual, Material Characteristics, …
    Basic, Advanced, Export Modes
XML Tag and schema Definitions for
  Feature Templates Ready for review
  Reference Tables Ready for review
  Extension of the vector data properties, and In progress
  Use of XML constructs in Comment nodes of 3D Models In progress

## Slide 73: The Experts’ Corner
Experts interested in details of the following topics can consult the listed documents/sections:
Topic | In Product 1 | In Product 2
RPM Stages (details) | § 4.2.2 and 4.2.3 | -
RADM Component (details) | § 4.3.3 | § 5.2
Spatial Referencing | § 4.3.3.2.5 | -
Tiling (details) | § 4.3.3.2.7 | -
3D Model Structure (details) | § 4.3.3.2.15 | § 5.3.8
Library Concepts | § 4.3.3.2.6 | -
Feature Templates (Object reuse) | § 4.3.3.2.14 | § 5.3.6
Reference Tables | § 4.3.3.2.17 | § 5.3.10
Material-related Semantics |  | § 5.3.10.5
XML Tag and Schema Definition |  | § 6.4
Profiles | § 4.7 | § 7
Conformance | § 5 | § 9
Metadata details | § 4.3.3.4 | -
Introducing new formats in RIEDP | § 4.6 | 

## Slide 74: RIEDP and the other Initiatives
How do they relate ?

## Slide 75: RIEDP and other Initiatives - Process view
SEDRIS Scope
AFCD / NPSI Scope
SE Core Scope
CDB scope
RIEDP Scope
use of RPM for comparison!

## Slide 76: Comparison of different database sharing solutions
Expressed
Non-existent or unexpressed
Partial or specific or limited
Topics | SEDRIS | AFCD | NPSI | CDB | SECORE | RIEDP
Process Model | û | û | û | û | ü | ü RPM
Data Model | ü DRM | û | û | K | û | ü RADM
Attribution | ü EDCS | û | û | ü | ü | ü EDCS +
Spatial Reference | ü SRM | K | K | ü | ü | ü 3 SRF
Formats | ü STF | ü COTS | ü COTS | ü COTS | ü COTS | ü COTS
Physical Org | ü STF | K | K | ü | ü | ü
Metadata | ü | û | K | K | K | ü
Profile | K | û | û | û | û | ü
Scope (vs RIEDP/RPM) | All stages but "RT Target Gen" | Until stage "Align…" | Until stage "Align…" | "RT Target Gen" | All stages | All stages but "RT Target Gen"

## Slide 77: Summary & Conclusion

## Slide 78: RIEDP – Two Products
RIEDP provides what is needed to share Environmental data :
  A Reference Process Model
  A Reference Abstract Data Model
  A Tiling Scheme and Spatial Referencing
  A List of Formats from the GIS and M&S worlds
  A Consistent Semantics (through Features, attribution rules)
  An Organization on the Media
  A Metadata structure
  A set of Exchange Profiles
RIEDP Data Model Foundations
RIEDP Detailed Features Description

## Slide 79: Take away
RIEDP
  Takes benefit of the lessons learnt from all related Initiatives
  Reuses and relies on existing standards (such as SEDRIS ISO/IEC standards and PNG ISO/IEC standard), as well as formats commonly used in the community
  Represents the best common denominator by providing a Reference Process Model (RPM), a formal Reference Abstract Data Model (RADM), relying on use of existing Formats, specifying unique Profiles, and focusing on metadata and attribution semantics
  Does not impose internal solutions on producers
  Provides a common data sharing approach that relies on a formal abstract data model (RADM), along with specific metadata and attribution (Product #2)
This allows the best sharing of data, independently from target applications implementation,
  with a current scope addressing static terrain.
  See NATO Group MSG-156 on dynamic terrain and weather

## Slide 80: Tutorial Objectives (reminder)
At the completion of this tutorial the attendee will be able to:
  Identify the main interoperability and reuse issues associated with use of terrain/environmental data in distributed simulation
  Discuss the general process steps in creation of environmental databases, and the various data involved
  Describe the two SISO RIEDP Products, their role, and their main components
  Employ the appropriate RIEDP products and principles to efficiently share environmental databases
  Contrast details of the RIEDP components with the issues to solve
  Judge the use of RIEDP in a simulation project
  Support the evolutions of the RIEDP Products
Product = Result of a SISO standardization effort
Non-commercial !
(updated)

## Slide 81: Q & A
More information:
  Download the Specification from www.sisostds.org
    PDG SISO Library File Folder – Access PDG Documents
    Select SISO Digital Library > Development Groups > RIEDP PDG
  Get involved in RIEPD PDG and EDRS PSG
Any questions on:
  The Requirements ?
  The RIEDP Products ?
  How is RIEDP different ?
  Other challenges for Environmental databases ?
  Any other Environmental Data related subject ?

## Slide 82: Backup slides for the Q&A session

## Slide 83: RIEDP-Required formats Guidelines for Evaluation of Candidate Formats
For the exchange of RIEDP-compliant products and databases, RIEDP specifies existing file formats applicable to the various layers of the RADM.
In response to dynamic changes in technology and evolving requirements, the list of RIEDP-exchange formats may be extended, updated, or modified through amendment or revision of this specification.
All changes shall conform to the following criteria:
  Preservation of RADM and/or RPM compatibility shall be the primary objective, when modifications or replacement of existing formats are being considered.
  Candidate formats shall comply with the RADM principles.
  For instance, the addition of a new 3D model or feature format shall include the definition and compliancy of the corresponding attributes and attribution rules. As needed, open and free tools will be provided to ensure conversion to and from the candidate format are possible.
This is to be analyzed during the Support Phase.

## Slide 84: Current Status of RIEDP Products
Product n°1
  RIEDP Data Model Foundations
    SISO Guidance Document
    Submitted to Balloting : During March ’18
    Approval During Fall ’18 SIW
    Published
Product n°2
  RIEDP Detailed Features Description
    SISO Standard Document
    Providing non-proprietary solutions for representing semantics
    Development initiated Summer 2017
    Conclusion expected 2023
RIEDP DM Foundations
V 1.2a
(updated)