## Slide 1
Mr. Jack “Jake” Borah
Simulation Conceptual Modeling Theory and Application
jborah@sprynet.com
(407) 929-9370

## Slide 2: Learning Objectives
After this tutorial, the attendees should be able to
  List five purposes for simulation use
  Define simulation conceptual modeling (SCM) terminology
  Describe SCM development phases
  Explain differences between informal and formal SCMs
  Describe how to use tools for conceptual modeling

## Slide 3: Tutorial Outline
Conceptual Modeling Background
Modeling and Simulation (M&S) Development
Simulation Conceptual Model (SCM) Construction
SCM Best Practices Guidance

## Slide 4: Why have this tutorial?
“Conceptual Models” and “Conceptual Modeling” are nebulous terms for most simulation developers
Work by Haddix (2001) and Lacy (2001) have highlighted the need to reconcile multiple views of conceptual modeling
A critical shortcoming is that the purpose and impact of conceptual models has not been clearly understood in the community

## Slide 5: Modeling and Simulation (M&S) Basics
Terminology
  Model (noun): “a pattern of something to be made”
  Model (verb): “to produce a representation of or simulation of”
  Simulation: “the imitative representation of the functioning of one system or process by means of the functioning of another”
  The terms Model and Simulation are often incorrectly used
    The subtle but very important difference is that simulation is a model implemented over time
    This implies that models are static while simulations are dynamic

## Slide 6
The military definition of a model being “a physical, mathematical, or otherwise logical representation of a system, entity, phenomenon, or process” is a good starting point, however, a major part is missing
The definition of a “model” from simulation experts supplies the missing part: the motivation for building the model and subsequently the simulation
  A representation of a system for the purpose of studying the system. (Banks, 1996)
  A set of assumptions about how a system works in the form of mathematical or logical relationships which is used to try to gain some understanding of how the corresponding system behaves. (Law, 2000)
The Reason for Simulation

## Slide 7
Or in other words:
“… cost-effective use of something in place of something else for some purpose.” (Rothenburg, 1991)
In simulation, humans can:
  Simplify complex parts of the real world
  Abstract items or events of interest
  Synthesize simplified, or abstracted elements into an alternate arrangement
The Benefit of Simulation

## Slide 8
Five purposes have been generally established for simulation
  An aid for thought
  An aid to communication
  An aid for training and instruction
  An aid to experimentation
  A tool of prediction
But before starting simulation development a SCM should be constructed
  To help the simulation stakeholders understand what is going to built
Simulation Purposes

## Slide 9: SCM Features
An abstraction from either the existing or a notional physical world that serves as a frame of reference
Documents simulation-independent views of important entities and their key actions and interactions
Describes what the simulation will represent, the assumptions limiting those representations, and other capabilities needed to satisfy the stakeholder’s requirements
Bridges between these requirements, and simulation design
Notes: Read the bullet list

## Slide 10: SCM Considerations
Perhaps most complex task of M&S engineering
Method to transform human ideas into executable hardware and software components
An evolutionary simulation artifact
Simulation development begins with sponsor/user interaction
Proceeds through several diverse working groups prior to delivery in final form
  Core engineering team
  Simulation designers
  Systems and network administrators
  Software engineers
  Verification and validation team
Notes: Each Group has a DIFFERENT PERSPECTIVE

## Slide 11: Simulation Development Steps
Problem Formulation / System Definition
Data Collection
Model Conceptualization
Model Validation
Model Translation
Model Verification
Model Production
Model Acceptance Testing
Model Delivery
Model Support / Maintenance
Notes: SIMULATION USERS FREQUENTLY HAVE MULTIPLE PERSPECTIVES AS WELL

## Slide 12: Simulation Development Process Flow
Real World
Done?
Establish Purpose & Scope
Formulate Conceptual Model
Acquire & Analyze Data
Design Detailed Model
Verify & Validate Model
Design Experiments
Execute Simulation
Analyze Output
Refine & Optimize Model
0
0
0
0
Model
Development
Model
Application
Start
Yes
No
Fig. 1: The Simulation Modeling Process
Notes: Contributor: M. L. Loper.

## Slide 13
Failure to have a well-defined set of objectives at the beginning
Failure to communicate with sponsors on a regular basis
Inappropriate level of model detail
Inconsistent level of model detail
Treating using simulation as if it were primarily a complicated exercise in computer programming
Failure to test simulation incrementally during construction
Mistakes Made During M&S Development

## Slide 14: Simulation Development Elements
Model
Real System
Computer
Modeling
Simulation
“A Bridge”
Simulation Conceptual Model - a Communications Bridge
Notes: Dr. Bernard Zeigler presented this diagram in his book Theory of Modeling and Simulation
In his view there are 3 fundamental elements in a simulation development process. This figure shows them and how they are related
We model when we extract from the real world the key factors we think influence the problem we are attempting to study or the process we are trying to imitate
We simulate when we transform our model into computer code and observe the changes in our model over time

## Slide 15: Communicating Through SCMs
Conceptual modeling supports communication
  “The long term contribution of any modeling effort lies in the benefits it affords, either by direct use or by guidance for further development, to science and industry” (Zeigler, 1976)
Communication is achieved through:
  Informal description of the model
  Formal description of the model structure

## Slide 16: SCM Construction
Informal and formal models are built during the simulation development process for differing audiences
A transformation process underlies simulation development
  The real world is too complex to be understood much less modeled by humans
  Most practical approach is to abstract key elements forming reasonable approximation of real world

## Slide 17: SCM Transformations
Simplification- analytical technique in which unimportant details are removed in order to define simpler relationships
  A problem solving technique to produce useful approximations of complex problems that yield usable results
Abstraction- an intuitive technique transforming the essential features of a real system into a different form
  A model demonstrating the qualities and behaviors of the real system without being a direct emulation of the system

## Slide 18: The Resultant Model
It represents an idealized approximation of the original complex real world system
Result of the “Art of Modeling” or the process of analysis, abstraction, simplification, and synthesis within a simulation development project
  Synthesized combination of simplified and abstracted parts of real world
Part of Rothenburg’s cost-effective model constructed for a cognitive purpose
Embodiment of the communications of Zeigler’s modeling process

## Slide 19: Formal and Informal SCMs
Real System
Computer
Modeling
Simulation
Informal
Formal
Conceptual Model

## Slide 20: Informal SCM
Publications
Regulations
Structured, Synthesized
Information
1.
2.
3
1.
2.
1.
2.
3
1.
2.
1.
2.
3
1.
2.
Domain Experts
Legacy Systems
Domain Analysis
Problem
Domain

## Slide 21: The Informal SCM
Written using natural language and contains assumptions made during its construction
Plays fundamental role during the period of activity when the modeler conceives, programs, debugs, and tests models
Helps users and colleagues comprehend basic outline of the model from their perspective on how the real world operates
Notes: These are the characteristics of the informal model--<read the bullet list>

## Slide 22: Informal SCM Representations
Natural Language Requirement
Shortcomings of specialized syntax and semantics tools
  Unfamiliarity
  Complexity
  Cost
General purpose office suite
  Word processor
  Graphics or Drawing application
  Spreadsheet
Notes: Go with slide bullets

## Slide 23: Informal SCM (Example in a Tabular Format I)

## Slide 24: Informal SCM (Example in a Tabular Format II)

## Slide 25: Informal SCM (Example in a Tabular Format III)

## Slide 26: Informal SCM (Example in a Document Format I)

## Slide 27: Informal SCM (Example in a Document Format II)

## Slide 28: Informal SCM (Example in a Mind Mapping Format)
The informal SCM is first component of full and complete SCM
Freemind Mind (freeware) mapping software was used to frame this informal SCM
Notes: Go with slide bullets

## Slide 29: Mind Mapping Software
General purpose office suite shortcoming
  “Expressive Power”
Mind mapping software
  Organizing tool for disorganized mind
  A diagram used to represent words, ideas, tasks or other items linked to and arranged radially around a central key word or idea. … It is an image-centered diagram that represents semantic or other connections between portions of information
  Expressive
  Transportable
  Inexpensive
Notes: Go with slide bullets

## Slide 30: Mind Mapping Informal SCM (Overview)

## Slide 31: Mind Mapping Informal SCM (CM Expanded)

## Slide 32: Mind Mapping Informal SCM (Scenario Expanded)

## Slide 33: Formal Simulation Conceptual Modeling
Domain Analysis
Domain Modeling
Dynamic Structure Diagrams
Use Case
Sequence
Collaboration
Static Structure Diagrams
“IS-A”
“HAS-A”
Associations
Problem
Domain

## Slide 34: The Formal SCM
Unambiguous description of model structure separated from software implementation
Useful once users and colleagues understand informal model and want more detail
Used as an aid to detect omissions and inconsistencies and resolve ambiguities inherent in informal models
Notes: These are the characteristics of the formal model --<read the bullet list>

## Slide 35: Formal Conceptual Model as UML Diagram

## Slide 36: Conceptual Modeling and the DSEEP
IEEE Recommended Practice for Distributed Simulation Engineering and Execution Process (DSEEP)
  IEEE Std 1730TM-2022
Step 2 “Perform Conceptual Analysis”
  Develop an appropriate representation of the real-world domain that applies to the defined problem space
Activity 2.2 “Develop Conceptual Model”
  Implementation-independent representation
  Vehicle for transforming objectives into functional and behavioral descriptions
  Crucial traceability link between objectives and design implementation
Notes: Read the bullets

## Slide 37: DSEEP Activity 2.2 Recommended Tasks
Choose conceptual modeling technique and model format
Identify and describe all relevant entities
Define static and dynamic relationships between entities
Identify events of interest
Capture concept of operations
Document the conceptual model and modeling decisions
Have stakeholders verify conceptual model contents
Notes: Read the bullets

## Slide 38: Conceptual Models / Conceptual Scenarios
Guideline on Scenario Development for Simulation Environments
  SISO-GUIDE-006-2018
  DSEEP Step 2 Activity 2.1 “Develop Scenario”
Conceptual model describes entities and their interrelationships
Conceptual scenario is detailed description of a part of the real world chosen for simulation
Conceptual models and conceptual scenarios must be aligned for completeness and consistency
Notes: Read the bullets

## Slide 39: SCM / Digital Engineering Strategy
DoD Digital Engineering Strategy June 2018
  Use of digital representations of systems and components as a technical means of communication across a diverse set of stakeholders
Strategic Goal #1 “Formalize the development, integration, and use of models to inform enterprise and program decision making”
  Formal planning, development and use of models as part of engineering activities across the lifecycle
  A continuous end-to-end digital representation of the system of interest
Strategic Goal #2 “Provide an enduring, authoritative source of truth”
  A common set of digital models and data enables access, management, analysis, use and distribution of information
Notes: Read the bullets

## Slide 40: Precepts of Simulation Conceptual Modeling I
A SCM should be malleable and adopt a coherent form located within one model appropriate for each particular simulation development phase
Highly unstructured, informal models are sufficient during early simulation definition
Structured and enhanced formal models appropriate during simulation development
Notes: Read the bullets

## Slide 41: Precepts of Simulation Conceptual Modeling II
No single conceptual model due to the essence of the “Art of Modeling”
Multiple iterations of a SCM which evolve as required in simulation development
A “living” document that grows from an informal description to a formal description to communicate between the diverse groups (sponsors/users, modelers, systems engineers, and software developers) participating in a simulation development
A “roadmap” to guide the current development team and to educate / orient new teammates
Notes: Read the first bullet. Perhaps I should have stated “fixed” or “stand-alone” Conceptual Model
Read the second bullet. Here multiple iterations could also be thought of as “extensions” or “embellishments”
Read the last bullet

## Slide 42
Simple to understand by the user
Goal or purpose oriented
Robust, in that it does not give absurd answers
Easy for the user to control and use
Complete on important issues
Adaptable (in a maintenance sense)
Malleable (grow in sophistication over time)
Well-formed SCM Characteristics

## Slide 43: SCMs Observations
A simulation developer’s method of translating modeling requirements into a detailed design framework (Pace, 2003)
Result of the “Art of Modeling” or the process of analysis, abstraction, simplification, and synthesis within a simulation development project
A role of the SCM is to document all requirements of the system and subsequent requirements and analysis of the models/federations
  Enables an orderly systems engineering flow during the simulation development
Notes: Which leads us to the question of what is the role of a Conceptual Model
Here is what has been presented before at the SIWs

## Slide 44: Simulation Conceptual Modeling Problems
No hard and fast rules concerning model formulation (Uncertainty for both the developer and user)
  What does a Conceptual Model look like?
No magic formulas governing what should be included in a model in the form of variables and parameters, descriptive relationships and constraints, or criterion for judgment of effectiveness (Lack of Standardized Processes)
  What should a Conceptual Model contain?
Nobody solves the problem, rather everybody solves the model that they have constructed of the problem (Diversity and Inherent Incompatibility)
  What technique to use? UML, DoDAF, IDEF0,….
Notes: LET’S TRANSITION FROM A THEORETICAL DISCUSSION TO PRACTICAL EXAMPLES.

## Slide 45: Example SCM- Problem Definition
Constructive Air Warfare Simulation
  A tool to support Air Component Staff training in Command and Control procedures
  The simulation will provide credible representations of offensive and defensive air and ground forces present in the Joint Force Area of Responsibility
  The Air Component Staff will be the training audience
    Higher and lower echelons will be simulated through automation or by role players
  The Air Component Staff will interface with the simulation through real world C4I systems
    Simply stated the simulation is the data engine for the training environment
Notes: Read the bullets

## Slide 46: Example SCM - Purpose Definition
  Should the simulation be stochastic or deterministic?
    Stochastic would produce variable outcomes based upon random variables in probabilistic algorithms
    Deterministic would produce consistent outcomes based nonrandom variables in ordered algorithms
  A simulation used for training should generate consistent outcomes
    Instructors will want a simulation that produces predictable outcomes so that training objectives will be met
  A simulation used for analysis should generate variable outcomes
    Analysts will want to approximate the characteristics of a study population
  The purpose of the simulation will have an impact during the implementation phase of the simulation
Notes: IMPORTANT POINT- EVENTUAL USERS OF SIMULATION DID NOT APPRECIATE THIS ASPECT OF SIMULATION DESIGN. ONE SPECIFIC SUBGROUP WANTED THE SIMULATION TO PROVIDE THE EXACT SAME RESULT EACH EVENT, WHILE OTHER USERS WERE COMFORTABLE WITH VARIABLE RESULTS.

## Slide 47: Example SCM- Model Conceptualization
How to provide credible representations of offensive and defensive air and ground forces present in the Joint Force Area of Responsibility?
First Step
  Document the key entities which should be represented in the training environment
Second Step
  Document the behaviors of the key entities which should be represented in the training environment
  Important to remember this is a simulation not an emulation of the real world
  Just because it exists in the real world is not automatic justification to include it a simulation
Notes: Read the bullets

## Slide 48: Model Conceptualization- Static View
Aircraft
Munitions
Targets
Notes: Read the bullets

## Slide 49: Model Conceptualization- Dynamic View
Preflight Maintenance
Taxi
Outbound Flight
Target Attack
Return Flight
Recovery
Repair
Rearm
Offensive Aircraft Flight Operations
Notes: Read the bullets

## Slide 50: Use Case 1 – Lack of Attention to Detail
How to represent global flight paths?
Several coordinate systems describe the Earth
  Latitude and Longitude
  Universal Transverse Mercator (UTM)
  Universal Polar Stereographic (UPS)
  Geodetic Height
  Cartesian Coordinates
The one chosen for simulation implementation:
  Latitude and Longitude
Notes: Read the bullets

## Slide 51: Use Case 1 – Lack of Attention to Detail
If using latitude and longitude, then global flight path becomes an algorithm calculating latitude and longitude coordinates
Simple solution for modeling in the most of the world
Except for the coordinate system boundaries
Notes: Read the bullets

## Slide 52: Use Case 1 – Coordinate Boundaries
Latitude / Longitude coordinate system boundaries
  The Equator
  The North and South Poles
S
Equator
N
  The Greenwich Meridian
  The Anti-Meridian
N
S
Greenwich
Notes: Read the bullets

## Slide 53: Use Case 1 – Coordinates-What could go Wrong?
Why are these boundaries a problem?
  First, boundary needs to be recognized
  Second, calculation algorithm needs to transpose coordinates
Simple solution to implement
  Unless the developer does not know the boundary definitions and/or the correct methods to transpose coordinates when crossing boundaries
Notes: Read the bullets

## Slide 54: Use Case 1 – Latitude Basic Considerations
The Equator:
  0 degrees Latitude: Direction reverses N > S, S > N
The North and South Poles:
  90 degrees Latitude: Value increases toward pole, decreases away from pole
S 90o
Equator
N 90o
0o
N 30o
S 30o
S 60o
N 60o
Notes: Read the bullets

## Slide 55: Use Case 1 – Longitude Basic Considerations
The Greenwich Meridian:
  0 degrees Longitude: Value decreases approaching meridian, increases away from meridian, Direction reverses E > W, W > E
The Anti-Meridian
  180 degrees Longitude: Value increases approaching meridian, decreases away from meridian, Direction reverses E > W, W > E
N
S
Greenwich
0o
E 090o
W 090o
N
Greenwich
Anti-Meridian
E 045o
E 135o
180o
W 135o
W 045o
Notes: Read the bullets

## Slide 56: Use Case 1 – When the Problem Appears
  Simulation A is used to support an intelligence training scenario
    Multiple logistics aircraft flights are scripted to indicate activity
    One aircraft given a flight path which parallels a longitude meridian to the North Pole
  Simulation B crashes in the middle of the night during scenario flight out
    Developer doesn’t find a reason for crash
Notes: Read the bullets

## Slide 57: Use Case 1 – Lost Aircraft Flight Path
  Simulation B crashes second time during repetition scenario
    Developer discovers Simulation B receives “unallowable” flight position coordinates from Simulation A
    “Unallowable” coordinate is a 3 digit Latitude value in excess of 90 degrees
    Post-event a Change Request is written to remedy this miscalculation
Equator
N 90o
0o
Notes: Read the bullets

## Slide 58: Use Case 1 – How the Problem Propagates
  Simulation A developer writes new software for Change Request
    Asks Change Request Submitter to review new software
  Submitter discovers the developer doesn’t understand physics of problem
    Developer correctly limits latitude maximum value to 90 degrees
    Developer correctly calculates the latitude increases toward the North Pole, decreases away from North Pole
    Developer incorrectly calculates the longitude coordinates once aircraft “flies” over the North Pole
Notes: Read the bullets

## Slide 59: Use Case 1 – Lost Aircraft Lost Again
  Developer did not understand the difference between latitude and longitude calculations
    Developer incorrectly assumed that longitude would only require change of direction
    Correct solution would also require transposition of longitude value from “X” to “180-X” in addition to change of direction
E 090o
W 090o
N
E 045o
E 135o
180o
W 135o
W 045o
W 030o
E 030o
E 150o
Notes: Read the bullets

## Slide 60: Use Case 1 – Problem Impacts
Primary effects
  Initial problem occurrence disrupts training event operations
    Simulation A generates incredible simulation results
    Simulation A causes Simulation B to crash
  Waste of Time and Resources
    Simulation B Developer spends time investigating Simulation B crash
Secondary effects
  Additional waste of Time and Resources
    Simulation A Analyst spends time investigating Simulation A behavior
    Simulation A Developer develops initial solution for problem
    Simulation A Analyst identifies error in solution
    Simulation A Developer revises problem solution
Notes: Read the bullets

## Slide 61: Use Case 2 - Simulation Implementation
How to represent air-to-ground and ground-to-air interactions?
First Method
  Designate target
  Employ Munitions
  Calculate Munitions Time of Flight
  Calculate Munitions Effect based upon Cumulative Probabilities
Second Method
  Designate target
  Employ Munitions
  Calculate Munitions Effect using Probability of Destruction Random Number table
Notes: Read the bullets

## Slide 62: Use Case 2 - Model Conflict
Either Method could provide realistic results
But… What happens when there are 2 developers working independently on different parts of the simulation?
And... Developer 1 simulates offensive operations uses the First Method while Developer 2 simulates defensive operations uses the Second Method?
Notes: Read the bullets

## Slide 63: Use Case 2 - Simulation Provides Incredible Results
In 1 game turn, 1 obsolete SAM system shoots down 4 Fighters and 16 air-to-ground missiles
Notes: Read the bullets

## Slide 64: Use Case 2 – The Cause
  Lack of an Overarching SCM
    Allowed the developers to employ two credible simulation methods in a conflicting manner
    Masked a ground-based SAM system self defense behavior that took precedence over other simulation activities
    Hid a simulation interdependency which was that the reload rate for a missile site was based upon the simulation visual display refresh rate
Notes: Read bullets

## Slide 65: Use Case 2 – The Impacts
  The Impacts
    Immediate: Exercise cadre forced to perform immediate triage to prevent incredible results from reaching the training audience
    Immediate and Long Term: Exercise director mandates manual control of air defense engagements to maintain desired attrition rates
    Long Term: Unplanned work to troubleshoot the scenario then develop and test simulation software
Notes: Read bullets

## Slide 66: Benefits of Building a SCM
A Well-Formed SCM should provide:
  Assumptions and limitations for model
  Interconnections and dependencies within a model
  A method to detect internal model conflicts
  A preview of possible model output
  A means to discover missing parts
Early detection of problems prevents wasteful expenditure of limited resources
Notes: Read bullets

## Slide 67: Building Versus Using a SCM
Facilitates
Communication
Between
the Developer
and the End User
Notes: CONCEPTUAL MODELING WOULD ALSO BE A KEY ENABLER FOR GAO REPORT 17-77 “DETAILED SYSTEMS ENGINEERING PRIOR TO THE PRODUCT DEVELOPMENT POSITIONS PROGRAMS FOR SUCCESS”

## Slide 68: Where To Go For Guidance?
  Limited Authoritative Reference Material on how to do Conceptual Modeling as a part of Simulation Development Process
  “Conceptual Modeling” is not a term discussed in modeling and simulation textbooks
  Web searches on “Conceptual Modeling” have led to a diverse set of web sites that contributed little if anything the body of knowledge
    Most often “Conceptual Modeling” was in relation to Database Modeling
Notes: Read bullets

## Slide 69: One Helpful Resource
Final Report of MSG 058
RTO-TR-MSG-058 - Conceptual Modeling (CM) for Military Modeling and Simulation (M&S) Modélisation conceptuelle (MC) pour la modélisation et la simulation (M&S) militaires
ISBN 978-92-837-0150-7
https://www.sto.nato.int/publications/pages/results.aspx?k=final report of msg 058&s=Search ALL STO Reports
Notes: Read bullets

## Slide 70: MSG-058 Report - CM Development Process Phases (PP)
PP 1
INITIATE
CM Development
PP 2
DEFINE
CM Requirements
PP 3
ACQUIRE
CM Knowledge
PP 4
DESIGN
Conceptual Model
PP 5
BUILD
Conceptual Model

## Slide 71: MSG-058 Report - INITIATE CM Development Process Activities (PA)
PA 1.1
Identify and Map Stakeholder Responsibilities
PA 1.2
Define Purpose and Intended Use
of Modeling and Simulation Effort
PA 1.3
Identify Constraints on
the Modeling and Simulation Effort
PA 1.4
Impose Mandatory Enterprise Policies

## Slide 72: MSG-058 Report - DEFINE CM Requirements Process Activities (PA)
PA 2.1
Identify, Analyse and Record CM,
Mission and Simulation Space Requirements
PA 2.2
Verify Requirements with respect to
Needs, Constraints and Policies
PA 2.3
Synergize CM, Mission
and Simulation Space Requirements
PA 2.4
Derive Mission and
Simulation Space Knowledge Needs

## Slide 73: MSG-058 Report - ACQUIRE CM Knowledge Process Activities (PA)
PA 3.1
Identify Authoritative Knowledge Sources
PA 3.2
Search for Re-usable Knowledge
PA 3.3
Identify Knowledge Gaps and Bounds
PA 3.4
Gather, Structure and Document Knowledge
PA 3.5
Generate/Extend a Domain Ontology
PA 3.6
Review Validity of Knowledge wrt
Authoritative Knowledge Sources

## Slide 74: MSG-058 Report - DESIGN CM Process Activities (PA)
PA 4.1
Search for Existing CMs that may be Partially
or Fully Re-used to Support CM Development
PA 4.2
Identify and Select Conceptual Primitives and
Model Kinds to Represent Acquired Knowledge
PA 4.3
Select Formalism(s) for CM Specification
PA 4.4
Select Views to Support Stakeholders
PA 4.5
Select a Notation Suitable
to Express the Chosen Formalism
PA 4.6
Evaluate Design for Adequacy/Relevance
With respect to Requirements

## Slide 75: MSG-058 Report - BUILD CM Process Activities (PA)
PA 5.1
Populate the CM Using the Chosen Primitives,
Model Kinds, Formalism and Notation
PA 5.2
Create the Specified Views
PA 5.3
Verify CM Consistency with respect to CM Design
PA 5.4
Validate CM Consistency with respect to
Mission Space and Simulation Space Knowledge
PA 5.5
Ensure Acceptance of CM
by Authorized Stakeholder

## Slide 76: MSG-058 Report - Phase Diagrams
act PP1 Activity Diagram: Initiate CM Development
PA1.1 Identify and Map
Stakeholder
Responsibilities
PA1.2 Define Purpose and
Intended Use of M&S Effort
PA1.3 Identify Constraints
on the M&S Effort
PA1.4 Impose Mandatory
Enterprise Policies
Start PP1
P1.1 Stakeholder
Description
P1.2 Need
Statement
P1.3 Constraints
and Policies
End PP1

## Slide 77: MSG-058 Report - CM Development Products
PP 1
INITIATE
CM Development
PP 2
DEFINE
CM Requirements
PP 3
ACQUIRE
CM Knowledge
PP 4
DESIGN
Conceptual Model
PP 5
BUILD
Conceptual Model
P 1.4 Conceptual Model Metadata
P 1.1
Stakeholder
Description
P 1.2
Need
Statement
P 1.3
Constraints and
Policies
P 2.1
CM
Requirements
Specification
P 2.2
CM Knowledge
Acquisition
Needs
P 3.1
Validated
Knowledge
P 4.1
Conceptual Model
Design
P 5.1
Conceptual Model

## Slide 78: References I
Slide | Reference Data
4 | Haddix, Furman, “Conceptual Modeling Revisited: A Developmental Model Approach for Modeling & Simulation” Paper 01F-SIW-098, Proceedings of the Fall 2001 Simulation Interoperability Workshop, September 9-14, 2001, Orlando, FL.
4 | Lacy, Lee, Youngblood, S., and Might, R., “Developing a Consensus Perspective on Conceptual Models for Simulation Systems”, Paper 01S-SIW-074, Proceedings of the Spring 2001 Simulation Interoperability Workshop, March 26-30, 2001, Orlando, FL
5 | Merriam-Webster Unabridged. Retrieved from http://unabridged.merriam-webster.com
6 | Banks, J., J.S. Carson, and B.L. Nelson, Discrete Event Simulation, 2nd ed., Prentice Hall, New Jersey, 1996.
6 | Law, Averril M., Simulation Modeling & Analysis, 3rd ed., McGraw-Hill, New York, 2000.
7 | Rothenburg, Jeff, “Knowledge-Based Simulation at the RAND Corporation”, Knowledge-Based Simulation: Methodology and Application, Fishwick and Modjeski (eds.), Springer-Verlag, 1991.

## Slide 79: References II
Slide(s) | Reference Data
12 | Benjamin, P., Patki, M, and Mayer, R., “Using Ontologies for Simulation Modeling”, Proceedings of the Winter Simulation Conference, 2006.
15 | Zeigler, Bernard P., Theory of Modeling and Simulation, Wiley, New York, 1976.
38 | Pace, Dale K., “Thoughts About the Simulation Conceptual Model”, Paper 03S-SIW-009, Proceedings of the Spring 2003 Simulation Interoperability Workshop, March 30-April 4, Orlando, FL.
67 | Gushue, John, “What the Customer Really Wanted, Revisited”, Retrieved from http:/johngushue.typepad.com/bolg/2009/08/what-the-customer-really-wanted-revisited.html
69-77 | Final Report of MSG 058. Retrieved from https://www.sto.nato.int/publications/pages/results.aspx?k=final report of msg 058&s=Search ALL STO Reports

## Slide 80: References III
Additional References
Olivé, A., Conceptual Modeling of Information Systems, Springer-Verlag, New York, 2007.
Roca, Ric, Pace, D., Robinson, S., Tolk, A., and Yilmaz, L., “Paradigms for Conceptual Modeling”, Proceedings of the 48th Annual Simulation Symposium, 2015.
Pace, Dale K., “Ideas About Simulation Conceptual Model Development”, Retrieved from https://pdfs.semanticscholar.org/7100/0df6164dce9f4e948e48688378291fa34528.pdf
Pace, Dale K., “Conceptual Model Development for C4ISR Simulations”, Retrieved from http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.536.1247&rep=rep1&type=pdf
Parsons, Jeffery, and Cole, L., “What do the pictures mean? Guidelines for experimental evaluation of representation fidelity in diagrammatical conceptual modeling techniques”, Data & Knowledge Engineering, 55: 327-342; doi: 10.1016/j.datak.2004.12.008, 2005.
Wand, Yair, and Weber, R., “Research Commentary: Information Systems and Conceptual Modeling—A Research Agenda”, Information Systems Research, 13 (4): 363-376; doi: 10.1287/isre.13.4.363.69, 2002.

## Slide 81: Learning Objectives
Now, the attendees should be able to
  List five purposes for simulation use
  Define simulation conceptual modeling (SCM) terminology
  Describe SCM development phases
  Explain differences between informal and formal SCMs
  Describe how to use tools for conceptual modeling

## Slide 82: Conclusion
Questions / Comments?
Contact Information
  Mr. Jack “Jake” Borah
  Phone: (407) 929-9370
  E-mail: jborah@sprynet.com