## Slide 1
Transportation Systems: A Survey of
M&S Applications in Mobility, Sustainability, and Logistics
Kevin F. Hulme, Ph.D., CMSP

## Slide 2: Agenda
Introduction (5 mins)
  Tutorial Learning Objectives
  I/ITSEC 2023 themes
  CMSP relevance
M&S in Transportation Systems (60 mins)
  Examples: core/foundational
  Examples: emerging
Tutorial Summary (10 mins)
  Confirm Learning Objectives
  Acknowledgements
  Bibliography
Q/A (15 mins)

## Slide 3: Introduction
Tutorial Learning Objectives
Describe basic concepts (M&S) that are foundational to I/ITSEC.
Classify applications in M&S with relation to transportation and human mobility.
Analyze modeling methods and implementations aligned with NTSA CMSP.
Distinguish mathematical fundamentals related to mobility, sustainability, logistics.
Formulate future pathways to advance sustainable human mobility in a digital world.
Anderson et al., 2001

## Slide 4: Introduction
2023 I/ITSEC themes
“Sustaining a Global Force in a Digital World”
This Tutorial addresses as follows:
Technological sustainment: Evolution of sustainable technologies to improve mobility
Global: SCM technologies to advance a broad workforce amidst uncertainty
Digital engineering: A cornerstone of M&S implementations for Transportation
NTSA, 2023

## Slide 5: Introduction
Tutorial content can assist with M&S certification preparation
Certified Modeling & Simulation Professional (CMSP)
Provides the M&S community with its own professional certification
Host Organizations
  The National Training and Simulation Association (NTSA)
  The National Defense Industrial Association (NDIA)
Program is now three-tiered
  Apprentice, Practitioner, and Master
Core CMSP Modeling Methods prevail in this Tutorial
Oswalt, 2022

## Slide 6: M&S in Transportation Systems
Transportation Systems
Mobility Fundamentals (terminology/basics)
  Transportation: movement of humans/goods/services
    Intermodal: multiple modes of transport | different carriers
    Multimodal: multiple modes of transport | same carrier
  Sustainability: fulfilling today’s needs without compromising tomorrow
    Green concerns: protecting environment (fuel/noise/emissions)
    Life cycle: managing a product from inception to disposal
  Logistics: process of moving resources from source to destination
    Supply Chain: management of the flow of goods and services (SCM)
    SCM works toward improving processes to create competitive advantages
    Logistics emphasizes meeting customer needs/expectations
Vanek et al., 2014

## Slide 7: M&S in Transportation Systems
Transportation Systems
Modeling & Simulation (M&S)
  Model: A product (physical or digital) that represents a system of interest
  Simulation: Using a model to study the performance of an actual system
High-level overview of common modeling methods
  Targeted focus on topics related to:
    Human mobility & multimodal transportation
    Sustainability | Life cycle
    Supply chain and logistics
Media-driven examples
  Problem description | Mathematical model | Simulation implementation

## Slide 8: M&S in Transportation Systems
Transportation Systems
Subject Matter (both Foundational and Emerging)
  Core/Foundational topics:
    Conceptual Modeling | Physics-based Modeling
    Monte Carlo/Stochastic | Finite Element Modeling (FEM)
    Discrete Modeling | Continuous Modeling
    Human Behavior Modeling | Multi-Resolution Modeling (MRM)
    Semi-automated Forces (SAF) | Human-computer Interaction (HCI)
  Emerging/Innovative technologies:
    Virtual Environments | Game Engines
    eXtended Realities (XR) – VR/MR/AR
    Machine Learning (ML) | Artificial Intelligence (AI)
DoD, 1998

## Slide 9: M&S in Transportation Systems
Conceptual Modeling: the abstraction of a model from the real-world system that is being simulated (i.e., what to/not model, assumptions, constraints)
Within a simulation study, Conceptual Modeling is typically the most difficult, least understood, and most critical task
  How to state versus how to solve the problem
  Required early in the design cycle when change/revision is less costly
Robinson, 2000

## Slide 10: M&S in Transportation Systems
Conceptual Modeling (example)
  Problem statement: Conceptual Modeling for Supply Chain Resilience
  Tutorial focus area: Supply Chain & Logistics
Disruptions (COVID-19, wartime situations) impact global supply chains
Need to improve supply chain robustness
In this research, a theoretical framework and conceptual model is applied
ρ = math model for Resilience Loss
Alvim et al., 2022
Supply Chain disruption (COVID-19)

## Slide 11: M&S in Transportation Systems
Conceptual Modeling (example)
Framework: Supply Chain Resilience (SCR) concept model, which includes a supply chain digital twin
  Enables automatic actions for certain events (e.g., activating a virtual Distribution Center)
Scope: deliver an outcome to support decision-making, minimize cost and build resilience against supply chain disruptions
Barykin et al., 2020

## Slide 12: M&S in Transportation Systems
Physics-based Modeling: a mathematical representation that incorporates physical characteristics (e.g., forces, moments, accelerations) directly into the model
A cross-disciplinary (e.g., math, physics, computer graphics) approach to model and visualize motions of rigid objects, often for animation/simulation
In Transportation: spring-mass-damper second order differential equation
Avesh & Srivastava, 2020

## Slide 13: M&S in Transportation Systems
Physics-based Modeling (example)
  Problem statement: Modeling tools for autonomous driving behaviors
  Tutorial focus area: Transportation/Mobility
Mixed-traffic: transition period during which autonomous and conventional human drivers share the roadways
Car-following and lane-changing behaviors of autonomous vehicles (AVs) require specialized modeling efforts
Ahmed et al., 2021

## Slide 14: M&S in Transportation Systems
Physics-based Modeling (example)
Framework: existing models for human-driven vehicles
  Car-following model (i.e., acceleration)
  Collision-avoidance (i.e., safety distance)
  Perceptual threshold (i.e., headway/speed)
Scope: modifications for AVs are necessary
  Optimal Velocity Model (OVM)
  Intelligent Driver Model (IDM)
  Adaptations of automated cruise control (ACC) approaches
IDM: physics-based model
desired (headway) gap: S*
time change in velocity (acceleration) of vehicle: α
Albeaik et al., 2021

## Slide 15: M&S in Transportation Systems
Monte Carlo / Stochastic Methods: modeling approaches that approximate solutions to problems through statistical sampling
The inputs describing a system are uncertain (i.e., each has a probability distribution) hence the predicted system output is also uncertain
In Transportation: microsimulations predict traffic flow and density with uncertain parameters (e.g., day of week, time of day, weather, construction, accidents)
Wuthishuwong & Traechtler, 2019

## Slide 16: M&S in Transportation Systems
Monte Carlo (example)
  Problem statement: Environmental impacts of alternative fuels | liquefied natural gas (LNG)
  Tutorial focus area: Life Cycle (sustainability)
LNG is a more expensive option than compressed natural gas (CNG); often used in heavy-duty vehicles for longer range requirements
This study demonstrates a Monte Carlo simulation to evaluate the potential environmental benefits of promoting LNG heavy-duty diesel vehicles
AFDC, 2023
Model for Environmental Benefit (EB):
Environmental Impact (EI) of LNG:
Monte Carlo analysis variable

## Slide 17: M&S in Transportation Systems
Monte Carlo (example)
Simulations investigated utilization, energy consumption, emissions
Life cycle environmental benefit: 50,000 Monte Carlo simulations
Global Warming Potential (GWP):
  Μ = −1.55% | σ = 2.18%
  Probability that LNG has a reduced GWP impact compared to diesel: 76.2%
Sun & Ertz, 2020
 | Min | Avg | Max | σ
Filling station utilization | 30% | 58% | 86% | 0.0933
LNG energy consumption | 10% | 15% | 20% | 0.0167
Methane emissions | 0.4% | 0.8% | 1.2% | 0.0013

## Slide 18: M&S in Transportation Systems
Finite Element Modeling (FEM): identifying approximate solutions to boundary value problems for partial differential equations
Subdivide a large system into smaller objects (i.e., a “mesh”) called finite elements
System of equations models the entire system
In Transportation: determine vehicle stresses, displacements under extreme load conditions
Harish, 2022

## Slide 19: M&S in Transportation Systems
Finite Element Modeling (example)
  Problem statement: Hull strength of container ships
  Tutorial focus area: Supply Chain & Logistics
Objective: apply FEM to analyze extreme loading conditions on container ships in the oblique sea
Mesh models: 4M degrees-of-freedom | 60 hours to calculate ultimate strength for one sea state
Boundary conditions: four boundary nodes selected based on buoyancy/hydrodynamic equilibrium
very fine mesh region
wave amplitude
wave length
ship length
Darie & Rörup, 2017

## Slide 20: M&S in Transportation Systems
Finite Element Modeling (example)
Loading conditions: full spectrum hydrodynamic analysis includes torsion, and horizontal/vertical bending moments (HBM/VBM)
Outcomes: critical situations were analyzed for three container ship sizes (“TEU”) by systematically varying length/position/heading of incoming waves
Ergin et al., 2007

## Slide 21: M&S in Transportation Systems
Discrete Modeling: a model that emulates the system as a discrete sequence of events in time
  Only alters when some “change of state” occurs
In Transportation: (discrete) state of a signalized intersection (“go” or “stop” or “caution”)
Continuous Modeling: a model that continuously monitors a system response (i.e., time and space)
  Typically derived from the laws of physics
In Transportation: (continuous) flow behavior of vehicles in an intersection
Mumayiz, 1990

## Slide 22: M&S in Transportation Systems
Discrete Modeling (example)
  Problem statement: Airport Terminal passenger flow
  Tutorial focus area: Human mobility
Mobility at airports - a series of discrete events:
  Enter terminal | obtain boarding pass | bag check
  Security line | shuttle to gate | standby at gate | board
Objective: Apply discrete event theory to optimize operations within an airport terminal (Naples, IT)
  Passenger experience – minimize wait times
  Airport resources – total expense
Guizzi et al., 2009

## Slide 23: M&S in Transportation Systems
Discrete Modeling (example)
Objective function (cost) model:
  Opening check-in desk
  Opening security checkpoints
  Associated customer inconvenience metrics
Outcomes: Preliminary model feasibility to produce a logical and rational management of check-in and security checkpoints inside the airport terminal
Demonstrated future potential for model adaptation to enhance operations at other airport terminals
Guizzi et al., 2009
Terminal 1: Naples Capodichino Airport

## Slide 24: M&S in Transportation Systems
Continuous Modeling (example)
  Problem statement: Aircraft routing and climate modeling
  Tutorial focus area: Sustainability/environment
Objective: Implement continuous modeling for estimation of climate change mitigation
Simulation objectives:
  Optimize flight trajectories
  Minimize fuel consumption
Flight trajectory optimization components:
  Fuel, emissions, operating cost, contrail avoidance
  Climate impact (global temperature response: ATR20)
Yamashita et al., 2020
a)
b)

## Slide 25: M&S in Transportation Systems
Continuous Modeling (example)
Optimization Model considerations:
  Oxone, methane, water vapor, carbon dioxide, and contrails
Outcomes:
  Operating cost: inversely proportional to flight time and fuel use
  ATR20 minimization tends to increase aircraft operating costs
  Trade-off between aircraft operating costs/climate impact
  Confirms data observed in previous literature
Yamashita et al., 2020

## Slide 26: M&S in Transportation Systems
Human-behavior modeling: process that replicates how humans perform, given assignment of initial conditions
Typically, not implemented to predict human behavior
  May instruct a new behavior
  May influence frequency of a previously learned behavior
  May increase frequency of a similar behavior
In Transportation: often implemented to understand the aggregate outcome of a complex system (e.g., pedestrian behavior; the “shortest path” principle)
Zou & Liu, 2022
Kim, 2012

## Slide 27: M&S in Transportation Systems
Related modeling approaches:
Social learning theory emphasizes 4 components:
  Attention | Retention | Reproduction | Motivation
The DISC model assumes that individuals tend to follow patterns of behavior
  Dominant – confident; focus on results
  Influence – place emphasis on relationships
  Steadiness – are dependable and cooperative
  Conscientiousness – emphasize accuracy and competency
Marston, 1928
Bandura, 1977

## Slide 28: M&S in Transportation Systems
Human-behavior Modeling (example)
  Problem statement: Cognitive behavior modeling of pedestrian behavior in large crowds
  Tutorial focus area: Human mobility
Objective: Apply cognitive heuristics to achieve an improved understanding of crowd dynamics
  Crucial for future preparation of large events
Guided by visual information - pedestrians apply simple cognitive procedures to adapt walking speeds and directions (i.e., to avoid collisions)
Moussaïd et al., 2011
Distance to destination

## Slide 29: M&S in Transportation Systems
Human-behavior Modeling (example)
With overcrowding, physical interactions may occur, causing unintentional movements – less predictable
Outcomes: model predicts the emergence of self-organization phenomena (e.g., stop-and-go waves)
  Integrated handling of human interactions overcomes limitations of physics-based modeling approaches
Future applications: biological swarms; autonomous technologies (e.g., vehicles/drones)
Moussaïd et al., 2011

## Slide 30: M&S in Transportation Systems
Multi-Resolution Modeling (MRM): construction of a single model (or family of models) to describe the same system at different resolutions
A trade-off between a high-resolution model that may be unnecessarily rich with detail and a simpler low-resolution model that is not as accurate
Often implemented for LVC interoperability to integrate pre-existing model characteristics
Also implemented to vary finite element mesh density (e.g., high stress concentration)
Davis & Bigelow, 1988
Lee et al., 2020

## Slide 31: M&S in Transportation Systems
Multi-Resolution Modeling (example)
  Problem statement: Macro, Meso, & Microscopic Modeling for Traffic Simulation
  Tutorial focus area: Transportation/Mobility
Objective: develop an integrated transport framework that combines three modeling fidelities:
  Macro: traffic stream characteristics like density, flow, mean speed – like a fluid (aggregated)
  Meso: imparts simplified flow dynamics
  Micro: emulate the dynamics of individual vehicles; car-following/lane-changing (disaggregated)
Kesting et al., 2008
Casas et al., 2011

## Slide 32: M&S in Transportation Systems
Multi-Resolution Modeling (example)
Origin-destination (OD) matrix maps demand to maintain network consistency under assumption of (static/dynamic) equilibrium
Outcomes:
  Computer modeling: established an approach to overcome the limitations of transport models based on different network representations
  Traffic modeling: demonstrated compatibility between system representations implemented at each level
Barceló et al., 2005
Winder & Lutz, 2016

## Slide 33: M&S in Transportation Systems
Semi-automated forces (SAF): Standardized military software frameworks (e.g., JSAF, OneSAF, ModSAF)
Computer-controlled networked assets that appear as though commanded by human operators
Typically implemented for realistic training/evaluation on a virtual battlefield
  Opposing forces (to train against)
  Friendly forces (to practice unit coordination)
Fawkes, 2017

## Slide 34: M&S in Transportation Systems
Semi-automated forces (example)
  Problem statement: Automated Air Traffic Simulation for Traffic Flow Management
  Tutorial focus area: Sustainability/resilience
The resources and time required to conduct real-time human-in-the-loop (HITL) analysis limits the number of experimental conditions that can be examined
Objective: Leverage an automated simulation capability to analyze the impact of varying levels of airline participation on ground delay and flight time
Liu et al., 2022

## Slide 35: M&S in Transportation Systems
Semi-automated forces (example)
Newark (EWR) used for scenario testing
  195 total flights
  66 different origin airports
Outcomes:
  Parametric studies quantify the impact of departure uncertainty on flow management delays
  Help determine scheduling paradigms that prioritize internal departures or airborne flights
Arneson et al., 2018

## Slide 36: M&S in Transportation Systems
Human-computer Interaction (HCI): analysis of how humans and computers interact
  Human: e.g., communication theory, cognitive psychology, human factors
  Machine: e.g., computer graphics, operating systems, programming languages
Design an interface that can accommodate persons with different learning styles
  Left-brained: logic, analysis (linear)
  Right-brained: creativity, imagination (visual)
Katona, 2021
Brosnan, 2004

## Slide 37: M&S in Transportation Systems
Human-computer Interaction (example)
  Problem statement: Simulation analysis of human factors related to autonomous driving
  Tutorial focus area: Mobility/Automation
The facilitation of takeover requests by the automated system is an emerging issue (in HCI) to ensure the safety and control of drivers
Objective: Analyze driver acceptance associated with autonomous control
Salubre & Nathan-Roberts, 2021
Dix, 2023

## Slide 38: M&S in Transportation Systems
Human-computer Interaction (example)
Simulator HCI efforts have numerous advantages:
  Identify human tolerances to accelerate the adoption of advanced autonomous technologies (i.e., safety)
  Reference point for optimizing route capacity of next-generation transportation systems (i.e., efficiency)
Outcomes:
  As headway increases – elevated participant ratings (e.g., acceptance) and reduced driver workload
  Most drivers prefer spacing between vehicles by relying on distance, rather than headway (time)
Hou et al., 2014
An et al., 2020
25 mph
Rating (0-10)
Headway (seconds)

## Slide 39: M&S in Transportation Systems
Virtual Environments and Game Engines:
Tools that optimize and simplify the development of vehicle simulations (e.g., digital twins) for applications in training and research
Game Engines integrate graphics rendering (2D/3D), physics, sound, and animation with artificial intelligence (AI) for gameplay
  Unity3D – popular game engine, based in C#, large asset availability, very good graphics
  Unreal Engine – cross-platform game engine, based in C++, exceptional graphics capabilities
Hulme et al., 2023

## Slide 40: M&S in Transportation Systems
Virtual Environments and Game Engines
Emerging vehicle technologies mandate M&S:
  Connected and autonomous vehicle (CAV) systems
  Advanced driver assistance systems (ADAS)
Game-based platforms (e.g., CARLA) feature sensors (e.g., LIDAR, radar, HD cameras), environmental conditions, static/dynamic actors (i.e., vehicles, pedestrians, traffic signals), terrain maps
Dosovitskiy et al., 2017

## Slide 41: M&S in Transportation Systems
eXtended Realities (XR): VR/AR/MR
XR (aka cross reality): umbrella term for several different but related technologies:
Virtual Reality (VR) – a virtual (immersive) experience where entire field of vision is the device’s display
Augmented Reality (AR) - captures live surroundings and adds (augments) artificial visual elements to it
  Mixed Reality (MR) – an interactive combination of VR (immersion) and AR (augmentation)
RubyGarage, 2020
Virtual
Reality (VR)
Interact in a fully
artificial environment
Augmented
Reality (AR)
Virtual objects overlaid on real-world environment
Mixed
Reality (MR)
Virtual environment combined with real-world
Full immersion in virtual environment
The real world enhanced with digital objects
Interact with both the real-world and the virtual environment

## Slide 42: M&S in Transportation Systems
eXtended Realities (XR): VR/AR/MR
Analyze user preferences and safety issues for AR windshield displays in automated driving
  Single (S) vs Multiple (M) windows
  Baseline vs. Personalized context
NASA Task Load Index (TLX) used to assess workload ratings across standard categories
  Users prefer customizable, multi-window setups that visualize content-type specific applications
Findings help automotive interface designers to improve experiences in automated vehicles
Riegler et al., 2022

## Slide 43: M&S in Transportation Systems
Machine Learning (ML) and Artificial Intelligence (AI)
AI: the application of computers to mimic human decision-making and problem-solving logic capabilities
  In Transportation: machine vision and voice recognition are commonly applied in automated vehicle (AV) technologies
ML: a data-driven approach that allows computers to imitate human learning capabilities (a subset of AI)
  Modeling approaches: neural networks and deep learning
  Big data analytics often required to process massive datasets (e.g., e.g., real-time HD video)
Samuel, 1959
Somers & Weeratunga, 2015

## Slide 44: M&S in Transportation Systems
Transportation AI market share (by 2030): $13T USD
Benefits of AI in this sector:
  Increased network efficiency | Improved operations
  Safety (pedestrians and drivers)
  Reduced costs | Eco-friendliness
Applications:
  Autonomous Vehicles (i.e., cars, trucks, ships, drones)
  Intelligent Transportation Systems (e.g., V2X)
Haponik, 2021
Behrooz & Hayeri, 2022

## Slide 45: Tutorial Summary
Transportation Systems Modeling & Simulation (M&S)
Transportation: broadly impactful upon everyone on this planet
M&S: subject matter is an ideal vessel for core/fundamentals training
Certification: content of this Tutorial can assist with CMSP preparation
2023 I/ITSEC priorities: digital technologies continue to enable global readiness

## Slide 46: Tutorial Summary
Confirm satisfaction of Learning Objectives
Describe basic concepts (M&S) that are foundational to I/ITSEC.
Classify applications in M&S with relation to transportation and human mobility.
Analyze modeling methods and implementations aligned with NTSA CMSP.
Distinguish mathematical fundamentals related to mobility, sustainability, logistics.
Formulate future pathways to advance sustainable human mobility in a digital world.

## Slide 47: Acknowledgements
The Stephen Still Institute for Sustainable Transportation and Logistics (SSISTL)
  Major topics in this Tutorial serve as the charter of our Institute

## Slide 48: Bibliography (1/7)
Albeaik et al., 2021
  Limitations and Improvements of the Intelligent Driver Model (IDM)
  https://arxiv.org/pdf/2104.02583.pdf
Alternative Fuels Data Center (AFDC), 2023
  How Do Liquefied Natural Gas Trucks Work?
  https://afdc.energy.gov/vehicles/how-do-lng-cars-work
Ahmed et al., 2021
  A Review of Car-Following Models and Modeling Tools for Human and Autonomous-Ready Driving Behaviors in Micro-Simulation
  https://doi.org/10.3390/smartcities4010019
Alvim et al., 2022
  Supply chain resilience in turbulent times: conceptual model and real-world use case
  https://doi.org/10.1016/j.ifacol.2022.09.372
An et al., 2020
  Car-following model for autonomous vehicles and mixed traffic flow analysis based on discrete following interval
  https://doi.org/10.1016/j.physa.2020.125246
Anderson et al., 2001
  A taxonomy for learning teaching and assessing a revision of Bloom's taxonomy of educational objectives
  https://www.researchgate.net/publication/235465787
Arneson et al., 2018
  Using an Automated Air Traffic Simulation Capability for a Parametric Study in Traffic Flow Management
  https://doi.org/10.2514/6.2018-3665

## Slide 49: Bibliography (2/7)
Avesh & Srivastava, 2022
  Active Suspension System Modeling for a Passenger Car Subjected to Random Road Profile Inputs
  https://link.springer.com/chapter/10.1007/978-981-15-8704-7_53
Bandura, 1977
  Social Learning Theory
  https://doi.org/10.1177/105960117700200317
Barceló et al., 2005
  Methodological Notes on Combining Macro , Meso and Micro Models for Transportation Analysis
  Corpus ID: 17864092
Barykin et al., 2020
  Concept for a Supply Chain Digital Twin
  https://doi.org/10.33889/IJMEMS.2020.5.6.111
Behrooz & Hayeri, 2022
  Machine Learning Applications in Surface Transportation Systems: A Literature Review
  https://doi.org/10.3390/app12189156
Brosnan, 2004
  The neuropsychology of Human Computer Interaction (HCI)
  https://www.witpress.com/Secure/elibrary/papers/CI04/CI04003FU.pdf
Casas et al., 2011
  The need to combine different traffic modelling levels for effectively tackling large-scale projects adding a hybrid meso/micro approach
  https://doi.org/10.1016/j.sbspro.2011.08.031

## Slide 50: Bibliography (3/7)
Darie & Rörup, 2017
  Hull girder ultimate strength of container ships in oblique sea
  https://doi.org/10.1201/9781315157368-27
Davis & Bigelow, 1988
  Experiments in Multiresolution Modeling (MRM)
  https://apps.dtic.mil/sti/pdfs/ADA355041.pdf
Dix, 2023
  Human-Computer Interaction (HCI)
  https://www.interaction-design.org/literature/topics/human-computer-interaction
DoD, 1998
  DoD 5000.59-M, DoD Modeling and Simulation (M&S) Glossary
  https://biotech.law.lsu.edu/blaw/dodd/corres/pdf/500059m_0198/p500059m.pdf
Dosovitskiy et al., 2017
  CARLA: An Open Urban Driving Simulator
  https://doi.org/10.48550/arXiv.1711.03938
Ergin et al., 2007
  Hydroelastic Analysis of a 1900 TEU Container Ship Using Finite Element and Boundary Element Methods
  Corpus ID: 110317632
Fawkes, 2017
  Developments in Artificial Intelligence – Opportunities and Challenges for Military Modeling and Simulation
  Corpus ID: 140113139

## Slide 51: Bibliography (4/7)
Guizzi et al., 2009
  A discrete event simulation to model passenger flow in the airport terminal
  https://dl.acm.org/doi/10.5555/1949006.1949078
Haponik, 2021
  AI, big data, and machine learning in transportation
  https://addepto.com/blog/ai-big-data-and-machine-learning-in-transportation/
Harish, 2022
  Finite Element Method – What Is It? FEM and FEA Explained
  https://www.simscale.com/blog/what-is-finite-element-method/
Hou et al., 2014
  A Validated and Integrated Simulation Framework for Human Factors Analyses
  https://cse.buffalo.edu/CTS/papers/IITSEC14_14006.pdf
Hulme, 2022
  The I/ITSEC Professional Development Primer: M&S Fundamentals, Certification, and Contemporary Applications
  NTSA I/ITSEC 2022 (Tutorial)
Hulme et al., 2023
  Game Engine Modeling & Simulation (M&S) implementations to evaluate Human Performance in Transportation Engineering
  NTSA MODSIM World 2023 (Paper)
Katona, 2021
  A Review of Human–Computer Interaction and Virtual Reality Research Fields in Cognitive InfoCommunications
  https://doi.org/10.3390/app11062646

## Slide 52: Bibliography (5/7)
Kesting et al., 2007
  General Lane-Changing Model MOBIL for Car-Following Models
  https://doi.org/10.3141/1999-10
Kim, 2012
  Human Resource Management – Chapter 11: Behavior Modeling
  https://doi.org/10.1002/9781118364741.ch11
Lee et al., 2020
  A Systematic Review of the Multi-Resolution Modeling (MRM) for Integration of Live, Virtual, and Constructive Systems
  https://doi.org/10.3390/info11100480
Liu et al., 2022
  Intelligent Management of Air Traffic Flow Based on Intelligent Motion Coordinate Data Model
  https://doi.org/10.1155/2022/3628798
Marston, 1928
  Emotions of Normal People
  https://doi.org/10.4324/9781315010366
Moussaïd et al., 2011
  How simple rules determine pedestrian behavior and crowd disasters
  https://doi.org/10.1073/pnas.1016507108
Mumayiz, 1990
  Overview of Airport Terminal Simulation Models
  https://onlinepubs.trb.org/Onlinepubs/trr/1990/1273/1273-002.pdf

## Slide 53: Bibliography (6/7)
NTSA, 2023
  2023 Call for Presentations – Sustaining a Global Force in a Digital World
  https://www.iitsec.org/-/media/sites/iitsec/get-involved/2023/iitsec2023callforpresentations.pdf
Oswalt, 2022
  Certified Modeling and Simulation Professional 3.0
  https://content.trainingsystems.org/-/media/sites/ntsa/cmsp/iitsec-2021---cmsp-pdw---course---20211202.ashx
Riegler et al., 2022
  Towards Personalized 3D Augmented Reality Windshield Displays in the Context of Automated Driving
  https://doi.org/10.3389/ffutr.2022.810698
Robinson, 2000
  Simulation Model Verification And Validation: Increasing The Users' Confidence
  https://doi.org/10.1145/268437.268448
RubyGarage, 2020
  VR vs AR vs MR: Differences and Real-Life Applications
  https://rubygarage.org/blog/difference-between-ar-vr-mr
Salubre & Nathan-Roberts, 2021
  Takeover Request Design in Automated Driving: A Systematic Review
  https://doi.org/10.1177/1071181321651296
Samuel, 1959
  Some Studies in Machine Learning Using the Game of Checkers
  https://doi.org/10.1147/rd.33.0210

## Slide 54: Bibliography (7/7)
Somers & Weeratunga, 2015
  Automated vehicles: are we ready? Internal report on potential implications for Main Roads WA
  https://trid.trb.org/view/1346030
Sun & Ertz, 2020
  Life cycle assessment and Monte Carlo simulation to evaluate the environmental impact of promoting LNG vehicles
  https://doi.org/10.1016/j.mex.2020.101046
Vanek et al., 2014
  Sustainable Transportation Systems Engineering, 1st Edition
  https://www.accessengineeringlibrary.com/content/book/9780071800129
Winder & Lutz, 2016
  Computational Ants: Agent Based Visualization Technique with CDR OD Matrix
  https://ira.mit.edu/blog/agent-based-visualization
Wuthishuwong & Traechtler, 2019
  Distributed control system architecture for balancing and stabilizing traffic…using feedback consensus and route assignment method
  https://doi.org/10.1007/s40747-019-00125-3
Yamashita et al., 2020
  Newly developed aircraft routing options for air traffic simulation in the chemistry–climate model
  https://doi.org/10.5194/gmd-13-4869-2020
Zou & Liu, 2022
  Modeling Pedestrian Motion in Crowded Scenes Based on the Shortest Path Principle
  https://doi.org/10.3390/app12010381

## Slide 55: Contact Information | Q&A
Kevin F. Hulme, Ph.D., CMSP
Program Manager
The Stephen Still Institute for Sustainable Transportation and Logistics (SSISTL)
University at Buffalo
204 Ketter Hall
Motion Simulation Laboratory (MSL) | 106 Furnas Hall
716-645-5573
hulme@buffalo.edu