## Slide 1
Evolution of RF Signal Visualization from Spectrum Analyzers to Augmented Reality (#23T33)
Jad Meouchy, BadVR
Suzanne Borders, BadVR

## Slide 2: Tutorial Overview
5 min | Introduction and Learning Objectives
10 min | Background on Radio Frequencies
15 min | Traditional Signal Visualization
25 min | Immersive Signal Visualization
10 min | Summary and Conclusions
5 min | Acknowledgements
10 min | Q&A

## Slide 3: Learning Objectives
Understand challenges of existing tools for RF signal analysis and visualization
Differentiate between 1D, 2D, and 3D signal visualizations
Comprehend fundamentals of immersive technologies like AR/VR and potential applications for signals intelligence, visualization, and military communications
Identify best practices and applied theory to the design of next-generation signal analysis user interfaces

## Slide 4: Terminology and Concepts
Fourier Transform – Mathematical function that converts time-domain signal data into frequency-domain magnitudes and phases
Modulation/Demodulation – Encoding and extracting information from a carrier wave
RSSI – Received signal strength indication, a measurement of received power
TSCM – Technical Surveillance Countermeasures, colloquially understood as “bug hunting”
Immersion, AR, VR – a collection of holographic technologies including Augmented Reality and Virtual Reality
Metaverse – Umbrella buzzword representing the next generation of 3D computing and connectivity
SIGINT – Signals Intelligence, intelligence gathering by interception of signal communications between people
Spatial Anchors – Specific locations in virtual space that persist in the real world

## Slide 5: Challenge
Complicated
Cumbersome
Distracting
Slow
Traditional visualization tools are no longer suitable to address the scale and complexity of modern signals
Signals analysis is currently a niche engineering field requiring extensive technical education and training

## Slide 6
Wireless devices and networks are a primary attack vector
Backdoors are hidden inside chip firmware
290 million people were affected by data breaches in 2021 alone
Security Implications
Defense industry spends billions each year for SIGINT, EW, and wireless security
Secure facilities do not allow most wireless devices, and are swept continuously
Meeting rooms are shielded from RF

## Slide 7: Impact
Training
Experiential learning
Signal propagation communication
Modeling
Mathematical model visualization incl. AI/ML
Ideation and predictive analytics
Simulation
Reproduction of complex signal fields
Comms systems planning and testing
Notes: What is the FCC

## Slide 8: Immersive Signal Visualization

## Slide 9: Background on Radio Frequencies

## Slide 10: Introducing the Spectrum
The Electromagnetic Spectrum
Hz
Hz
Notes: From kilohertz to gigahertz

## Slide 11: Radio Frequencies
TeraSense

## Slide 12: DoD Use of Radio Spectrum
Notes: Source:
U.S. Government Accountability Office, Spectrum Management: Federal Relocation Costs and Auction
Revenues, 13-472, May 2013, p. 6, https://www.gao.gov/assets/660/654794.pdf.

## Slide 13: Satellite Frequency Bands

## Slide 14: Starlink Example

## Slide 15: Notable Moments in RF History
First television broadcast
NAVSTAR 1
GPS satellite
Digital broadcasting gains popularity
5G, smart cities, self-driving cars
1928
1890s
1978
1990s
Present
1934
Testing radio transmissions
FCC is formed
Notes: Primarily used for communication

## Slide 16: Regulating the Spectrum
Federal Communications Commission (FCC)
Assign operating ranges of RF spectrum in the US for civ & mil
Prevent interference and promote efficient use
Certify RF-emitting devices
Notes: What is the FCC

## Slide 17: Anechoic Chambers
Fully shielded room with RF-absorbing wall materials
Measurement of antenna’s gain, efficiency, and radiation pattern
For controlled evaluation of radio frequency emissions
Critical for ensuring compliance with emission standards
Notes: What is the FCC

## Slide 18: Examples of Lab Testing Reports
FCC (2017)
Notes: What is the FCC

## Slide 19: Common Laboratory Equipment
Spectrum Analyzer
Oscilloscope
Analyze time
Analyze frequency
HouseTechLab
There are many categories and classes of commercial signal analysis tools; the following are among the most used:
Graphical indication of voltage change
Plot of 1D signal over time
Measure signal power across a freq range
Display amplitude over signal frequency
Notes: Really high level, groups/classifications of tools and techniques
Scopes
Spectrum analyzers
Emissions graphs

## Slide 20: Portable Analysis Tools
In the field, measurement tools are made portable with mounted screens and audio outputs, across a wide range of sizes and form factors

## Slide 21: Traditional Signal Visualization

## Slide 22: 1D Signal Visualization
High information density
Frequently on laptops and tablets
Continuous scrolling top to bottom
Low information density
Small display sizes
Needs logging
Oscilloscope
Waterfall Display

## Slide 23: 2D Signal Visualization
Reflects real world space
Green is good, red is bad
Typically extrapolated
Heatmaps represent X-Y samples and projected values of signal strength
“Can you hear me now?” only shows outdoor coverage
***These visualizations show the highest available speeds;
more and better coverage may be available at slower speeds

## Slide 24: 3D Signal Visualization
Adds Z dimension
Performs advanced modeling
Uses graphics and gaming engines
Notes: Define it, explain how it’s valuable
https://www.researchgate.net/figure/The-RF-Map-and-Sampling-Points-in-a-Geographical-Area_fig1_263889159
https://www.researchgate.net/figure/Visualisation-of-RF-radiation-indoor-with-use-of-special-3D-graphic-effects-in-a-single_fig1_228832254

## Slide 25: Antenna Radiation Patterns
FrontierUS
Graphic of the directional (Angular) dependence of the strength of the radio waves from the antenna or other source, power based on distance
Notes: Define it, explain how it’s valuable

## Slide 26: Real World Behavior
All objects, manufactured and natural, interact with wireless signals, especially in dense urban environments

## Slide 27
Modern steel/concrete/tinted glass buildings are “radio opaque”
Material density causes attenuation
Trees and foliage can block RF
Metallic surfaces can cause counterintuitive radio reflections
Human bodies interfere also; remember “antenna gate”
Anderson (2017)
Interference

## Slide 28
There are a fixed number of Wi-Fi, Bluetooth, Cell, etc. channels
With too many connected devices, channels become saturated
Net result is denial of service
Infrastructure was never designed for this volume of devices
IoT is already a worst-case scenario
Anderson (2017)
Channel Congestion

## Slide 29: Challenges of 5G & LEO
 | 5G | LEO
Infrastructure | Build 1M small cells and base stations | Manufacture and launch 30K satellites
Spectrum | Businesses fight for access to frequency bands | Managing constellations is highly technical
Interference | mmWave blocked by foliage and buildings | Weather, handover, doppler shift, coexistence
Latency | Needs edge compute resources | Large distances, must obey laws of physics

## Slide 30: Signals Intelligence (SIGINT)
Ability to seize, retain and exploit the spectrum is critical to battlefield superiority
SIGINT & EW capabilities are being added to manned and unmanned vehicles
BAE

## Slide 31
Live Virtual Constructive (LVC) training environments
Testing and sims to prepare for varying conditions and cyber threats
Need reliable communications fabric for multidomain ops
Ex. Low band RF mesh network with connected Android Tactical Assault Kits (ATAK) during live training
Rockwell Collins (2016)
Resilient Training Environments
Notes: https://militaryembedded.com/radar-ew/test/lvc-demonstration-completed-by-rockwell-collins-in-france-u-k-and-u-s http://www.ds2.com/Services/Training/ATAK

## Slide 32: Immersive Signal Visualization
Definition and Impact

## Slide 33: Immersive / AR / VR / Metaverse

## Slide 34: Augmented Reality (AR)
Overlay holograms into real-world objects and environments
Merge the real and the virtual using sensors and trackers

## Slide 35: Examples

## Slide 36
Spatial Awareness
Spatial mapping and computational geometry understand your physical space to provide situational awareness

## Slide 37: Equipment
Popular current and upcoming AR headsets
Magic Leap 2
Qualcomm (Reference Design)
Microsoft HoloLens 2

## Slide 38: Pros and Cons
Weaknesses
Limited FOV
Durability & brightness
High hardware cost
Opportunities
Size and weight
Integrated biometrics
AI/ML assistants
Strengths
Good battery life
Wireless connectivity
Spatial awareness

## Slide 39: Increased Adoption
Pandemic sped adoption of immersive technologies
Enhanced use in education, training, virtual events, etc.
Example: US Army immersive combat training in Synthetic Training Environment
Ball et. Al, 2021, World Economic Forum, 2022

## Slide 40: AR Signal Visualization
Mainstream implementations of AR signals (early days)
ARSensor, ARWave, NBC (2015), Pieper (2018)

## Slide 41: AR Signal Visualization
Koutitas et. Al. (2020)
Research focusing on AR, spatial mapping and ray tracing channel prediction algorithms to visualize wireless channels in real-time

## Slide 42: Immersive Signal Visualization
Design & Development

## Slide 43
Design Considerations
Hardware Display
Field-of-view (FOV) limitations
Indoor and outdoor lighting conditions can affect holograms
Hands-free interaction ability with gesture and voice recognition

## Slide 44
User Interface
Ergonomics of interactables
Direct interaction with objects versus onscreen controls
Colors, shapes, and symbology
Multi-User interactions
Design Considerations
Wikitude (2021)

## Slide 45: Example of 3D Spatial Signals
Intuitive perception of Relative Signal Strength Indicator (RSSI)
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 46: Interaction Methods
Enable user to access contextual information with simple movements and gestures
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 47: Holograms
To skeumorphism or not?
Density of information
Sizing of symbols
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 48: Example: Direction Finding
Find the strongest emitting device
Show relative distance and bearing, for navigation
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 49
Heads-Up Display
Persistent information
Track head angle
Clear center area
HUD

## Slide 50: Relative Positioning
Show user in context with all available data
Track according to reference point
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 51: User Engagement
Augment user’s senses with surface patterns and a “slicing” tool
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 52: Bridging 2D to AR

## Slide 53: Spatial Signal Simulation
Spatial representation of observable signals
Highly dynamic indoor environment
Used for modeling networks
Signal source

## Slide 54: Model Validation
On-site signal collection in network telecoms lab
Walk along path with device away from signal source
Collect data on position, direction and signal strength
Notes: What is the FCC

## Slide 55: Affiliation with AI/ML
On-the-fly control and interaction with the AI/ML algorithms
to assist the user in their quest for discovering insight
Notes: https://app.slack.com/client/T654F77ME/search/search-eyJkIjoiZmluZGVyJTIwYW5kJTIwLnBuZyIsInEiOiJVMDFEVDZMRk5UVSIsInIiOiJmaW5kZXIlMjBhbmQlMjAucG5nIiwicyI6InJlY2VudE1lc3NhZ2VzIn0=/files/F01Q177T46S?cdn_fallback=1

## Slide 56: Defensive vs. Offensive
Find transmitting devices inside SCIF
Decrypt wireless traffic
Identify and locate target device, disable it
Model EW jamming range and source
Detect incoming drones

## Slide 57: Testing and Tuning
Only 3-5 min hands-on training
Swift detection of random spectrum attack
Full physical discovery of source attack device

## Slide 58: Operational Deployment

## Slide 59
Leverage real-world concepts
Draw inspiration from media
Add visual/auditory feedback
Embrace ergonomics
Minimize text
Anderson (2017)
Best practices

## Slide 60: Summary and Conclusion

## Slide 61
(c) 2019 Magic Leap, Inc.
Smart Cities
IoT sensor networks
5G, 6G, 7G, and beyond
Construction preplanning
Transportation
Aviation systems
Connected mobility
Traffic smart metering
Health
Safe training
Remote surgery
Extrasensory perception
Alharbi et. Al. (2019)
Future Work
Notes: CASSIE
Thank you, Naomi and the team from Magic Leap, BadVR and the German Space Agency. I hope you have enjoyed the talk and understand how spatial computing can help us meet the challenges of climate change. The team will be around for the next few days to answer questions and give demos. Our big ask is for you to please reach out to us and see where this platform is able to help your country with climate change. This project is going to be developed over the coming years and for 2021 we will be engaging with all 170 of our offices about this platform.

## Slide 62: Additional Signals
Chemical, biological, radiological and nuclear (CBRN) sensor data
Software Defined Radios (SDR)
Ubertooth/Bluetooth devices
Medical devices
Utilize AI/ML
NIH (2022) , Wikimedia (2005)

## Slide 63: Into Space
Space Defense
Improve modeling effectiveness
Anti-Access/Area denial strategies target RF communications to inhibit movement
Jamming of signals for low-power satellites, and counter-jamming
Reduce freedom of action
Airbus
Notes: What is the FCC

## Slide 64: Takeaway
Immersive technology will enhance modeling of signals in real world
Cumbersome, focused on screen instead of scene, 1D/2D
Preserve use of hands, ​maintain situational awareness,​ expand comprehension in 3D

## Slide 65: Revisit Goals
Confirm Learning Objectives
Understand challenges of existing tools for RF signal analysis
Differentiate between 1D, 2D, and 3D signal visualizations
Discover fundamentals of immersive technologies like AR/VR and potential applications for signal intelligence and visualization
Identify best practices and applied theory to the design of next-generation signal analysis user interfaces
Notes: Add bloom triangle but with no words
https://bloomstaxonomy.net/

## Slide 66: Bibliography
Airbus. https://airbusus.com/laser-communication/
Anderson (2017). “Reduce EMI to Improve Radio Range”. https://medium.com/tempo-automation/improve-radio-range-by-lowering-emi-dac7135f77f9
Alharbi et. Al. (2019). “Roles and Challenges of Network Sensors in Smart Cities”. https://iopscience.iop.org/article/10.1088/1755-1315/322/1/012002/pdf
Altium (2017). “How to Choose a Test Lab for FCC Certification of IoT Products”. https://www.altium.com/subscription
Antenna Test Lab. “What is an Anechoic Chamber?”. https://antennatestlab.com/antenna-education-tutorials/what-is-an-anechoic-chamber
ARSensor. https://play.google.com/store/apps/details?id=com.ken.arsensor&hl=en_US&gl=US
ARwave. https://apps.apple.com/us/app/ar-wave-visualization-of-wifi/id1470866212
Army Futures Command (2022). “Synthetic Training Environment offers multi-dimensional combat preparation”. https://www.army.mil/article/254005/synthetic_training_environment_offers_multi_dimensional_combat_preparation
Ball et. Al. (2021). “Virtual reality adoption during the COVID-19 pandemic: A uses and gratifications perspective”. https://www.sciencedirect.com/science/article/pii/S0736585321001672
BAE. "Unmanned SIGINT/Electronic Warfare". https://www.baesystems.com/en/product/unmanned-sigint-electronic-warfare
Bloom (2001). “What is Bloom’s Taxonomy”. https://bloomstaxonomy.net/
FrontierUS. https://frontiercomputercorp.com/specifying-the-right-antenna/

## Slide 67: Bibliography
HouseTechLab. “Difference between spectrum analyzer and oscilloscope” https://housetechlab.com/difference-between-spectrum-analyzer-and-oscilloscope/
iBWave. https://info.ibwave.com/augmented-reality/
Koutitas et. Al. (2020). “In Situ Wireless Channel Visualization Using Augmented Reality and Ray Tracing”. https://www.mdpi.com/1424-8220/20/3/690/htm
McKinsey (2018). “The road to 5G: The inevitable growth of infrastructure cost”. https://www.mckinsey.com/industries/technology-media-and-telecommunications/our-insights/the-road-to-5g-the-inevitable-growth-of-infrastructure-cost
NBC (2015). “App Visualizes Radio Waves From Cell Towers, Satellites Around You”. https://www.nbcnews.com/tech/innovation/app-visualizes-radio-waves-cell-towers-satellites-around-you-n469781
NIH (2022). “Electric & Magnetic Fields”. https://www.niehs.nih.gov/health/topics/agents/emf/index.cfm
NTIA (2016). https://www.ntia.doc.gov/files/ntia/publications/january_2016_spectrum_wall_chart.pdf
Pieper (2018). “Introducing WiFiman”. https://blog.ui.com/2018/12/11/introducing-wifiman/
RF Page (2021). “What are Radio Frequency bands and its uses?”. https://www.rfpage.com/what-are-radio-frequency-bands-and-its-uses/
Rockwell Collins (2016). "LVC demonstration completed by Rockwell Collins in France, U.K., and U.S." https://militaryembedded.com/radar-ew/test/lvc-demonstration-completed-by-rockwell-collins-in-france-u-k-and-u-s
TeraSense. “Radio Frequency Bands”. https://terasense.com/terahertz-technology/radio-frequency-bands/

## Slide 68: Bibliography
Wikimedia (2005). https://commons.wikimedia.org/wiki/File:An_instructor_at_the_Defence_NBC_Centre_operates_the_Manportable_Chemical_Agent_Detector_MOD_45148143.jpg
Wikitude (2021). “How to Apply UX Design Principles in Augmented Reality”. https://www.wikitude.com/blog-ux-design-for-augmented-reality/
World Economic Forum (2022). “Immersive Media Technologies: The Acceleration of Augmented and Virtual Reality in the Wake of COVID-19”. https://www3.weforum.org/docs/WEF_Immersive_Media_Technologies_2022.pdf

## Slide 69: Contact Info
BadVR, Inc.
10312 Norris Ave. Ste. D​
Pacoima, CA 91331
(833) 600-DATA
Jad Meouchy, CTO​
jad@badvr.com
Suzanne Borders, CEO​
suzanne@badvr.com