## Slide 1
Making the Case: Building Strong M&S Verification and Validation Evidence
Simone M. Youngblood
The Johns Hopkins University Applied Physics Laboratory
240-228-7958 Simone.Youngblood@jhuapl.edu
Katherine M. Ruben
The Johns Hopkins University Applied Physics Laboratory
240-228-9148 Katherine.Ruben@jhuapl.edu

## Slide 2: Making the Case Tutorial Learning Objectives
Primary Objective: Identify the key steps that can be taken to build strong Verification & Validation (V&V) evidence while accounting for resource impacts.
Key Learning Objectives:
  Define and distinguish key verification and validation terms
  Identify important characteristics of available verification test strategies
  Construct an effective referent in non-ideal circumstances
  Recognize the key elements (metrics, methods) that support rigorous validation.
  Match validation methods to the available referent
  Identify applicable V&V templates and tools

## Slide 3: Presentation Outline
Definitions that establish the common lexicon
  Terms
  Setting boundaries by defining the intended use
Building a strong verification case
  Defining M&S Requirements
  Leveraging existing verification data
  Leveraging developer testing
  Supplemental V&V testing
Building a strong validation referent
  Developing the referent as the basis for validation comparison
  Challenges and obstacles to developing the referent
  Best practices and obstacle mitigation
  Examples
Building a strong validation case
  Defining validation metrics
  Selecting and applying the appropriate method
  Quantifying validation uncertainty
  Examples
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 4: Learning Strategy
Learning Strategy | Define and distinguish key verification and validation terms | Identify important characteristics of available verification test strategies | Construct an effective referent in non-ideal circumstances | Recognize the key elements (metrics, methods) that support rigorous validation | Match validation methods to the available referent | Identify applicable V&V templates and tools
Definitions that establish a common lexicon |  |  |  |  |  | 
Building a strong verification case |  |  |  |  |  | 
Building a strong validation referent |  |  |  |  |  | 
Building a strong validation case |  |  |  |  |  | 
Documentation tools and templates and tools |  |  |  |  |  | 

## Slide 5: Tutorial Motivation
Historically V&V tutorials focused on
  Fundamental relationships and processes
  Validation techniques
  Recommended Practices and Guidance documents
Rigorous V&V
  Ensures credible simulation of complex systems
  Reduces risk of negative training
V&V continues to evolve to address
  Advances in simulation technology
  Integration with agile software development and project management strategies
  Increasingly sparse real world referent data
  Adoption and integration with Digital Engineering paradigms
  Updates to relevant M&S Policies

## Slide 6: Presentation Outline
Definitions that establish the common lexicon
  Terms
  Setting boundaries by defining the intended use
Building a strong verification case
Building a strong validation referent
Building a strong validation case
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 7: Terms: Verification and Validation
Verification. The process of determining that a model or simulation, and its associated data, accurately represents the developer’s conceptual description and specifications. [DOD, 2009]
  Transformational accuracy [Balci, 2002]
    Transform specifications to code
  Software engineering quality
    Software engineering methods apply
Validation. Determining the degree to which a model or simulation, and its associated data, are an accurate representation of the real world from the perspective of the intended uses of the model. [DOD, 2009]
Comparing model results with experimental data [Velten, 2009]
  Representational accuracy [Balci, 2002]
    Recreate simuland with results
  Modeling quality
    Special validation methods needed

## Slide 8: Terms: Simuland and Referent
Simuland. The subject of a model or simulation.
  A real-world (or notional) system of interest
  Object, phenomenon, or process to be simulated
Referent. A codified body of knowledge about something being modeled or simulated.
  Quantitative and formal, e.g., differential equations for aircraft flight dynamics
  Qualitative and informal, e.g., pilot’s expectation of buffet before stall
Referent: “The best of most appropriate codified body of information available that describes characteristics and behavior of the reality represented in the simulation from the perspective of validation assessment for the intended uses of the simulation.”

## Slide 9: Terms: Accreditation, Acceptance, and Certification
Accreditation The official certification that a model, simulation, or distributed simulation is acceptable for use for a specific purpose [DOD, 2009].
  Evidentiary requirements and acceptance / acceptability criteria are set by the accreditation authority
  Accreditation authority is granted by instruction
  Accreditation agents (usually independent of the developers and the accreditation authority organization) can be used to coordinate activities, provide assessment and make recommendations
Acceptance is a concept applied by organization if formal accreditation is not specified.
  Certification and / or accreditation is the outcome from an acceptance process
  Establishing acceptance / acceptability criteria is fundamental to the process
Model developer / Proponent may provide accreditation recommendation letters that a particular model or simulation provides a credible representation compared to the test objectives and intended use.
  Methods, techniques, and criteria are at the discretion of the developer

## Slide 10: Terms: Intended Use
Intended use. The purpose for or function of a model; what the model will be used for; the problem to be addressed by the model. [DOD, 2012]
Characteristics [Piersall, 2014]
  “Not a capability, solution, or implementation”
  Expressed from the perspective of the user
  Should be formally specified
“Modeling and simulation is always goal-driven, … , we should know the purpose of our potential model before we sit down to create it.” [Cellier, 1991]
“Any attempt to suppress the role of the intentions of the investigator, B, leads to circular definitions or to ambiguities about essential features ...” [Minsky, 1965]

## Slide 11: Intended Use Categories
Modeling and Simulation Intended Use Descriptions [Piersall, 2015]
  Concept Evaluation
  Developmental Engineering
  Testing and Verification
  Assessment
  Training
  Operational Support

## Slide 12: The VV&A Proces Overlaid onto the M&S Use Process
Accreditation / Certification Process
PROBLEM SOLVING PROCESS
Establish
Objectives
Define Problem
Accept & Record
Solution
Analyze Results
Non-M&S Methods
M&S USE PROCESS
Select
Approaches
Apply
Results
Repository
Verification and Validation Process
M&s Development/Preparation Process
Execute and Prepare Results
yes
no
Make Accreditation Decision
Define
M&S Rqmts
Plan
Approach
M&S Method
Prepare M&S for Use
Define Intended Use

## Slide 13: Level of Interoperability
interoperability: The ability of a member application to provide services to and/or accept services from other member applications and to use the services so exchanged to enable the member applications to operate effectively together.
technical interoperability: A state of a distributed simulation characterized by implementation of a communication protocol for exchanging data between member applications (adapted from [Tolk, 2006])
syntactic interoperability: A state of a distributed simulation characterized by implementation of a common structure to exchange information (adapted from [Tolk, 2006])
semantic interoperability: A state of a distributed simulation characterized by use of a common information exchange model
logical interoperability: A state of a distributed simulation characterized by understanding of the member applications of the context within which information is being exchanged (adapted from [Tolk, 2006])
substantive interoperability: A state of a distributed simulation characterized by understanding of the state changes in the assumptions and constraints of each member application and the ability of the member applications to react to those changes (adapted from [Tolk, 2006])

## Slide 14: Setting V&V Boundaries on Intended Uses
Empirical Data |  |  |  | 
Simulation Data |  |  |  | 
Theoretical Data |  |  |  | 
SME Knowledge |  |  |  | 
Referent Quality
V&V Rigor
Subject Matter Expert (SME) Recommendation
Verification
Certification
Validation
Developmental Engineering
Concept Evaluation
Operational Support
Assessment
Testing and Verification
Training
Intended Uses

## Slide 15: Verification and Validation Composite Model
Plan the V&V Effort
  Develop the V&V Approach
  Identify the V&V Resources
  Build the V&V Schedule
  Estimate the V&V Costs
  Prepare the V&V Plan
  Execute & Evolve the V&V Plan
Apply Relevant Historical Information
  Collect & Analyze Developer Accounts of Simulation Capabilities & Limitations
  Collect & Analyze the V&V and Testing Histories
  Collect & Analyze Prior Use History
  Integrate & Employ the Historical Evidence
Verify & Validate the Simulation Conceptual Model
  Verify the Simulation Conceptual Model
  Validate the Simulation Conceptual Model
  Verify & Validate Available Scenarios
  Integrate & Employ the Conceptual Model V&V Evidence
Perform Supplemental Verification
  Determine the Scope of Supplemental Verification Needed
  Verify the Simulation Design Products
  Verify the Simulation Object Code
  Verify the Simulation Executable
  Verify the Development Products against the Simulation Conceptual Model
  Verify the Development Products for Standards Compliance
Apply the Verification Products to Validation
  Infer the Simulation Capabilities from the Verification Products
  Infer the Simulation Limitations from the Verification Products
  Infer the Information Gaps from the Verification Products
  Employ the Verification Evidence
Verify & Validate the Data & Knowledge Sets
  Identify the Data & Knowledge Sources & Their Pedigrees
  Verify the Data & Knowledge Sets
  Validate Data & Knowledge Sets Where Needed
  Integrate & Employ the Data & Knowledge V&V Evidence
Validate Simulation Results
  Leverage Developer Test Results for Results Validation
  Derive Results Validation Test Scenarios
  Plan for Results Validation
  Collect Simulation Output for Results Validation
  Integrate & Employ the Validation Testing Results
Integrate the V&V Evidence
  Integrate the V&V Evidence
  Prepare the V&V Report
  Support Any Archival of the V&V Products
[NATO, 2012]

## Slide 16: Tailoring the VV&A Processes
Every Verification, Validation, and Accreditation (VV&A) problem differs in:
  Uses of simulations
    M&S requirements
    Tolerable use risks
  Resource constraints
    Available information
    People & skills
    Funding
    Time
  When VV&A starts in the simulation life cycle
No single set of VV&A activities & tasks can efficiently accommodate all of these differences.
Use Risks
VV&A Resources
Time Available to Perform VV&A
Personnel Required to Perform VV&A
Information Available to Support VV&A
Use Risk from Unknown Simulation Uncertainties
Use Risk from Uncertainties in V&V Results
Consequences of Any Simulation Limitations on the Intended Use

## Slide 17: Presentation Outline
Definitions that establish the common lexicon
Building a strong verification case
  Defining M&S Requirements
  Leveraging existing verification data
  Leveraging developer testing
  Supplemental V&V testing
Building a strong validation referent
Building a strong validation case
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 18: M&S Requirements Framework
M&S
  Chosen as part of the solution to a program question
  Represents real-world entities, effects and phenomena
Specific Intended Use (SIU)
  Describe decisions and information used for that decision that will be provided by the M&S
  Are narratives written from the perspective of the user
High Level Requirements (HLRs)
  Capability statements derived from SIUs
  Intended as executive summary of M&S scope
  Describe general categories of the simulation environment
  Describe logical groupings of disciplinary factors and effects
Detail Level Requirements (DLRs)
  Mandatory provisions written as obligatory “shall” statements
  Derived from HLRs
  Trace directly between user needs and what developer provides
  Ultimate guidance to design, development, and testing activities
  Address representational and operational needs

## Slide 19: Defining M&S Requirements
Assessment Driven M&S Needs
Stakeholder Intended Uses
Assessment Metrics
Blue Force, Red Force,
Communications, Natural Environment
Scenarios
Analysis and Assessment
Assessment Plan
Simulation Conceptual Model
Data for Assessment
M&S Execution
M&S Integration and V&V Testing
M&S Design and Development
M&S System Requirements Document

## Slide 20: Simulation Conceptual Modeling
Model Based Systems Engineering (MBSE) offers a rich framework for capturing conceptual model artifacts and information; e.g. Use Case, Sequence and Block Definition diagrams

## Slide 21: Leveraging Existing Simulation Verification Data
Downloaded from [NASA, 2023] on 6/21/23
Necessitated by widespread adoption of agile software development practices
Supported by rigorous configuration management of M&S requirements, developmental M&S products and strict version control
Enabled by the use of integrated requirements management and testing tools
  Evolving requirements
  Requirements attributes enabling dynamic status tracking
  Synchronous requirements and verification test development
  Automated traceability views
Sample Documentation

## Slide 22: Leveraging Developer Testing
Federation / distributed simulation development often undergoes levels of testing
  Unit
  Pairwise
  Multi-way
  Integrated
  At scale
Simulation environment differences
Testing within federated environments
  Substitutes for interactions with M&S participants
Testing scope and negative testing

## Slide 23: Supplemental Simulation Verification Testing
Supplemental is not Regression
Regression implies an exact duplication of previously executed testing
Supplemental may be
  Additional test at the same level
  Test case replication at a different levels
  Comparison between levels
Benefits from / for digital engineering

## Slide 24: Presentation Outline
Definitions that establish the common lexicon
Building a strong verification case
Building a strong validation referent
  Developing the referent as the basis for validation comparison
  Challenges and obstacles to developing the referent
  Best practices and obstacle mitigation
  Examples
Building a strong validation case
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 25: Essential Steps for Validating Models and Simulations
Retrieved from MSE VV&A RPG content
Downloaded from [NASA, 2023] on 6/21/23
Sample Documentation

## Slide 26: The Ideal Referent
Covers the operational/domain space of interest as bounded by the intended use [Gilmore, 2016]
  Provides data on the aspects of the operational envelope/behavior space that will be covered by the M&S
  Addresses variations in factors affecting performance/behavior w. r. t. response variables of interest
  Supports interpolation between known data points vice extrapolation
Is drawn from observations of the simuland [RPG, 2011]
  Under controlled circumstances such as tests and experiments
  Under natural or operational circumstances
Is drawn from authoritative data
  Test data adjudicated by Data Authentication Group review to address measurement errors, incomplete data, etc. [ATEC, 2004]
Identifies any areas of known uncertainty

## Slide 27: Referent Sources
Empirical data; observations of the simuland, collected either under controlled circumstances, e.g., tests or experiments, or in the field
Theoretical data; calculated using equations or algorithms that describe simuland characteristics, behaviors, and relationships; equations known or assumed to be correct
Simulation data; results generated by simulations; models known or assumed to be valid
Subject Matter Expert knowledge
Combinations of these

## Slide 28: Referent Challenges and Obstacles
Ill defined intended use
  Lack of definition of the model/simulation’s coverage of the domain space
  Lack of test scenarios that will align test and simulation data
Inconsistencies between referent and simulation data
  Metrics of interest
  Factors that affect performance
Limited/no referent data available
  Complexity of system/behaviors represented imposes limitations (e.g., resource, economic) on the development of quantitative referent data
  Domain of Interest does not support quantitative referent development (e.g., Department of Energy, NASA)
Economic limitations

## Slide 29: Referent Best Practices
Start early – validation referents take time to develop
  Need to identify scope of information needed
  Need to coordinate with others (e.g., testers, SMEs) to produce referent data
  Need to budget for referent development
Ensure accreditation authority concurrence
“Grow” referent information over time
  Leverage all sources of test data (e.g., ground test, Hardware in the Loop (HWIL), live fire)
Maximize extent of referent coverage of the operational/behavioral space as defined by the intended use
Define areas of uncertainty
  Limitations of M&S coverage
  Limitations of referent data

## Slide 30: AIM9X: Simulation Enhanced Operational Test
Limited test shots, with maximum operational envelope coverage to support validation referent development
Adopted Model-Test-Model [Mansager, 1994] paradigm to continually assess validation referent development
Applied a statistical methodology (Fisher Test) to validate the simulation
Validated M&S used to satisfy all system performance requirements [IDA, 2001]
Significantly decreased the number of test shots (DT and OT) needed [DOT&E, 2000]
AIM9X awarded NTSA 2001 M&S Industry Award
AIM9X Missile

## Slide 31: Developing a Rigorous SME Referent
Validation focus was a campaign-level simulation that modeled multi-sided joint theater warfare
No real world referent available for comparison, thus reliant on SME assessment
Increase SME sample size (from one to multiple)
Apply best practice in survey research to develop questionnaire
Statistical aggregation of survey results enables identification of common trends as well as the meaningful assignment of uncertainties to the referent characteristics
Knowledge of referent uncertainty is necessary for evaluating the risk of using a simulation
Simulation Results
Simulation Referent
Validation Results
Confidences
Accuracies
Student’s T-test
Differencing

## Slide 32: Challenges Associated with Rigorous Validation
Referent
  Coverage
  Availability
Selection of Validation Method
  Driven by available Referent Data
  Characteristics of Validation Metric (e.g., point value, time series, multimodal)
Viability of Validation Method
  Measuring the performance of the validation methods used to assess model accuracy
Understanding Uncertainty

## Slide 33: Presentation Outline
Definitions that establish the common lexicon
Building a strong verification case
Building a strong validation referent
Building a strong validation case
  Defining validation metrics
  Selecting and applying the appropriate method
  Quantifying validation uncertainty
  Examples
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 34: Motivation
Decision makers are demanding that previous “informal” methods of validation be supplemented or replace with quantitative, defensible, rigorous methods
All M&S, when used to support operational tests and evaluations, should not be accredited until a rigorous comparison of live data to the model's predictions is done … and those predictions are found to have replicated live results with sufficient accuracy for the intended evaluation in the intended domain [Gilmore, 2016]
I expect the validation of M&S to include the same rigorous statistical and analytical principles that have become standard practice when designing live tests. [Gilmore, 2016]

## Slide 35: Validation Metrics
Coming from Accreditation Authority
What if this doesn’t exist
  User: Final Measures/Metrics
    Not measurable
    Many times a result of post-processing
  Collaboration with the Test and Evaluation (T&E) community
  Basis of Comparison
    Accessible measures that combine to create metrics
    Insight into performance for the sake of comparison
    Relatable to the referent

## Slide 36: Deriving Measures and Acceptability Criteria

## Slide 37: V&V Methods Considerations
Method
Model
Referent
Skills
Resources
Certain methods apply best to specific types of model
Certain methods require specific types or amounts of referent data
Some methods require more resources than others
Some methods require specific skills to apply
01010100010100101
10010101000100101
10101011101010111
10110010100101000
10010101101010101
h(t) = –4.9t2 + vt + s
Problems can arise if the considerations conflict

## Slide 38: Referent to Validation Method Mapping
Paired observations
Sources of
referent information
Forms of referent information
Applicable rigorous
validation methods
Empirical data
Single observation or few observations
Confidence intervals
Multivariate confidence intervals
Theoretical data
Hypothesis tests for means, variances, proportions, and distributions
Simulation data
Regression analysis
Subject Matter
Expert knowledge
Expectations and
experience
Structured face validation
Turing test
Many observations

## Slide 39: Confidence Intervals
Validation concept and interpretation
  Useful when only one (or few) simuland observations available
  Determine if simuland observation consistent with model results
  Calculate confidence interval for model response variable
  If confidence interval contains observed simuland value(s), then model considered valid for that response variable
Comments
  Interval calculated from simulations is for model, not simuland
  Population is all possible simulations with the model, sample is the simulations actually executed
  No statistical justification or refutation for validation interpretation

## Slide 40: Confidence Interval Example
Comparison of simuland value with model mean
Simuland
  Seaport of Trabzon Turkey
  Quays for berthing, unloading, loading ships
  Three types of ships: G1, G2, G3
Model
  Discrete event simulation
  Represents ships, cargos, quays, warehouses, cranes

## Slide 41: Confidence Interval Calculations
Mean processed (count) for each ship type and total
Sample size (number of model runs) n = 45
Confidence level c = 0.95 (95%)
Distribution: Student t
Degrees of freedom d.f. = n – 1 = 44
Critical value tc = 2.015
Ship Type | Simuland count 0 | Model |  | Confidence interval |  | Within Interval?
 |  | Mean x̅ | Std dev s | L | U | 
G1 | 109 | 111.14 | 14.45 | 106.8 | 115.5 | Yes
G2 | 169 | 174.42 | 16.07 | 169.6 | 179.2 | No
G3 | 19 | 17.28 | 5.26 | 15.7 | 18.8 | No
All Types | 297 | 303.68 | 35.89 | 292.9 | 314.5 | Yes
2 of 4 Intervals Contain Simuland Value
Notes: Confidence interval procedure
  Select model response variable x to use for validation
  Select number of model executions, i.e., sample size n
  Execute model n times, producing sample x1, x2, … xn
  Calculate sample mean x̅ and sample std dev s
  Select distribution normal z or Student t
  Select confidence level c
  Calculate confidence interval [L, U]
  If known simuland value y within [L, U], i.e., L ≤ y ≤ U, declare model valid (or not invalid) for x

## Slide 42: Hypothesis Testing
Validation concept and interpretation
  Useful when multiple simuland observations available
  Test whether simuland observations consistent with model results
  Perform hypothesis test comparing means, variances, and/or distributions of simuland and model for response variable
  If hypothesis test does not reject assumption of validity, then model considered valid for that response variable
Comments
  Simuland population is all possible observations, sample is the observations actually obtained
  Model population is all possible simulations with the model, sample is the simulations actually executed
  Conventional assumption (null hypothesis) is that the parameters being tested are equal, i.e., model is valid

## Slide 43: Hypothesis Test Example
  Test statistic F calculated from simulation results
  P-value: probability of test statistic value, assuming H0 true
  Test: P-value < α → reject H0
  Interpretation: Do not reject H0 → results match, i.e., model valid for x, y variances
F distribution P-value in Excel =FDIST(F,d.f.N,d.f.D)
} Model
} Live
s1 | 535.08 | 85.75
s2 | 558.52 | 90.35
F | 1.0895 | 1.1102
d.f.N | 5 | 5
d.f.D | 799 | 799
P-value | 0.3646 | 0.3534
Source | x err s | y err s | n
Model | 535.08 | 85.75 | 800
Live | 558.52 | 90.35 | 6
Notes: F-test: Hypothesis test for equality of variances
Obtain samples, calculate sample statistics
Set notation so that
Select level of significance α; often α = 0.05
Formulate hypotheses H0 and H1
Calculate test statistic F using formula
Given F, find P-value (table or software)
If P-value ≤ α, then reject H0, else accept H0

## Slide 44: Point Value Referent Data vs Time Series
Point Value: A single sample metric from a referent data set
  Examples:
    Miss distance
    Time of flight
    Percent of time in a specific mode
Time Series: A time series of single sample metrics from a referent data set
  Examples:
    Position
    Orientation
Regardless of time series or point value, both are considered a single sample of the underlying distribution, since the flight test represents only one sample.

## Slide 45: Time Series Example: Red Force Casualties
Red casualties at time 50 only
Model  simuland
 Model valid?
1 “trial” of simuland, e.g., data from actual battle
15 trials (executions) of a model of the same battle
Red casualties at times 0–50
Model mostly  simuland
 Model not valid?
[Petty, 2021]

## Slide 46: Time Series Validation: Advanced Methods
ε = time step value error tolerance
OOB = time steps out of bounds
Method | Simuland Trials | Model Trials | Interval Bounds | OOB Limit | Examples & Sources
A | 1 | 1 | Simuland ± SME ε | SME | [Engel, 1954] [Petty, 2010]
B | 1 | Multiple | Model 95% c. i. | SME | [Herington, 2002] [Champagne, 2007]
C | Multiple | Multiple | Simuland 95% c. i. Model 95% c. i. |  | [Law, 2015]
[Petty, 2021]

## Slide 47: Time Series Method A
SME: ε = 5, Out of Bounds (OOB) limit = 10% = 5 time steps
Simuland: 1 trial with  SME ε interval per time step
Model: 1 trial
OOB time steps > OOB not valid
[Petty, 2021]

## Slide 48: Time Series Method B
SME: OOB limit = 10% = 5 time steps
Simuland: 1 trial
Model: 15 trials with 95% confidence interval per time step
OOB time steps > OOB limit  model not valid
[Petty, 2021]

## Slide 49: Time Series Method C
SME: OOB limit = 10% = 5 time steps
Simuland: 15 trials with 95% confidence interval per time step
Model: 15 trials with 95% confidence interval per time step
OOB time steps > OOB limit  model not valid
[Petty, 2021]

## Slide 50: Advanced Validation Methods
Spectral analysis [Fishman, 1967] [Naylor, 1971] [McNickle, 2004]
Parametric time series model [Hsu, 1977]
Standardized time series [Schruben, 1983] [Chen, 1987] [Goldsman, 1990]
Regression analysis [Kleijnen, 1998]
Bootstrapping [Kleijnen, 2000] [Kleijnen, 2001]
Granger causality [Granger, 1969]

## Slide 51: Presentation Outline
Definitions that establish the common lexicon
Building a strong verification case
Building a strong validation referent
Building a strong validation case
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 52: Templates and Tools
Basis: MIL-STD-3022
Building the template easily facilitated within many reporting tools
Available as functions in “enterprise” level tools (e.g. IBM DNG)
Opportunities for simplification and efficiency
  Base reports with update addenda
  Test reporting as Checklists
  Linking test automation to reporting and requirements management tools
Advanced visualization methods
Adopting Digital Engineering
  Improved integrity
  Increased efficiency
  Timeliness required to support Agile development
  Creating effective collaboration infrastructure

## Slide 53: New Ways of Looking at Data
Modern Tools and Collaboration Platforms
Enable Automated V&V Workflows

## Slide 54: Standards, Policy, and Guidance
DoD VV&A Policy: DoDI 5000.61 “DoD M&S VV&A”
DoD VV&A Guidance: The VV&A Recommended Practices Guide (RPG)
IEEE 1730.2 “VV&A Overlay to the Distributed Simulation Engineering and Execution Process”
MIL-STD-3022 “Documentation of VV&A for M&S”
Derived policy, standards and guidance within the Services
Generic Methodology for Verification and Validation (GM-VV) Volumes 1(SISO-GUIDE-001.1) Introduction and Overview, 2) (SISO-GUIDE-001.2 Implementation Guide) and 3 (SISO-REF-2013 Reference Manual) / NATO MSG 073
Risk Based Assessment / NATO MSG 054
M&S Use Risk Methodology / NATO MSG 139
V&V Composite Model, Accreditation Composite Model / NATO MSG 019 and 054
Applying the Levels of Conceptual Interoperability Model in Support of Integratability, Interoperability, and Composability for System-of-Systems Engineering, Andreas TOLK, Saikou Y. DIALLO, Charles D. TURNITSA

## Slide 55: Presentation Outline
Definitions that establish the common lexicon
Building a strong verification case
Building a strong validation referent
Building a strong validation case
Standards, Guidance, Templates, and Tools
Conclusions

## Slide 56: Conclusions and Recommendations
Verification activities provide a necessary foundation for rigorous validation
Quality and quantity of referent effects validation rigor
  Rigorous validation is possible, but it depends on an effective referent, i.e., sufficient data, well aligned with the model’s intended use
  Acquiring an effective referent should be started early in the simulation life cycle
  Given the best possible referent, a range of quantitative validation methods are available
Application of statistical validation methods
  Most quantitative (statistical) validation methods make specific assumptions
  If a statistical method is used when the assumptions are not met, its results are meaningless and potentially misleading
Validating time series data
  Validating a model using output at a single time step can be misleading
  Methods exist to validate models using time series output
    Confidence interval methods; relatively simple
    Advanced methods; mathematically complex

## Slide 57: Contact Information
Simone M. Youngblood
  The Johns Hopkins University Applied Physics Laboratory
  240-228-7958
  Simone.Youngblood@jhuapl.edu
Kathy M. Ruben
  The Johns Hopkins University Applied Physics Laboratory
  240-228-9148
  Katherine.Ruben@jhuapl.edu

## Slide 58: References and bibliography (1 of 4)
[ATEC, 2004] Army Test and Evaluation Command (ATEC) Pamphlet 73-1, System Test and Evaluation Procedures, April 19 2004.
[Balci, 1998] O. Balci, “Verification, Validation, and Testing”, in J. Banks (Editor), Handbook of Simulation: Principles, Methodology, Advances, Applications, and Practice, John Wiley & Sons, New York NY, 1998, pp. 335-393.
[Balci, 2002] O. Balci, R. E. Nance, J. D. Arthur and W. F. Ormsby, “Expanding Our Horizons in Verification, Validation, and Accreditation Research and Practice”, Proceedings of the 2002 Winter Simulation Conference, San Diego CA, December 8-11 2002, pp. 653-663.
[Brase, 2015] C. H. Brase and C. P. Brase, Understandable Statistics: Concepts and Methods, Eleventh Edition, Cengage Learning, Stamford CT, 2015.
[Cellier, 1991] F. E. Cellier, Continuous System Modeling, Springer-Verlag, New York NY, 1991.
[Chen, 1987] B. Chen and R.G. Sargent, “Using Standardized Time Series to Estimate the Difference between Two Stationary Stochastic Processes,” Operations Research, Vol. 35, 1987, pp. 428-436.
[Champagne, 2007] L. E. Champagne and R. R. Hill, “Agent-Model Validation Based on Historical Data”, Proceedings of the 2007 Winter Simulation Conference, Washington DC, December 9-12 2007, pp. 1223-1231.
[DOD, 2009] Department of Defense, Instruction 5000.61, M&S VV&A, 2009.
[DOD, 2011] The DoD Verification, Validation, and Accreditation Recommended Practices Guide Website, January 2011,
[DOD, 2012] Department of Defense Standard Practice, MIL-STD-3022 with Change 1, Documentation of Verification, Validation, and Accreditation (VV&A) for Models and Simulations, April 5 2012.
[DOT&E, 2000] DOT&E Report, AIM-9X Sidewinder Air-to-Air Missile, 2000.

## Slide 59: References and bibliography (2 of 4)
[Engel, 1954] J. H. Engel, “A Verification of Lanchester’s Law”, Journal of the Operations Research Society of America, Vol. 2, No. 2, May 1954, pp. 163-171.
[Fischer, 2001] K. Fischer, “AIM-9X…Surpassing the M&S Challenge,” Unpublished presentation, 2001.
[Fishman, 1967] G. S. Fishman and P. J. Kiviat, “The Analysis of Simulation-Generated Time Series”, Management Science, Vol. 13, 1967, pp. 525-557.
[Gilmore, 2016] Director Operational Test and Evaluation Memorandum, Guidance on the Validation of Models and Simulation used in Operational Test and Live Fire Assessments, 14 March 2016.
[Goldsman, 1990] D. Goldsman and L. Schruben, “Confidence Interval Estimators Using Standardized Time Series”, Management Science, Vol. 36, No. 3, March 1990, pp. 393-397.
[Granger, 1969] C. W. J. Granger, “Investigating Causal Relations by Econometric Models and Cross-spectral Methods”, Econometrica, Vol. 37, No. 3, pp. 424-438.
[Herington, 2002] J. Herington, A. Lane, N. Corrigan, and J. A. Golightly, “Representation of Historical Events in a Military Campaign Simulation Model”, Proceedings of the 2002 Winter Simulation Conference, San Diego CA, December 8-11 2002, pp. 859-863.
[IDA, 2001] AIM-9X: A Modeling and Simulation Success Story, IDA Research Summaries, Vol. 8, Number 1, Summer/Fall 2001, pp. 8-12.
[Kleijnen, 1998] J. P. C. Kleijnen, B. Bettonvil, and W. Van Groenendaal, “Validation of Trace-Driven Simulation Models: A Novel Regression Test”, Management Science, Vol. 44, 1998, pp. 812-819.
[Kleijnen, 2000] J. P. C. Kleijnen, R.C.H. Cheng, and B. Bettonvil, “Validation of Trace-Driven Simulation Models: More on Bootstrap Techniques”, Proceedings of the 2000 Winter Simulation Conference, Orlando FL, December 10-13 2000, pp. 882-892.
[Kleijnen, 2001] J. P. C. Kleijnen, R.C.H. Cheng, and B. Bettonvil, “Validation of Trace-Driven Simulation Models: Bootstrap Tests”, Management Science, Vol. 47, 2001, pp.1533-1538.

## Slide 60: References and bibliography (3 of 4)
[Law, 2015] A. M. Law, Simulation Modeling and Analysis, Fifth Edition, McGraw-Hill Education, New York NY, 2015.
[McNickle, 2004] D. McNickle, G. C. Ewing, and K. Pawlikowski, “Refining Spectral Analysis for Confidence Interval Estimation in Sequential Simulation”, Proceedings of the 16th European Simulation Symposium, Budapest Hungary, October 17-20 2004, pp. 99-103.
[Mansager, 1994] B. Mansager, Model Test Model, Naval Postgraduate School Technical Report NPS-MS-94-007.
[Minsky, 1965] M. L. Minsky, Matter, Mind, and Models, Artificial Intelligence Memo No. 77, Massachusetts Institute of Technology, March 1965, Online at http://dspace.mit.edu/bitstream/handle/1721.1/6119/AIM-077.pdf ?sequence=2, Accessed, July 19 2015.
[NASA, 2023] Requirements Verification Matrix, downloaded from https://www.nasa.gov/sites/default/files/thumbnails/image/seh_app-d_table_d1.jpg on 6/21/23.
[NATO, 2012] NATO RTO Technical Report “Risk-Based Tailoring of the Verification, Validation, and Accreditation/Acceptance Processes”, TR-MSG-054, February 2012
[Naylor, 1971] T. H. Naylor, Computer Simulation Experiments with Models of Economic Systems, John Wiley & Sons, New York NY, 1971.
[Petty, 2010] M. D. Petty, “Verification, Validation, and Accreditation”, in J. A. Sokolowski and C. M. Banks (Editors), Modeling and Simulation Fundamentals: Theoretical Underpinnings and Practical Domains, John Wiley & Sons, Hoboken NJ, 2010, pp. 325-372.
[Petty, 2012] M. D. Petty, “Calculating and Using Confidence Intervals for Model Validation”, Proceedings of the Fall 2012 Simulation Interoperability Workshop, Orlando FL, September 10-14 2012, pp. 37-45.

## Slide 61: References and bibliography (4 of 4)
[Petty, 2013] M. D. Petty, “Advanced Topics in Calculating and Using Confidence Intervals for Model Validation”, Proceedings of the Spring 2013 Simulation Interoperability Workshop, San Diego CA, April 8-10 2013.
[Petty, 2021] M. D. Petty and S. M. Youngblood, “Addressing the Challenges of Rigorous Validation” presented at the 2021 I/ITSEC, November 2021.
[Piersall, 2014] C. H. Piersall and F. E. Grange, “The Necessity of Intended Use Specification for Successful Modeling and Simulation of System-of-Systems”, CrossTalk, September/October 2014, pp. 20-24.
[Piersall, 2015] W. Seay, C. H. Piersall, D. Lucia, and K. Englander, MDA report 20-MDA-10542, March 2015, (approved for public release 30 Jul 20)
[RPG, 2011] DoD VV&A Recommended Practices Guide, RPG Validation Referent Special Topic Paper, https://www.cto.mil/sea/vva, January 2011.
[Schruben, 1983] L. Schruben, “Confidence Interval Estimation Using Standardized Time Series”, Operations Research, Vol. 31, No. 6, November-December 1983, pp. 1090-1108.
[Tolk, 2006] W. G. Wang, A. Tolk and W. P. Wang, "The levels of conceptual interoperability model: Applying systems engineering principles to M&S," in Proceedings of the 2009 Spring Simulation Multiconference, San Diego, March 22-27, 2009.
[Velten, 2009] K. Velten, Mathematical Modeling and Simulation, WILEY-VCH, Weinheim Germany, 2009.