## Slide 1
Optical See-Through as a Cybersickness Mitigation Strategy in Extended Reality Helicopter Flight Simulation
Boris Englebert (presenter)
Roemer Bakker
Tanja Bos
Tobias Tanis

## Slide 2: Why Extended Reality in Flight Simulation?
‘Conventional’ helicopter flight simulation
Extended Reality (XR) helicopter flight simulation
[2]
+
Cost-effective
Flexible Usage
Cybersickness
+
-

## Slide 3: Extended Reality Flight Simulation and Cybersickness
Motion sickness triggered by virtual environments - cybersickness
Higher incidence of motion sickness in XR flight simulation compared to conventional flight simulation
Visual sensory inputs from virtual environment do not correspond with the motion that is felt
Causes and exacerbates cybersickness
Negatively impacts training effectiveness
Occurrence of visual-vestibular conflict
Prevents adoption of VR training environments
Mitigating visual-vestibular conflict to alleviate feelings of cybersickness
In the virtual environment, provide a visual reference to the actual environment that corresponds with the motion that is felt
Cybersickness
-
XR – umbrella term spanning concepts like Virtual Reality (VR) and Mixed Reality (MR)

## Slide 4: Previous Cybersickness Mitigation in Flight Simulation Research
Blend the virtual environment with the actual environment – Mixed Reality (MR)
Virtual Environment
Actual Environment
Mixed Reality
Without physical motion – MR reduces cybersickness
-
MR breaks immersion, and negatively affects pilot performance and training effectiveness
In the virtual environment, provide a visual reference to the actual environment that corresponds with the motion that is felt
+

## Slide 5
Optical See-Through Mixed Reality for Cybersickness Mitigation
In the virtual environment, provide a visual reference to the actual environment that corresponds with the motion that is felt
Virtual (Outside) Environment
Real Cockpit Environment
OST MR
Combine a purely virtual outside environment with an optical see-through view of the real cockpit environment – Optical See-Through Mixed Reality (MR OST)
How does Optical See-Through Mixed Reality (OST MR) affect the development of cybersickness compared to Virtual Reality (VR), in helicopter flight simulation?

## Slide 6: Experiment Setup – Flight Simulation Environment
Human-in-the-loop experiment - participants performing predetermined helicopter flying tasks
Simulation Setup - Hardware
Physical cockpit mock-up
Control loaded flight controls
AS532 ‘Cougar’ helicopter flight model
Half-mirror and combiner-based OST HMD
‘Open’ downview
Virtual Environment and Flying Task
Visualization of flight simulation environment
Fixed track consisting of ADS-33E-PRF Mission Task Elements (MTEs)
Hover
Depart-Abort
Slalom
Sloped landing
Lateral sidestep
Vertical remask
Hovering turn
Pirouette
Example of Pirouette MTE in virtual environment

## Slide 7: Experiment Setup – Experiment Conditions
In the virtual environment, provide a visual reference to the actual environment that corresponds with the motion that is felt
Regular VR (baseline)
Virtual Cockpit + Virtual Environment
OST MR
Physical Cockpit + Virtual Environment

## Slide 8: Experiment Setup – Participants and Dependent Measures
Five pilots completed the experiment, all of whom held an active MPL(H) or CPL(H)
Subjective cybersickness dependent measures
MIsery SCale (MISC) scores, evaluated after completion of each ADS-33 MTE
Between subjects experiment design
Simulator Sickness Questionnaire (SSQ) scores
Objective cybersickness dependent measures
Amount of head movement in VR versus OST MR for the pirouette MTE
Standard deviation of lateral and vertical head position
4-point Likert scale for severity of most common sickness symptoms

## Slide 9: Experiment Results – MIsery SCale (MISC) Scores
Minimal difference in progression of MISC scores between VR and OST MR conditions
Slightly higher median max. MISC score for VR than for OST MR – identical mean max. MISC score
Condition | Median Max. MISC
VR | 4 (μ = 3.20, σ = 1.17)
OST MR | 3 (μ = 3.20, σ = 1.17)
Progression of mean MISC scores
Maximum MISC scores statistics

## Slide 10: Experiment Results – Simulator Sickness Questionnaire Scores
 | SSQ Scores |  |  |  |  |  | 
Condition | P1 | P2 | P3 | P4 | P5 | μ | σ
VR | 29.9 | 44.9 | 67.3 | 7.5 | 44.9 | 38.9 | 19.7
OST MR | 15.0 | 44.9 | 67.0 | 18.7 | 74.8 | 44.1 | 24.4
Individual differences for sickness severity
Higher sickness scores in VR than OST MR: P1
Higher sickness scores in OST MR than VR: P4, P5
Slightly higher mean SSQ score in OST MR than VR

## Slide 11: Experiment Results – Head Movement
Lateral head movement
Vertical head movement
Statistically significantly more lateral and vertical head motion in VR than in OST MR
No observable differences for the MISC scores between conditions after pirouette MTE completion
High within-pair correlation (r > 0.8), implying statistical power despite small sample size
No correlation between the MISC scores and lateral/vertical head motion

## Slide 12: Conclusions and Future Research
How does Optical See-Through Mixed Reality (OST MR) affect the development of cybersickness compared to Virtual Reality (VR), in helicopter flight simulation?
No clear benefit of OST MR compared to VR for the mitigation of cybersickness
Minimal difference between OST MR and VR in MISC score progression, maximum MISC scores, and mean SSQ scores
Individual differences in reported SSQ scores imply that individual preferences may exist in terms of comfort in extended reality helicopter flight simulation
Despite observable differences in the amount of lateral and vertical head motion, no correlation with cybersickness severity
Pilots reported that the real world cockpit in OST MR did provide additional useful visual cues for the execution of the MTEs
Visual cues from OST MR real-world cockpit did not meaningfully contribute to visual motion perception

## Slide 13: Conclusions and Future Research
How does Optical See-Through Mixed Reality (OST MR) affect the development of cybersickness compared to Virtual Reality (VR), in helicopter flight simulation?
Pilots reported that the real world cockpit in OST MR did provide additional useful visual cues for the execution of the MTEs
Visual cues from OST MR real-world cockpit did not meaningfully contribute to visual motion perception
Future research efforts on cybersickness mitigation in extended reality helicopter flight simulation:
Focus on the area of the field-of-view that elicits the strongest motion perception
OST MR HMD vertical field-of-view: 72 degrees, vertical field-of-views larger than 50 degrees do not contribute significantly to motion perception
Minimize immersion deterioration as a result of visual cybersickness mitigation measures