## Slide 1
Mesh-as-a-Service:
Automated 3D Modeling Fast as L-AI-ghtning
Mathijs Henquet / Thomas Bellucci,
Royal NLR – Netherlands Aerospace Centre
Co-authors: Chihab Amghane, Jasper Steringa, Lodewijck Foorthuis

## Slide 2: Background: Training at RNLAF
Training complex helicopter operations by the Royal Netherlands Air Force (RNLAF)
RNLAF is developing a Multi-Ship-Multi Type (MSMT) Simulator center
Requires development of many virtual components with different fidelity levels / interactions.

## Slide 3: Background: Traditional 3D modelling
Requires detailed schematics
Requires 3D modeler or artist
Expensive!

## Slide 4: Request & Contents
NLR was asked to make a 3D model of the gas turbine auxiliary power unit (APU) for the CH-47F Chinook Rear Crew Trainer
How we made the APU model
  Pose detection with background segmentation
  3D reconstruction (Gaussian Splatting with Surface Alignment)
  Mesh extraction and texturing
Mesh-as-a-Service: Our pipeline as an asset generation service

## Slide 5: Challenge
The APU was recorded with a consumer grade photo camera
  Inconsistent background and lighting, no prior instruction
Many conventional methods require some form of depth sensing
  Laser (LIDAR), Stereovision or structured light scanning
Off-the-shelf RGB only (no depth data) methods did not work
  Struggle with required quality: glossy surfaces and small details
  Failed to reconstruct due to the inconsistent background

## Slide 6: Conventional Multi-view Reconstruction
Step 1: Pose detection
Step 2: 3D reconstruction
Image set
Images with accurate poses
3D representation
Step 1
Step 2

## Slide 7: Challenge: Background Segmentation
Challenge: The changing backgrounds in the APU dataset made pose detection impossible.
Solution: Semi-automatic background segmentation

## Slide 8: Background segmentation
Using CLIP model (OpenAI 2021) we can generate the point prompts automatically.
“Airplane”
Using Segment Anything Model (Meta 2023) we can automatically segment based on point prompts

## Slide 9: Background Segmentation
Semi-automatic background segmentation of the dataset
Use only foreground to do pose detection, ignore features from the background

## Slide 10: 3D reconstruction
3D Gaussian Splatting (2023)
Represents the scene as a set of Gaussians
  Oriented blobs in space
  Angle dependent appearance
  Can represent glossy surfaces / specular highlights
Position, size and color of Gaussians are optimized using gradient descent

## Slide 11: 3D reconstruction
This works extremely well!

## Slide 12: Challange: Towards a Mesh
In order to extract a usable Mesh there are 2 challenges to overcome:
Despite great visual reconstruction, surfaces are generally rough
  Especially at homogeneous appearing surfaces
Objects of interest have to be separated from the background

## Slide 13: Surface Alignment
RGB Reference
Vanilla 3D Gaussian Splatting
With Surface Alignment
Surface Aligned Gaussians (SuGaR 2023)
Ensures Gaussians are locally aligned
Notes: The colors in these images display the normals, left is a close up

## Slide 14: 3D Segmentation
Hierarchical 3D Segmentation using GARField (2024)
Lifts 2D segmentation using SAM to 3 dimensions
Works by scale dependent clustering of scene primitives to imitate SAM masks

## Slide 15: 3D Segmentation
Coarse segmentation
Fine segmentation
Notes: Left pipistrel, right boeing planes
Top coarse scale, bottom fine scale

## Slide 16: Mesh Extraction & Texturing
Mesh extraction
  using Poisson reconstruction
  simplified using quadratic error metric to obtain a mesh with desired fidelity
Texturing
  optimized a texture using differentiable rendering pipeline

## Slide 17: Results
The APU for the RNLAF was successfully reconstructed
Left: results of the pipeline with NLR made datasets.
Ground truth
Textured mesh
Notes: Top: pipistrel, bottom: boeing airplane seats

## Slide 18: Discussion
Comparison to conventional 3D modelling methods
Notes: Comparison to alternatives

## Slide 19: Limitations
Image Dataset Quality can hinder reconstruction accuracy
  Can we use drones to automate capture of complex objects?
Reflective Surfaces cause problems for 3D reconstruction
  Semi-transparent surfaces can indicate reflective surfaces
Mesh Reconstruction loses detail from the Gaussian Splatting scene

## Slide 20: Question
How can we make 3D mesh reconstruction accessible?
Pose detection
Model training
3D Segmentation
Mesh extraction
Texturing
Mesh in simulator
Input images / Video
Background removal
Input images / Video
Mesh-as-a-Service
Mesh in simulator

## Slide 21: Concept of Operations
Should enable the use of this pipeline with an intuitive interface
Semi-automated with the ability of a human to intervene and correct
Further explored with 2 use cases

## Slide 22: Use case: Own-Ship
Objective: Create detailed 3D models of platforms (e.g., military vehicles, aircraft, naval vessels).
Process:
  Users capture images of platform parts without specialized training.
  Images processed by Mesh-as-a-Service to generate meshes with polygon budgets.
Key Feature: Hierarchical 3D segmentation for detailed subcomponent modeling.

## Slide 23: Use case: Own-Ship
Hierarchical Segmentation
  Break down platforms into subcomponents (e.g., cockpit parts).
  Produces assets with articulatable parts
  Assign material properties to parts
Tools & Interface
  Develop tools for picking the hierarchical subdivisions.
  User-friendly interface for review and adjustment.
Advantage: Flexibility and ease of adjustment for immersive training scenarios.

## Slide 24: Thank you
Questions?