## Slide 1
Uncertainty Aware Distributional Ensemble Reinforcement Learning for Flight Control
Micah Bryant, GA-ASI
Joseph D. Gleason, GA-ASI
Anastacia Macallister, GA-ASI

## Slide 2: We Want to Automate the Warfighter
Find
Fix
Track
Target
Engage
Assess
Track
Follow Track
Target
Weapons Targeting
Find
Hold CAP
There are various segments of an aircraft’s mission that need to be automated

## Slide 3: Use Controls or Reinforcement Learning
Actions
States, Rewards, Terminations
Reinforcement Learning
Control Theory
Traditional controls offer stability and reinforcement learning offers complexity
Controls uses model of system to create predictable and stable solutions
RL learns model of system and trains Neural Network to solve problem

## Slide 4: Overview of Reinforcement Learning
Observations
Environment
Rewards
Algorithm
Policy
Actions

## Slide 5: Benefits of Reinforcement Learning
RL shines in high dimensional, dynamic environments, that are not easily modellable
Vinyals, O., Babuschkin, I., Czarnecki, W.M. et al. Grandmaster level in StarCraft II using multi-agent reinforcement learning. Nature 575, 350–354 (2019).
OpenAI et al. “Dota 2 with Large Scale Deep Reinforcement Learning.” ArXiv abs/1912.06680 (2019): n. pag.

## Slide 6: Drawbacks of Reinforcement Learning
Uses NN instead of kinematic model
State
Action
Next State
Base optimization can lean toward high-risk high-reward inherently

## Slide 7: Methods to Solve Issues
Use ensemble of models to estimate uncertainty
Critics output distributions of Q values
20
10
5
11.67
±6.24

## Slide 8
PROPOSED METHOD

## Slide 9: Critic Modifications
Actor
Environment
Observation
Replay Buffer
Action
Temperature
Action Log Probability
Critic
Critic
Critic
Uncertainty
Training Tuples
Risk Distorted Q Value

## Slide 10: Critic Output
Critic
Critic
Critic
Critic is modified to output randomly sampled quantiles

## Slide 11: Risk Distortion
Apply a distortion to minimize for the lowest 70% of Q values to lower high-risk high reward strategies

## Slide 12: What is Uncertainty?
Epistemic Uncertainty
Aleatoric Uncertainty
Epistemic uncertainty is due to a lack of information about the environment, aleatoric uncertainty is the irreducible randomness in the environment

## Slide 13: Estimating Epistemic Uncertainty
Increasing variance in the predictions corresponds to increasing epistemic uncertainty
2000
40
-100
Std
±958.7
2
1.8
2.2
Std
±0.163
High Epistemic Uncertainty
Low Epistemic Uncertainty

## Slide 14: Estimating Aleatoric Uncertainty
Increasing standard deviation correlates to increasing aleatoric uncertainty
High Aleatoric Uncertainty
Low Aleatoric Uncertainty

## Slide 15: Usage of Uncertainty in Deployment
When deploying can turn off agent when it goes into regions of high uncertainty

## Slide 16
TESTING & RESULTS

## Slide 17: Scenario for Testing
6 nmi
20 nmi
25 nmi
Tested both SAC and DESAC against sensor with exponential detection probability

## Slide 18: Results in Path
DESAC takes much wider approach from the radar resulting in lower detection rate
Algorithm | Detection %
SAC | 24.7%
DESAC | 13.0%

## Slide 19: Visualization of Uncertainty
Epistemic (left) and Aleatoric (right) uncertainties visualized of the scenario

## Slide 20: Differences in Performance
 | SAC | DESAC
Min Reward | 2.665e-5 | 1.455e-5
Mean Reward | 76.286 | 88.082
Max Reward | 101.312 | 101.311
Reward Variance | 1907.600 | 1163.115
Detection Probability | 0.247 | 0.130
DESAC had significantly lower reward variance and detection probability than SAC

## Slide 21
CONCLUSION

## Slide 22: Conclusion
Have demonstrated increase in safety as well as applicable visualizations for deployable autonomy
Increase in safety over base SAC
Visualizations and metrics given to operators
Notes: Tie this back to the intro better