## Slide 1: A biosensor solution for real-time and prognostic health monitoring
Paulien Roos, PhD, Nathan Pickle, PhD, Joshua Hogue, PhD, Philip Whitley, PhD
CFD Research Corporation, Huntsville, AL
JoEllen Sefton, PhD
Auburn University, AL
Contact: paulien.roos@cfd-research.com

## Slide 2: Acknowledgements & Disclosure
This material is based upon work supported by the Army Futures Command (AFC) and Army Applications Lab (AAL) under Contract No. W911NF-22-C-0011.
Thank you to Andrea Taylor and Chad Hearing for their support of this work.
Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily represent the official views of the US Government, the Dept. of Defense, Army Futures Command (AFC), or the Army Applications Lab (AAL).

## Slide 3: Battlefield of the future
Free image from unsplash.com
Notes: Extensive suite of sensors available that can monitor physiological status.
Challenges in interpretation and presentation of data in a meaningful way to facilitate informed decision making

## Slide 4: Urgent Need
At-a-glance data interpretation
Good
Needs immediate attention
Needs attention soon

## Slide 5: Objectives
To develop a comprehensive warfighter health status assessment that:
Uses an open, extensible software architecture for fusing diverse biosensor data into a comprehensive warfighter health status assessment that runs on a mobile device using the Android Tactical Assault Kit (ATAK)
Is sensor agnostic with the prototype set to automatically scan for generic skin temperature, pulse oximeter, heart rate, and inertial measurement sensors.

## Slide 6: Our Solution
INTEGRATE data streams into the ATAK platform
FUSE data using novel equations for energy expenditure
VISUALIZE data intuitively for actionable insights
PREDICT future physiological status for mission planning

## Slide 7: Approach
Design
User informed
Platform
Android
ATAK integration
Software
Extensible
Modular
Visualization
At-a-glance insights
Rank-based
Sensors
Sensor agnostic
Direct connect to device

## Slide 8: Sensor Integration
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | lasdfk
Column1 | 10 | 10 | 10 | 10
Cross-platform, extensible sensor hub (Java)
Publisher/subscriber design
  Sensors, simulations, and analyses provide publish or subscribe to data as they become available
  Enables straightforward integration of new components
Tested on Windows and Android
Multiple Bluetooth sensors currently integrated
  Heart rate, pulse oximeter, skin temperature, inertial measurement unit (IMU)
  Easy to add additional sensors
  Network connectivity not required
Demonstrated real-time integration of sensor data with BioGears simulation on Android
PUBLISHER SUBSCRIBER
Heart rate
Pulse oximetry
IMU
OUTFLOW
SIMULATION
ANALYSIS
SENSORS
Visualization
Network
Physiology
Biomechanics
Thermal injury
Musculoskeletal
injury

## Slide 9: ATAK Integration
Android Team Awareness Kit
  ATAK-CIV, ATAK-GOV, ATAK-MIL
Situational awareness tool
  Team location
  Environmental information
  Communication
  Mission planning
  Photo/video
Extensible via plugins
“TAK is the core of a suite of georeferenced imagery and communications tools that allow for scaled operational planning, data sharing, visualized elevation data, and target management. With TAK, your team can get oriented quickly, make better informed decisions and quickly respond to threats.”
Aspen
JoshLG
Galaxy

## Slide 10: Prognostics – BioGears Physiology Engine
Improved physiology predictions
  Integrated body systems
  Improved accuracy
  Expanded prediction scenarios
Cross-compiled for Android
~3x real-time speed on Android (with ATAK app also running)
BioGears simulations regularly updated
  Environmental conditions and metabolic cost
Metabolic cost – Load Carriage Decision Aid (velocity and slope from ATAK)
Algorithms turn outputs BioGears into actionable insights
Cold stress
Heat stress
BIOGEARS
Fatigue
Metabolic Cost (W) - LCDA
Environmental conditions – ATAK
Humidity
Temperature
Visibility (not needed?)
Wind speed (not needed)
Atmospheric pressure
User specifications:
  Sex
  Height
  Weight
  Age
  VO2max
  Resting heart rate
  Resting skin temperature
  Load carried
  Clothing
ALGORITHMS
BioGears output:
Time
SpO2
Heart rate
Skin temperature
Core temperature
Breathing rate
Sweat rate
Actionable insights

## Slide 11: Actionable Insights
Musculoskeletal injury risk
  Tibial acceleration (overuse injury)
  Gait changes (acute injury)
Fatigue
  Fractional Heart Rate Ratio
  Gait changes
Traumatic brain injury
  Gait stability (nRMS)
Medical
  Cold stress (CSI)
  Heat stress (PSI)
  Medical triage (STAR)
Comparison to nearby warfighters to exclude terrain effects
Comparison to baseline data to identify sudden changes
Data flow and actionable insights

## Slide 12: Experimental Evaluation
Experimental study at Auburn Warrior Research Center:
  Challenging protocol:
    Heat chamber
    30% body weight backpack
    Inclined march
    Up to 40 mins or exhaustion
Outcomes:
  Verification of BioGears for ruck marching scenario
    Heart rate
    Respiratory rate
    Skin and estimated core temperature

## Slide 13: BioGears Simulations compared to Experimental Data
Subject specific models and simulations
BioGears vs Experimental data:
  Heart Rate:
    48% < 10% difference
    67% < 20% difference
  Respiratory rate:
    57% > 30% difference
    Possible initial conditions issues
  Skin temperature:
    100% < 10% difference
    58% < 5% difference
  Core temperature:
    100% < 5% difference
    Differences must be small (37-39oC is 5.4% increase)
Percent Difference | Heart Rate (BPM) | Respiration Rate (RPM) | Skin Temperature (C) | Est Core Temperature (C)
<10% | 48% | 9% | 100% | 100%
10-20% | 19% | 14% | 0% | 0%
20-30% | 21% | 21% | 0% | 0%
>30% | 12% | 57% | 0% | 0%

## Slide 14: Demonstration – long duration march
Open source BioGears engine [1]
  Available parameters
    Fitness and anthropometry
    Temperature and humidity
    Clothing thermal properties
    Oxygen levels
  Mobile and desktop platforms
Test scenario: Pikes Peak ruck march
  7,000 to 14,000 ft elevation
    Elevation profile from Pikes Peak Highway
  0.8 m/s with 10-minute rest every 50 minutes
  Clothing 1 CLO (similar to battle dress uniform)
  Added rucksack at 30% and 40% body weight
1. Baird, A., McDaniel, M., White, S., Tatum, N., & Marin, L. (2020). BioGears: A C++ library for whole body physiology simulations. Journal of Open Source Software, 5(56), 2645. https://doi.org/10.21105/joss.02645
Hogs555, CC BY-SA 3.0, via Wikimedia Commons

## Slide 15: Results
Notes: Successfully completed simulation of 12-hour ruck march
Reasonable physiological responses to exertion, temperature, oxygen
Demonstrates proof-of-concept for simulating long-duration missions
More validation is needed

## Slide 16: Results
Notes: Successfully completed simulation of 12-hour ruck march
Reasonable physiological responses to exertion, temperature, oxygen
Demonstrates proof-of-concept for simulating long-duration missions
More validation is needed

## Slide 17: Demonstration
Squad Leader
Individual Users

## Slide 18
Platoon Sergeant

## Slide 19: Conclusions
Achievements
Aggregated sensor and device data into actionable insights
Extensible & agnostic – sensors, algorithms, devices, simulations, etc.
Insights into musculoskeletal injury, TBI, fatigue, and medical emergencies
Prognostic insights
Demonstrated in laboratory environment
What’s next?
Validation and refinement with field data
Collect large dataset for injury prediction
Integrate with existing frameworks and military health records
Expand algorithms
Closed loop simulations / digital twin
Point of contact:
Paulien Roos, PhD
Manager, Biomechanics
paulien.roos@cfd-research.com