## Slide 1
See Like a Satellite:
Adapting Human Vision to Complex Sensing Technologies with Adaptive Synthetic Aperture Radar Image Recognition Training (ASIRT)
Presented by: Kimberly Pollard, DEVCOM Army Research Laboratory
Spencer Lin, USC Institute for Creative Technologies, MxR Lab
UNCLASSIFIED
Kimberly A. Pollard, Benjamin T. Files, Brent Lance DEVCOM Army Research Laboratory
David Nelson, Ben Nye, Rhys Yahata, Spencer Lin USC Institute for Creative Technologies

## Slide 2: Synthetic Aperture Radar (SAR)
SAR Remote Sensing Technology
Powerful
Works at night
Sees through clouds, rain, even fabric!
Works at great distances
Indispensable for understanding who, what, where, when
Challenging
Images are difficult for humans
Images violate natural visual expectations
Too many images for people to ever view
UNCLASSIFIED

## Slide 3: The JOYS of SAR
UNCLASSIFIED

## Slide 4: SAR’S Peculiar PROPERTIES
Image courtesy Sandia National Labs
Layover
Multipath
SAR images differ from visual light images 5-7,11
  Shadows point away from sensor
  Geometric distortions
  Layover, where tall objects look closer
  Multipath reflections add repeats and ghosts
  Microwaves interact with materials differently than visible light
  Differences in resolution based on ground slope
  And more!
Why can’t AI already do this?
  Not enough labeled training data
UNCLASSIFIED
Notes:   Sensor angle changes appearance
  Stars from trihedrals

## Slide 5: How do we quickly train humans to label SAR?
Current approach:
  Currently training methods are somewhat limited 8-10
  Training is largely knowledge-based.
Our approach:
  Combine adaptive learning methods with a perceptual learning (perceptual adaptation) approach
Sachse, P., Beermann, U., Martini, M., Maran, T., Domeier, M., & Furtner, M. R. (2017). “The world is upside down”–The Innsbruck goggle experiments of Theodor Erismann (1883–1961) and Ivo Kohler (1915–1985). Cortex, 92, 222-232.
PHYSICS
Current training for SAR labelers
UNCLASSIFIED

## Slide 6: Using Perceptual Learning for SAR
Human visual system - 3D perspective over time (temporal Association) to learn objects 12-16
SAR in augmented reality!
Immersive, interactive training systems - perceive objects through the “eyes” of the sensor
Develop an intuitive understanding of SAR images
First: formal user study to assess effectiveness and inform AR design
Original renders of publicly available models using F/OSS software
UNCLASSIFIED
Notes: Human visual system uses 3D perspective over time (temporal association) to learn objects 12-16
Let’s do that with SAR in augmented reality!
Develop immersive, interactive training system to allow humans to perceive objects as if through the “eyes” of SAR
Develop an intuitive understanding of SAR images
Before we make the jump to augmented reality, we did a user study to assess effectiveness and help inform design

## Slide 7: User Study
UNCLASSIFIED

## Slide 8: Overall Performance improves after training
UNCLASSIFIED

## Slide 9: Accuracy improvement varies by relationship of test to training
UNCLASSIFIED

## Slide 10: Participants explored SAR Domes
UNCLASSIFIED

## Slide 11: SAR-AR
A mobile-based Augmented Reality (AR) application to sharpen the acumen of SAR interpreters.
Next Steps

## Slide 12: SAR-AR
Smartphone/Tablet-based augmented reality interaction for use in future user-study.
UNCLASSIFIED
Notes: This training application will be used in the design of a comparable study to the one already conducted. We will investigate whether immersive/interactive engagements like this one can even more greatly improve SAR image identification.

## Slide 13: SAR-AR
Handheld smart device allows user to engage with augmented reality view of the scene.
User can toggle between SAR and optical views and can walk around the scene to see different angles.
UNCLASSIFIED
Notes: This training application will be used in the design of a comparable study to the one already conducted. We will investigate whether immersive/interactive engagements like this one can even more greatly improve SAR image identification.

## Slide 14
Spatially orient users to build intuition of how SAR technologies work
Interactive way of learning the properties of SAR imaging
Mobile platform is easy to distribute and vastly portable
More engaging AR-based user interface lowers the friction of learning
Value-Added
UNCLASSIFIED
Notes: Spatially orient users to build intuition of how SAR technologies work
Interactive way of learning the properties of SAR imaging
Mobile platform is easy to distribute and vastly portable
More engaging AR-based user interface lowers the friction of learning

## Slide 15: Future Work
Conduct a formal user study to compare the efficacy of SAR-AR with traditional desktop-based trainers
Design an interactive module to engage users and strengthen knowledge absorption and retention
Upgrade textures of models to be more realistic
AI Generated Art: David Nelson
AI Generated Art: David Nelson
UNCLASSIFIED

## Slide 16: See Like A Satellite
Thanks! Visit us in the demonstration hall to interact with the SAR-AR training system!
https://sar-training.pages.sitcore.net/sarTrainer/prolific.html
Try the online trainer used in the experiment!
Try the hands-on SAR-AR training system!
Contacts:
Kimberly Pollard:
kimberly.a.pollard.civ@army.mil
Ben Files: benjamin.t.files.civ@army.mil
David Nelson: dnelson@ict.usc.edu
Ben Nye: nye@ict.usc.edu
Spencer Lin: slin@ict.usc.edu
UNCLASSIFIED
Notes: This training application will be used in the design of a comparable study to the one already conducted. We will investigate whether immersive/interactive engagements like this one can even more greatly improve SAR image identification.

## Slide 17
Backup slides
UNCLASSIFIED

## Slide 18: References
  1. Seitz, A. R. Perceptual learning. Current Biology 27, R631–R636 (2017).
  2. Fiorentini, A. & Berardi, N. Perceptual learning specific for orientation and spatial frequency. Nature 287, 43–44 (1980).
  3. Ball, K. & Sekuler, R. Adaptive Processing of Visual Motion. Journal of Experimental Psychology: Human Perception and Performance 7, 780–794 (1981).
  4. Sagi, D. Perceptual learning in Vision Research. Vision Research 51, 1552–1566 (2011).
  5. van Zyl, J. & Kim, Y. Synthetic Aperture Radar Polarimetry. (John Wiley & Sons, Inc., 2011). doi:10.1002/9781118116104.
  6. Doerry, A. W. & Dickey, F. M. Synthetic Aperture Radar. Optics & Photonics News 15, 28 (2004).
  7. Stone, J. V., Kerrigan, I. S. & Porrill, J. Where is the light? Bayesian perceptual priors for lighting direction. Proc. R. Soc. B. 276, 1797–1804 (2009).
  8. Conway, E. D. An introduction to satellite image interpretation. (Johns Hopkins University Press, 1997).
  9. Johnston, I. A. et al. Perceptual Learning of Appendicitis Diagnosis in Radiological Images. Journal of Vision 20, 16 (2020).
  10. Chen, W., HolcDorf, D., McCusker, M. W., Gaillard, F. & Howe, P. D. L. Perceptual training to improve hip fracture identification in conventional radiographs. PLoS ONE 12, e0189192 (2017).
  11. Hogan, D. & Brown, J. SAR 101: An Introduction to Synthetic Aperture Radar. Capella Space https://www.capellaspace.com/sar-101-an-introduction-to-synthetic-aperture-radar/ (2020).
  12. Li, N., & DiCarlo, J. J. (2010). Unsupervised natural visual experience rapidly reshapes size-invariant object representation in inferior temporal cortex. Neuron, 67(6), 1062-1075.
  13. DiCarlo, J. J. & Cox, D. D. Untangling invariant object recognition. Trends in Cognitive Sciences 11, 333–341 (2007).
  14. Rolls, E. T. Learning Invariant Object and Spatial View Representations in the Brain Using Slow Unsupervised Learning. Front. Comput. Neurosci. 15, 686239 (2021).
  15. Wiskott, L. & Sejnowski, T. J. Slow Feature Analysis: Unsupervised Learning of Invariances. Neural Computation 14, 715–770 (2002).
  16. Peters, B. & Kriegeskorte, N. Capturing the objects of vision with neural networks. Nature Human Behavior 5, 1127–1144 (2021).
UNCLASSIFIED

## Slide 19: Simulating SAR images
UNCLASSIFIED

## Slide 20: More accurate for trained classes (and untrained: Car)
UNCLASSIFIED

## Slide 21: Fewer Confusions after Dome Viewing
UNCLASSIFIED

## Slide 22: Enabling a different kind of human/AI teaming
Better Training
Improved AI
Better understanding of the world around us
helicopter
Faster, more accurate image labeling
nnnn
nnnn
nnnn
helicopter
helicopter
helicopter
helicopter
helicopter
More labeled data
helicopter
Q: Why can’t AI already do this?
UNCLASSIFIED
Notes: Mention the crowd source thing
And how we’ll still need labelers after this
To combat adversarial stuff, to handle new objects, etc.

## Slide 23: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
https://sar-training.pages.sitcore.net/sarTrainer/prolific.html
UNCLASSIFIED
Notes: 23 participants
Recruited from the general population using Prolific
Web-based experiment

## Slide 24: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
UNCLASSIFIED

## Slide 25: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
UNCLASSIFIED

## Slide 26: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
UNCLASSIFIED

## Slide 27: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
UNCLASSIFIED

## Slide 28: User Study
Instructions
Interacting with the system
Introduction to SAR
Pre-test (x 30)
Static SAR image
Collect object class and self-reported confidence
Training (x 6)
Static SAR image, response
SAR + EOx2 Domes, identify correct class
Post-test
(x 30)
Questionnaire
Object classes and photographic examples
Static SAR image
Multiple choice and open-ended.
SAR Dome, response
Collect object class and self-reported confidence
UNCLASSIFIED

## Slide 29: SAR-AR
Smartphone/Tablet-based augmented reality interaction developed for follow on user-study.
UNCLASSIFIED
Notes: USC-ICT in collaboration with ARL developed an innovative prototype designed to leverage immersive 3D interactive training material to enhance the ability of analysts-in-training to identify and analyze SAR images.
USC-ICT is in the process of developing a more immersive, interactive training engagement that leverages phone/tablet based augmented reality. Where the trainee will use the tablet/phone as a representative SAR sensor, hovering over a virtual scene anchored to a surface in the room. They’ll be able to move around the scene to see it from different vantage points…

## Slide 30
See Like A
You too can …
UNCLASSIFIED
Notes: This training application will be used in the design of a comparable study to the one already conducted. We will investigate whether immersive/interactive engagements like this one can even more greatly improve SAR image identification.

## Slide 31
SAR-AR: Adapting Human Vision to Complex Sensing Technologies with Adaptive Synthetic Aperture Radar Image Recognition Training (ASIRT)
04 December 2024
Kimberly A. Pollard, Benjamin T. Files, Brent Lance DEVCOM Army Research Laboratory
David Nelson, Ben Nye, Rhys Yahata, Spencer Lin USC Institute for Creative Technologies
UNCLASSIFIED