## Slide 1
Elements of Unsupervised Testing for Software Systems of Autonomous Vehicles
Sean Hickey, Nickolas Vlahopoulos, University of Michigan
Geng Zhang, Michigan Engineering Services
Jonathon M. Smereka, US Army DEVCOM GVSC
Paper 24346

## Slide 2: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 3: Overall Scope
Type of faults:
Implementation errors
Errors in logic
From ARC 2023 meeting
Notes: Make clear: node interception, monitoring of errors, automatically launch multiple runs -> properly formulate fitness function and run GA
These are the main developments in the first 9 months of the project.

## Slide 4: Research Questions
How effective is an unsupervised process in testing autonomy-focused software systems?
How can the automated process generate diverse input selections and discovered faults?
How much more efficient is a genetic algorithm in discovering faults compared to random search?

## Slide 5: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 6: Establishing a Simulation Harness at UM Autoware Universe (ROS2)

## Slide 7: High-Level RTK/ARCS Architecture

## Slide 8: High-Level Autoware Architecture

## Slide 9: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 10: Mapping Data Flow
Using ROS2 commands we can do the following:
  List subscribers, publishers, services, actions for a target node, along with message type of each
  Analyze message types to understand information that can be intercepted
  Perform topic remapping to alter communication pathways

## Slide 11: ROS2 Message Interception
Publisher Node
Subscriber Node
Modified Msg
Interceptor Node
Original Msg
Original Message Flow
Modified Message Flow

## Slide 12: Interception Strategy for a ROS2-Based Code
Choose the topics to manipulate and intercept these by modifying launch files
Automatically generate an input file to specify messages to drop or modify
Use a single interceptor node to read inputs and apply modifications at specified times
* Unmodified messages are sent through interceptor node without changing the behavior of the system

## Slide 13: Message Modifications
Types of modifications:
  Message dropping
  Modified data
Specified by:
  When the modification should start
  How long it should last
  Modified message (if modifying data)
Notes: Message dropping – sensor not operating properly
Modifies data – errors in communication system
Generally sensor malfunctions

## Slide 14: ROS2 Message Interception Example
Control Execution Node
Shift Decider Node
Modified Command Msg
Interceptor Node
Control Command Msg
Trajectory Follower Node
Vehicle Command Gate Node

## Slide 15: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 16: Running an Autoware Simulation Automatically
Launch Autoware in terminal window
Define initial pose in Rviz window
Define target pose in Rviz window
Stop Autoware by ctrl_c in terminal window
Set engagement in Rviz window
Launch Autoware by shell command
Define initial pose by command
Define target pose by command
Stop Autoware by process killing command
Set engagement by command
Manual Run
Automatic Run

## Slide 17: Termination of an Autoware Simulation
*Simulation termination command: kill –SIGINT process_id
Process alive?
Target achieved?
Zero speed for extended period?
Total time exceeds limit?
*Terminate simulation
Continue simulation
No
Yes
Yes
Yes
Yes
No
No
No
Simulation
Self-terminated
Crushed
Success
Hung
Other issues
Ongoing

## Slide 18: Automating Multiple Runs of Autoware

## Slide 19: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 20: Lightweight Simulator
Emulates Autoware control module
ROS2 environment for accelerated development
Simpler and faster simulations
Ability to insert intentional bugs to test detection performance

## Slide 21: Genetic Algorithm
NSGA-II algorithm for non-dominated multi-objective optimization
Generates fault-causing test cases using fitness function
  Fault severity
  Input diversity
  Fault diversity
Discovers vehicle collisions, system crashes, and timeout faults

## Slide 22: Genetic Algorithm Results
Initial Generation (Random Search)
Final Generation (After GA)
Population size = 20, Generations = 15
Notes: Have initial successful results. Focus on future is refining objective function to gain better performance. Adding a term to encourage instability in results

## Slide 23: Outline
Overall Scope
Establishing a simulation harness at UM
Intercepting messages and changing data flow
Running a simulation multiple times automatically and monitoring termination
Using a lightweight simulator to implement and test new features
Next steps

## Slide 24: Next Steps
GA: custom selection and crossover methods
Working with the Army Ground Vehicle Systems Center to get involved in related projects
Duplicate node interception, automated execution, and error detection in ARCS and Project GL

## Slide 25: Questions