## Slide 1
Soldier Centric Design of Mixed Reality Reconfigurable Virtual Collective Trainers
Dennis Joseph
Cole Engineering Services, Inc

## Slide 2: What is the Reconfigurable Vehicle Collective Trainer (RVCT)
Base Set
Ground
Vehicle Kit
Air Vehicle Kit
Army’s new collective vehicle simulators developed for STE
Collective training simulator
Works with TSS/TMT
Reconfigurable and deployable
Setup by the Soldiers
Reconfiguration
In operation

## Slide 3: Current RVCT Vehicle Types

## Slide 4: Current RVCT Air (Pilot/Copilot) Station Simulations
Including Integrated Helmet and Display Sight System (IHADS) simulation
Including Night Vision Goggle (NVG) simulation

## Slide 5: Introduction to the RVCT Air Stations
Collective Training - Pilots must be able to fly the aircraft and operate the systems with eyes-out of the aircraft as needed during live maneuvers
Instrument panels, center, side and overhead panels have full functional and physical fidelity
Cyclic, collective and pedals include electronic control loading with realistic flight models
Reconfigurable to each aircraft type
Powered by the Training System Software (TSS)

## Slide 6: Key Challenges for RVCT Air Stations
Deployment Challenges
Computational Challenges
Instrument Panel Display Challenges
One common compute kit per vehicle runs the pilot, copilot and sensor visual channels
Each platform must run off a single 20-amp circuit
Cockpit Display | Approx Viewing Distance | Display Size (HxV) | Pixels | Pixels per Inch | Pixels per Degree
CH-47F MPD | 36” | 6” x 8” | 480 x 640 | 80 | 50
UH-60M MFD | 36” | 8 x 6” | 640 x 480 | 80 | 50
AH-64E MPD | 36” | 6” x 6” | 768 x 768 | 128 | 80*
AH-64E TEDAC | 23” | 5” x 5” | 960 x 960 | 190 | 76*
*Visual acuity ~60 PPD (1 arc minute) for typical viewers
AH-64E MPDs
AH-64E TEDAC
High resolution sensor, map and symbology content must be clear through HMD
Open room environments
No control of ambient lights
Must simulate all Day to Night conditions
Deployable by the soldiers

## Slide 7: Soldier Centric Design Process
RVCT conducted over 60 soldier touchpoints to review and adjust the prototypes
Continuous iterative development and improvement of the initial capability by TSS
Development included three generations of RVCT Stations before production contract
Began with Fidelity Analysis developed with the users

## Slide 8: HMDs Evaluated at Program Startup (2019)
SA-147/S
NVIS 106391
SA-92
Varjo XR-1
XTAL 5k w MR
HoloLens 2
Valve Index
PiMax Vision 8KX
Varjo VR-1
GOOVIS Pro (P2)
Optical Pass- Through (MR)
Camera Pass- Through (MR)
Virtual Reality (VR) Only
SR-100A
Magic Leap 1
(AVCATT)

## Slide 9: Application of VR-Only HMDs to RVCT Air Stations
Displays, instruments and panels are rendered as part of the VR scene
  Physical controls / surfaces can still provide tactile feel
  Reduces hardware, weight and cost
  Provides isolation from exterior environment
Technical challenges
  Realistic view of hands while working controls
  Merging of high-resolution cockpit display content into the VR scenes
  Alignment and stability of the VR with the physical surfaces with head motion
Solutions to the technical challenges were judged to be too high risk

## Slide 10: Optical Pass-Through / Legacy (AVCATT) Mixed Reality
AVCATT Manned Module
(Head Mounted Displays Containerized in Trailer)
Eyepoint
Combiner
Element
Optics
VR Source (with mask)
Beam Splitter
Physical
View
Black 3D
(Cockpit)
Mask
Combined View
VR image reflects off beamsplitter, combiner, and back to eyepoint
VR scene is computed with black cockpit view
Full resolution of cockpit displays is preserved (Brightness attenuation only)
Physical cockpit is seen through the beamsplitter and combiner
The Aviation Combined Arms Tactical Trainer (AVCATT) was the predecessor to RVCT Air

## Slide 11: Initial RVCT Air Prototype (2020)
SA-147/S
The SA-147S HMD was selected for the RVCT Air Prototype
See-through combiner (Same principle as AVCATT)
Resolution and weight enhancements over AVCATT
No adequate camera pass-through HMDs were available
Varjo XR-1 had insufficient pass-through resolution to clearly display the instrument panel display content
See-through combiner HMD limitations
Operation in an open room environment
Support for night simulation

## Slide 12: 2nd Generation RVCT Air Prototype (2021)
JVC VS-1W HMD
Became available April 2021
Non-pupil forming Eliminates user adjustments to align to pupils
120° H x 45° V FOV
32 PPD
Significant improvement of ease of use for the soldiers
JVC VS-1W at Soldier Touch Point
(With Polhemus Viper tracker / Integrated with TSS)
Still a see-through combiner HMD subject to limitations
Operation in an open room environment
Support for night simulation

## Slide 13: Evolution of Head Tracking on RVCT Air
Polhemus Viper (Common to all RVCT HMDs) was changed to SteamVR tracking on RVCT Air
EMI Induced Noise/Jitter
From HMD components
Resolved by offsetting sensor from HMD, reducing emitter distance, & filtering
Distortion of Tracker Space
Distortion of tracking space from metallic surfaces
Determined to be an issue
Mitigation by 6DOF mapping
Visual Latency
TSS measured latency of IG scene between Viper and SteamVR tracking
Major issue with soldiers
Could not be resolved
SteamVR Implementation
Four base stations per vehicle
Includes blinders to limit coverage to vicinity of the vehicle
EMI, Distortion and Visual Latency issues were resolved by using SteamVR tracking
Viper sensor “tierra” on JCV HMD
Distortion Measurement
Visual Latency Measurements
SteamVR Base Stations

## Slide 14: RVCT Issues Using See-Through Optics
RVCT operates in uncontrolled room environments
  Multiple vehicles / No control of room lighting / ambient conditions
  AVCATT utilized isolated / dark room environments
See-Through Optics Limitations
  The room is visible through the optical combiner
  Especially an issue for night simulation
  Portable Tenting / Room Dividers Requires additional soldier setup, air flow and storage
Example of the RVCT “Open Room” environment

## Slide 15: Key Advantage of Camera Pass-Through MR on RVCT
View of the Open Room
Pilot’s Mixed Reality View
Physical View
VR View
If done properly, the MR isolates the users from the external surroundings

## Slide 16: Pursuit of a Camera Pass-Through (MR) HMD
SOURCE IMAGE
XR-3 Vari-Focus
TEST RESULT IMAGE
Varjo HMD | Standard XR-3 | XR-3 Vari-Focus
Virtual Image | Foveated View 27° x 27° (70 PPD) Background View 106° x 90° (16 - 35 PPD) | Foveated View 27° x 27° (70 PPD) Background View 106° x 90° (16 - 35 PPD)
Video Pass-through | Foveated View 27° x 27° (35 PPD) Background View 106° x 90° (16 PPD) | Foveated View 27° x 27° (49 PPD) Background View 63° x 53° (16 PPD)
RVCT provided images of MFD content and viewing distances to assist HMD developers to understand what was needed
Varjo developed the “Vari-Focus” version of the XR-3
Achieved 49 PPD image quality for the camera pass-through
Traded-off reduction of the camera pass-through FOV
Also implemented variable focus distance based on LiDAR
XR-3 Vari-Focus
Considered ready to demo to soldiers

## Slide 17: XR-3 Vari-Focus Evaluations & HMD Fly-Off
Initial XR-3 Vari-Focus touch point with DOS and USARNG demonstrated suitability of the HMD camera pass-through image quality (December 2022)
Pass-through camera quality was judged adequate to support training
Subsequent Flyoff between the JVC and Varjo “HMD Rodeo” demonstrated capabilities and limitations to support training scenarios (March 2023)
Key discriminator for the XR-3 “Vari-Focus” was ability to isolate the simulated environment from the exterior room
Soldier preference was the XR-3 Vari-Focus

## Slide 18: Mixed Reality Day/Night Simulation
The XR-3 Vari-Focus pass-through camera exposure and gamma settings are continuously adjusted for time-of-day
Scenes with identical ambient room light conditions

## Slide 19: IHADSS and NVG Simulation
Aircraft head-worn display content is merged through Varjo’s multi-app interface by a fully-programmable TSS app
AH-64E Copilot/Gunner Left & Right Eye Views (IHADSS on Right Eye)
AH-64E Pilot Right Eye View (with IHADSS)

## Slide 20: Crewmember Avatars
Pilots expressed the desire to see their copilot
Showing the actual pilot (using an accurate dynamic pass-through mask) was not within the current capabilities
Other crewmembers could be physically located remote from the pilot/copilot station
TSS leveraged head tracker data from the pilot/copilot and non-rated crew members (NRCM) to animate avatars in the VR scene
CH-47F Pilot View
Door gunner avatar
Copilot avatar
Door Gunner Station
Copilot

## Slide 21: HMD Progression Summary
Mixed Reality
Upgrade (2023)
Ease of Use
Upgrade (2021)
Initial Baseline Selection (2020)
XR-3 Vari-Focal
Camera Pass-Through
106°H x 90°V
39/49 PPD (VR/MR)
1.3 lb.
SA-147/S
See-Through Optics
120°H x 45°V
32 PPD / 1.4 lb.
SA-147/S
See-Through Optics
143°H x 33°V
36 PPD / 1.2 lb.
RVCT Baseline
SR100A
See-Through Optics
90°H x 52°V
20 PPD / 2.5 lb.
XR-1
Camera Pass-through
106°H x 90°V
60/30 PPD (VR/MR)
Dark Room Only
Open Room Compatible
Production Baseline
2nd Prototype Baseline

## Slide 22: Next Steps for RVCT Mixed Reality
RVCT Air
  Varjo XR-4 (Planned for RVCT 2025 Production)
  Varjo XR-4 Inside-Out tracking
RVCT Ground and NRCM
  Deploy the MR concepts using Magic Leap 2 (leveraging ML2 segmented dimming)
  Smaller form factor / less immersive
Continue to monitor new and emerging products and technologies