## Slide 1
Original: Establishing Best Practices to Apply a Generic Point Cloud Model (GPM) to High Resolution Data
Amy Neuenschwander Ph.D, University of Texas at Austin Center for Space Research
Eric Guenther, University of Texas at Austin Center for Space Research
Donald Maze-England, University of Texas at Austin Center for Space Research
Thomas Bakewell, University of Texas at Austin Center for Space Research
Lori Magruder Ph.D, University of Texas at Austin Center for Space Research
Updated: Computing Predicted Errors and Uncertainty for High Resolution Photogrammetric 3D Data
This research was funded by U.S. Army Simulation and Training Technology Center

## Slide 2: Motivation
Collections of UAS-based Photogrammetric 3D data is becoming more common
Small UAS systems have less-precise GPS resulting in less accurate geolocations
Knowing the per-point error/uncertainty for a data collection provides insight on the usability of that collection
  Does the data resolution meet my requirements?
  How accurate is the geolocation associated with this data?
  Can this data be used with other data sets without registration?
Most operational collections may not have reference data to compare against
Can we predict what the uncertainties are?

## Slide 3: Motivation
Problem: Army has flown a sUAS-Photogrammetric Survey and we want to know the overall accuracy of the data.
AND we’d like to know the per-point error/uncertainty of the collected data.
Ft Moore/Selby CACTF sUAS-Photogrammetric (SkydioXD2) collected November, 2023

## Slide 4: Errors Associated with 3D Data
6 axis linear transformation to determine registration parameters
Registered Input Point Cloud
Reference Point Cloud
difference
Per Point Measurement error converted into Sigma-R, Sigma-Z
Reference Point Cloud
Registration Errors
dX, dY, dZ, dqx, dqy, dqz,
Scale factor
Measurement Uncertainty
Measured Errors
Input Point Cloud
Error ellipsoid around each point
With reference data, an error ellipse can be calculated for each point (Per-Point-Error)

## Slide 5: Can Predicted Errors can Approximate Measured Errors
Input Point Cloud
GPSBase
Bias_H, Bias_Z;
RMS_H, RMS_Z
GCPs
RMS_Hi , RMS_Zi
Reconstruction Errors
Predicted Errors
GPS Errors
6 axis linear transformation to determine registration parameters
Registered Input Point Cloud
Reference Point Cloud
difference
Per Point Measurement error converted into Sigma-R, Sigma-Z
Reference Point Cloud
Registration Errors
dX, dY, dZ, dqx, dqy, dqz,
Scale factor
Measurement Uncertainty
Measured Errors
Input Point Cloud
Assumption: no registration errors

## Slide 6: Collection Details
SkyDioX2D photogrammetric drone was flown over entire site
iTwin (Context Capture) was used to generate High Resolution Mesh from photographs
10 cm GSD point cloud was derived from High Resolution Mesh
Ground Control Points were used in this collection
Terrestrial Lidar Scanner (TLS) data were collected (yellow box) at the same time for data validation
Trimble RTX was used to collect 3D position information
Ft Moore/Selby CACTF sUAS-Photogrammetric (SkydioX2D) collected November, 2023

## Slide 7: Importance of Controlled sUAS Collection
 | dX | dY | dH | dZ
without GCPs | -0.356 (0.398) | -0.794 (0.253) | 0.980 (0.139) | -8.656 (0.863)
with GCPs | -0.006 (0.045) | 0.023 (0.064) | 0.059 (0.056) | -0.075 (0.058)
Ft Moore/Selby MOUT sUAS-Photogrammetric (SkydioXD2) collected November, 2023
The computed mean and Standard Deviation registration errors (meters) of the Selby 3D data relative to GCPs
For a typical survey (~0.15 km2), we distribute 6 – 15 GCPs across the AOR.
Each GCP is 48” x 48” black and white tarp and the center XYZ location is surveyed with DGPS.

## Slide 8: Importance of Controlled sUAS Collection
Using GCPs during a data collection is critical to minimize distortions and warping due to camera distortions and poor GPS information on photo tags
Absolute 3D error of data processed with and without GCPs

## Slide 9: Examples of SfM Reconstruction Errors
Reconstruction Errors
UAS-EO
TLS

## Slide 10: Calculating the Reconstruction Errors
3D Distance (m)
0.40
0.50
0.0
0.20
0.10
0.30
Data Validation: Per-point Measurement Error
Difference of TLS – sUAS-Photogrammetric Point Clouds
Most of the reconstruction errors occur in doorways, window opening, beneath patio covering or along walls with low contrast between photos.
This 3D per-point measurement error along with the overall mean/RMSE errors provide a more complete representation of the actual errors/uncertainty for a sUAS collect.

## Slide 11: Calculating the Reconstruction Errors
3D TLS scan used as reference data

## Slide 12: Building a Predicted Uncertainty Model
3D Distance (m)
0.50
0.0
0.20
0.10
0.30
Normal Vectors, 20 cm radius
Normal Vectors, 50 cm radius
angle (deg)
90
0
45
Generated “Features” from the input photogrammetric point cloud to predict against
Measurement Error is what we want to predict
0.40

## Slide 13: Prediction Error/Uncertainty Model
Predicted Error
Measured Error
We used a Gradient Boosted Regression (GBR) model to predict our per-point-uncertainties.
0
20
10
cm

## Slide 14: Prediction Error/Uncertainty Model
0
20
10
cm
Higher errors under eaves and in porch/entryways (as we expect)
Highly pitched roof of church and steeple creates higher than desired uncertainty
Remedy: Need more representation in training data
Predicted Error of photogrammetric 3D point cloud

## Slide 15: Limitations of the Model
Model currently applies only to open terrain and buildings.
  Vegetation has not been tested yet, but potentially could be included
  Terrain beneath vegetation is generally not visible in sUAS-Photogrammetric surveys
Need more data to improve model of reconstruction errors
Holes in reconstruction

## Slide 16: Conclusions
Prediction Uncertainty Model was developed to create Per-Point-Errors (PPE) of sUAS Photogrammetric 3D data
  PPE informs data quality of sUAS survey
  PPE, combined with known and unknown errors contribute to the NGA Generic Point Cloud Model (GPM)
  Model currently consumes features from the input point cloud only
  Can be applied to ANY Photogrammetric point cloud
  Model assumes data is from a controlled Survey No Registration Errors
Predicted Per-Point-Error