## Slide 1
Developing a Novel UAS Flight Planning and Reconstruction Software Package
Mike Alonzo, The Applied Research Laboratories at The University of Texas at Austin (ARL:UT)
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited. OPSEC #9017

## Slide 2: Overview
Introduction
Improving Unmanned Aerial System (UAS) Flight Planning Capabilities
  2.1 Optimizing Flight Paths Through Complex Survey Polygons
  2.2 Advancing UAS Collision Avoidance
Optimizing 3D Reconstructions from UAS Imagery
  3.1 Determining Optimal UAS Image Overlap Through Simulation
  3.2 Analyzing Terrain-Based Image Capture Methods Through Simulation
Conclusion
Questions

## Slide 3: 1. Introduction
Imagery from a UAS can be used to create 3D reconstructions of real environments for both commercial and operational use cases, such as:
  Mission planning
  Simulation-based training
  Damage assessment
Current UAS flight planning capabilities can be improved by:
  Minimizing flight times with efficient UAS flight paths that adhere to survey bounds
  Adding functionality to help avoid collisions with potentially hazardous obstacles
  Utilizing the underlying terrain to adapt UAS image locations that aid 3D scene reconstructions
Simulated environments can help test UAS flight methods by:
  Reducing time, cost, and wear-and-tear on the UAS
  Avoiding weather and logistical restrictions that affect safe UAS operation
  Providing more diversity in survey areas

## Slide 4: 2. Improving UAS Flight Planning Capabilities
With some current UAS flight planners, complex survey polygons can lead to:
  Sub-optimal UAS flight paths
  UAS flight paths outside of the survey boundary
  A single mission divided into several surveys to handle interior avoidance zones
These limitations may make it difficult to:
  Minimize flight times to conserve battery life and/or avoid detection
  Automate avoiding obstacles like electrical utility equipment, trees, buildings, or restricted areas within a survey area
  Have a single mission to cover the survey area
2.1 Optimizing Flight Paths Through Complex Survey Polygons
Example UAS Flight Plan Using Commercial Flight Planning Software

## Slide 5: 2. Improving UAS Flight Planning Capabilities
A polygon decomposition algorithm can be used to:
  Decompose the original polygon into smaller, constituent trapezoids
  Generate more efficient flight paths through each polygon and stay within each boundary
  Assign final waypoints and camera trigger locations in a flight plan for execution by a UAS
2.1 Optimizing Flight Paths Through Complex Survey Polygons
Polygon Decomposition of UAS Survey Area
Sample User-Defined UAS Survey Area
New Flight Plan over UAS Survey Area
1
3
0
2
4

## Slide 6: 2. Improving UAS Flight Planning Capabilities
This flight optimization method will help with complex surveys by:
  Minimizing UAS flight times by generating more efficient flight paths through the survey area
  Ensuring that the UAS does not fly over avoidance zones or other restricted areas
  Maintaining a single mission plan to cover the full survey area
2.1 Optimizing Flight Paths Through Complex Survey Polygons
315 m
255 m
Note: Both flight plans generated using 70% overlap at 40 m altitude
Mission Planner Flight Time: 20.6 min | Images: 246
New Method Flight Time: 14.7 min | Images: 213

## Slide 7: 2. Improving UAS Flight Planning Capabilities
UAS collisions are a major potential hazard during flights
  The UAS operator holds the main responsibility for collision avoidance mitigation by identifying obstructions and manually adjusting the flight plan accordingly
  Some common hazardous obstacles to a UAS include radio communication towers and electrical equipment
The ability to properly identify hazardous obstacles in the planning stage can help:
  Provide safer UAS flight plans
  Allow a UAS to fly lower and collect better data
  Avoid signal interference from radio communication towers and electrical equipment during operation
2.2 Advancing UAS Collision Avoidance
Example Hazardous Obstacles

## Slide 8: 2. Improving UAS Flight Planning Capabilities
Two automated methods to identify and avoid potential hazardous obstacles were created:
  Method 1: Using an object avoidance file, currently set to the Federal Aviation Administration (FAA) Digital Obstacle File
  Method 2: Using a known digital surface model (DSM) that provides the heights of buildings, vegetation, and other obstructions
Potential Limitations:
  Method 1: Publicly sourced files may contain inaccuracies in obstacle locations and heights
  Method 2: Availability of DSM data at a high enough resolution to capture obstructions
2.2 Advancing UAS Collision Avoidance
Example Communication Tower Obstacle from FAA File (2021)
Safe Altitude UAS Flight Path Using a DSM

## Slide 9: 3. Optimizing 3D Reconstructions from UAS Imagery
Simulate Camera Captures
Conducting a UAS flight each time a user needs to test and validate new algorithms is difficult due to:
  Time
  Cost
  Weather
  Wear-and-tear on UAS
  Lack of diversity of survey areas
  Potential hazardous locations
As a result, a simulated environment was built to test new UAS flight algorithms quicker and easier
3.1 Determining Optimal UAS Image Overlap Through Simulation
Simulated Dataset Creation and Validation Workflow
Use 3D Data
Make DSM
Make Mesh
Make DSM
Error Metrics
Make 3D Reconstruction
Reference Dataset
Simulated Dataset

## Slide 10: 3. Optimizing 3D Reconstructions from UAS Imagery
Example of gathering virtual images over a reference dataset to create a simulated dataset:
Frontlap and Sidelap can be Varied in the Simulated Environment
UAS Image
UAS Flight Path
Frontlap
Sidelap
UAS Image
Simulated Environment
3.1 Determining Optimal UAS Image Overlap Through Simulation

## Slide 11: 3. Optimizing 3D Reconstructions from UAS Imagery
Comparing and validating the reference and simulated datasets:
Reference
Simulated
3.1 Determining Optimal UAS Image Overlap Through Simulation
Elevation (m)
Distance (m)
A
B
B
A
A
B

## Slide 12: 3. Optimizing 3D Reconstructions from UAS Imagery
The simulated testing environment shows a decrease in elevation error with increasing sidelap and frontlap (up to a limit)
  There is a tradeoff in the amount of image overlap desired versus the time it takes to generate a 3D reconstruction based on the increase in the number of UAS images used (note that increasing the sidelap also increase UAS flight time)
  For this reason, a safe recommendation is around 70% image overlap for most UAS missions to balance accuracy, 3D reconstruction time, and UAS flight time
These results are consistent with current UAS guidance and trend with real-world expectations
3D Reconstruction Time
Frontlap (%)
Sidelap (%)
Elevation Mean Absolute Error
Error (m)
Time (s)
Sidelap (%)
Frontlap (%)
3.1 Determining Optimal UAS Image Overlap Through Simulation

## Slide 13: 3. Optimizing 3D Reconstructions from UAS Imagery
The simulated environment was also used to test methods for adapting the UAS image capture locations based on the underlying terrain:
  This method uses the scale invariant feature transform (SIFT) algorithm to determine areas from a satellite image where more/less UAS images are needed based on the features present
3.2 Analyzing Terrain-Based Image Capture Methods Through Simulation
Regular Spacing
Variable Spacing
SIFT Feature Density

## Slide 14: 3. Optimizing 3D Reconstructions from UAS Imagery
Adapting UAS image capture locations based on the underlying terrain can potentially create 3D reconstructions with higher elevation accuracy
  Areas with a lot of color homogeneity, fewer features, and flatter elevations can make it harder for the 3D reconstruction algorithms to identify feature matches in the UAS imagery which may decrease the accuracy of the 3D reconstruction
  This information can help identify an automated method to generate flight plans based on the underlying terrain for optimal 3D reconstructions
  The flight plans that perform well in the simulated environment need to be tested further in the real world to fully validate this process
3.2 Analyzing Terrain-Based Image Capture Methods Through Simulation
Regular
Variable
Probability Density
Elevation Difference (m)
Histograms for Regular vs. Variable Spacing

## Slide 15: 4. Conclusion
Imagery from a UAS can help create realistic 3D reconstructions for a variety of use cases in both commercial and operational settings
While there are many UAS flight planning software platforms currently available, most flight planners are limited when it comes to:
  Minimizing UAS flight time
  Adhering to UAS survey boundaries
  Identifying and avoiding collisions during flight
  Allowing users to vary UAS image capture locations based on the underlying terrain
Improvements were made to create optimal UAS flight plans that:
  Adhere to survey polygons of varying complexities which may contain interior avoidance zones using polygon decomposition
  Reduce the possibility of UAS collisions during flight through the use of the FAA Digital Obstacle File or an existing DSM

## Slide 16: 4. Conclusion
Analysis was also done through simulation to understand the:
  Tradeoff between UAS image overlap desired versus 3D reconstruction elevation accuracy while considering the amount of time it takes to generate the 3D reconstruction, enabling the user to make an informed decision based on their own needs and objectives
  Impact of variable UAS image captures with respect to the underlying terrain and how utilizing the amount of features in an area can be used to toggle the amount of UAS images needed to improve the accuracy of the output 3D reconstruction
The results from the simulation trend with what can be expected in the real world, thus strengthening the effectiveness of using simulated environments for testing methods employed on a UAS

## Slide 17: 5. Questions?
The Authors Would Like to Thank:
  Will Manning Army Research Office, University Technology Development Division
  John Aughey I/ITSEC bird dog
  The Campus Geospatial Assets Group The University of Texas at Austin