## Slide 1
IEEE 1278TM Standard for Distributed Interactive Simulation (DIS):
Concepts and Techniques
Robert Murray, SimPhonics, Inc.
bobmurray222@gmail.com
Lance Call, AFRL/CAEUSA
lance.call.ctr@us.af.mil
Oct 2, 2024

## Slide 2: Disclaimer
Any comments and interpretations of the Institute of Electrical and Electronics Engineers (IEEE) Standards discussed in this tutorial do not represent the view of the IEEE, IEEE-Standards Association its members or affiliates

## Slide 3: Learning Objectives
The student will be able to explain the capabilities of DIS
  What problems it solves
  Capabilities for Live-Virtual-Constructive (LVC) Simulation Networking
The history of DIS will allow the student to discuss:
  How it has evolved
  Its future direction
The student will be able to explain the key definitions and concepts of DIS
The student will be able to describe the technical details of:
  The type of information conveyed by DIS
  Techniques for distributing real-time high-fidelity simulation data over wide area networks

## Slide 4: Intended Audience
Modeling and simulation implementors and managers who require an understanding of
  Distributed simulation in the Live, Virtual, and Constructive (LVC) domains
  Specifics of how DIS meets of the requirements of interoperability between the widely varying types of geographically distributed LVC simulations
DIS based Secure LVC Advanced Training Environment (SLATE) Pod – Nellis 2018
Photo by RHA (Will Graver)

## Slide 5: Tutorial Outline - Goals
Goal - LVC
The Past
  History of networked simulation
The Present
  The IEEE 1278TM DIS standard and how it is developed
  Key definitions and concepts
  Function and organization of DIS Protocol Data Units
  Technical details of providing high-fidelity real-time information exchange
  Improvements from the 1995 to the 2012 DIS (DIS V7) standards
The Future: The development of the next version of the DIS (DIS V8)

## Slide 6: LVC Simulation
Live – real humans operating real systems not in actual warfare
Virtual – real humans operating simulated systems
Constructive – simulated humans operating simulated systems
LVC is the common term for simulations suitable for:
  Integrating live platforms into a simulation environment
  Constructive simulations to add realism to human training or mission system test
Live
Virtual
Constructive
Photo by RHA
Graphic by RHA
Photo by RHA (Will Graver)

## Slide 7: Goal is Fully Integrated LVC
1553/1760 Bus
Radar
A/C TSPI
RWR/ESM
Voice Radio
ECM
HMD
Pod/LRU
Link16
DIS
Voice Radio
UHF/VHF
DIS Standard Link16
DIS LAN/WAN
Computer
Generated Forces
Weapon
Servers
DIS Voice Radios
4th Gen
5th Gen
Red Air /
Aggressor
AWACS/GCI
JTAC
UAV
5G-ATW
L
V
C
MADL
DIS Standard MADL
C-DIS
Encrypt
Future
Photo by Lance Call
Photo by RHA
Graphic by RHA
Graphic by RHA
Photo by RHA

## Slide 8: Desired Capabilities of LVC Networking
Real-time simulation at entity level (weapons platforms, munitions, etc.)
Generally, effects-based or basic physics simulation instead of highly detailed physics models
Simulation interoperability of:
  See and be seen with accurate visual and time-space-position information (TSPI)
  Weapons engagement with fair fight damage assessment
  Radar, infrared sensors, laser designators, underwater acoustics, and associated jamming
  Radio and Network communications models for Voice and Data
  Collisions, Logistics, Synthetic Environment, Information Operations
Simulation Management
  Start/Stop, simulator initialization and control, data logging, analysis and debrief

## Slide 9: Tutorial Outline - History
Goal - LVC
The Past
  History of networked simulation
The Present
  The IEEE 1278TM DIS standard and how it is developed
  Key definitions and concepts
  Function and organization of DIS Protocol Data Units
  Technical details of providing high-fidelity real-time information exchange
  Improvements from the 1995 to the 2012 DIS (DIS V7) standards
The Future: The development of the next version of the DIS (DIS V8)

## Slide 10: The Beginning
Pre-1990’s custom interfaces - limited networks
The Defense Advanced Research Projects Agency (DARPA) created the SIMNET program in the 1980’s to test simulation networking techniques
In 1989 DIS workshops started and went until 1996 leveraging SIMNET
Decision to involve IEEE to learn how to create and publish standards
The first DIS standard in 1993 based on SIMNET
Refinements in 1995 & additions in 1998
The 1995/1998 standard became widely implemented

## Slide 11: SISO
Simulation Interoperability Standards Organization (SISO) (Non-Profit) created in 1997 which replaced the DIS workshops
SISO is an approved IEEE standards committee for simulation standards
  IEEE Std 1278™ DIS
  IEEE Std 1516™ High Level Architecture (HLA)
  IEEE Std 1730™ Distributed Simulation Engineering and Execution Process (DSEEP)
SISO also develops a wide range of non-IEEE simulation standards
  Command and Control, Distributed Debrief, Common Image Generator Interface, Coalition Battle Management Language, Military Scenario Definition Language, and many more
  Guidance and Reference products e.g., simulation enumerations
Anyone can join SISO and participate

## Slide 12: DIS Versions
V1 - DIS PDU version 1.0 (May 1992)
V2 - IEEE Std 1278TM-1993 (Gen 1)
V3 - DIS PDU version 2.0 – draft (May 1993)
V4 - DIS PDU version 2.0 – draft (Mar 1994)
V5 - IEEE Std 1278.1TM-1995 (Gen 2)
V6 - IEEE Std 1278.1aTM-1998 (Gen 2)
V7 - IEEE Std 1278.1TM-2012 (Gen 2)
V8 - IEEE Std 1278.1TM – Next Version (Gen 3) In Work

## Slide 13: Tutorial Outline - Present
Goal - LVC
The Past
  LVC simulation and its use for training, R&D, and engineering
  History of networked simulation
The Present
  The IEEE 1278TM DIS standard and how it is developed
  Key definitions and concepts
  Function and organization of DIS Protocol Data Units
  Technical details of providing high-fidelity real-time information exchange
  Improvements from the 1995 to the 2012 DIS (DIS V7) standards
The Future: The development of the next version of the DIS (DIS V8)

## Slide 14: Current DIS Development Process
SISO holds a yearly workshop in Orlando in February
  Simulation Innovation Workshop (SIW)
  But most standards development work is done virtually
Weekly telecons to review proposed standards content
When a significant amount of content is ready, the drafting process starts
  This begins the formal IEEE process, expected to be done within 4 years
The draft standard content is reviewed, and comments submitted
Voting process resolves conflicts (SISO members vote)
When draft is ready, it is handed to IEEE for the final balloting process
  Balloting is open to a larger population, even outside of SISO
IEEE publishes the standards after a final edit

## Slide 15: IEEE 1278 Distributed Interactive Simulation
Distributed Interactive Simulation (DIS)
  Time and space coherent synthetic representation of world environments
  Designed for linking the interactive, free-play activities of participants in operational simulation exercises
  Synthetic environment is created through real-time exchange of data units between distributed, computationally autonomous simulation applications
  Simulators may be present in one location or may be distributed geographically
  Defined by the IEEE 1278™ family of standards
DIS defines standard network Protocol Data Units (PDUs)
  Syntax (data format) and semantics (rules) for data exchange and simulation interoperability

## Slide 16: Distributed Mission Operations Network

## Slide 17: Protocol Data Unit (PDU) Entity State V7 Example
Operating System network stack inserts PDU in datagram / packet for transfer on network

## Slide 18: DIS Documentation Relationships
Distributed Interactive Simulation standards, recommended practices, and related documents
IEEE Std 1278.1TM- 2012
Standard for DIS
—
Application Protocols
SISO-REF-010 Enumerations for Simulation Interoperability
IEEE Std 1278.2TM-
2015
Standard for DIS
—
Communications Services and Protocols
IEEE 1730TM-2010
Distributed Simulation Engineering and Execution Process
IEEE 1278.4TM-1997
Rec. Prac. for DIS —
Verification, Validation, and Accreditation
Current DIS V7

## Slide 19: DIS Documentation Relationships
Distributed Interactive Simulation standards, recommended practices, and related documents
IEEE Std 1278.1TM- 202X
Standard for DIS
—
Application Protocols
SISO-REF-010 Enumerations for Simulation Interoperability
IEEE Std 1278.2TM-
2015
Standard for DIS
—
Communications Services and Protocols
IEEE 1730TM-2010
Distributed Simulation Engineering and Execution Process
IEEE 1278.4TM-1997
Rec. Prac. for DIS —
Verification, Validation, and Accreditation
SISO-REF-030 Records for DIS Extensions
Future DIS V8

## Slide 20: Key DIS Concepts
No central computer controls the entire simulation exercise
  No single point of failure
Autonomous simulation applications are responsible for maintaining the state of one or more simulation entities
A standard network protocol is used for communicating ground truth data
  Changes in the state of an entity are communicated by its controlling simulation application
Perception of entities or events is determined by the receiving application
Dead reckoning algorithms are used to reduce communications processing
Stateful information is sent at a minimum heartbeat rate or when an error threshold is exceeded

## Slide 21: Key DIS Definitions
Simulation application:
  Executing software on a host computer that models all or part of the representation of one or more simulation entities and/or phenomena in the virtual world
  Receives and processes information concerning entities created by peer simulation applications through the exchange of DIS PDUs
  More than one simulation application may simultaneously execute on a host computer
Host Computer:
  Computer connected to simulation network that supports one or more simulation application
Simulation entity:
  An object in the synthetic environment that is created and controlled by a simulation application and affected by the exchange of DIS PDUs IEEE Std 1278.1TM-2012, Clause 3.1

## Slide 22: Key DIS Definitions (cont.)
Simulation exercise:
  An exercise that consists of one or more interacting simulation applications
  Simulations participating in the same simulation exercise share a common identifying number called the exercise identifier
  Simulations utilize correlated representations of the synthetic environment in which they operate
Simulation environment:
  The operational virtual environment surrounding the simulation entities
  Includes terrain, atmospheric, and oceanographic information
  Participants in the same DIS exercise will be using environment information that is adequately correlated for the type of exercise to be performed IEEE Std 1278.1TM-2012, Clause 3.1
1
1
1
1
1
1
9
9
9
DIS Net
Exercise ID
Exercise ID

## Slide 23: Network Considerations
PDUs are sent using broadcast or multicast addressing (one to many simultaneous)
Broadcast – every computer on the Local Area Network will receive the PDU
  Broadcast does not work on Wide Area Networks
  Some type of gateway is necessary at the LAN/WAN boundary to translate addresses
Multicast – every computer that has joined the multicast address group will receive the PDU, an efficient publish/subscribe mechanism
  Multicast on WANs is now possible, or use Generic Routing Encapsulation (GRE) to tunnel
PDUs are almost always sent using User Datagram Protocol (UDP/IP) transport
  Best effort – no guarantee of delivery, but networks can be designed to be very reliable
Unicast addressing with TCP/IP* (reliable) transport can be used, but uncommon
IEEE 1278.2™-2015 has details of design for real-time networks
* Transmission Control Protocol / Internet Protocol

## Slide 24: DIS PDUs by Families
Entity information/interaction
  Entity State – fundamental position and appearance of an entity
  Collision – convey details of tactically significant collisions
  Attribute PDU (new in V7) – adds PDU extensibility and partial updates
Warfare
  Fire – launch munitions or expendables, fire a gun
  Detonation – details of a weapons hit or explosion
  Directed Energy Fire (new in V7) – deposition of an energy weapon
  Entity Damage Status (new in V7) – damage fed back to firing entity

## Slide 25: DIS PDUs by Families (Cont)
Logistics
  Service Request
  Resupply Offer, Resupply Received, Resupply Cancel
  Repair Complete, Repair Response
Simulation Management
  Create Entity, Remove Entity
  Start/Resume, Stop/Freeze
  Acknowledge
  Action Request, Action Response
  Data Query, Set Data, Data
  Event Report, Comment
  Application Control (new in V8)

## Slide 26: DIS PDUs by Families (Cont)
Distributed Emission Regeneration
  Electromagnetic Emission – Radar and radar jamming, Infrared Jamming
  Designator (being renamed to Laser in V8) – all uses of lasers that are not a weapon
  Underwater Acoustics – Sonar, passive acoustic sensors
  IFF – Identification Friend or Foe, military and civilian transponders and interrogators
Communications
  Transmitter, Communications Node – state of radios and comm nodes (intercoms, phones)
  Signal – transfer of communications voice and data
Entity Management
  Aggregate State – entity grouping
  Transfer Ownership – hand off control of an entity to another simulator

## Slide 27: DIS PDUs by Families (Cont)
Synthetic Environment
  Environmental Processes – smoke, contrails, dust, obscurants, toxic chemicals
  Gridded Data – dynamic terrain, soil, vegetation, weather
  Point, Linear, and Areal Objects - dynamic objects such as craters, trenches, cultural features with damage
    Environment Objects are combining with Entities in DIS V8
  Weather based on Common Image Generator Interface (CIGI)(new in V8)
Information Operations (new in V7)
  Simulate the use of electronic warfare, computer network attack, military deception to influence or disrupt decision making
  Information Operations Action – transmits predicted effects of an attack
  Information Operations Response – reports actual effects

## Slide 28: World Coordinates
a = major axis
b = minor axis
X,Y,Z = GCC position
Φ = latitude
λ = longitude
Z
North Pole
Prime Meridian
X
Y
a
a
b
Y
Z
X
r
p
Equator
Φ
λ
Geocentric Cartesian Coordinates
  Position and Orientation
WGS-84 elliptical Earth model
Units in meters and radians
DIS V8 will clarify that geoid gravity model is not included
  Mean Sea Level is modeled as the WGS-84 ellipsoid
  Altitude is height above ellipsoid

## Slide 29: Entity Type Identification
Hierarchical designation of Entity Type
Enumerations are listed in SISO-REF-010
  Over 20,000 entity types
ENTITY TYPE RECORD | 
Entity Kind | 8-bit enumeration
Domain | 8-bit enumeration
Country of design | 16-bit enumeration
Category | 8-bit enumeration
Sub-Category | 8-bit enumeration
Specific | 8-bit enumeration
Extra | 8-bit enumeration

## Slide 30: Examples of Type Enumerations
 | Kind | Domain | Country | Category | Sub-Category | Specific | Extra
F-35A CTOL | 1 | 2 | 225 | 1 | 12 | 1 | -
Platform
Air
USA
Fighter
F-35
A
Kind
Platform
Munition
Life Form
Environmental
Cultural feature
Supply
Radio
Expendable
Sensor/Emitter
Notes: Kind – 1 – Platform
Domain – 2 – Air
Country – 225 – USA
Category – 1 – Fighter/Air Defense
Sub-Category – 12 – F-35
Specific – 1 – F-35A CTOL

## Slide 31: Examples of Type Enumerations
 | Kind | Domain | Country | Category | Sub-Category | Specific | Extra
F-35C Naval | 1 | 2 | 225 | 1 | 12 | 2 | -
Platform
Air
USA
Fighter
F-35
C
Kind
Platform
Munition
Life Form
Environmental
Cultural feature
Supply
Radio
Expendable
Sensor/Emitter
Notes: Kind – 1 – Platform
Domain – 2 – Air
Country – 225 – USA
Category – 1 – Fighter/Air Defense
Sub-Category – 12 – F-35
Specific – 2 – F-35C NAVAL

## Slide 32: Examples of Type Enumerations
 | Kind | Domain | Country | Category | Sub-Category | Specific | Extra
AA-10C Alamo | 2 | 1 | 222 | 1 | 10 | 3 | -
Munition
Anti-Air
Russia
Guided
AA-10
C
Kind
Platform
Munition
Life Form
Environmental
Cultural feature
Supply
Radio
Expendable
Sensor/Emitter
Notes: Kind – 1 – Platform
Domain – 2 – Air
Country – 225 – USA
Category – 1 – Fighter/Air Defense
Sub-Category – 12 – F-35
Specific – 2 – F-35C NAVAL

## Slide 33: Entity Instance Identification
Combination of 3 numbers identify individual instances of entities and objects
  Exercises assign site numbers
  Sites assign numbers to simulations at the site
  Sims assign entity numbers
Site | 16-bit unsigned integer | 14 (AFRL)
Application | 16-bit unsigned integer | 100 (NICE)
Entity | 16-bit unsigned integer | 1(1 to N)
14:100:1
14:100:2
14:100:3
14:100:4

## Slide 34: Dead Reckoning Basics
Entity sender publishes state and information needed to predict state over time
  Velocity (rate of change), acceleration
Receivers dead reckon (extrapolate) between updates
Sender also extrapolates its own entity to know what receivers see
New PDU issued when error between truth and extrapolation exceeds a threshold
Dead reckoning solves three problems
  Significantly reduces the PDU issuance rate, requiring less network bandwidth
  Compensates for network latency
  Corrects position error due to unsynchronized simulation frame times

## Slide 35: Fixed Update vs Dead Reckoning
10 Updates
3 Updates

## Slide 36: Dead Reckoning and Smoothing
Entity sends update when error > threshold (Error checked in each of 3 axes)
If any exceeds threshold, send update
Receiver extrapolates between updates
Spatial jump at update is smoothed over the next few seconds (Velocity error)
Green Line: Internal “truth” model (sender)
Red Line: Dead Reckoned (extrapolated) model
(sender and receiver)
Blue Line: Smoothing model (receiver)
Error 1 meter

## Slide 37: Positional Dead Reckoning, “World” DRA 2-5
Dead Reckoning Algorithm 2 and 3
  P = Pupdate + VΔt (1st Order)
  where Δt is time since last update
Dead Reckoning Algorithm 4 and 5
  P = Pupdate + VΔt + ½AΔt2 (2nd Order)
Extrapolates to a parabolic path through space
Parabolic
Linear

## Slide 38: Positional Dead Reckoning, “Body” DRA 6-9
DRA 6-9 use rotation rate and body coordinate velocity and acceleration to achieve better prediction of turning vehicles
Extrapolates to a circular or spiral path through space
  Math is more complicated and not used as much as DRA 2-5
  But it performs much better in some situations, should be used more
No change in DIS V7 but errors in the math formulas were fixed
See E.7.3 in IEEE Std 1278.1TM-2012
Pos = Pos0 + [R0]b->w([R1]*Velb + [R2]*Acelb)
Circular

## Slide 39: Rotational Dead Reckoning
DRA 2, 5, 6, 9 have no rotational dead reckoning
DRA 3, 4, 7, 8 all have the same rotational DR formula
  [RD]w->b = [DR][R0]w->br
  Rotation rates are required
Entity State PDU: rotation rates are given as a vector ω in body coordinates
  Direction of vector is axis of rotation
  Magnitude |ω| is rate of rotation about axis
Receivers extrapolate orientation by rotating an entity about the axis by angle |ω|Δt, used to form the [DR] matrix
There is no acceleration in this math
  (1st Order)

## Slide 40: Dead Reckoning for DIS V8
DIS V8 makes distinction between “algorithm” and “formula”
Position DR formulas renamed
  Parabolic Formula (formerly World algorithms 2-5)
  Circular Formula (formerly Body algorithms 6-9)
Only one algorithm for moving entities
  Algorithm chooses the best DR formula
  Now called the Combined Parabolic Circular (CPC) Dead Reckoning Algorithm
  CPC algorithm enumeration is 10

## Slide 41: Formula Results Comparison
This shows a 500 knot turning aircraft with 20 seconds of extrapolation
Circular vs Parabolic is apparent
  ~1200 meter error
See SISO paper
  2019-SIW-034
CPC algorithm in DIS V8 chooses the best formula
  Circular if applicable
  Parabolic otherwise

## Slide 42: CPC DRA Code Implementation
A reference code implementation of the CPC DR Algorithm is available in SourceForge, Version 1.0 matches DIS V8 Draft 1
  https://sourceforge.net/projects/dsu/
  Written in C for easy use by multiple languages
  Implements both position extrapolation formulas
  Implements rotation extrapolation
  Includes the improved orientation threshold method
Coordinate Conversion code (Lat/Lon/Alt to Earth Centered Earth Fixed) included
  Not needed for CPC DRA, but helps in testing it
Have converted the C-Code to Java in 3 days

## Slide 43: Consequences of DR
Less Bandwidth Required
Updates may occur at any time, not at fixed time intervals
Data rate is variable, higher when A/C are performing maneuvers, and lower when flying straight and level, leading to variability in traffic and therefore required bandwidth is more difficult to determine
Stationary entities only update at heartbeat period (30-120 Stationary ≈ 1 moving)
Number of entities is a lousy measure of network bandwidth!
Latency in sending or processing an update will result in positional errors larger than the threshold value
If thresholds are checked at a low rate the errors are larger than the threshold value

## Slide 44: Heartbeats and Timeouts
PDUs are categorized as stateful (persistent info) or transient (one-time event)
Stateful PDUs are issued at least at the minimum heartbeat rate
This solves two problems
  Late joiners get the full state of the exercise within one heartbeat period
  If a PDU is dropped due to network error, the next update arrives within a heartbeat period
The default heartbeat period for each PDU type is listed in the DIS standard
  Heartbeats vary from 5 to 60 seconds depending on PDU type and conditions
  Exercises can change heartbeat periods by agreement
Receivers keep a timeout timer for each entity
  If no information has arrived within 2.4 heartbeat periods, the entity is discarded
  Solves the problem of simulation crashes or if the entity deactivation PDU is dropped

## Slide 45: Techniques to Solve Network Issues
Network latency and jitter – due to speed of light and network processing time
  Dead Reckoning compensates for position error due to network delay and frame differences
  Issuance and receipt rules mitigate effects of latency
    e.g., sender transmits that detonation or collision hit target, receiver determines damage
Bandwidth – both the size and number of PDUs consume network resources
  Efficient PDU design with a binary format to send the minimum data necessary
  PDU sent only when a parameter change exceeds a threshold value
  Dead Reckoning - TSPI data sent every few seconds instead of every simulation frame
  Design for reduced data, e.g. receiver lookup table with a single index in PDU
Network Reliability – PDUs get lost, it’s rare but it happens
  Efficient PDU design helps prevent overloading networks, reduces dropped data
  State data repeated at least at regular heartbeat interval

## Slide 46: DIS 2012 (V7)
New and improved rules vs V5/6
  Lessons learned from over 15 years of use
Additional Annexes and extensive clarifications
The 2012 standard is 747 pages
The 1995 and 1998 standards combined were 330 pages
V7 Uses former padding fields to maintain compatibility with Versions 5/6
  V7 sims can add new information, old sims ignore it
Rules for interoperability between Version 5/6 and V7 are defined
  Mixed version exercises are allowed
  A single sim may issue version 5, 6 and 7 PDUs
IFF
  Mode 5 and Mode S added
Five new PDUs (see DIS PDU by Families slides)

## Slide 47: Other Simulation Networking Standards
Test and Training Enabling Architecture (TENA)
  Connects systems on a live training range – uses US Government owned middleware
Common Training Instrumentation Architecture (CTIA)
  Connectivity for live soldier training
Compressed DIS (SISO-STD-023.2024) (For DIS V7)
  New SISO standard that compresses DIS data to connect over low bandwidth networks/busses (e.g. LVC), designed to be easily translated to/from regular DIS
HLA – High Level Architecture
  IEEE Std 1516™ High Level Architecture (HLA)
  A general-purpose network solution to connect any type of simulation
  Includes time management services for discrete event simulation
  Private company Run Time Interface (middleware)

## Slide 48: An LVC Exercise with DIS/C-DIS/HLA
Manned Flight Simulator (MFS)
SAIL
Live
F/A-18E/F
Virtual
F-35
Pax RRU
Constructive Weapons Fly-out
Constructive Threats
Atlantic Test Range (ATR)
Live
EA-18G
Virtual
MH-60R
Westover RRU
SLATE Ground Station
& Link Inject to Live (LITL)
LEGEND
Blue Live
Blue Virtual
Red Constructive
5GATW
NCTE
SDREN
Virtual
F/A-18E/F
(F/A-18 Cockpit Surrogates)
(F-35 Effects Based Sim)
(LCTs)
NAS JAX
Virtual
MH-60R
(BFTT)
Live Guised Red Air
NAVAIR Public Release 2021-394 Distribution Statement A - "Approved for public release; distribution is unlimited"
C-DIS
DIS
HLA

## Slide 49: How HLA is Different than DIS
The High Level Architecture standard has three parts
  Framework and Rules
  Application Programming Interface (API) specification
  Object Model Template specification
    Template for creating a Federation Object Model (FOM)
HLA provides publish/subscribe services for distributing data and managing time
  But doesn’t specify what that data is (syntax) or rules of using it (semantics)
Each federation of simulations is responsible for defining its FOM
  Typically, a consensus design among all the simulations that are being federated
The Run-Time Infrastructure (RTI) is middleware that implements the HLA API
  The network protocol is designed by the RTI developers, not standardized

## Slide 50: How HLA/TENA are Different than DIS
SIM 1
SIM 2
Know format
PDU over Ethernet
SIM 1
SIM 2
Unknown Format over any Transport
API
API
HLA & TENA
DIS
RTI
Middleware
RTI
Middleware
Publish/Subscribe
Multicast
Publish/Subscribe
Vendor Specific
Version Specific

## Slide 51: RPR FOM
LVC must be standardized well beyond the HLA spec
  Reference FOMs were conceived as the solution for this
SISO developed the Real-time Platform Reference FOM (RPR FOM)
  SISO-STD-001
Converts DIS PDU contents into an HLA FOM
  SISO standard is the Guidance, Rationale, and Interoperability Modalities (GRIM) 2015
  Still need the DIS standard for the semantics, i.e., the rules for using the FOM
    For example, the DIS is the only standard that defines Dead Reckoning, weapon interactions, etc.
  RPR FOM Versions
    RPR FOM 2 (2015) matches DIS V6
    RPR FOM 3 (2025?) matches DIS V7
    RPR FOM 4 (202X) is planned for DIS V8

## Slide 52: HLA-TENA-DIS Translation
 | DIS | HLA | TENA
Interface | Ethernet | API/RTI | API/RTI
Transport | Ethernet Known Message formats | Not Defined | Not Defined
Syntax | DIS | FOM | OM
Semantics | DIS | FOM | OM
Translation between DIS/HLA/TENA requires equivalent FOM/OM (RPR) representations to DIS
Translatable
RPR
RPR

## Slide 53: HLA-TENA-DIS Translation
 | DIS | HLA | TENA
Interface | Ethernet | API/RTI | API/RTI
Transport | Ethernet Known Message formats | Not Defined | Not Defined
Syntax | DIS | FOM | OM
Semantics | DIS | FOM | OM
Translation between DIS/HLA/TENA requires equivalent FOM/OM (RPR) representations to DIS
NOT Translatable

## Slide 54: Tutorial Outline - Future
Goal - LVC
The Past
  History of networked simulation
The Present
  The IEEE 1278TM DIS standard and how it is developed
  Key definitions and concepts
  Function and organization of DIS Protocol Data Units
  Technical details of providing high-fidelity real-time information exchange
  Improvements from the 1995 to the 2012 DIS (DIS V7) standards
The Future: The development of the next version of the DIS (DIS V8)

## Slide 55: Currently in Development - DIS V8
We have learned a lot in the 30 years since DIS was originally developed
Computers are way faster, graphics way better, much higher fidelity is possible
We are running out of tricks to extend the protocol and maintain compatibility
The time is right for DIS V8 to have a new generation PDU design
This requires breaking PDU compatibility with previous versions of DIS
  V8 is being designed for “Translation Compatibility” so that run-time translation to/from V7 is practical, although not necessarily trivial

## Slide 56: Consistent PDU Design
Every PDU type will have this basic format:
  Header
  Fixed Body
  Any number of Extension Records – allows added fidelity & extensibility
The fixed body has the basic fidelity information
  Fixed in format and length, no variability allowed
  Quick initial processing by receiver for interest management
Extension Records allow additional information/fidelity

## Slide 57: Example DIS V8 Entity State PDU
Fixed Header
Fixed Body
Variable
Extension
Records

## Slide 58: PDU Extensibility
DIS V8 breaks direct compatibility to allow more extensibility
DIS V8 users can add custom extension records to PDUs to meet their unique needs
We expect many extension records in the future to support higher fidelity
  Basic required/existing information extension records documented in IEEE1278.1
  SISO-REF-030 documents new standardized extension records
    Expected to be updated yearly using the SISO standards process
  Range of Extension Record IDs reserved for user defined custom extension records
  Users/groups can define proprietary or classified custom extension records and document them internally rather than putting them in SISO-REF-030

## Slide 59: Machine Readable Syntax Definition
Clean PDU design enables formal language to describe PDU format
<DISsyntax xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
xsi:noNamespaceSchemaLocation="DISsyntax.xsd">
<PDU name="Entity State" PDUType="1" protocolFamily="1" baseLength=“96">
<FixedRecordField name="Header" type="HeaderRecord"/>
<FixedRecordField name="Entity ID" type="EntityIdentifierRecord"/>
<EnumField name="Force ID" type="enum8" enumTableUID="6"/>
<EnumField name="Dead Reckoning Algorithm" type="enum8" enumTableUID="44"/>
<FixedRecordField name="Entity Type" type="EntityTypeRecord"/>
<AdaptiveRecordField name="Entity Appearance" type="EntityAppearanceRecord"
discriminant="Entity Type" field1=“Entity Kind" field2="Domain"/>
<AdaptiveRecordField name="Capabilities" type="CapabilitiesRecord"
discriminant="Entity Type" field1=“Entity Kind" field2="Domain"/>
<FixedRecordField name="Entity Location" type=“WorldCoordinatesRecord"/>
<FixedRecordField name="Entity Orientation" type="EulerAnglesRecord"/>
<FixedRecordField name =“Entity Marking” type="EntityMarkingRecord"/>
<NumericField name="Padding" type="uint32"/>
<NumericField name="Padding" type="uint16"/>
<ExtensionRecordSet>
<CountField name="Number of Extension Records" type="uint16"/>
<ExtensionRecordFields/>
</ExtensionRecordSet>
</PDU>
</DISsyntax>
  Enables auto code generation
    Wireshark dissectors
    Marshalling code

## Slide 60: Interest Management
Interest Management reduces sim workload by eliminating unwanted PDUs
  Send-side interest management possible using multicast addressing
    Sent only to simulators that have subscribed to that multicast address
  Receive-side interest management is commonly called filtering
    Software filters (discards) PDUs as efficiently as possible (Most Common)
V8 PDU design rules promote interest management
  Put interest management information in fixed body rather than optional variable records
IEEE Std 1278.2TM-2015 DIS Communication Services and Profiles
  Formalized terminology for DIS Interest Management
  Explains how to multicast including over a WAN

## Slide 61: More Improvements in DIS V8
Support for AESA radar and advanced jamming (see 2023-SIW-001)
  Re-design of EE PDU, 12 new extension records for high fidelity radar and jamming
New SIMAN Application Control PDU
  Simulator device discovery, exercise control, and simulator health monitoring
Communications improvements
  Better definition of radio vs non-radio communication (intercom, telephone, etc.)
  Transmitter and Communications Node PDUs better align with Information Operations PDUs
Gridded Data PDU overhauled to simplify use & support weather
New Weather PDU easier to define conditions that are not on a regular grid
  Patterned somewhat after CIGI (SISO-STD-013-2024) weather
There will be a Compressed DIS Version for DIS V8

## Slide 62: Yet More Improvements for DIS V8
Better, simpler timestamp
  64-bit integer, microseconds since Jan 1, 1970, no rollover
Combine entities and environmental objects
  Point, Linear, Areal objects now use Entity State PDU
  Avoids duplication between the old environmental object types and entity types
New Multiple Entity records to update a very large number of entities efficiently
  Large exercises of 100K to a million entities envisioned
  DIS V7 uses up to 41X PDUs 4X bandwidth
Single Dead Reckoning Algorithm that works for all moving entities
New IFF Interactive PDU for higher fidelity IFF interrogation
Will reduce PDU count from 72 to 43 (40% reduction)

## Slide 63: Status of DIS V8
8 years of work by Product Support Group (PSG) within SISO
Product Development Group (PDG) stood up in 2021, starting the IEEE drafting process (4-year time limit)
Draft 3 published in April 2024 – about 90% of content in this draft
Draft 4 planned by end of 2024 – about 98% of content
  Roughly 500 pages, all sections of the standard have near-final content
  All 43 PDUs, many extensions records, 4 annexes
  About 200 comments on Draft 3, most resolved and incorporated into Draft 4
Remaining work
  Comment review of Draft 4 and resolution of all comments
  Create Draft 5, ballot to determine if it is ready to submit to the IEEE process
  IEEE balloting, comment resolution, and publishing

## Slide 64: Obtaining the DIS Standard
The DIS standard can be purchased directly from IEEE
Many companies have access to IEEE products for their employees
SISO members have access to IEEE standards developed by SISO
  Annual membership is $95, less than the cost of an IEEE standard publication
  Or, 1 year of membership is included in the SISO workshop registration fee
Any SISO member can join the DIS Product Development Group (PDG), get access to the DIS V8 drafts, and participate creating the standard and balloting

## Slide 65: What You’ve Learned
The problem DIS solves
The capabilities of Live-Virtual-Constructive (LVC) Simulation Networking
The history of DIS
  How it has evolved
  Future direction
Key Definitions and Concepts
Technical details of
  The type of information conveyed by DIS
  Techniques for distributing real-time high-fidelity simulation data

## Slide 66: Questions?
Image by RHA
Image by pixabay
Image by RHA
Graphic by RHA
Image by pixabay
Image by RHA