## Slide 1
Evolution of RF Signal Visualization from Spectrum Analyzers to Augmented Reality – Topic #24T49
Jad Meouchy, BadVR, Inc.
Suzanne Borders, BadVR, Inc.

## Slide 2: Tutorial Overview
5 min | Introduction and Learning Objectives
10 min | Background on Radio Frequencies
10 min | Traditional Signal Visualization
30 min | Immersive Signal Visualization
10 min | Summary and Conclusions
5 min | Acknowledgements
10 min | Q&A
2

## Slide 3: Learning Objectives
Understand challenges of existing tools for radio signal analysis and visualization
Discover new AR/VR & AI immersive technologies for signals intelligence, electronic warfare, and communications networking
Develop technical insight into applying new tools in both real and simulated environments
Assess future impact of 3D signal visualization on modeling, simulation, and training

## Slide 4: Terminology and Concepts
Fourier Transform – Mathematical function that converts time-domain signal data into frequency-domain magnitudes and phases
Modulation/Demodulation – Encoding and extracting information from a carrier wave
RSSI – Received signal strength indication, a measurement of received power
TSCM – Technical Surveillance Countermeasures, colloquially understood as “bug hunting”
Immersion, AR, VR – a collection of holographic technologies including Augmented Reality and Virtual Reality
Metaverse – Umbrella buzzword representing the next generation of 3D computing and connectivity
SIGINT – Signals Intelligence, intelligence gathering by interception of signal communications between people
Spatial Anchors – Specific locations in virtual space that persist in the real world

## Slide 5
The Challenge
Complicated
Cumbersome
Distracting
Slow
Traditional modeling and visualization tools are no longer suitable to address the scale and complexity of modern signals

## Slide 6: Security Implications
Wireless is a primary attack vector
Backdoors are hidden inside chip firmware by foreign manufacturers
100’s millions people affected by breaches
Defense industry spends billions each year for SIGINT, EW, and wireless security
Secure facilities typically restrict wireless
Meeting rooms are shielded from RF

## Slide 7: Impact
Training
Reduce education burden for learning RF
Increase access to signals awareness
Modeling
AI/ML-powered radio propagation
Ideation and predictive analytics
Simulation
Reproduction of complex signal fields
Comms systems planning and testing

## Slide 8: Immersive Signal Visualization

## Slide 9
Background on Radio Frequencies

## Slide 10: Introducing The Spectrum
The Electromagnetic Spectrum
Hz
Hz

## Slide 11: Radio Frequencies
TeraSense

## Slide 12: Notable Moments in RF History
First television broadcast
NAVSTAR 1
GPS satellite
Digital broadcasting gains popularity
5G, smart cities, self-driving cars
1928
1890s
1978
1990s
Present
1934
Testing radio transmissions
FCC is formed

## Slide 13: DoD Use Of Radio Spectrum

## Slide 14: Satellite Frequency Bands

## Slide 15: Starlink Example

## Slide 16: Regulating The Spectrum
Federal Communications Commission (FCC)
Assign operating ranges for civ/mil
Certify RF-emitting devices
Prevent interference

## Slide 17: Anechoic Chambers
Fully shielded room with RF-absorbing wall materials
Measure antenna gain, efficiency, and radiation pattern
Controlled evaluation of RF emission
Ensure compliance with standards

## Slide 18: Examples of Lab Testing Reports

## Slide 19: Common Laboratory Equipment
Spectrum Analyzer
Oscilloscope
Graphical indication of voltage change
Plot of 1D signal over time
Measure signal power across a freq range
Display amplitude over signal frequency

## Slide 20: Portable Analysis Tools
Field tools are made portable with mounted screens and audio outputs

## Slide 21
Traditional Signal Visualization

## Slide 22: 1D Signal Visualization
High information density
Frequently on laptops and tablets
Continuous scrolling top to bottom
Low information density
Small display sizes
Needs logging
Oscilloscope
Waterfall Display

## Slide 23: 2D Signal Visualization
Reflects real world space
Typically extrapolated
Heatmaps represent X-Y samples and projected values of signal strength
“Can you hear me now?” only shows outdoor coverage
***Shows highest speeds; better coverage may be available at slower speeds

## Slide 24: 3D Signal Visualization
Adds Z dimension
Performs advanced modeling
Uses graphics and gaming engines
Important to keep up w/UAS tech progress

## Slide 25: Antenna Radiation Patterns
Graphic of the directional (Angular) dependence of the strength of the radio waves from the antenna or other source, power based on distance

## Slide 26: Real-World Behavior
All objects, manufactured and natural, interact with wireless signals, especially in dense urban environments

## Slide 27: Interference
Modern steel/concrete/tinted glass buildings are “radio opaque”
Material density causes attenuation
Trees and foliage can block RF
Metallic surfaces can cause counterintuitive radio reflections
Human bodies interfere also; remember “antenna gate”
Anderson (2017)

## Slide 28: Channel Congestion
There are a fixed number of Wi-Fi, Bluetooth, Cell, etc. channels
With too many connected devices, channels become saturated
Net result is denial of service
Infrastructure never designed volume
IoT is already a worst-case scenario

## Slide 29: Challenges of 5G & LEO
 | 5G | LEO
Infrastructure | Build 1M small cells and base stations | Manufacture and launch 30K satellites
Spectrum | Businesses fight for access to frequency bands | Managing constellations is highly technical
Interference | mmWave blocked by foliage and buildings | Weather, handover, doppler shift, coexistence
Latency | Needs edge compute resources | Large distances, must obey laws of physics

## Slide 30: Signals Intelligence (SIGINT)
Ability to seize, retain and exploit the spectrum is critical to battlefield superiority
SIGINT & EW capabilities are being added to manned and unmanned vehicles

## Slide 31: Resilient Training Environments
LVC Simulation
Everyone expects reliable comms fabric
Must create testing/sims to prepare for degraded / disconnected activity
Model jamming, injection, and cyberattacks
Support both BLUFOR and OPFOR endeavors (comms, intel, EW, etc.)
EXAMPLE: RF mesh network with connected ATAK during live training

## Slide 32
Immersive Signal Visualization
Definition and Impact

## Slide 33: Immersive / AR / VR / Metaverse

## Slide 34: Augmented Reality (AR)
Overlay holograms into real-world objects and environments
Merge the real and the virtual using sensors and trackers

## Slide 35: Examples

## Slide 36: Spatial Awareness
Spatial mapping and computational geometry understand your physical space to provide situational awareness

## Slide 37: Equipment
Popular current and upcoming AR headsets
Magic Leap 2
Qualcomm (Reference Design)
Microsoft HoloLens 2
Meta Orion

## Slide 38: Device Pros and Cons
Weaknesses
Limited FOV
Durability & brightness
High hardware cost
Opportunities
Size and weight
Integrated biometrics
AI/ML assistants
Strengths
Good battery life
Wireless connectivity
Spatial awareness

## Slide 39: Increased Adoption
Pandemic sped adoption of immersive technologies
Enhanced use in education, training, virtual events, etc.
Example: US Army immersive combat training in Synthetic Training Environment
Ball et. Al, 2021, World Economic Forum, 2022

## Slide 40: AR Signal Visualization
Early mainstream implementations of AR signals

## Slide 41: AR Signal Visualization (cont’d)
Research focusing on AR, spatial mapping and ray tracing channel prediction algorithms to visualize wireless channels in real-time

## Slide 42
Immersive Signal Visualization
Design & Development

## Slide 43: Design Considerations
Hardware Display
Field-of-view (FOV) limitations
Indoor/outdoor affects holograms
Hands-free w/ gesture and voice

## Slide 44: Design Considerations (cont’d)
User Interface
Ergonomics of interactables
Direct interaction with objects versus onscreen controls
Colors, shapes, and symbology
Multi-User interactions

## Slide 45: Example of 3D Spatial Signals
Intuitive perception of Relative Signal Strength Indicator (RSSI)

## Slide 46: Interaction Methods
Enables users to access contextual information with simple movements and gestures

## Slide 47: Holograms
To skeuomorphism or not?
Density of information
Sizing of symbols

## Slide 48: Example: Direction Finding
Find the strongest emitting device
Show relative distance and bearing, for navigation

## Slide 49: Example: HUD
Heads-Up Display
Persistent information
Track head angle
Clear center area

## Slide 50: HUD Implementation
View seen through lens of heads-up display

## Slide 51: Example: Relative Positioning
Show user in context with all available data,
track according to a single reference point

## Slide 52: User Engagement
Imbue tracked hands with surface modeling to “feel” wireless signals
Augment user’s senses with surface patterns and a “slicing” tool
Cut into 3D RF model volume to perform cross-section analysis

## Slide 53: Integration of Sensor Peripherals
Ubertooth One
RTL-SDR
Enterprise SDR

## Slide 54: Common Operating Picture
Paint simulated signals and effects into a mission planning interface

## Slide 55: Bridging 2D to AR

## Slide 56: Spatial Signal Simulation
Spatial representation of observable signals
Highly dynamic indoor environment
Used for modeling networks
Signal source

## Slide 57: Model Validation
On-site signal collection in network telecoms lab
Walk along path with device away from signal source
Collect data on position, direction and signal strength

## Slide 58: Affiliation With AI/ML
On-the-fly control and interaction with the AI/ML algorithms
to assist the user in their quest for discovering insight

## Slide 59: Defensive vs. Offensive
Find transmitting devices inside SCIF
Identify and locate target device, disable
Model EW jamming range and source
Detect incoming drones

## Slide 60: Testing and Tuning
Only 3-5 min hands-on training
Swift detection of random spectrum attack
Full physical discovery of source attack device

## Slide 61: Operational Deployment

## Slide 62: Best Practices
Leverage real-world concepts
Draw inspiration from media
Add visual/auditory feedback
Embrace ergonomics
Minimize text

## Slide 63
Summary and Conclusion

## Slide 64: Future Work
Smart Cities
IoT sensor networks
5G, 6G, 7G, and beyond
Construction preplanning
Transportation
Aviation systems
Connected mobility
Traffic smart metering
Health
Safe training
Remote surgery
Extrasensory perception
Alharbi et. Al. (2019)

## Slide 65: Additional Signals
Chemical, biological, radiological and nuclear (CBRN) sensor data
Software Defined Radios (SDR)
Ubertooth/Bluetooth devices
Medical devices
Utilize AI/ML
NIH (2022) , Wikimedia (2005)

## Slide 66: Into Space
Space Defense
Improve modeling effectiveness
Anti-Access/Area denial strategies target RF communications to inhibit movement
Jamming of signals for low-power satellites, and counter-jamming
Reduce freedom of action
Airbus

## Slide 67: Takeaway
Immersive technology will enhance modeling of signals in real world
Cumbersome, focused on screen instead of scene, 1D/2D
Preserve use of hands, ​maintain situational awareness,​ expand comprehension in 3D

## Slide 68: Revisit Goals
Confirm Learning Objectives
Understand challenges of existing tools for radio signal analysis and visualization
Discover new AR/VR & AI immersive technologies for signals intelligence, electronic warfare, and communications networking
Develop technical insight into applying new tools in both real and simulated environments
Assess future impact of 3D signal visualization on modeling, simulation, and training

## Slide 69: Bibliography
Airbus. https://airbusus.com/laser-communication/
Anderson (2017). “Reduce EMI to Improve Radio Range”. https://medium.com/tempo-automation/improve-radio-range-by-lowering-emi-dac7135f77f9
Alharbi et. Al. (2019). “Roles and Challenges of Network Sensors in Smart Cities”. https://iopscience.iop.org/article/10.1088/1755-1315/322/1/012002/pdf
Altium (2017). “How to Choose a Test Lab for FCC Certification of IoT Products”. https://www.altium.com/subscription
Antenna Test Lab. “What is an Anechoic Chamber?”. https://antennatestlab.com/antenna-education-tutorials/what-is-an-anechoic-chamber
ARSensor. https://play.google.com/store/apps/details?id=com.ken.arsensor&hl=en_US&gl=US
ARwave. https://apps.apple.com/us/app/ar-wave-visualization-of-wifi/id1470866212
Army Futures Command (2022). “Synthetic Training Environment offers multi-dimensional combat preparation”. https://www.army.mil/article/254005/synthetic_training_environment_offers_multi_dimensional_combat_preparation
Ball et. Al. (2021). “Virtual reality adoption during the COVID-19 pandemic: A uses and gratifications perspective”. https://www.sciencedirect.com/science/article/pii/S0736585321001672
BAE. "Unmanned SIGINT/Electronic Warfare". https://www.baesystems.com/en/product/unmanned-sigint-electronic-warfare
Bloom (2001). “What is Bloom’s Taxonomy”. https://bloomstaxonomy.net/
FrontierUS. https://frontiercomputercorp.com/specifying-the-right-antenna/

## Slide 70: Bibliography (cont’d)
HouseTechLab. “Difference between spectrum analyzer and oscilloscope” https://housetechlab.com/difference-between-spectrum-analyzer-and-oscilloscope/
iBWave. https://info.ibwave.com/augmented-reality/
Koutitas et. Al. (2020). “In Situ Wireless Channel Visualization Using Augmented Reality and Ray Tracing”. https://www.mdpi.com/1424-8220/20/3/690/htm
McKinsey (2018). “The road to 5G: The inevitable growth of infrastructure cost”. https://www.mckinsey.com/industries/technology-media-and-telecommunications/our-insights/the-road-to-5g-the-inevitable-growth-of-infrastructure-cost
NBC (2015). “App Visualizes Radio Waves From Cell Towers, Satellites Around You”. https://www.nbcnews.com/tech/innovation/app-visualizes-radio-waves-cell-towers-satellites-around-you-n469781
NIH (2022). “Electric & Magnetic Fields”. https://www.niehs.nih.gov/health/topics/agents/emf/index.cfm
NTIA (2016). https://www.ntia.doc.gov/files/ntia/publications/january_2016_spectrum_wall_chart.pdf
Pieper (2018). “Introducing WiFiman”. https://blog.ui.com/2018/12/11/introducing-wifiman/
RF Page (2021). “What are Radio Frequency bands and its uses?”. https://www.rfpage.com/what-are-radio-frequency-bands-and-its-uses/
Rockwell Collins (2016). "LVC demonstration completed by Rockwell Collins in France, U.K., and U.S." https://militaryembedded.com/radar-ew/test/lvc-demonstration-completed-by-rockwell-collins-in-france-u-k-and-u-s
TeraSense. “Radio Frequency Bands”. https://terasense.com/terahertz-technology/radio-frequency-bands/

## Slide 71: Bibliography (cont’d)
Wikimedia (2005). https://commons.wikimedia.org/wiki/File:An_instructor_at_the_Defence_NBC_Centre_operates_the_Manportable_Chemical_Agent_Detector_MOD_45148143.jpg
Wikitude (2021). “How to Apply UX Design Principles in Augmented Reality”. https://www.wikitude.com/blog-ux-design-for-augmented-reality/
World Economic Forum (2022). “Immersive Media Technologies: The Acceleration of Augmented and Virtual Reality in the Wake of COVID-19”. https://www3.weforum.org/docs/WEF_Immersive_Media_Technologies_2022.pdf

## Slide 72: Contact Info
BadVR, Inc.
10312 Norris Ave. Ste. D​
Pacoima, CA 91331
(833) 600-DATA
Jad Meouchy, CTO​
jad@badvr.com
Suzanne Borders, CEO​
suzanne@badvr.com