## Slide 1
Harnessing Physiology for Peak Human Performance in Training and Simulation
Audrey Zlatkin, Ph.D., Design Interactive, LLC.
Charles Rowan, Ph.D., Interim Director, The MOVES Institute at the NPS
Victoria Olko, Design Interactive, LLC.

## Slide 2: What You’ll Learn
Learners will remember and understand how physiological measurements can be beneficial to training and simulation environments by providing at least three example use cases.
Learners will be able to evaluate physiological data test plans in accordance with best practices.
Learners will be able to apply the eight recommended steps of integrating physiological sensing. ​
1
2
3
LO = Learning Objective

## Slide 3: Tutorial Overview
Harnessing Physiology for Peak Human Performance in Training and Simulation
Current State of the Field
Areas of Opportunity
Recommended Approach & Best Practices
Tools to Enable This Process
Take Home Messages
Q&A
3

## Slide 4: Speakers
Victoria Olko, B.S.
Research Associate II at Design Interactive
Charles Rowan, Ph.D.
Interim Director, The MOVES Institute at the NPS
Audrey Zlatkin, Ph.D.
RDT&E Portfolio Manager at Design Interactive
4

## Slide 5: Current State of the Field
Areas of Opportunity
&
LO 1
Use Cases for Training & Simulation
Barriers to Success​
Definitions of Physiological Monitoring
Significance to Training and Simulation
5

## Slide 6: Defining Physiological Monitoring Options
Who: | Clinical, Academia, Industry, Military
What: | Individual On-body Sensors, Group Monitoring
When: | Real-time, Post Processing, Longitudinal
Where: | Clinical Settings, Research, Training, Operations
Why: | Health Status, Performance Level, Training Support
How: | On-body, Off-body, Multimodal Devices
LO 1

## Slide 7: Defining the Training Ecosystem
National Defense Magazine
Army Technology
Argon Electronics
Who: | Academies, School Houses
What: | Basic Training, Career Training, Cognitive Skills, Physical Abilities
When: | Throughout Careers
Where: | Field, Outdoor, Indoor, Simulators
Why: | Proficiency, Readiness, Amplifying Human Talent and Performance
How: | Courses, Practice, Assessments
Modern War Institute
Alessi 1988
LO 1

## Slide 8
Achieve intimate HMI to increase coordination and collaboration between humans and training systems
Tying Human and Training Together
Improve Training (e.g., Austere Environments)
Aid Decision Support
Global Performance Optimization
Safety (Heat, Skill Erosion, Altered Decision Making, Chem/Bio)
Increased Team Dynamics
Research (Lab, Training, Operational Environment)
Automated Detection
Automating Documentation (Medic)
Predictive Modelling
Actions
Mechanisms
Outcomes
Data Visualizations (Individual, Squad, Command)
Physio Data Capture
LO 1
Data Comprehension

## Slide 9: Use Cases for Physiological Sensing in Training & Simulation
LO 1
Adaptive Optimized
Learning
Aid Decision
Support
Identify & Align
Training with
Mission Goals
Optimize Training
Realistic Scenario
Creation
Debrief & Feedback
Collaborative AI
Competency-Based
Training
Human Digital Twin
Monitor & Ensure
Safety
Career Field Planning
Training Effectiveness
Evaluation

## Slide 10: Potential Risks
LO 1
Current Silos
of Effort
Deployment
Limitations
Infrastructure
Limitations
& Data Access
Rapid Development of
New Technology
Leadership & Service
Member Adoption
Need for Synergized
Approach

## Slide 11: Recommended Approach & Best Practices
LO 2
​Eight Steps for Physiological Monitoring
11

## Slide 12
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
12

## Slide 13: Characterizing Environments & Stakeholders
Environmental considerations in ensuring good data and long-term adoption
Context: Tasks, equipment,
  networks, security
Environmental: Lighting,
  time of day, temperature, humidity, electrical noise
Short-term: Link human data to training performance data
Long-term: Link bi-directional communication from human and training
Adoption: Plan for user acceptance early, constant communication throughout the process
LO 2

## Slide 14: Characterizing Environments & Stakeholders
Delineating varied stakeholder and organizational needs
Medical/Health
Scientist/Researcher
Observer Coach / Trainer
Command Ops Lead
LO 2
Trainee

## Slide 15: Persona Example
The Observer Coach/Trainer aims to successfully address and adapt the multifaceted aspects of enhancing soldier readiness, safety, and performance evaluation. Wearable sensors allow them to monitor soldiers' physical and cognitive performance during training. Their insights, strategies, and training methodologies, in turn, benefit the accuracy, security and impact of wearable sensors for training evaluation and improvements.
Although the Observer Coach/Trainer works with trainees day-to-day to provide instruction, feedback, and evaluation directed at skill and performance enhancement, they also coordinate closely with command leadership, other trainers, analysts, health professionals, R&D teams, and logistics/support staff and allies. This diverse range of collaborators are essential for their development of effective training programs and the successful integration of sensor technologies.
Maximizing training effectiveness | Providing safety & situational awareness | Enhancing skill acquisition & retention
LO 2

## Slide 16
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
16

## Slide 17: Relevant Human States
Understanding the breadth of human states and selecting states of interest
Understand current problems (have a purpose)
Focus on states that will enable actionable changes
What are individuals repeatedly experiencing?
LO 2
User States
  Sleep
  Fatigue
  Readiness
  Stress
  Emotion
  Cognitive State
  Heat Stress
  Attention
  Repetitive Motion
  Activity​
  Team Effectiveness ​
  Motion Sickness ​
  Engagement ​
  Resilience​
  Position​
  Exposure​
  Illness ​

## Slide 18: Relevant Human States
Critical user states in learning and their benefits for training and simulation
Engagement
Stress
Mental Acuity
Resilience
Workload
Confidence
Competency & Performance
LO 2

## Slide 19
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
19

## Slide 20: Understanding Physiological Changes
Mapping primary and downstream physiological changes to user states
Acute Response to Exercise
Longitudinal Effects of Exercise
Hawley et al., Cell (2014)
Moreira et al., Nature Metabolism (2020)
LO 2

## Slide 21: Understanding Physiological Changes
Contextual considerations for physiological changes
Individual Differences
Age, gender, skill-level, anthropometry, personality, chronic conditions
Tying to longitudinal digital twin
Correlated Changes
Exercise
Overlapping changes (e.g., stress & workload)
Environmental Effects
Humidity, lighting, seasonality
LO 2

## Slide 22
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
22

## Slide 23: Selecting Appropriate Sensors
Current market, innovations, and evaluation criteria
Innovations:
Increased availability of EDA
Flexible materials (e-tattoos, fabrics)
Off-body sensing (voice, IR cameras)
What to Look For:
Supported Data Streams
Data Integration Considerations
Data Benchmarking & 3rd Party Validation (accuracy)
Use Cases & Context
LO 2

## Slide 24: Selecting Appropriate Sensors
Military considerations for device selection
Multi-Sensing
Use Case Specific
Security
Network
Scalability
Form Factors
LO 2
Sensor Types
  Accelerometers
  ECG
  Thermometers
  PPG
  Eye Tracking
  EDA
  Respiration Bands
  Video
  Hydration Patches
  Microphones
  EEG
  Gyroscope
  Magnetometer
  GPS
  System Clock
Data Features
  Heart Rate
  Heart Rate Variability (time & frequency)
  Pulse Rate Variability
  Oxygen Saturation (SpO2)
  Respiration Rate
  Pupillometry
  Fixation (location and time)
  Saccade
  Blink
  Smooth Pursuit
  Visual Search
  Skin Conductance Level
  Linear Acceleration
  Rotational Acceleration
  Magnitude of Magnetic Fields
  Facial Expression
  EEG Waves (across frequencies)
  ACH Level
  Lactose Level
  Glucose Level
  Location

## Slide 25
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
25

## Slide 26: Analyzing Data
Data science methods and current trends for physiological data
Features
Classifiers
    Data synchronization methods
    Various data science methods
    Model validation levels
      Within training set, cross-validation, generalization
    Multimodal data (losing signal, look at the next)
LO 2

## Slide 27: Analyzing Data
Critical data considerations for contextual interpretation
Individualization of data
Tying data to larger context (scenario, environment)
Scalability of analytics (e.g., containerization, on-device computing)
Acknowledgement and mitigation of potential researcher biases
Winslow, et al. Front Psych (2016)
LO 2

## Slide 28
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
28

## Slide 29: Storing Data
Trends in physiological data management and military considerations
    Location Options: On device, mesh networks, cloud, secure servers
    Common Data Standards: No widely accepted data model – though people are making recommendations
    Longitudinal Data Tagging: Metadata information, unique person identifiers across systems
LO 2

## Slide 30: Storing Data
Standardized data supporting digital transformation
Connected
Digital Twins
Cognitive State
Psychomotor Behavior
Physiological State
Asset Twins
Process Twins
Performance Twins
Connected
Digital Phenotypes
Existing Workflows
+
Knowledge
+
Context
+
Human State
Close the Human-System Loop & Increase ROI/Impact
LO 2
Descriptive Intelligence
Predictive Intelligence
Prescriptive Intelligence
Symbiotic Intelligence

## Slide 31
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
31

## Slide 32: Taking Action
Bridging the gap between new data analytics and implementation
    How to quickly convey real-time data to trainers?
    User interface/interaction considerations
    Integration with military systems
    Track behavioral changes, command-level changes
LO 2

## Slide 33: Taking Action
Supporting actions through physiological data integration in training and simulation
Optimized Learning
Individualized Instruction
Individual Insights
Holistic & Longitudinal Performance
Proficiency Tracking
Realistic & Adaptive Training
LO 2

## Slide 34
LO 2
​Eight Steps for Physiological Monitoring
Recommended Approach & Best Practices
34

## Slide 35: User Acceptance
User acceptance models for physiological devices and actionable tools
    Models of Acceptance: Technology acceptance model (TAM), unified theory of acceptance and use of technology (UTAUT)
LO 2
Venkatesh et al., 2003

## Slide 36: User Acceptance
Gaining user buy-in and overcoming resistance
    Adoption and Trust: Requires bi-directional feedback and communication. Start early in training pipeline.
    Various Echelons: Tie back to personas and what each level of user requires – evaluate appropriately.
LO 2

## Slide 37: Available Tools
Example Roadmap
&
LO 3
Hypothetical implementation and how to follow the 8-step guide.
Common Hardware
Common Software
Available Infrastructure
Other resources
37

## Slide 38: Tools to Enable the Process
    Hardware
    Software
    Infrastructure
    Other Resources
    Commercial Devices (e.g., Garmin, Fitbit, Oura)
    Emerging Sensors from Academia and Industry
    Proprietary Device Packages
    Multi-device Synchronization
    Data Analytics Platforms
    AI/ML Systems
    Avoid ‘Black Box’
    Data Lakes
    Common Data Models
    Edge Computing
    Longitudinal Tracking (Common Identifiers)
    Best Practice Guides
    DoD Reviews and Existing Personas
LO 3

## Slide 39: Physiological Integration Scenario
Typical Approach:
An organization wants to increase performance metrics
from their simulated training environment. They believe
physiological monitoring is the way to go. They did the
following:
  Searched online for a device that gives them physiological data
  Purchased 500 new wearable devices
  Had trainees start wearing the devices during training
  Had trouble accessing parts of the data
  Aren’t sure what to do with the data they have
  Stored data on separate devices
  Thus far, they’ve invested $250K+ in equipment and over 600 labor hours
LO 3

## Slide 40: Optimizing an Integration Approach for Success
Consider the intended audience and long-term needs – constant communication
Consider the nuances of their training environment
Plan what user states and performance outcomes that will be useful
Talk to SMEs to understand what physiological responses will associate with those outcomes
LO 3
40

## Slide 41: Optimizing an Integration Approach for Success
Conduct market research
    Look for benchmarked and validated devices
    Look for data availability, especially for military environments
Selecting Appropriate Sensors
    Individualize the data
    Ensure the data formats align with needs
    Make a plan to transform raw data into performance metrics
LO 3

## Slide 42: Optimizing an Integration Approach for Success
Make a plan to store data. Don’t keep data on separate machines in various formats.
Integrate data into existing training performance reviews
Ensure constant communication to relevant stakeholders and end users.
Don’t wait until the end and have to combat negative impressions based on limited feedback and demonstrated benefit.
LO 3

## Slide 43: Take Home Messages
  Summary:
  Bi-directional human-system information flow and communication will be critical as technology moves into Industry 5.0.
  Don’t wade into these waters blindly. Setting a strategic plan will make all the difference and prevent common roadblocks.
  Don’t need to stand-up a program of record to do this – leverage the experts and existing tools and resources.
  Remember the end goal: empowering humans to optimize training and workflows, ensure faster cross-training, develop human-autonomy configurations, and ensure readiness.

## Slide 44: Acknowledgments & How to Reach Us
  Next Steps:
  We’re here to help – connect with us.
  Take information back to your communities
  Acknowledgements:
  Special thank you to our I/ITSEC bird dog, Major Justin McNealy.
  I/ITSEC Committee
  Contact Us:
  audrey.zlatkin@designinteractive.net
  victoria.olko@designinteractive.net
  charles.rowan@nps.edu

## Slide 45: Question & Answer
45

## Slide 46: References
Slide 7
https://www.argonelectronics.com/blog/army-cbrne-training-how-to-prepare-for-major-chemical-weapons-events
https://www.nationaldefensemagazine.org/articles/2019/12/2/army-spending-big-on-training-modeling-simulation
https://www.army-technology.com/features/live-vs-virtual-training/
https://mwi.westpoint.edu/flight-simulator-fight-simulator-vr-war/
https://www.radiant.digital/does-fidelity-matter-in-simulation-based-learning/
Slide 20
Hawley JA, Hargreaves M, Joyner MJ, Zierath JR. Integrative biology of exercise. Cell. 2014 Nov 6;159(4):738-49. doi: 10.1016/j.cell.2014.10.029. PMID: 25417152.
Moreira JBN, Wohlwend M, Wisløff U. Exercise and cardiac health: physiological and molecular insights. Nat Metab. 2020 Sep;2(9):829-839. doi: 10.1038/s42255-020-0262-1. Epub 2020 Aug 17. PMID: 32807982.
Slide 27
Winslow BD, Chadderdon GL, Dechmerowski SJ, Jones DL, Kalkstein S, Greene JL and Gehrman P (2016) Development and Clinical Evaluation of an mHealth Application for Stress Management. Front. Psychiatry 7:130. doi: 10.3389/fpsyt.2016.00130
Slide 35
Venkatesh, Viswanath, et al. “User Acceptance of Information Technology: Toward a Unified View.” MIS Quarterly, vol. 27, no. 3, 2003, pp. 425–78. JSTOR, https://doi.org/10.2307/30036540.
46