## Slide 1
The 20th International Joint Conference on Computer Science and Software Engineering
Enhanced Bluetooth with Low-Density Parity-Check Codes
Pawarit Manakul
Usana Tuntoolavest
La-or Kovavisaruch
Kazuhiko Fukawa
28th June-1st July 2023
Naresuan University Phitsanulok, THAILAND
Department of Electrical Engineering
Kasetsart University

## Slide 2: Outline
Background
  Bluetooth low energy specification
  Low-density parity-check (LDPC) code
  Gaussian frequency-shift keying (GFSK) signal model
  Viterbi demodulator
Proposed method
  Modified Soft-Viterbi demodulator
  Bluetooth LDPC
Simulation setup
Results
Discussions
Conclusions

## Slide 3: Background
Bluetooth low energy (BLE) coded PHY
  Use forward error correction in BLE
  Provide more reliable communication
  Adding redundancy bits
LDPC code
  Widely used in Wi-Fi, WiMAX and 3GPP
  Near Shannon limit
Proposed method: Bluetooth LDPC
  Provide better performance
  Lower redundancy bits
  Shorter decoding time

## Slide 4: Bluetooth Low Energy
BLE
  Lower energy consumption
  Error detection: Cyclic redundancy check (CRC)
    Access address is incorrect
    There are some errors in the payload
    Good transmission requirement: bit error rate is equal to 0.1% or lower
PHY mode: physical layer configurations
  BLE 2M PHY: 2 mega-symbols per second
    Increase data rate
  BLE coded PHY: concatenated coding
    Extend the communication range (more reliable communication)
    Without increasing transmission power
    Packet is dropped

## Slide 5: BLE coded PHY
BLE coded PHY: concatenated coding
  Convolutional coding and pattern mapping
There are 2 coding schemes: and
  S represents the number of output bits
(2,1,3) Convolutional code with a rate 1/2 and memory of 3
Pattern mapper
Input bit | Output bit | 
0 | 0 | 0011
1 | 1 | 1100
Input bit | Output bit | 
0 | 0 | 0011
1 | 1 | 1100

## Slide 6: BLE coded PHY Block diagram
Error detection part
Forward error correction part
Modulation part

## Slide 7: LDPC code
Parity check matrix is a sparse matrix
  Consist of mostly “”
  Can reach a performance close to the Shannon limit
Represented by Tanner graph
  Variable nodes
  Check nodes
Decoding: Belief Propagation (BP)
  Message passing to perform inference in graphical models
  Require log likelihood ratio (LLR) as input

## Slide 8: LLR
Codeword
Modulated signal
  represents bit 1
  represents bit 0
Additive white Gaussian noise (AWGN) channel
LLR
  Two possible symbols, ‘+1' and ‘-1’
  Logarithm of the ratio between the probability that ‘+1' was sent and the probability that ‘-1' was sent

## Slide 9: High Throughput LDPC code
IEEE 802.11
Constructed from the concept of Quasi-Cyclic LDPC (QC-LDPC)
  Parity matrix can be generated from the prototype matrix
  Each element in must be integers in range , when is block size
  ‘-1’ indicates zeros submatrix
  Other values indicate right-cyclically shifted version of diagonal matrix

## Slide 10: Example: QC-LDPC code
If block size
Element in must be integers in range to represent submatrices
represent
represent
represent
represent

## Slide 11: High throughput LDPC code
Prototype matrix of High throughput LDPC code with rate

## Slide 12: GFSK signal model
GFSK is a Continuous Phase Frequency Shift Keying (CPFSK)
  belongs to the digital Continuous Phase Modulation (CPM)
  High power and spectral efficiency
Phase of the signal changes according to input symbol
Modulation order (binary)
Modulation index
  Yield maximum phase change of π/2 over a symbol
Pulse length is set to cover 3 symbols
Gaussian filter is used as pre-filtering
  Control the modulated signal bandwidth

## Slide 13: GFSK signal model
Create trellis diagram
  Represent the transition over symbol interval
  Transmitted and received signal are represented as states
  is the phase memory
  is input symbol when -1 represents ‘0’ and +1 represents ‘1’

## Slide 14: 2-GFSK trellis diagram

## Slide 15: Viterbi demodulator
Use Viterbi algorithm for demodulation
  Trellis diagram of GFSK signal
  Traditional demodulators do not provide LLR as output
  Better than FM and Phase shift discrimination
Maximum Likelihood Sequence Estimation (MLSE)
  Maximizing the log likelihood function
  Relate to Euclidean distance
    Received signal
    Reference signal
  Maximizing the correlation

## Slide 16: Modified Soft-Viterbi demodulator
LLRs can be obtained during Viterbi demodulation using
  Estimated input symbols from transition input matrix
  Correlations from survival and non-survival matrix

## Slide 17: Proposed method: Bluetooth LDPC
Use LDPC instead of concatenated code
  Soft-Viterbi demodulator
  High throughput LDPC code with code rate =
  Block size
Expected results
  Better performance
  Lower redundancy bits
  Shorter decoding time

## Slide 18: Bluetooth LDPC Block diagram
Forward error correction part

## Slide 19: Simulation setup
Simulation is done using MATLAB R2022b
Compare performance of various coding schemes
  Packet error rate (PER)
  Bit error rate (BER)
  Average number of iterations
  Average decoding time
AWGN channel
Message sequence
  Probability of each bit is equally likely

## Slide 20: Simulation parameters
Parameter | Values
Modulation type | GFSK
Modulation order | 2
Modulation index | 0.5
SNR range | [1:12]
Channel model | AWGN
Message length (bits) | 2052
Pulse shaping length (symbols) | 3
Traceback depth | 16
Maximum number of iterations | 200

## Slide 21: Results
Best case
2nd best
Worst case
PER Comparison of Bluetooth LDPC and BLE coded standard
PER of Bluetooth LDPC = 0.047
PER of BLE coded S8 = 0.9995
PER of Bluetooth LDPC
PER of BLE coded S8

## Slide 22: Results
BER Comparison of Bluetooth LDPC and BLE coded standard
Best case
2nd best
Worst case

## Slide 23: Results
0.006 seconds
0.102 seconds
Average decoding time of each coding scheme
0.003 seconds
17 times faster

## Slide 24: Results
Bluetooth LDPC average number of iterations

## Slide 25: Discussions
Performance
  Bluetooth LDPC is better than both BLE coded schemes when SNR ≥ 3 dB
Good transmission
  Bluetooth LDPC: at SNR ≥ 3 dB
  BLE uncoded: at SNR ≥ 8 dB (channel coding is unnecessary)
Average decoding time
  Bluetooth LDPC is 16.954 times faster than BLE coded S8

## Slide 26: Discussions
Redundancy bits
  Bluetooth LDPC is equal to 2,100 bits
  6.9314 times lower than 14,556 bits that BLE coded S8 required
Average number of iterations
  SNR increases
  The complexity of Bluetooth LDPC decoding rapidly decreases
Maximum number of iterations can be set
  Suit the channel’s SNR
  Reduce the time consumption and the number of unnecessary iterations

## Slide 27: Conclusion
The proposed Bluetooth LDPC
  Better performance than other BLE coded schemes at SNR equal to 3 dB or higher
  Lower complexity
  Fewer redundancy bits compared to BLE coded S8
Bluetooth LDPC can be a good alternative for future Bluetooth
  fast and reliable transmission of long packets

## Slide 28: THANK YOU
QUESTION & ANSWER

## Slide 29: Bluetooth specification
2.4 GHz Industrial-Scientific-Medical (ISM) band
  Bluetooth
  Wi-Fi
  Cordless telephones
Frequency hopping spread spectrum (FHSS)
  Mitigate interferences
Transmission rate = 1 Mbps
Modulation
  Binary Gaussian frequency-shift keying(mandatory mode)
  π/4-Differential Quadrature phase-shift keying (enhanced data rate mode)

## Slide 30: Example of Viterbi demodulation in MATLAB
-1e7
-1e7
-1e7
0
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
+1
-1
Tempsum =
0.01
0.01
0.01
0.01
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
-1e7
0.05
0.05
0.05
0.03
0.03
0.03
Survival matrix will record
  the current state that gives the highest value
Transition input matrix will record
  The estimated input symbol
Normalize
  Minus all value with max value
  If the result < -1e7 set it to -1e7
0
0
0
-0.02
0
-0.02
0.03
0.05