## Slide 1: CH 10: Implementing Operational Procedures
Use Appropriate Safety Procedures
Environmental Impacts and Controls
Create and Maintain Documentation
Use Basic Change Management Best Practices
Implement Disaster Prevention and Recovery Methods
Basic Scripting Concepts
Professionalism and Communication

## Slide 2: Topic A: Environmental Impacts and Controls

## Slide 3: Power Issues
Caused by building power failures, not the computer’s power system.
Surge: Abrupt, but brief change in the value of the voltage.
Spike: A powerful surge, such as that caused by lightning.
Sag: Power supply to components briefly dips below required levels.
Brownout: Power from the wall socket is insufficient to allow devices to function correctly.
Blackout: Complete loss of electrical power.
Notes: Teaching Tip: This topic should be straightforward. You may want to designate it for self-study. Focus on power protection in class.

## Slide 4: Power Protection Controls
Devices require stable power supply
Electrical events can crash devices
Use power protection devices to mitigate issues
Surge protector: A device intended to protect electrical devices against the damaging effects of a power spike.
Line conditioner: A device that adjusts voltages in under-voltage and over-voltage conditions to maintain a 120 V output.
Power Distribution Unit (PDU): A device designed to provide power to other devices that require it.
Uninterruptible Power Supply (UPS): A battery powered device designed to provide an alternative AC power supply during a power failure.

## Slide 5: Power Protection Controls
Surge protectors:
Low cost
Protect one or two devices
Rated by various standards
  UL 1449
Characteristics:
  Clamping voltage
  Joules rating
  Amperage
Line conditioners:
Protect from surges or brownouts
Cannot protect from blackouts

## Slide 6: Power Protection Controls
Battery backups and UPS:
Power redundancy:
  Protection against blackouts
  Battery backups provide temporary power at the component level
  UPSs provide temporary power at the system level
Length of protection depends on load and battery capacity
Allows time to:
  Switch to alternate power source
  Shut down device properly
  Save files

## Slide 7: Power Protection Controls
UPS sizing:
Considerations when purchasing UPS:
  Reliability
  Cost
  Uptime
  Maintenance
  System performance and features
Notes: Teaching Tip: Explain why the inverter is needed. The PC's PSU is connected to the UPS and needs AC power to function.

## Slide 8: Environmental Impacts
Mean Time Between Failures (MTBF): The rating on a device or component that predicts the expected time between failures.
Environment affects:
Operation
Lifespan
Keep away from:
Extreme temperatures
Dampness and dust
Regularly inspect and clean surroundings
Notes: Teaching Tip: If you have them, showing examples of the various cleaning products will liven up the presentation for this section.

## Slide 9: Dust and Debris
Dust/airborne particles:
Drawn in through ventilation holes
Can prevent heat dissipation
Can clog keyboards and mice
Can make displays hard to read
Control dust by:
Cleaning devices
Maintaining HVAC filters
Maintaining fan inlet air and dust filters
If necessary, placing a system in enclosure with its own air filters and fans
Notes: Interaction Opportunity: Ask learners if they have come across computer components that were in bad condition due to dust and debris. Mention that in different environments, the dust and debris may be more intense depending on the location of the computers.

## Slide 10: Temperature, Humidity, and Ventilation
Excessive heat affects computer reliability:
Direct sunlight
Placement near a heat source
Airflow
Humidity levels:
High can cause condensation
Low can cause ESD risks
Strive for around 50% relative humidity
Allow moved equipment to adjust to room temperature before running
Make sure HVAC system adequately maintains proper temperature, humidity, and ventilation.

## Slide 11: General Preventive Maintenance
Wear a mask and gloves when you are:
  Using compressed air.
  Working around toner spills or in a dusty environment.
Compressed air dislodges dust from hard-to-reach areas.
  Be aware of risk of contaminating the environment with dust.
  Use in a controlled work area.
  Use air filter mask and safety goggles.
Use vacuums with caution.
  For removing dust from inside a system unit, use a PC vacuum or one with a natural bristle brush.
  Do not use home appliances due to ESD.
  For toner spills, verify the vacuum is labeled “toner safe.”
    Alternatively, use a toner cloth.
Notes: Teaching Tip: Exam candidates will need to know what materials can and can't be used to clean each type of PC component.

## Slide 12: Peripheral Device and Laptop Maintenance
Clean peripherals with wipes or cloths and cleaning solutions designed for PC components:
  Mice
  Keyboard
  Displays
Laptop maintenance:
  Keep vents clear of dust and debris
  Use on a flat surface to allow airflow
  If used on a lap, use a chiller pad or mat to allow airflow
  Use compressed air to clean keyboard
  Use soft cloth and approved cleaner for screen, touchpad, and case

## Slide 13: Disposal, Recycling, and Compliance
OSHA-compliant employers must provide:
  Workplace free of recognized hazards.
  Personal protective equipment.
  Labeling, MSDS, and hazmat training.
Your responsibility:
  Be informed of potential hazards.
  Always use safe practices.
Environmental protection:
  Comply with environmental control requirements.
  MSDS documentation for identifying potentially hazardous substances.
Notes: Teaching Tip: Point that use of dangerous substances in the workplace and transport and disposal of materials are usually tightly regulated by workplace and environmental legislation. Discuss the legislation relevant to your own country.
Interaction Opportunity: You may want to show and discuss some government websites: www.epa.gov, www.environment-agency.gov.uk, and www.environ.ie.

## Slide 14: Discussing Environmental Impacts and Controls
What are the principal characteristics of a surge protector?
ANSWER:
  This is a circuit designed to protect connected devices from the effect of sudden increases or spikes in the supply voltage and/or current. Surge protectors are rated by clamping voltage (low values are better), joules rating (higher values are better), and amperage (the maximum current that can be carried).

## Slide 15: Discussing Environmental Impacts and Controls
When you are sizing the load for a UPS, how would you calculate the power used by a PC component?
ANSWER:
  Multiply its Voltage (V) by the Current (I) it draws to calculate power drawn in Watts (W=V*I). You may then need to convert this to a VA rating by multiplying by 1.67. When power is supplied, some is lost through the function of inverters and capacitors. This means that the supply, measured as VA, must exceed the watts drawn by about 70%. This ratio is also described as the Power Factor (PF).

## Slide 16: Discussing Environmental Impacts and Controls
Why should you never use a home vacuum cleaner to clean a PC?
ANSWER:
  Because they generate large amounts of static electricity that may damage sensitive components.

## Slide 17: Discussing Environmental Impacts and Controls
What are the principal environmental hazards to consider when installing PC equipment?
ANSWER:
  Heat and direct sunlight, excessive dust and liquids, and very low or high humidity. Equipment should also be installed so as not to pose a topple or trip hazard.

## Slide 18: Discussing Environmental Impacts and Controls
When might you need to consult MSDS documentation?
ANSWER:
  A Material Safety Data Sheet (MSDS) should be read when introducing a new product or substance to the workplace. Subsequently, you should consult it if there is an accident involving the substance and when you need to dispose of the substance.

## Slide 19: Topic B: Create and Maintain Documentation

## Slide 20: Equipment Inventory
Well-documented inventory is crucial:
  All hardware deployed
  Spare systems and components
  Network appliances and infrastructure
  Software
Asset management database
Asset: Hardware and software items found in an organization.
Asset management: A set of policies that includes information about the financial and contractual specifications of all hardware and software components present in an organization's inventory.
Radio Frequency ID tag (RFID tag): A tag that can be read by using a radio transmitter/receiver device.
Notes: Teaching Tip: Stress the importance of updating configuration baselines and network diagrams following changes.

## Slide 21: Equipment Inventory
Typical assets:
Standard and specialty workstations
Servers
Connectivity and backup hardware
Operating system software
Productivity and application software
Maintenance utilities
Backup documentation
Overall asset inventory

## Slide 22: Network Topology Diagrams
Network topology: Physical or logical shape or structure of the network.

## Slide 23: Schematic Block Diagram
Schematic: A simplified representation of a system.
Show the general placement of equipment and rooms
Show device and port IDs
Can represent the logical structure of the network
Security zones
VLANs
Subnets
Can be drawn manually or compiled automatically

## Slide 24: Reference Documentation
User and Installation manuals
Internet and web-based resources
  Knowledge bases
  Wikis
  Articles
  Quick reference materials
Training materials

## Slide 25: Incident Documentation
Incident management: A set of practices and procedures that govern how an organization will respond to an incident in progress.
Job ID
Contact
Priority
Problem description
Asset
Details
Follow up
Dates

## Slide 26: Organizational Policies
Standard: A measure for evaluating compliance with a policy.
Procedure: Inflexible, step-by-step listing of actions that must be completed for any given task. Also referred to as Standard Operating Procedure.
Guidelines: For areas of policy where there are no procedures, or where it is appropriate to deviate from a specified procedure.
Enforcement matters!
Personnel management policies:
  Recruitment and hiring
  Operation
  Termination or separation
Password policies
Acceptable use policy (AUP):
  Rules of behavior
  Use of work devices for personal use
  Use of personal devices at work
Notes: Teaching Tip: Password policies were covered previously, but they are part of organizational policies, so are mentioned here. Also remind learners that regulated data policies should be considered organizational policies and were covered previously in the course.

## Slide 27: Guidelines for Creating and Maintaining Documentation
Keep accurate records for hardware and software:
  Deployed hardware (complete systems and components).
  Deployed software (applications and OSs).
  Spare hardware (complete systems and components).
  Software that is not currently installed (applications and OSs).
Use asset tags to track equipment.
Document network components (physical and logical topology).
Maintain a library of reference documentation, including:
  User and installation manuals.
  Links to Internet and web-based resources.
  Training materials.

## Slide 28: Ticketing Systems
User information
Device information
Description of problems
Categories
  Requests, incidents, problems
  Customer-selectable categories
Severity
  Critical, major, minor
Notes: Describe the core fields and the function they serve in recording, prioritizing, and progressing support cases.

## Slide 29: Ticket Management
Escalation levels
  To third-party
  To higher level of seniority
  Support tiers
Clear, concise written communication
  Problem description
  Progress notes
  Problem resolution
Incident report
  Lessons learned/after action analysis and reporting
Notes: Discuss how a ticketing system supports effective teamwork only if fields are completed clearly and concisely. Escalation is covered in Core 1 as part of the troubleshooting model, but remind students of the main routes (senior staff, management, vendors, sales/conflict resolution) here.

## Slide 30: Discussing Documentation Creation and Maintenance
What role do barcodes play in managing inventory?
ANSWER:
  An inventory is a list of assets. To compile a list of assets, you must be able to identify each asset. A barcode label is a good way of doing this. You can use a scanner to link to the asset within the inventory database automatically, avoiding delays and mistakes that might be made by typing an asset ID.

## Slide 31: Discussing Documentation Creation and Maintenance
What are the two main types of network topology diagrams?
ANSWER:
  You can create diagrams to show the physical topology or the logical topology. The physical topology shows the location of cabling and ports plus their bandwidth. The logical topology shows IP addresses and subnets plus security controls such as firewalls. There are lots of other types of network topology diagrams, of course, but physical and logical are the two basic distinctions you can make. It is best practice not to try to create a diagram that shows both.

## Slide 32: Discussing Documentation Creation and Maintenance
What is the purpose of a KB?
ANSWER:
  A Knowledge Base (KB) is a reference to assist with installing, configuring, and troubleshooting hardware and software. A KB might be created by a vendor to support their products. A company might also create an internal KB, populated with guidelines, procedures, and information from service tickets.

## Slide 33: Discussing Documentation Creation and Maintenance
What three broad types of incident documentation might a business require?
ANSWER:
  Incidents can be categorized as support/troubleshooting, security, and accident (whether to personnel or to assets). You should also consider the effect compliance with regulatory or legal requirements has on the documentation that must be kept.

## Slide 34: Discussing Documentation Creation and Maintenance
While you are answering a service call on a computer that is located in a common area of the office, you come across information showing that some unauthorized websites have been viewed. The activity has been linked to a particular user account. What is the appropriate action to take?
ANSWER:
  This is likely to demonstrate a clear breach of Acceptable Use Policies (AUP) and will be the subject of disciplinary action by HR. You should not over-assume or over-react, however. Take care to follow best practices for incident response, such as establishing unambiguous evidence and documenting the entire incident.

## Slide 35: Topic C : Use Basic Change Management Best Practices

## Slide 36: Change Management
Configuration management: The practice of identifying all component of the ICT infrastructure and their properties.
Change management: The practice of adopting policies to reduce the risk of infrastructure changes affecting service or operations.
ITIL configuration management model:
  Service assets
  CIs
  Baselines
  CMS
Information and communications technology (ICT)
Documenting changes:
  Configuration information
  List of patches applied
  Backup records
  Details of suspected breaches
  Hash result printouts

## Slide 37: Documented Business Processes
Level and degree of documentation varies by organizational needs
At a minimum:
  Document systems for new employees
  Changes to the systems when an employee leaves
  Document how tasks are completed
SOPs and work instructions
Change management documentation
  RFCs
Change Advisory Board

## Slide 38: Process for Instituting Change to Operational Policies and Procedures
Implementation of changes should be carefully planned
Organizations should attempt a trial implementation for major changes
Create a rollback or remediation plan
Schedule changes to have minimal impact on workflow
After the change is implemented, assess its impact
Review the process and document the outcomes
Can be used to improve the process for future change management projects

## Slide 39: Guidelines for Using Change Management Best Practices
Create a separate document for each item:
  Describe its initial state
  Identify all subsequent changes
ITIL configuration management includes documenting:
  Service assets
  CIs
  Configuration Management Database (CMDB)
  Baselines
  Configuration Management System
Use RFCs to document the need or desire for a change.
  RFCs should be considered at the appropriate level and affected stakeholders should be notified.

## Slide 40: Guidelines for Using Change Management Best Practices
Major or significant changes:
  Could be managed as a separate project.
  Might require approval through a Change Advisory Board.
Follow documented SOPs Standard Operating Procedure and Work Instructions.
Implementation of changes should be carefully planned.
  How will the change affect dependent components?

## Slide 41: Guidelines for Using Change Management Best Practices
For most significant or major changes, use trial implementations.
Always have a rollback (or remediation) plan.
Schedule changes to minimize system downtime.
When the change has been implemented:
  Assess its impact, and review the process to identify any outcomes that could help future change management projects.

## Slide 42: Discussing Change Management Best Practices
Why are documented business processes essential for effective change management?
ANSWER:
  Without documented processes, you do not have a means of measuring or specifying the effects of change. Of course, you could be introducing a change to start using documented business processes! But from that point, any project can be measured and evaluated by the changes it makes to documented procedures. Changes that are supported by documented procedures can also be communicated more clearly to staff.

## Slide 43: Discussing Change Management Best Practices
What are the main components of an RFC?
ANSWER:
  A Request for Change (RFC) sets out the purpose and scope of the proposed change and a documented plan for carrying out the change. Ideally, it should perform a risk analysis of both performing the change and not performing the requested change. It should state the measures by which the change can be judged to have been completed successfully. Ideally, it would also include a backout plan for reversing the change.

## Slide 44: Discussing Change Management Best Practices
What is a change board?
ANSWER:
  A change board is a committee of stakeholders who can approve the planned change.

## Slide 45: Topic D: Implement Disaster Prevention and Recovery Methods

## Slide 46: Disaster Prevention and Recovery
Disaster Recovery Plan (DRP): A documented and resourced plan showing actions and responsibilities to be used in response to critical incidents.
Identify scenarios for natural and man-made disasters and options for protecting systems.
1
Identify tasks, resources, and responsibilities for responding to a disaster.
2
Train staff in the disaster planning procedures and how to react well to change.
3

## Slide 47: Data Backup and Restoration (Slide 1 of 4)
Data backup: A system maintenance task that enables you to store copies of critical data for safekeeping.
Data restoration: A system recovery task that enables you to access and restore the backed-up data.
Create data backups by:
Copying files and folders to local or network locations.
Using dedicated backup software and hardware.
Levels:
File
Image
Critical applications
When you use cloud storage, the service provider does the backups.
Notes: Teaching Tip: Point out that it is not necessary to back up OS files, but configuration files should be part of the backup.

## Slide 48: Data Backup and Restoration
Backup management:
Plan execution and frequency of backups.
Identify the recovery window via business continuity planning.
Long- and short-term retention.

## Slide 49: Data Backup and Restoration
Recovery images
Windows computers come with a recovery image, but the image does not get updated unless you do it.
Custom recovery image should contain current OS state plus all desktop apps installed at the boot partition.
Any changes to apps or configuration requires a new recovery image to be created.
Use recovery images to restore a PC’s or VM’s functionality (OS and apps).
Use file-level backups to restore user profile information and data.
Notes: Teaching Tip: Point out that "refresh" and "reset" mean specific things in Windows. The recovery image isn't at all like a refresh, because it will delete personal files. It's not a reset of vanilla Windows, but it is akin to a factory reset. An OEM recovery image will have the shareware installed by default, so it IS a reset in terms of reverting to a tested build.

## Slide 50: Backup Testing
Try restoring some of the backed-up data into a test directory.
Make sure you don't overwrite any data when testing.
Configure the backup software to verify after it writes
Verify that the backup contains all the required files.
Test backup devices and media on a regular basis.
Notes: Interaction Opportunity: Ask if anyone has had experience expecting they were safe because they performed backups, only to find when they went to restore their data, that the backup was not current or was corrupted in some way.

## Slide 51: Off-site and Local Storage
Backups are usually stored offsite.
  In case of disaster at the server, the backup media is not lost as well.
  Safety deposit box or with a firm that specializes in securely storing backups.
Keep a backup set on site for instant access
  In case of accidentally deleted or corrupted files.
  Consider using a fire-proof safe.
Environmental considerations must be considered.
  Do not store backups where there is high heat or humidity.
  Do not store backups near magnetic equipment.
Notes: Interaction Opportunity: Ask learners if their organizations use a third-party storage facility such as Iron Mountain, store backups at another one of their own facilities, or use a bank security deposit box or some other location to store their off-site backups.

## Slide 52: Off-site and Local Storage
Backup storage security:
Authentication of users and backup clients to the backup server.
Role based access control lists for all backup and recovery operations.
Data encryption options for both backup transmission and storage.
Backup of remote clients to a centralized location behind firewalls.
Default data storage locations must be standardized.
Create a policy that defines where documents are backed up from.
Use segregation of duties enforced by policy for all personnel handling backup data.
Document all access, testing, backup, and restore cycles.

## Slide 53: Account Recovery
Different things can happen to prevent logon.
Mistyped or forgotten password.
Error processing smart card or biometric credentials.
Many systems support account recovery through the use of challenge questions.
If account recovery methods don’t work, you might need to re-create the account.
You will need to import backed-up data to the new account.
You will also need to reconfigure file permissions and group memberships.
Notes: Interaction Opportunity: Ask if anyone has needed to use account recovery for any OS, app, or website, and what the experience was like.

## Slide 54: Guidelines for Implementing Disaster Recovery and Prevention Methods
Remember
Remember, restoring data from backup provides data that is only as current as the last backup.
Test
Test backups after they are created.
Determine
Determine where backups will be stored both locally and offsite.
Document
Document the account recovery methods that will be needed for any systems, applications, or websites used by the organization.

## Slide 55: Discussing Disaster Prevention and Recovery
At which general levels are backups made to facilitate disaster recovery?
ANSWER:
  Backup levels include file, image, and critical application.
  File level backups allow restoration of user-generated data files in a shared folder or user profile.
  An image-level backup records a whole installation (OS, third-party software and drivers, and custom settings). This can be used to reinstall a computer or recover a Virtual Machine (VM).
  A critical application backup saves data and settings kept by a specific software product. This is likely to involve some sort of database backup.

## Slide 56: Discussing Disaster Prevention and Recovery
What tests can you perform to ensure the integrity of backup settings and media?
ANSWER:
  You can perform a test restore and validate the files.
  You can run an integrity check on the media, such as using chkdsk on a hard drive used for backup. Backup software can often be configured to perform an integrity check on each file during a backup operation.
  You can also perform an audit of files included in a backup against a list of source files to ensure that everything has been included.

## Slide 57: Discussing Disaster Prevention and Recovery
For which backup/restore issue is a cloud-based backup service an effective solution?
ANSWER:
  The issue of provisioning an offsite copy of a backup. Cloud storage can also provide extra capacity.

## Slide 58: Discussing Disaster Prevention and Recovery
What provisions can you make for account recovery?
ANSWER:
  You might implement a password recovery mechanism for users who have forgotten a password, though this mechanism can itself represent a security risk.
  You should ensure that profile data is backed up so that it can be restored in the event of file corruption or damage to a disk. If a profile cannot be restored, the account would have to be recreated. This means that the account will have to be reassigned security group memberships and permissions.
  This is easier if the allocation of those permissions has been well documented in the first place. There may also need to be some provision for configuring a recovery key to restore encrypted data.

## Slide 59: Topic E: Basic Scripting Concepts

## Slide 60: Script Files
You may need a command interpreter to execute the script.
You can open scripts in text editors or IDEs.
(Integrated Development Environment).
Script file: A text document containing OS commands or instructions from a scripting language.
Scripting language: A programming language that is not compiled, and must be run within a particular environment.
Notes: Teaching Tip: Determine learners' current level of knowledge about programming, and in particular about scripting, so you have an idea on how deeply to cover this information.

## Slide 61: Scripting Languages
Types of instruction sets:
  Compiled programs (CPU performs instructions)
  Scripts (OS or command interpreter performs instructions)
File extensions differ for each scripting language:
  Windows batch file: .bat
  PowerShell script: .ps1
  Linux shell script: .sh
  VBScript file: .vbs
  JavaScript file: .js
  Python script: .py
Scripts often used for smaller, repetitive tasks
Notes: Interaction Opportunity: Ask learners if anyone has experience with any of the scripting languages listed.
Teaching Tip: Point out that Java (a compiled programming language) is different than JavaScript (an interpreted scripting programming language).

## Slide 62: Scripting Languages
Batch files
Stored in a .BAT file
Usually run end to end
  Limited user input

## Slide 63: Scripting Languages
Windows PowerShell
Perform administrative tasks
Can use PowerShell ISE
Integrated Scripting Environment

## Slide 64: Scripting Languages
Linux shell scripts:
Equivalent of batch files
Starts with a line to designate the interpreter
Automates commands for:
  System administration
  Troubleshooting
  Simple applications
  Manipulation of text or files

## Slide 65: Scripting Languages
VBScript:
Used for administrative tasks
Run from command line or Windows GUI
Must run within host environment
  Internet Explorer
  IIS
  Windows Script Host (WSH)

## Slide 66: Scripting Languages
JavaScript:
Used for interactive web-based content and web apps
Automatically executed by placing the script in web page HTML code

## Slide 67: Scripting Languages
Python:
General purpose programming language
Designed to be easy to read and program
Code runs in an interpreter
  Windows default is CPython

## Slide 68: Basic Script Constructs
Each script language has its own structure and syntax.
Similarities occur, but using the correct syntax for a particular language decreases the chances of errors.

## Slide 69: Identifiers
Identifier: A computer programming component used to access program elements such as a stored value.
Labels for program components.
Identifiers that store data are either variables or constants.
Variables contain values that can change during program execution.
Constants contain values that do not change during program execution.

## Slide 70: Environment Variables
Environment variable: A storage location in the OS command shell.
Shell recognizes some variables and replaces with correct path.
Common environment variables include:
%SystemDrive%—for example, "C:"
%SystemRoot%—for example, "C:\Windows“
View Windows environment variables with the set command or through System Properties→Advanced.
View Linux environment variables with the printenv or env command.

## Slide 71: Branches and Loops
Most scripts run from top to bottom unless you specify otherwise.
You can specify logical conditions to change the order of execution.
  Branches provide flow control
  Loops provide repetition
Comparison operators help define the condition.
Logical operators enable testing multiple conditions simultaneously.
Branch: A programming technique used to control flow based on a logical condition and implemented with if or goto statements.
Loop: A programming technique used to repeat a task until a logical condition is met and implemented with for or while statements.

## Slide 72: Basic Data Types
Data Type | Description
Integers | Whole numbers. For example: 5, 21, or 65536. An integer data type consumes 1 to 8 bytes of computer storage.
Floating Point Numbers | Supports decimal fractions such as 4.1, 26.4, or 5.62. Consumes between 4 and 8 bytes of storage. Can store a whole number too (4.0, for instance).
Boolean Values | Indicates that something is either TRUE or FALSE (with a 1 or 0). Consumes a single bit of storage.
Characters | A single textual character. For example: a, D, 7, $, @, #. These consume one byte of storage. Numbers cannot be used in computation.
Strings | A string of text characters. For example: XYZ, Hello world. Storage size varies. Generally string length is determined when you define the data type.
Notes: Teaching Tip: Ensure learners understand the difference between integers and strings. Provide examples or ask learners to provide examples.

## Slide 73: Basic Data Types
Escape character: A character used to allow alternate use of a reserved character within a particular programming language.
Scripting Language | Escape Character
Batch file | %%
PowerShell | There are different escape characters for different circumstances. --% ` \
VBScript | To escape a single quote, enter two single quotes: '' To escape a double quote, enter two double quotes: "" Use the Escape(charString) function
Linux Bash Shell script | \
Python | \
JavaScript | \

## Slide 74: Discussing Scripting
What is the file extension for Python script files?
ANSWER:
  .py.

## Slide 75: Discussing Scripting
Which batch or scripting language is represented here?
ANSWER:
  VBScript.

## Slide 76: Discussing Scripting
What are the characteristics of a variable?
ANSWER:
  A variable is a construct within programming code for some sort of value that can change during the execution of the script. The variable must be given a name.
  A variable also has a data type, such as string or integer. The data type can be explicitly declared or set when the variable is initialized (given its first value). It is good programming practice to declare variables before they are used.

## Slide 77: Discussing Scripting
What command can you use to define an environment variable?
ANSWER:
  In Windows, environment variables are defined using set.
  In Linux, there are not only environment variables (env and printenv), but also variables specific to the current shell.
  Shell variables are configured with set. The syntax of set is different between Windows and Linux

## Slide 78: Discussing Scripting
What type of script construct is "For ... Next" an example of?
ANSWER:
  The For ... Next statement is one kind of loop. The script will execute statements within the loop repetitively until a logical condition is met.

## Slide 79: Discussing Scripting
What is a string?
ANSWER:
  A string is a data type that represents a series of text characters.

## Slide 80: Topic E: Professionalism and Communication

## Slide 81: Customer Service Attitude
Be a good communicator:
Competent technicians with poor communication skills do not impress customers
Customers are any users or clients of a support service
Good customer service:
Be positive
Be clear, concise, and direct
Be consistent, fair, and respectful

## Slide 82: Communication Skills
Use proper language.
  Avoid the use of jargon, acronyms, and slang when applicable.
Actively listen to the customer.
  Avoid interrupting.
  Use open and closed questions to elicit information.
Provide feedback to gain rapport.
  Avoid implying blame or responsibility.

## Slide 83: Professionalism
Proper documentation helps you set realistic expectations.
  Contact information
  Hours of operation
  Items that are supported
  How long to resolve incidents
  When an item will be replaced rather than repaired
Problem management
  Clarify customer expectations of what will be done and when
  Address customer concerns about cost or impact on business processes
  Your constraints regarding time, parts, costs, contractual obligations, etc.
  Reach a course of action that is realistic and achievable
Notes: Interaction Opportunity: Ask learners if they have been in situations where they had to refuse a request. What are some good ways of saying "No"?

## Slide 84: Professionalism
Use a ticketing system to support proper documentation of all support requests.
  Use proper spelling and grammar.
  Be clear in case others need to use the information to resolve the issue.
  Be aware that the customer might receive the contents of the ticket.

## Slide 85: Professionalism
Strive
Strive for resolution in one service call.
When this is not possible, manage customer expectations.
Communicate
When the issue is resolved, communicate the general cause and solution to the customer and thank them for their assistance.
Prioritize
Prioritize your work.
Be
Be punctual and accountable.
Be
Be flexible, and seek compromise when necessary.

## Slide 86: Respect
Avoid
Avoid distractions during a service call:
Don’t take personal calls or use texting
Don’t post on social media
Be
Be respectful of property and confidentiality:
Don’t use customer equipment or services without permission
Don’t help yourself to food or drink, and don’t snoop
Ask before using the restroom
Notify customers if confidential materials are in sight so they can deal with them
Maintain a tidy work environment
Be
Be culturally sensitive:
Don’t make assumptions
If language or accents are making things difficult:

## Slide 87: Customer Complaints
Maintain a positive attitude, Be accurate and honest
When dealing with a difficult customer:
  Identify signs that a customer is becoming angry
  Don’t take complaints personally
  Listen and let the customer explain the problem
  Hang up if the customer is abusive or threatening
    Issue a caution first
    Warn them about their behavior
    End the call if they don’t act reasonably
Notes: Teaching Tip: Ask learners if they have experienced customer complaints in their jobs, either in computer support or another area, or if they ever complained about a service or experience.

## Slide 88: Discussing Customer Service and Communication Skills
How would you cope with a user who is struggling to explain the problem that they are experiencing?
ANSWER:
  Use closed questions that allow the user to give simple yes or no answers.

## Slide 89: Discussing Customer Service and Communication Skills
You have received an off-site service call to service a network printer at a customer location. When you arrive, the user is at the printer and starts talking about how the printer is not working properly, and he cannot get his reports handed in on time. How should you approach this user?
ANSWER:
  Demonstrate empathy with the customer's situation and use active listening skills to show that you understand the importance of the issue and make the customer confident that you can help. Then use closed questioning techniques to start to diagnose the problem.

## Slide 90: Discussing Customer Service and Communication Skills
How would you deal with a customer who is becoming abusive because you have taken three separate calls to deal with their problem?
ANSWER:
  Explain why the problem is taking so long to resolve, and get them to focus on helping you, rather than hindering you. If the abuse continues, warn them that it cannot be tolerated and that you will have to end the call if it persists.

## Slide 91: Discussing Customer Service and Communication Skills
You are trying to troubleshoot a problem over the phone and need to get advice from your manager. How should you handle this with the customer?
ANSWER:
  Advise them that you will put them on hold while you speak to someone else or arrange to call them back.

## Slide 92: Discussing Customer Service and Communication Skills
You are troubleshooting a print problem, which turned out to be caused by user error. The user is not confident that the problem is solved and wants more reassurance. You have already explained what the user was doing wrong in some detail. What should you do?
ANSWER:
  Run through the print process step-by-step to show that it works. It is very important to get a customer's acceptance that a problem is "closed."

## Slide 93: Discussing Customer Service and Communication Skills
A user known to your department as a "frequent flyer" with regard to support requests calls in with a genuine but non-urgent problem. You are in the middle of another important job that is urgent. What would be the best approach?
ANSWER:
  Confirm that the problem is not impacting their work and get them to email a support request, which you will attend to within 48 hours.

## Slide 94: Discussing Customer Service and Communication Skills
What should you be wary of if a customer phones in with a problem you think you have solved already?
ANSWER:
  Do not assume—allow the customer to describe the problem fully then make a proper assessment.

## Slide 95: Discussing Customer Service and Communication Skills
You are working on the training documentation for new A+ technicians in the organization. What should you include for dealing with difficult customers or situations?
ANSWER:
  Answers will vary, but might include the following. Do not argue with customers and/or be defensive. Avoid dismissing customer problems and do not be judgmental. Try to calm the customer and move the support call towards positive troubleshooting diagnosis and activity, emphasizing a collaborative approach. Do not disclose experiences via social media outlets.