## Slide 1: CH 9: Supporting and Troubleshooting Mobile Devices
Secure Mobile Devices
Troubleshoot Mobile Device Issues

## Slide 2: Topic A: Secure Mobile Devices
Secure Mobile Devices
Troubleshoot Mobile Device Issues

## Slide 3: Popular Security Controls for Mobile Devices
Organizations security practices, including
  Policies
  Procedures
  Training
Keep these mobile devices secure physical infrastructure.
Do not leave mobile devices unattended.
Notes: Teaching Tip: This topic starts to look at the mobile objectives and content examples from the Core 2 exam objectives.

## Slide 4: Mobile Device Access Control
Screen locks and biometric authentication
  Screen locks require:
  Password, Passcode
  PIN, or Gestures
  Biometric authentication:
  Fingerprint
  Facial recognition
  Pattern

## Slide 5: Mobile Device Access Control
Lockout policies
  Limits failed logins.
  Lockouts can escalate in duration: 10 seconds for 1 lockout; 30 minutes for next.
Remote wiping
  Resets a stolen device to factory defaults.
  All personal data removed.
  Possibly erase memory cards, too.
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 6: Mobile Device Updates
Security
  Mobile devices can use the same classes of security software as PCs and laptops to
  protect against malware, phishing, and software exploits.
Patching/OS updates
  IOS: Settings > General > Software > Update
  App Icon Notifications on the app will make you aware of App updates.
  Android: Settings > System > Advanced > System updates
  Will uses the notification bar to deliver updates.
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 7: Mobile Device Antivirus
Antivirus/anti-malware
  Anti-malware designed for mobile devices work more like content filters to block access to known phishing sites and block adware/spyware activity by apps.
Antivirus
  Additional layer of protection to marketplace security
  Monitor app behavior and permissions requests
  Will detect configuration errors
  Monitor the permissions assigned to apps
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 8: Mobile Device Firewalls
Firewall apps
  Will monitor app activity and prevent connections to ports or IP addresses.
Firewall apps
  Filter outgoing connections
  Require Root level access to control
  VPN-based filtering (None Root Access)
Firewall apps
  Comodo
  Tiny Wall
  Net Defender
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 9: Mobile VPN Configuration
Virtual Private Network (VPN): A secure tunnel created via an unsecure network (typically the Internet).
Mobile VPN: A VPN that can maintain the VPN link across multiple carrier networks.
Tunnel contents is encrypted to secure communications.
Links maintained even in sleep mode.
Available as third-party apps for Android and iOS.

## Slide 10: Enterprise Mobility Management
Mobile device management (MDM)
  Enrollment
  App/feature control
  Profile of security requirements
Notes: Discuss some of the complexities of supporting BYOD and make sure students are aware of the general capabilities of MDM suites.

## Slide 11: Mobile MDM
MDM: (Mobile Device Management)
Is a class of enterprise software designed to apply security policies to the use of smartphones & Tablets
Mobile application management (MAM)
  Authentication policies
  Control device features (webcam/microphone)
  Remote device reset/data wipe
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 12: Mobile MDM: Encryption
Device Encryption:
  iOS, various levels of encryption.
  Encryption key is stored on the device.
  OS just deletes the key to Wipe the phone.
MDM Types:
  BYOD- Bring your own device
  COBO- Corporate owned, business
  COPE- Corporate owned, personally enabled
  CYOD- Choose your own device
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 13: Mobile MDM: Data Protection
Email Encryption:
  Email "Data Protection" option are subject to a second round of encryption using a key derived from the user’s credential.
Data Protection:
  Not all user data is encrypted by DP
  Options / Contacts / SMS messages /Pictures
  On Android -there are substantial differences to encryption options between versions
  IOS- DP is enabled automatically after passcode lock on the device.
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 14: Mobile Device: Locator Apps and Remote Wipe
GPS apps
  Requires line of sight to satellites.
  Geo-tracking related to Location Services.
  Location Services also supports apps like Find My Phone.
  IPS: (Indoor) uses location detection by triangulating its proximity radio sources, like Wi-Fi or Bluetooth beacons.
  The Location Service uses GPS and/or IPS to calculate a device's position on a map!
Notes: Teaching Tip: Share any stories from the news or your life, or ask learners to share stories about how locator apps have helped locate and recover mobile devices.

## Slide 15: Mobile Device Backup
Remote backup apps:
  iCloud, Google Sync or OneDrive
  Not Included - SMS and call history
IOS: macOS or Windows via iTunes program.
More options - MDM
Android: File explore, Droid Transfer, File Transfer to (Mac)

## Slide 16: Multifactor Authentication and Authenticator Applications
Factors:
  Something you know
  Something you are
  Something you have
  Somewhere you are
Multifactor authentication requires two different factors.
Authenticator apps help implement multifactor authentication.
  2-step verification: password/PIN (what you know) and cards (what you have).

## Slide 17: IOT Internet of Things Security
This describe the global network personal devices, home appliances, home control systems, vehicles,
These items have sensors, software, and network connectivity
Allowing them to communicate and pass data among themselves and computers
Mobile application management (MAM)
  Authentication policies
  Control device features (webcam/microphone)
  Remote device reset/data wipe
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 18: IOT Internet of Things Security
Security concerns
  Inadequate security monitoring/patching
  Weak defaults admin passwords
  Shadow IT- employees deploy a IOT device without going through management
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 19: IOT Internet of Things Security
Home Automation Systems:
  Hub/Control system: Talks to Wi-Fi, IOT are (headless) no user control interface, smartphone app or Voice to configure
  Smart device type: Most devices use a Linux or Android kernel
  Wireless mesh networking: coms between devices are likely to use mesh networking, such as Z-Wave or Zigbee.
Notes: Interaction Opportunity: Ask learners if they have experience with any remote wipe apps for mobile devices.

## Slide 20: Discussing Mobile Device Security
A company wants to minimize the number of devices and mobile OS’s to support but allow use of a device by employees or personal email and social networking.
What mobile deployment model is the best fit for these requirements?
ANSWER:
  Corporate owned, personally enabled (COPE) will allow standardization to a single

## Slide 21: Discussing Mobile Device Security
What two types of biometric authentication mechanism are supported on smartphones?
ANSWER:
  Fingerprint
  Facial

## Slide 22: Discussing Mobile Device Security
True or false? Updates are not necessary for iOS devices because the OS is closed source.
ANSWER:
  False— It is still subject to updates to fix problems and introduce new features.

## Slide 23: Discussing Mobile Device Security
What might a locator application be used for?
ANSWER:
  To identify the location of a stolen phone, find one's family member, and to provide localized services (Uber).

## Slide 24: Discussing Mobile Device Security
How can the use of mobile devices by employees affect the security of an organization as a whole?
ANSWER:
  Mobile devices can function much like regular computers
  They are used to send emails and to access systems and data network
  They are a vulnerability.

## Slide 25: Discussing Mobile Device Security
What technology mitigates against an online account being accessed from an unknown device?
ANSWER:
  Two-step verification—the site sends a code to a registered phone or alternative email address, prompting the user to verify the validity of the device.

## Slide 26: Discussing Mobile Device Security
What is MDM?
ANSWER:
  Mobile Device Management (MDM) is a class of management software designed to apply security policies to the use of smartphones and tablets in the enterprise.

## Slide 27: Topic B: Troubleshoot Mobile Device Issues

## Slide 28: Mobile OS Troubleshooting Tools
Adjust Settings
Close running apps
  Force stop
  Force Quit
Uninstall and reinstall apps
Reset the device
  Soft reset
  Forced restart
  Factory default reset
Android Force Stop
Notes: Teaching Tip: Note that mobile troubleshooting is covered on both Core 1 and Core 2 exams. The content examples on Core 1 are more weighted towards laptop troubleshooting and were covered elsewhere.
Core 2 duplicates some of the Core 1 content examples but is more exclusively focused on mobile OS troubleshooting
(though quite a few of the symptoms are hardware-related).
Teaching Tip: These explicit content examples have actually been removed in the new exam objectives, but learners should still know reset procedures to recover from faults such as "frozen system.”
Teaching Tip: You might want to mention that the terms used to speak about mobile reboots and resets are not always consistent. In usage with PCs, a soft reboot (or warm boot) means invoking the OS to perform the shutdown and restart procedure. A hard reboot (or cold boot) means holding down the power button to cut the power if the OS has stopped responding. On mobile devices, the term "soft reset" is used to mean powering off the device and then powering it back on again. As "hard reset" is quite widely used to mean a factory reset; we have used the term "forced restart" to mean cutting the power to force a reboot. Emphasize that the term "hard reset" could be used either to mean a forced restart or a factory default reset, depending on the context.

## Slide 29: Troubleshoot Device and OS Issues
OS fails to update
  Check compatibility, network, power, and storage and try restart
Device randomly reboots
  Check for hardware/overheating faults
  Check if issue persists after reboot/reset and isolate single app as cause
Device is slow to respond
  Check if issue persists after reboot/reset and isolate single app as cause
Screen does not autorotate
  Check configuration or isolate single app as cause

## Slide 30: Guidelines for Using Mobile Troubleshooting Tools
Adjust settings for the core OS and for apps.
Close running apps draining the battery or are unresponsive.
Uninstall apps that are no longer needed
Try a soft then a forced reset for frozen or unresponsiveness.
Perform a factory default reset

## Slide 31: Mobile OS Issue Troubleshooting
Dim display
Touchscreen unresponsive or inaccurate
External monitor issues
Sound issues
Overheating
Check for overheating
Check or change display brightness

## Slide 32: Guidelines for Troubleshooting Mobile OS Issues
Dim display.
  Open the Display settings and adjust the automatic brightness
  Check for apps that dim the backlight to conserve power.
Unresponsive or inaccurate touchscreen.
  Check screen protectors.
  Check that adequate resources available.
  Use a re-calibration utility.
Issues with external monitor.
  Verify that the cable is good.
  Verify that a casting dongle is configured correctly

## Slide 33: Guidelines for Troubleshooting Mobile OS Issues
Sound issues.
  Verify volume controls.
  Verify silent mode is not enabled.
  Check volume controls within the app.
  Verify if it is configured to use Bluetooth.
Overheating.
  Determine if the device is being used intensively.
  View battery status information.
  Direct sunlight or other heat sources.

## Slide 34: Mobile App Issue Troubleshooting
Apps not loading.
App log errors.
  Enter developer mode to view log files.

## Slide 35: Mobile App Issue Troubleshooting
Slow performance:
  Resources might be too low.
  Use an app such as CCleaner.
  Try soft resets, then factory default reset (as a last resort).
  Examine recently installed apps.

## Slide 36: Mobile App Issue Troubleshooting
Battery life:
  It will degrade over time.
  GPU and CPU intensive apps drain a battery quickly.
  Malicious apps using power-intensive services.
  Uninstall the app, or prevent it from running in the background.

## Slide 37: Guidelines for Troubleshooting Mobile App Issues
If an app is not loading:
  Verify that it wasn't installed on a memory card that is not in the mobile device.
  Verify that the app is not corrupted; uninstall and reinstall the app.
Put the device in developer mode to access log files.
Slow performance:
  Check for newer apps
  Check that apps are functioning correctly and are not running in the background.

## Slide 38: Troubleshoot Connectivity Issues
Signal strength and interference issues
  Move devices closer together and remove protective case or change hand position
Configuration issues
  Airplane mode or feature enable/disable
  Wi-Fi configuration and Bluetooth pairing
  Troubleshooting (NFC) Feature enable/disable or signal strength issue
Troubleshooting AirDrop issues
  iOS feature for file transfer between iOS and macOS devices vie Bluetooth
  The sender must be in the recipient’s contacts list, or AirDrop must be configured to receive files from everyone
  Bluetooth configuration and signal strength

## Slide 39: Mobile Wireless Issue Troubleshooting
Issues with any wireless connection type
  Wi-Fi
  Bluetooth
  Cellular radio
Determine whether
  Configuration error
  Hardware error
  Interference problem
    Wi-Fi analyzers
Notes: Teaching Tip: Refer learners back to the topic on network troubleshooting as well.

## Slide 40: Guidelines for Troubleshooting Mobile Wireless Issues
Interference issues
  Use a Wi-Fi Analyzer for signal strength.
Configuration issues
  airplane mode.
  a radio service (NFC) has not been disabled.
  Settings will verify that configuration are correctly configured.
  Wi-Fi access point supports same standard as mobile device.
If none of these are the issue, determine if an OS or firmware update is needed.

## Slide 41: Mobile Device Security Troubleshooting
Utilization symptoms
  Rogue apps running in background -power drain and high resource use
  Unauthorized location tracking
    Disable location services unless
    required by apps
  Install patches and upgrades

## Slide 42: Root Access Security Concerns
Owner-level permissions
  In iOS and Android, the user account created during setup can install apps, and configure settings. User are restricted from making any system-level changes.
  Users who want to avoid the restrictions that some OS vendors, and telecom providers must use some type of privilege escalation:
  Root access or custom ROM: (Android) Some vendors provide authorized mechanisms for access to the root account on their device.
  This may be necessary to exploit a vulnerability or use custom (firmware) a new Android OS image applied to the older device.

## Slide 43: Root Access Security Concerns
Root-level permissions
  Jailbreaking iOS is more restrictive than Android to gain Root privileges
  Sideload apps, change carriers, and customize the interface
Rooting or jailbreaking mobile devices involves subverting the security controls built into the OS to gain unrestricted system-level access
The device can no longer be assumed to run a trusted OS. (Warranty)

## Slide 44: Mobile App Soofing Security Concerns
App spoofing
  Rogue developers placing malicious apps in trusted stores
  Fake reviews and manipulated download figures
Bootleg app stores
  Pirated apps –looks like a legitimate app
Install apps by sideloading - This breaks licensing and copyrights laws, malware risks.
Under iOS, using the developer tools can be a means of installing apps from outside the App Store without having to jailbreak the device

## Slide 45: Mobile Device Security Troubleshooting
Enterprise apps and Android package (APK) sideloading
  Enterprise store distribution
  Android APK sideloading from untrusted sources
  System lockout:
  Forgotten password
  On purpose when the device is reported stolen or lost
Troubleshooting email problems:
  Verify credentials and email settings are correctly entered
  Verify corporate email password change is replicated to mobile devices
  Use digital certificates to encrypt messages

## Slide 46: Mobile Device Security Troubleshooting
User behavior issues
  Careless use
  Failure to follow security best practices
  Use of insecure hotspots
  Unintended Bluetooth pairing
System lockout
  Forgotten password
  On purpose when the device is reported stolen or lost
Troubleshooting email problems
  Verify credentials and email settings are correctly entered
  Verify corporate email password change is replicated to mobile devices
  Use digital certificates to encrypt messages

## Slide 47: Mobile Device Security symptoms
General symptoms
  High number of ads: Free apps are all supported by advertising
  Fake security warnings: (Scareware) is used by to persuade users to install an app or give a Trojan app additional permissions
  Sluggish response time: Malware is likely to try to collect data
  Limited/no Internet connectivity: Malware may corrupt the DNS and/or search provider to perform redirection and force users to spoofed sites.
  Unexpected application behavior
  Permissions and device usage
  High utilization and network traffic
  Leaked personal files/data
  Breach notification
  Unauthorized account access
  Location tracking

## Slide 48: Mobile Device Security symptoms
Unexpected app behavior
  Bootleg or spoofed app acts like a Trojan.
  Permissions and device usage camera/microphone
  High utilization and network traffic
Leaked personal files/data
  Compromised, files or personal data might be sold
  Unauthorized account access
  Location tracking
  Breach Notification - Notify users immediately that website or service had a data breach

## Slide 49: Troubleshooting Mobile Device Issues
True or false? A factory reset preserves the user's personal data.
ANSWER:
  False. Restoring to factory settings means removing all user data and settings.

## Slide 50: Troubleshooting Mobile Device Issues
What is the first step to take when an app no longer loads?
ANSWER:
  Try restarting the device. If that does not work, uninstall and then reinstall the app.

## Slide 51: Troubleshooting Mobile Device Issues
Your organization has several tablet devices that are loaned out as needed when employees are traveling. Some users have reported problems getting the Bluetooth keyboard to work with one of the tablets. What should you do?
ANSWER:
  There are a couple of issues that can cause Bluetooth connectivity problems. First, check whether the device batteries need replacing. Another possibility is that the tablet might need a system update. Finally, the devices might not have been set to discoverable mode. For security purposes, only enable discovery mode on your mobile device when want a Bluetooth device to find your device; otherwise, keep that setting disabled. The Bluetooth settings must be configured to allow devices to connect to the mobile device. This is also referred to as pairing.

## Slide 52: Troubleshooting Mobile Device Issues
A user reports that the touchscreen on his mobile device is not responding properly. What questions should you ask, and what steps might you take to resolve the issue?
ANSWER:
  You should ask if the touch screen is greasy, wet, or dirty. If it needs cleaning, remind the user to use only a soft cloth moistened with eye glass cleaner to gently wipe the screen. If cleaning is not an issue, ask if it appears to be scratched, cracked, or otherwise damaged. If so, make arrangements to have the touch screen replaced. If there is no visible damage, recalibrate the screen for the user, and check for updates.

## Slide 53: Troubleshooting Mobile Device Issues
What is a Wi-Fi Analyzer used for?
ANSWER:
  A Wi-Fi Analyzer is used to check connectivity issues with wireless. It can check for less congested channels.

## Slide 54: Troubleshooting Mobile Device Issues
What are the causes of severe battery drain?
ANSWER:
  The display, radio, and CPU are the components that draw the most power. If an app is overutilizing these resources, it could be faulty, badly written, or this could be a sign of malware activity.

## Slide 55
In your professional experience, have you supported mobile devices? If not, what kind of experience do you have with them?
What type of technical support do you think will be expected of an A+ technician as mobile devices become even more prominent within the workplace?