## Slide 1: CCNA 200-301, Volume 2
Chapter 6
Implementing Switch Port Security

## Slide 2: Objectives
Port Security Concepts and Configuration
Port Security Violation Modes

## Slide 3: Source MAC Addresses in Frames as They Enter a Switch

## Slide 4: Port Security Configuration Steps
Step 1: Use the switchport mode access or the switchport mode trunk interface subcommand to make the switch interface either static access or trunk interface.
Step 2: Use the switchport port-security interface subcommand to enable port security on the interface.
Step 3: (Optional) Use the switchport port-security maximum number interface subcommand to override the default maximum number of allowed MAC addresses associated with the interface (1).

## Slide 5: Port Security Configuration Steps (Continued)
Step 4: (Optional) Use the switchport port-security violation {protect | restrict | shutdown} interface subcommand to override the default action to take upon a security violation (shutdown).
Step 5: (Optional) Use the switchport port-security mac-address mac-address interface subcommand to predefine any allowed source MAC addresses for this interface. Use the command multiple times to define more than one MAC address.

## Slide 6: Port Security Configuration Steps (Continued)
Step 6: (Optional) Use the switchport port-security mac-address sticky interface subcommand to tell the switch to “sticky learn” dynamically learned MAC addresses.

## Slide 7: Port Security Configuration Example

## Slide 8: Variations on Port Security Configuration

## Slide 9: Configuration Added by the Port Security Sticky Feature

## Slide 10: Using Port Security to Define Correct MAC Addresses of Particular Interfaces

## Slide 11: Using Port Security to Define Correct MAC Addresses of Particular Interfaces (continued)

## Slide 12: Using the secure Keyword to See MAC Table Entries When Using Port Security

## Slide 13: Actions When Port Security Violation Occurs
Option on the switchport port-security violationComma nd | Protect | Restrict | Shutdown
Discards offending traffic | Yes | Yes | Yes
Sends log and SNMP messages | No | Yes | Yes
Disables the interface by putting it in an err-disabled state, discarding all traffic | No | No | Yes

## Slide 14: Confirming the Port Security Violation Mode

## Slide 15: Port Security Status in the Shutdown Mode After a Violation

## Slide 16: Summary of Actions: Port Security Violation Mode Shutdown

## Slide 17: Port Security Using Protect Mode

## Slide 18: Port Security Using Violation Mode Restrict

## Slide 19: Summary of Actions: Port Security Violation Mode Restrict