## Slide 1
Real-Time Radar (Features and Design)

## Slide 2: High-Level Requirements
The Radar must be able to maintain real-time performance
  And the radar should be able to run in a non-real time mode as well
An operator will have the ability to interact with the radar systems and view the raw video and plots (i.e., virtual mode)
  And the radar must be able to operate without operator interaction as well (i.e., constructive mode)
A single simulation application will need be able to run multiple, independent radars
  Hybrid applications must be able to contain radars that are operating as either constructive or virtual radars
The operator's graphical interface and the radar model will need be able to run in separate applications

## Slide 3: High-Level Requirements
The level of fidelity of the radar will need be scalable from a virtual radar station to a simple ‘spinner’
The radar will need to interact with locally generated players
The radar will need to interact with players generated by remote simulation applications
The radar will need to filter players by type, range, and aspect angles

## Slide 4: Example (Out of the Box Fidelity)

## Slide 5: Graphical View (testRadar)

## Slide 6: Example Inputs
Player definition consists of defining initial position, direction, velocity, etc... and the various components attached/associated with it.
Components consist of a collection of antennas and sensors
There are two antennas, both steered by a gimbal: one is used by radar system (“radar”), the other for a radar warning receiver (“rwr”)
There are two sensors: a track while scan (Tws) and a radar warning receiver (Rwr) – both reference the antenna components that are being steered by the gimbal

## Slide 7: A Comment About Inheritance
Class inheritance can lead to not only highly coupled code, but also relationships that make no sense
  We have some of this.... (e.g., an Antenna IS a Gimbal)
Example, antennas don’t have a search volume or commanded rates – our scan gimbal does
  The subclassing of an Antenna from Gimbal creates this mixture – our Antennas act like both “an antenna” –AND- “a scan gimbal”

## Slide 8: Example of Confounded Parameters
When parameters from one class are inherited by another conceptually unrelated class
The adjustable parameters associated with an Antenna include those defined & by a scan gimbal

## Slide 9: Adjustable Parameters

## Slide 10: Architecture & Implementation

## Slide 11: Application Pattern
Station
Simulation
Player List
DIS
HLA
TENA
PVIs
Linkage
Control
Loading
GUIs
Player
Player
IPlayer
Dynamics Model
(Auto) Pilot
Navigation
Onboard Computers
Datalink
Radios
Gimbals, Antennas and Seekers
R/F and IR Sensors
StoresMgr
Weapons
Routes
Track
Managers
Tracks
R/F & IR Signatures
External
Stores
Waypoints
…
…
IPlayer
OTW interfaces
Environments

## Slide 12: Application Pattern (Sim Exec, Environments & Player Lists)
Station
Simulation
Player List
DIS
HLA
TENA
PVIs
Linkage
Control
Loading
GUIs
Player
Player
IPlayer
Dynamics Model
(Auto) Pilot
Navigation
Onboard Computers
Datalink
Radios
Gimbals, Antennas and Seekers
R/F and IR Sensors
StoresMgr
Weapons
Routes
Track
Managers
Tracks
R/F & IR Signatures
External
Stores
Waypoints
…
…
IPlayer
OTW interfaces
Environments

## Slide 13: Simulation Class
Manages the player list
Manages the environment databases (e.g., Terrain Elevations)
Can be used to embed the simulation (library) into other simulation systems
Supports multiple time critical and background threads when processing the player list
Manages the frame, cycle and phase timing
  Phases
    P0 Dynamics
    P1 Transmitter Processing
    P2 Receiver Processing
    P3 Guidance And Management

## Slide 14: Frames & Phases
Frames, Phases and Cycles
  Frame rate is master clock rate:
    50 frames per seconds
  Frame time (i.e., delta time): frameTime = 1/frameRate
    20 Ms per frame
  Frame can be partitioned into phases
    4 phases per frame
  Frames can be grouped into cycles (usually a power of 2)
    16 frames per cycle
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
Phase 1
Phase 3
Phase 4
Time
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
Phase 1
Phase 3
Phase 4
Time
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
F
One Cycle (16 Frames)
Time
Phase 1
Phase 3
Phase 4
Phase 2

## Slide 15: Application Pattern (Players & Major Components)
Station
Simulation
Player List
DIS
HLA
TENA
PVIs
Linkage
Control
Loading
GUIs
Player
Player
IPlayer
Dynamics Model
(Auto) Pilot
Navigation
Onboard Computers
Datalink
Radios
Gimbals, Antennas, Beams and Seekers
R/F and IR Systems
StoresMgr
Weapons
Routes
Track
Managers
Tracks
R/F & IR Signatures
External
Stores
Waypoints
…
…
IPlayer
OTW interfaces
Environments

## Slide 16: Player Class
Purpose: provide a common interface for player ID, type, status, state vector, control flags, sub-systems, event handling, etc.
Player types (derived classes)
  Air vehicles
  Ground vehicles
  Ships
  Space vehicles
  Weapons
  Decoys
Major components
  Signatures (R/F and IR)
  Gimbals, Antennas and IR Seekers
  R/F systems
  IR systems
  On-board computer models & track managers
  Navigation models
  Datalinks
  Dynamics models
  Autopilot model
  Store management systems

## Slide 17: Application Pattern (Distributed Simulations)
Station
Simulation
Player List
DIS
HLA
TENA
PVIs
Linkage
Control
Loading
GUIs
Player
Player
IPlayer
Dynamics Model
(Auto) Pilot
Navigation
Onboard Computers
Datalink
Radios
Gimbals, Antennas and Seekers
R/F and IR Sensors
StoresMgr
Weapons
Routes
Track
Managers
Tracks
R/F & IR Signatures
External
Stores
Waypoints
…
…
IPlayer
OTW interfaces
Environments

## Slide 18: Application Pattern (Controls & Displays)
Station
Simulation
Player List
DIS
HLA
TENA
PVIs
Linkage
Control
Loading
GUIs
Player
Player
IPlayer
Dynamics Model
(Auto) Pilot
Navigation
Onboard Computers
Datalink
Radios
Gimbals, Antennas and Seekers
R/F and IR Sensors
StoresMgr
Weapons
Routes
Track
Managers
Tracks
R/F & IR Signatures
External
Stores
Waypoints
…
…
IPlayer
OTW interfaces
Environments
Ownship

## Slide 19: EW Radar Test Application
Station
Simulation
Player List
DIS
EW
Players
Target
Players
Navigation
Datalink
Antennas and Beams
Radars and
Channels
Target
IPlayers
User Interface
Environments
R/F Signatures
(Plots)
Ownship

## Slide 20: EW Radar
Beam Center
ECM Xmit
Radar Pulse
SOJ

## Slide 21: RF – Emission Path
EW Player
  Radar with transmitter and receiver functions
  Antenna assigned to the Radar
Target Player
  RWR and Jammer controlled by a Sensor Manager
  Antennas assigned to each
Player #2
  Requested emissions reflected from Player 2
Radar
RWR
Jammer
Transmitter
Receiver
Antenna
Antenna
Receiver
Antenna
Transmitter
Track Mgr
Sensor Manager
EW Radar Player
Target #2
Target Player

## Slide 22: RF– Emission Path (cont)
(1) EW Radar transmitter creates an RF emission packet, which contains the waveform parameters, and passes the packet to its antenna
(2) For each player of interest, the antenna clones the emission packet, added target player specific geometry and gain data, and sends emission packets to the target player
Radar
RWR
Jammer
(1)
(2)
(2)
Transmitter
Receiver
Antenna
Antenna
Receiver
Antenna
Transmitter
Track Mgr
Sensor Manager
EW Radar Player
Target #2
Target Player

## Slide 23: RF– Emission Path (cont)
(3) Using the waveform parameters and geometry from the emission packets, the target players compute their radar cross section (RCS) and send the modified packets back to the EW antenna
  (3a) And the packets are passed to any other player that requested them
(4) The target players can send the emission packets to their own onboard antennas for processing
Radar
RWR
Jammer
(1)
(2)
(3)
(4)
(3a)
(2)
Transmitter
Receiver
Antenna
Antenna
Receiver
Antenna
Transmitter
Track Mgr
Sensor Manager
EW Radar Player
Target #2
Target Player

## Slide 24: RF– Emission Path (cont)
(5) Antennas that are assigned to receivers will apply gains and pass the emission packets to their receivers
(6) The receivers apply any final effects (e.g., noise, ECM). Emissions that exceed a given threshold are sent as plot reports
(7) Track managers will generate tracks
Radar
RWR
Jammer
Plots
(3)
(4)
(5)
(5)
(6)
(6)
(3a)
(7)
Transmitter
Receiver
Antenna
Antenna
Receiver
Antenna
Transmitter
Track Mgr
Sensor Manager
EW Radar Player
Target #2
Target Player

## Slide 25: RF– Emission Path (cont)
(8) The jammer transmitter creates an ECM emission packet and sends it to its assigned antenna
(9) The jammer antenna after computing geometry and gains, sends ECM packets to other players
(10) Players pass the ECM packets to their own onboard antennas
(11) The antennas, which are assigned to receivers, will apply gains and pass the ECM packets to the receivers for processing
Radar
RWR
Jammer
(5)
(5)
(6)
(6)
(8)
(9)
(10)
(11)
(9)
(7)
Plots
Transmitter
Receiver
Antenna
Antenna
Receiver
Antenna
Transmitter
Track Mgr
Sensor Manager
EW Radar Player
Target #2
Target Player

## Slide 26: Emission Packets
SensorMsg Class
  Used to pass data and requests between sensors and players
    Used by R/F systems (via Emission class) and IR systems (via IrQueryMsg class)
  Contains standard geometry data between the ownship and target player
    Normalized ownship to target and target to ownship LOS vectors
    Angles to target in gimbal coordinates
    Range and range rate
    Target's Angle Of Incidence (AOI)
    Pointers to the players and systems
SensorMsg
Class
Emission
Class

## Slide 27: Emission Packets
Emission Class
  Used as the emission packet by RF systems and sensors (Radars, Radios, Jammers, etc.)
  Extends the SensorMsg with R/F waveform parameters
    Peak power, center frequency, PRF, pulse width, antenna gains, polarization, loses and the RCS from the target player
  Unique packet is generated for each transmitting antenna to target player pair
SensorMsg
Class
Emission
Class

## Slide 28: Target Signatures (RCS)
Signature Class
  Base class for all R/F signatures
  Is attached to the target players
    i.e., it’s not part of the radar system
  Defines a standard interface (virtual function) used to compute the RCS based on the waveform and geometry data in the emission packet
    rcs = getRCS(p);
      Where ‘p’ points to an instance of an Emission class (i.e., the emission packet received by the target player from a transmitting antenna)
      Where ‘rcs’ is the computed radar cross section in meters squared.
Signature
Class
Specific Signatures

## Slide 29: Target Signatures (RCS)
Specific Signature Classes
  Derived classes implement the specific signatures
    RCS is computed based on the geometry data and waveform parameters from the emission packet
    Can be simple or complex, as needed
  Several test Signature classes
    SigConstant – Constant RCS value
    SigSphere – Computes RCS for a sphere of a given radius
    SigPlate – Computes RCS for a plate with a given width and height, and always normal to the transmitter SigDihedralCR
    SigDihedralCR – Dihedral Corner Reflector based on edge length, and always facing the transmitter
Signature
Class
Specific Signatures

## Slide 30: R/F Static Class Structure
Antenna
ScanGimbal
Gimbal
Radar
RfSensor
RfSystem
1
System
Component
Tdb
Player
*
*
*
*
Gain Functions
0 .. 1

## Slide 31: Target Data Blocks
List of players of interest, with associated geometry data, used by an IR seeker, R/F antenna or beam
Created and managed by the Gimbal class
Filters players by type, range and aspect angles
Performs terrain occulting checks
Performs horizon masking checks
Computes radar to target geometry for each player of interest
Antenna
ScanGimbal
Gimbal
Tdb
Player
*
*
Gain Functions
0 .. 1

## Slide 32: Gimbal Class
Base class for all gimbals, RF antennas, IR seekers, etc
Position or Rate servo
  Mechanical or Electronic
Parameters
  Location of the gimbal in its parent’s coordinate system
  Angles (azimuth, elevation and roll)
Can contain other Gimbals as sub-components
Transformation matrix
  gimbal coordinates to/from ownship’s body coordinates
  Includes all parent gimbals
Antenna
ScanGimbal
Gimbal
Tdb
Player
*
*
Gain Functions
0 .. 1

## Slide 33: ScanGimbal Class
Implements a standard set of scan (search) patterns
  Horizontal bar scan
  Vertical bar scan
  Conical scan
  Circular scan
  Pseudo random scan
  Spiral scan
Antenna
ScanGimbal
Gimbal
Tdb
Player
*
*
Gain Functions
0 .. 1

## Slide 34: Antenna Class
Transmit
  Receives emission requests from its assigned transmitter
  Uses the current Tdb to compute geometry
  Applies antenna gain using an attached function
  Emissions that exceed a given threshold are sent to the target players
Receive
  Receives incoming emission packets
    Returns from own transmissions
    Emissions received by own Player that originated from other players
  Applies the antenna gain using an attached function
  Emissions that exceed a given threshold are passed to the receiver
Antenna
ScanGimbal
Gimbal
Tdb
Player
*
*
Gain Functions
0 .. 1

## Slide 35: Gain Functions
The antenna gain functions are implemented using standard Function and Table classes, which are part of the ‘basic’ library
One dimensional gain functions
  The dependent variable is the angle off the beam center to the target
Two dimensional gain functions
  First dependent variable is the azimuth angle off the beam center to the target
  Second dependent variable is the elevation angle off the beam center to the target
Antenna
ScanGimbal
Gimbal
Tdb
Player
*
*
Gain Functions
0 .. 1

## Slide 36: RfSystem Class
Antenna
Radar
RfSensor
1
Generic class for all R/F type systems
  Radars
  Jammers
  Radio: Datalink, Comm, NAV and SATCOM
Contains basic waveform parameters
  Frequency
  Bandwidth
  Peak Power
Antennas are attached to R/F systems
Can contain other R/F systems as sub-systems
Player
RfSystem

## Slide 37: RfSensor Class
Antenna
Radar
RfSensor
1
Base class for R/F Sensor Models
  Radars
  Radar Warning Receivers
  Jammers
Parameters
  Pulse Rate Frequency (PRF)
  Pulse Width
  Ranges
  Modes
Assigned an optional track manager
Can contain other R/F sensors as sub-systems (e.g., submodes)
Player
RfSystem

## Slide 38: Radar Class
Antenna
Radar
RfSensor
1
Brings together the various R/F components to function as a Radar systems
Synchronizes the transmission of the emission packets
Determines target detection and generates plots
Player
RfSystem

## Slide 39: Multi-Beam Radar
Multi-beam
Radar and Antenna

## Slide 40: High-Level Requirements
The radar model will need to generate multiple R/F beams, each with its own waveform parameters
  The waveform parameters will include the frequency, peak power, pulse width, and pulse rate frequency
Each of the R/F beams will have the ability to sequence through multiple waveform definitions
The beam gain patterns will be defined from an input file

## Slide 41: Multi-Beam Radar
Multi-beam is like a single antenna with additional antennas attached
Each additional antenna controls its own beam
Each additional antenna is controlled by its own R/F Channel within the multi-beam Radar
R/F Channel
R/F Channel
R/F Channel
Multi-Beam Radar
Multi-Beam Antenna

## Slide 42: Multi-Beam Radar System
R/F Beam
R/F Channel
R/F Beam
R/F Channel
R/F Beam
R/F Channel
R/F Beam
R/F Channel
Multi-Beam
Radar
Multi-Beam
Antenna
The multi-beam radar system is a composite of one or more sub-radars, each of which consists of a R/F channel/beam pair
The R/F channels are managed by their container multi-beam radar, which synchronizes their modes and operations
The R/F beams are slaved to their container multi-beam antenna, which control the overall azimuth and elevation angles of the search radar

## Slide 43: Multi-Beam Radar
RfBeam
Antenna
ScanGimbal
Gimbal
RfChannel
Radar
RfSensor
RfSystem
1
System
Tdb
Player
*
*
*
MultiBeam
Radar
MultiBeam
Antenna
Gain Function
0 .. 1
*
*

## Slide 44: TPS-43 Side Lobe Rejection
“A sidelobe reference antenna is mounted on the antenna assembly. The pattern coverage of this antenna approximately encompresses the sidelobe structure of the radar antenna and is use to minimize the detection of targets in the radar antenna sidelobes.” (ref)
An additional, auxiliary R/F channel and beam will be used to simulate this antenna
  The aux channel is receive only and will process the emissions sent by the main beams
  The Aux and main receiver signals are compared and if the aux signal is stronger, then the main signal is rejected

## Slide 45
Emission packets from each of the 6 beams being sent to target player
Target player sends emission packets back to the source antenna beam
Each RfBeam then pass along the same emission packet to the parent Multi-Beam antenna
Multi-Beam Antenna then pass the emission packets to the Aux RfBeam
RfBeam 1
R/F Channel
RfBeam 2
R/F Channel
RfBeam 3
R/F Channel
RfBeam 4
R/F Channel
RfBeam 5
R/F Channel
RfBeam 6
R/F Channel
EW Radar
Multi-Beam
Antenna
Aux
RfBeam
Aux
R/F Channel
Out Emissions
Target
Return Emissions
(1)
(2)
(3)
Return Emissions
(4)
Return Emissions
(5)
Emission Reports from RfBeams
Return Emissions
(6)
Emission Reports from Aux RfBeam
(7)
(8)
Design approach for adding Aux Beam to the EW Radar

## Slide 46
Aux RfChannel receives and process the emissions and generates reports
Aux RfChannel pass the emission reports to EWRadar
RfChannel pass the emission reports to EWRadar
EW Radar then compares the reports from 6 beams with reports from Aux beam and rejects signals that’s greater than signals from Aux Beam
Design approach for adding Aux Beam to the EW Radar
RfBeam 1
R/F Channel
RfBeam 2
R/F Channel
RfBeam 3
R/F Channel
RfBeam 4
R/F Channel
RfBeam 5
R/F Channel
RfBeam 6
R/F Channel
EW Radar
Multi-Beam
Antenna
Aux
RfBeam
Aux
R/F Channel
Out Emissions
Target
Return Emissions
(1)
(2)
(3)
Return Emissions
(4)
Return Emissions
(5)
Emission Reports from RfBeams
Return Emissions
(6)
Emission Reports from Aux RfBeam
(7)
(8)

## Slide 47
Basic Horizon Masking
Local tangent plane
Pa
Pt
horizon
r
Pa => Antenna Position
Pt => Target Position
r = local earth radius
A target is not horizon masked if …
The distance to the target is less than the distance to the horizon
Or, the local angle (up+) to the target is greater than the angle to the horizon
∴ The tangent of the local angle to the target is greater than the tangent of the angle to the horizon

## Slide 48: Basic Horizon Masking Distance & Angle to Horizon
r
ha
dh
qh
qh
dh => distance to horizon
qh => Angle to horizon
r = earth radius
ha = antenna height
a = r + ha
dh = sqrt (a2 – r2)
tan qh = dh / r
Pa

## Slide 49
qt
Tlos
Basic Horizon Masking Distance & Angle to Target
dt => distance to target
qt => Angle to target
Tlos => TGT LOS vector (NED)
dx => Tlos X Component
dy => Tlos Y Component
dz => Tlos Z Component
dxy2 = (dx2 + dy2)
dt = sqrt (dxy2 + dz2)
dxy = sqrt (dxy2)
tan qt = dz / dxy
dt
dxy
dz
Pa

## Slide 50
Over the Horizon Radars
Pa
Pt
Pa => Antenna Position
ha => Antenna Height (HAE)
Pt => Target Position
ht => Target Height (HAE)
dt => Distance to target
r => local earth radius
Some radars have the ability to detection targets at very long ranges
These radars make use of the refraction of the R/F beam by the earth’s atmosphere, which gives them the ability to detect targets over the horizon
This in effect creates a new horizon called the “radio horizon”
ha
ht
r
dt

## Slide 51
Over the Horizon Radars
r
The radio horizon can be simulated by expanding the earth’s radius, r’, while keeping the antenna and target heights and the distance to the target constant
As before, a target is not radio horizon masked if …
The true distance to the target is less than the distance to the radio horizon
Or, the new, expanded angle to the target is greater than the angle to the radio horizon
Radio horizon
r’
Pa
Pt
ha
ht
dt

## Slide 52: Over the Horizon Radars Distance & Angle to Radio Horizon
r’
ha
dh
qh
dh => Distance to horizon
qh => Angle to horizon
r’ = expanded earth radius
ha = antenna height
a = r’ + ha
dh = sqrt (a2 – r’2)
qh = acos( r’ / a )
Pa
r’

## Slide 53
Over the Horizon Radars
New Angle to Target
The angle to the target is computed using the law of cosines:
a2 = b2 + c2 - 2bc cos(qt’)
or
qt’ = acos( (b2 + c2 - a2) / 2bc )
Radio horizon
r’
Pa
Pt
ha
ht
b = dt
dt => True distance to tgt
qt’ => Angle to target
qt’
a = r’ + ht
c = r’ + ha
r’

## Slide 54: Elevation Posts
ALT[1]
ALT[2]
ALT[3]
ALT[N]
Terrain
Altitude =
Radar
Altitude
= ALT0
1*Max/N
2*Max/N
3*Max/N
N*Max/N
N = number of points in the array
Max = Maximum distance of array
For each azimuth ray, we generate an array of N terrain elevation samples, or posts, from the radar’s position to the maximum distance, Max.
The posts are evenly spaced with a spacing of Max/N.
Each post has a ground range, rg, equal to it’s index * Max/N
Although not shown, the elevation post values are modified to account for earth curvature.

## Slide 55: Terrain Shadow Areas
ALT[1]
ALT[2]
ALT[3]
ALT[N]
Terrain
Altitude =
Radar
Altitude
= ALT0
1*Max/N
2*Max/N
3*Max/N
N*Max/N
N = number of points in the array
Max = Maximum distance of array
For each elevation post, starting with the closest, the point is visible if the angle to the point is greater than all previous points.
A point is hidden, or in shadow, if the angle to the point is less than the angle to any previous point, Pmax. (see red dashed lines)
Pmax

## Slide 56: Terrain Tangents
ALT[1]
ALT[2]
ALT[3]
ALT[N]
Terrain
Altitude =
Radar
Altitude
= ALT0
1*Max/N
2*Max/N
3*Max/N
N*Max/N
N = number of points in the array
Max = Maximum distance of array
Dh => Height of the antenna minus the elevation post, ALT[i]
rg => Ground range to the elevation post
tan a = Dh / rg
rg
Dh
a
To increase performance, the tangent of the angle to each post can be used to compared with the previous posts.

## Slide 57: Target/Terrain Occulting
ALT[1]
ALT[2]
ALT[3]
ALT[N]
Terrain
Altitude =
Radar
Altitude
= ALT0
1*Max/N
2*Max/N
3*Max/N
N*Max/N
As defined by terrain shadows, a point is occulted, or hidden, when it has a smaller angle than an elevation post that is closer to the radar.
That is, for each elevation post with a range less than the target, the target is occulted if any post has an angle greater than the angle to the target.
To increase performance, the tangent of the angle to the target can be used to compare to the closer elevation posts.
Pmax

## Slide 58: Clutter Equivalent Cross Section (σ) Equation using DTED Terrain Data
Elevation View
Plan View
Radar
Radar
Patch
Area
Beam Width (Φ)
Beam Width (Φ)
Normal to Ground Vector (n)
Ө
Calculate DTED intersection point. If no intersection within max range then σ = 0
Check if it is in shadow. If yes then σ = 0
Calculate COSθ. If COSθ ≤ 0 then σ = 0 (This also indicates it is in shadow)
Otherwise calculate σ = σ0 A
Where:
σ0 = Clutter Coefficient predefined from table
A = Patch Area = 2π[R*tan(Φ /2)]2 / COS θ
Φ = Beam Width
R = Vector from Terrain Intersection to Radar
R = Magnitude of R = |R| , r = unit vector = R / R
n = normal to ground unit vector
COS θ = r ∙ n (unit vector dot product)
Note – These calculations assume constant surface normal over the patch area. A more accurate approach would evaluate each DTED facet across the patch area with the contribution from each facet added separately. This is not implemented due to processing speed considerations.

## Slide 59: Clutter Computations
ALT[1]
ALT[2]
ALT[3]
ALT[N]
Terrain
Altitude =
Radar
Altitude
= ALT0
Beam Elevation Angle
1*Max/N
2*Max/N
3*Max/N
N*Max/N
Loop through the Terrain Altitude Array from [i] = 1 to N,
IF OCC[i] = 0 (False) or if (i * Max/N) ≥ Maximum Clutter Distance,
Then
Equivalent Cross Section (σ) = 0.
Else,
Range to terrain element (R) = SQRT[ (i * Max/N)2 + (ALT[i] – ALT0) 2 ]
Off-Axis Elevation Angle from Antenna = ASIN[(ALT[i] – ALT0) / R] – Beam Elevation (Use for Antenna Gain Calculation)
Surface Normal = AAC[i] (array of terrain normals) = COS θ of Terrain for cross section calculation
OCC[1]
OCC[2]
OCC[3]
OCC[N]
Occulting
Flag =
AAC[1]
AAC[2]
AAC[3]
AAC[N]
Surface
Normal =

## Slide 60: Clutter Processing Integrated into the Radar Framework
RfBeam 1
R/F Channel
RfBeam 2
R/F Channel
RfBeam 3
R/F Channel
RfBeam 4
R/F Channel
RfBeam 5
R/F Channel
RfBeam 6
R/F Channel
EW Radar
Multi-Beam
Antenna
Aux
RfBeam
Aux
R/F Channel
Clutter Emission packet
(1)
In rfTransmit() method, add calculations to calculate clutter equivalent cross section for the DTED intersection point for the beam
Create the Emission packet with the clutter equivalent cross section and send the packet to the RfChannel. (call onRfEmissionReturnEventAntenna() method. The packet will have a null pointer for the target player
(2)
(3)
Emission Reports from RfBeams
Emission Reports from Aux RfBeam
Clutter Emission packet
Clutter Emission packet
Radar memory (Range bins)
(4)

## Slide 61: Clutter Processing Integrated into the Radar Framework
RfBeam 1
R/F Channel
RfBeam 2
R/F Channel
RfBeam 3
R/F Channel
RfBeam 4
R/F Channel
RfBeam 5
R/F Channel
RfBeam 6
R/F Channel
EW Radar
Multi-Beam
Antenna
Aux
RfBeam
Aux
R/F Channel
Clutter Emission packet
(1)
The packet will go though the same flow as other emission packets
The clutter emission data will then be written to the radar memory (range bins). To save CPU time, if radar is ground based, once the clutter data is written to memory, they won’t get erased, and RfBeams won’t generate new clutter emission packets once the radar completes 1 full sweep
(2)
(3)
Emission Reports from RfBeams
Emission Reports from Aux RfBeam
Clutter Emission packet
Clutter Emission packet
Radar memory (Range bins)
(4)

## Slide 62
Design approach for EW Radar Range Bin
4 rays / degree
512 bins / ray
Radar memory
RangeBinObj contains multiple RangeBinData objects
Radar memory is partitioned into 360 degree with 4 rays per degree, 512 range bins per ray, with each bin contains a single RangeBinObj which contains multiple RangeBinData objects. The data objects are created once and new data are copied to into these objects to reduce processing time.
Attributes included in RangeBinData object:
  Signal to noise ratio value at the time of detection
  Latitude, Longitude, Altitude of the detected target or clutter
  Range of the target or clutter
  Azimuth
  Range rate (Closure)
  Pointer to signal characteristics (emission packet)
  Pointer to the target
Each bin contains a single RangeBinObj

## Slide 63
Design approach for EW Radar Range Bin
4 rays / degree
512 bins / ray
Radar memory
RangeBinObj contains multiple RangeBinData objects
After detection reports generated from 6 main beams and evaluated against the reports from the Aux beam, a new RangeBinData object is created for each of the updated detection reports
The RangeBinData object is then written (stored) in the radar memory object based on the azimuth and range of the detected target/clutter
The range bins in each ray will be cleared after each sweep
The memory object can be retrieved by the radar scope for display
Currently we are assuming radar scope will handle the aging of the signal
Each bin contains a single RangeBinObj