## Slide 1: Visualization 201 Creating Great Images Easily With RealView and PhotoView 360
Ron Bates, Senior Manager – Graphical Applications
DS SolidWorks Corporation

## Slide 2: Presenter
Ron Bates – Ron.Bates@3ds.com
  Senior Manager - Graphical Applications
    Core graphics systems
    RealView Graphics
    PhotoView 360
    eDrawings

## Slide 3: Random Tidbits
You can get this material at http://robrodriguez.com/wordpress/
  Go to the “downloads” section and find plenty of other material there as well.
Renderings and some (older) video tutorials at www.solidworksgallery.com
FORUMS
Coming soon…
  PhotoRealistic Rendering Using SolidWorks and PhotoView 360 STEP-BY-STEP

## Slide 4: What we’ll discuss
Display Modes
Workstation Graphics
Appearances
  Types, hierarchy, adding/editing
Texture and decal mapping
RealView and lights
Big changes in 2011
  General changes
    New Display Manager
    Decals in core SW
    Custom scenes in core SW
    Custom appearances in core SW
  RealView changes
    Illumination controls
    Surface finish controls
  PhotoView 360 changes
    UI overview
    Additional appearance and scene controls
    Lighting
    Options
      Caustics
      Contour

## Slide 5: Display Modes
OpenGL (no RealView) is a platform independent programming API for doing basic 2D and 3D graphics requiring no special hardware.
  Material shading including color, ambient light, diffuse, specular, transparency, etc.
  Basic texture mapping
  Diffuse ground shadow
RealView is a GPU (Graphics Processing Unit) hardware accelerated mode allowing more advanced shading techniques and effects in real-time. RealView effects include:
  Advanced Shading
  Environment and Ground Reflections
  Self shadows, Accurate ground shadows
  Advanced texture mapping and bump maps
PhotoView 360 is ray tracing application which uses the CPU to calculate real world lighting and shading effects. They include all of the RealView effects but more accurate and additional effects
  Self-Reflection (reflection of objects in one another)
  HDRI (environment) lighitng
  Indirect/Global Illumination
  Caustics

## Slide 6: Display Modes
OpenGL
RealView
PhotoView 360
Environment Reflections
Ground Reflections
Directional/Self Shadows
Environment and inter-reflections
True transparency with IOR
Extremely accurate lighting and shadows

## Slide 7: Workstation Graphics – AMD / ATI and nVidia Offerings
Why “workstation” (professional) graphics?
Lifecycle
Certification/Testing
SUPPORT!
AMD / ATI FirePro™ www.amd.com/firepro
  Price Level Model Memory Bandwidth
    $ 109 Entry FirePro V3800 512MB 14 GB/sec
    $ 469 Mid FirePro V5800 1GB 64 GB/sec
    $ 799 High FirePro V7800 2GB 128 GB/sec
    $1499 Ultra High FirePro V8800 4GB 147 GB/sec
nVidia www.nvida.com
  Price Level Model Memory Bandwidth
    $ 169 Entry Quadro 600 1GB 25 GB/sec
    $ 449 Mid Quadro 2000 1GB 42 GB/sec
    $ 779 High Quadro 4000 2GB 90 GB/sec
    $1769 Ultra High Quadro 5000 2.5GB 120 GB/sec

## Slide 8: Appearances – Two Types; Procedural and Textural
Procedural Appearances
  Color (RGB value) uniformly defines appearance.
    Can consist of primary and secondary colors
Textural Appearances
  2D image defines appearance.
  Textural Appearances must be mapped to their correct size/orientation/location.
A procedural appearance that uses a surface finish must also be mapped.

## Slide 9: Appearances – Two Types; Procedural and Textural
2010 used different thumbnails to represent procedural and textural appearances
2011 uses the same thumbnails.
Mapping for textural appearances is denoted by presence of mapping controls when editing the appearance.
2010
2011

## Slide 10: Appearances – Hierarchy
Face
Feature
Feature
Body
Body
Part
Part
Component overwrites all part appearances…
Face
-Over-
-Over-
-Over-

## Slide 11: Appearances - Applying
Drag and drop appearances into SolidWorks Window results in
“Heads Up” Preview
Mouse over shows preview of
Appearance on that reference.
Mouse “away” to cancel
CLICK IT TO APPLY

## Slide 12: Appearances - Applying
Affects
PART
Affects
ASSEMBLY
COMPONENT

## Slide 13: Appearances – other ways of adding, editing, removing
Use Edit Appearance command (with or without pre-selections)
  Pre-selections feed the selection box in appearance property manager
  Or you can select items after the property manager comes up
  No pre-selections = selecting of top model (part or assembly) by default
  “old fashioned way”

## Slide 14: Appearances – other ways of adding, editing, removing
Double click the appearance in the taskpane
  Applies to whatever is pre-selected
  No pre-selections = selecting of top model (part or assembly) by default
Pre-Select and use the Add Appearance button
  Same as a double-click of the appearance

## Slide 15: Appearances – other ways of adding, editing, removing
Using the Display Pane (NO ACCESS TO FACES)

## Slide 16: Appearances – other ways of adding, editing, removing
Drag and Drop from the task pane
Hit ALT while dragging to immediately invoke the appearance PM to make known edits

## Slide 17: Appearances – other ways of adding, editing, removing
On-screen callouts
Recommended workflow
Exclusively drag/drop to apply
ALT if I know I’m going to tweak
Primarily use callouts to edit or delete

## Slide 18: Appearances - ownership
In assemblies, the display pane shows 2 triangles
Top triangle is component appearance
Bottom triangle is part (model) appearance
An extra note about the Display Pane in assemblies

## Slide 19: Appearances - ownership
Appearance “ownership”, and how the display pane can help
An appearance is “owned” by it’s TOP MODEL.
e.g. face,feature/body apperances are always owned by the part they are contained in.
If you add/delete a face appearance, you have MODIFIED that part.
In multi-level assemblies, component appearances may be owned by sub-assembly models!
You can tell by the faded/greyed hue of items in the taskpane.
Put another way, a component can be a component, in more than one assembly. Know which “owning assembly” the component appearance belongs to.

## Slide 20: Appearances - ownership
Appearance “ownership” and callouts
  Callouts cannot show N-instances deep of an assembly structure
  Component displayed at top of a callout is state of the component as seen by the currently opened assembly
Lighter<1>-Part016<1> doesn’t have a component level override, owned by the top level assembly in this case. Callout is correct.
The component override is owned by the Lighter1 sub-assembly itself. Display pane is correct.
To remove it, means modifying Lighter.sldasm. So we need to edit or open Lighter1

## Slide 21: Texture and Decal mapping – mapping types explained
XY Projection
XZ Projection
YZ Projection
Automatic (box) Mapping
Surface Mapping

## Slide 22: Texture and Decal mapping – mapping types explained
Spherical Mapping
Cylindrical Mapping
Multiple combined mapping types
Cylindrical
Spherical
Projection XZ
Projection XY

## Slide 23: Texture and decal mapping – using the manipulator
The same manipulator is used for textural appearances and decals
width
height
height/width handles
horizontal direction
vertical direction
rotation handle

## Slide 24: Decal mapping – some specifics
Decals don’t have automatic/box mapping
Decals default to label mapping on most surfaces
  Label Mapping works best on the simpler cases when spanning multiple faces (typically having linear edges)
  Think of a label mapped decal as a sticker. If the sticker would “crinkle” when going over the surface, label mapping is not a good choice.
When dropped on a parametrically spherical or cylindrical surface, decals will automatically choose spherical or cylindrical mapping accordingly

## Slide 25: Texture and decal mapping - example

## Slide 26: RealView and lights
Only first Light (Directional) source projects RealView shadow.
Self shadows
Enabled

## Slide 27
RealView and lights
Notes: 27
RON
“Garage” scene which has walls…
I manually resized the scene to make it smaller and reposition the light to cast a long shadow to illustrate the point here
NOTE the shadows on the walls

## Slide 28
RealView and lights
Notes: 28
RON
Removing the walls, we can still see the shadow on the floor

## Slide 29
RealView and lights
Notes: 29
RON
Here it is with just a “shadow” floor. Why is it important to understand this?

## Slide 30
RealView and lights
Notes: 30
RON
In this case, you got a weird looking shadow.
When the scene is added, the floor gets auto-positioned based on nearest XY, YZ, XZ plane. But the locked directional light means that now the light is “lower” (in this case) resulting in a very long casted shadow.

## Slide 31
RealView and lights
Notes: 31
RON
To fix it… I can simply edit the light and drag it to a more appropriate position.

## Slide 32
RealView and lights
Notes: 32
RON
Why locked?
Floating lights “dance” and it can be cool, but also “distracting”
Show videos of locked vs unlocked behavior…

## Slide 33: 2011: BIG CHANGES, BIG IMPROVEMENTS
Display Manager for all users
Decals, custom appearances, & custom scenes for all users
Simplified, unified, illumination controls
Enhanced RealView control for all appearances
PhotoWorks is gone, PhotoView 360 is in
  Added features previously missing PhotoView 360
    Animations, Direct lighting, direct caustics , contours, scheduled renders
  Retained simplified options, controls, ease-of-use, and performance of PhotoView 360

## Slide 34: 2011 General Changes – Display Manager
Display Manager – available to all users
Appearances
Decals
Scenes, Lights, and Cameras

## Slide 35: 2011 General Changes – Display Manager
Display Manager with PhotoView added-in
PhotoView Options
Scene Illumination
Physical Light states

## Slide 36: 2011 General Changes – Decals and Scenes
Decals
  No need for SolidWorks Office Professional license to use decal functionality
Scenes
  Simplified from PhotoWorks scenes (trimmed the fat)
    Removed walls/ceilings (rooms), depth cue, global lighting controls…
  Enhanced previous core SolidWorks scene property manager
    Full background controls
    Floor shadow/reflection toggles
  No need for SolidWorks Office Professional license to save/re-use custom scenes

## Slide 37: 2011 General Changes – Scenes

## Slide 38: 2011 General Changes – Custom appearances
Custom appearances can now be saved and reused by all users
  No need for SWOP

## Slide 39: RealView Changes – Illumination Controls
Consolidation of previous illumination controls
PW illumination controls consisted of many different “sets”
  Illumination “types” – anisotropic, dielectric, plastic, etc.  different sets of controls
PV illumination controls
  Simplified set for all appearances
  Same set used in OGL, RV, and PV

## Slide 40: RealView Changes – Illumination Controls
Previously, some illumination controls worked in OGL. Some did in RealView but only for select appearances.
NOW.. They all work in RV

## Slide 41: RealView Changes – Surface Finish Controls
All predefined bump maps can be used in RealView
Including custom “From File” bump maps
Limit 1 bump map per appearance
  Ie Appearance with a predefined bump, cannot have another bump added (only swapped).
Originally pre-defined surface finish (may be nothing). Like a “reset”
Custom bump map
Other predefined bump maps
No bump. Removes any predefined bump

## Slide 42: RealView Changes – Surface Finish Controls
Knurled and Dimpled provide some additional controls

## Slide 43: PhotoView 360 – some history
Released in 2009 as a companion, standalone rendering application
Remained a standalone product in 2010 alongside PhotoWorks integration
Fully integrated in 2011. Replaces PhotoWorks.
  Improved realism and performance over PhotoWorks
    Realtime preview
  Filled gaps from standalone PhotoView 360
    Animation support
    Physical light support
    Contour rendering, caustics
PhotoView 360 comes from Luxology, LLC
  Same technology that Luxology’s flagship product, Modo, is base on.
  We’ll continue to enhance PhotoView 360, but it will always remain a simpler, easier to use subset of what Modo can do.
  Strong partnership with Luxology
    If you need full/complete Modo capabilities, purchase Modo and read SW files directly

## Slide 44: PhotoView 360 – Derived from Modo

## Slide 45: PhotoView 360 – Derived from Modo

## Slide 46: PhotoView 360 – Derived from Modo

## Slide 47: PhotoView 360 – Derived from Modo

## Slide 48: PhotoView 360 – Derived from Modo

## Slide 49: PhotoView 360 – Derived from Modo

## Slide 50: PhotoView 360 – UI overview
Everything to this point uses core SolidWorks functionality
Enable PhotoView 360 like any other add-in
Customize Render Tools toolbar on Off by default

## Slide 51: PhotoView 360 – UI overview
Preview modes operate in “real time” updating as you continue to make most changes (adding/editing appearances, scenes, lights, camera changes)
  Delay to preview for some operations (geometry changes, switching document windows)
Separate preview window
  Good for multiple displays or large widescreen with extra real estate
  Good for keeping small window for rendering while working in SolidWorks graphics area
    Raytracing is “pixel bound”. Large window = more pixels = slower
Integrated preview works more like standalone PhotoView 360 2010
  Again, be mindful of the window size
3rd method – Integrated preview in a single viewport, of split viewports

## Slide 52: PhotoView 360 – UI overview

## Slide 53: PhotoView 360 – Additional appearance controls
Illumination controls
  Luminous intensity = actual light emitting material

## Slide 54: PhotoView 360 – Luminous Intensity = 0

## Slide 55: PhotoView 360 – Luminous Intensity = 1.7 w/srm^2

## Slide 56: PhotoView 360 – Luminous Intensity = 10 w/srm^2

## Slide 57: PhotoView 360 – Additional appearance controls
Index of refraction (IOR)
Refraction Roughness (new!)

## Slide 58: PhotoView 360 – Refraction Roughness

## Slide 59: PhotoView 360 – Additional appearance controls
Bump
  Not new/additional
    Ability to modify the bump is new over standalone PhotoView 360 2010
  Simulates a surface finish by modifying reflections and shading
  Enhanced by Luxology to provide more “displacement-like” results while maintaining performance advantages of traditional bump mapping
Displacement Mapping (new!)
  Actual geometry displacement
  Significant performance hit

## Slide 60: PhotoView 360 – Bump and Displacement

## Slide 61: PhotoView 360 – Bump and Displacement
Bump – 1mm

## Slide 62: PhotoView 360 – Bump and Displacement
Bump – 5mm
Notice the silhouette is still a smooth surface

## Slide 63: PhotoView 360 – Bump and Displacement
Displacement – 1mm
Notice the surface geometry now displaces

## Slide 64: PhotoView 360 – Bump and Displacement
Displacement – 5mm

## Slide 65: PhotoView 360 – Additional scene controls
Scene illumination controls are also made accessible from the Display Managers “Lights” folder

## Slide 66: PhotoView 360 – Physical Lights
By default, all lights are on in SolidWorks, and off in PhotoView
SolidWorks State
PhotoView State

## Slide 67: PhotoView 360 – Physical Lights
Light state and properties can be enabled in the “PhotoView” tab of the Light property manager.
  On/Off state
  Specific brightness control
    SW brightness of “0-1” has no meaning
  Shadow controls
    Soft edges on shadows
    Soft edge quality
Any physical light in PhotoView uses physically accurate “falloff”

## Slide 68: PhotoView 360 – Contours
Enabled in PhotoView options
  Contours Only
  Contours and Solid Model
  Line thickness
  Line color

## Slide 69: PhotoView 360 – Contours

## Slide 70: PhotoView 360 – Caustics
Indirect caustics – caustics from indirect (image based / HDR) lighting
Direct caustics – caustics from direct/physical lights (point, spot)
Refractive caustics – caustics resulting from refracted light through transparent objects
Reflective caustics – caustics resulting from reflected light off reflective surfaces
PhotoView 360 always gives indirect, refractive caustics
  Can be subtle, depending on the HDR environment image being used
  Currently cannot enable indirect, reflective caustics
Direct caustics (refractive and reflective) can be optionally enabled
  Requirements
    Real floor appearance (shadow catcher doesn’t receive direct caustics)
    A physical spot or point light enabled in photoview
    FINAL RENDER ONLY

## Slide 71: PhotoView 360 - Caustics
Direct caustics are enabled in PhotoView options
Recall from PhotoWorks…specify whether a given appearance cast and/or receive caustics, as well as set a physical light to cast # photon energy

## Slide 72: PhotoView 360 - Caustics

## Slide 73: PhotoView 360 - Caustics

## Slide 74: PhotoView 360 - Caustics

## Slide 75: PhotoView 360 - Caustics

## Slide 76: PhotoView 360 - Caustics

## Slide 77: PhotoView 360 - Caustics

## Slide 78: PhotoView 360 - Caustics